STE Reference Documentation, v1.00 for ST User CoverDisk

Another STE extra from Adam Greenwood

The following list is a complete reference for the STE, including 
all  new registers and variables plus original ones which are  of 
special interest on the STE.  This list is designed to be used in 
conjunction with the 'Inside the STE' series of articles.

=================
1. DMA SOUND CHIP
=================

1.1 SOUND CHIP REGISTERS:
-------------------------

$ff8900   (r/w)     enable register:
                    00 - disable sound (default state)
                    01 - enable sound, play once
                    11 - enable sound, loop forever

$ff8902   (r/w)     frame base address high
$ff8904   (r/w)     frame base addeess middle
$ff8906   (r/w)     frame base address low

$ff8908   (ro)      frame address counter high
$ff890a   (ro)      frame address counter middle
$ff890c   (ro)      frame address counter low

$ff890e   (r/w)     frame end address high
$ff8910   (r/w)     frame end address middle
$ff8912   (r/w)     frame end address low

$ff8920   (r/w)     sound mode control:
                    bit  7 6 5 4 3 2 1 
                    use  m . . . . r r
                    m - 0 = stereo mode, 1 = mono mode
                    rr - 00 = 6.258 kHz frequency
                         01 = 12.517 kHz
                         10 = 25.033 kHz
                         11 = 50.066 kHz

1.2 INTERRUPT CONTROL:
----------------------

MFP Interrupt vectors for sound control:

$134      Timer A vector
$13c      GPI(7) mono monitor detect vector

MC68901 MFP configuration registers for sound:

$fffa03   Active edge
$fffa07   Interrupt enable A
$fffa0f   Interrupt in service A
$fffa13   Interrupt mask A
$fffa19   Timer A control
$fffa1f   Timer A data

Timer A uses bit 5, GPI(7) bit 7

Shift mode register:

$ff8260   Shift mode

For interrupt at start of sample:

     Screen mode    Active edge
     -----------    -----------
     2 (mono)       Positive - or.b #$80 with edge
     0,1 (colour)   Negative - and.b #$7f with edge

1.3 VOLUME/TONE CONTROL:
------------------------

Microwire registers:

$ff8922   microwire data register
$ff8924   microwire mask register

Volume/Tone addresses and parameters:

Master Volume: 10 011 DDDDDD
Left Volume:   10 101 xDDDDD
Right Volume:  10 100 xDDDDD
Treble:        10 010 xxDDDD
Bass:          10 001 xxDDDD
Mix:           10 000 xxxxDD

Where x indicates don't care, and D is a data bit.

Volume/Tone data values:

Master Volume:      0 - 40 (0 = -80dB, 40 = 0dB)
Left/Right Volume:  0 - 20 (0 = -80dB, 20 = 0dB)
Treble/Bass:        0 - 12 (0 = -12dB, 6 = 0dB, 12 = +12dB)
Mix:                0 - 3  (0 = -12dB,  1 = Mix PSG, 2 = don't mix 
                            PSG, 3 = reserved)

=====================
2. VIDEO SHIFTER CHIP
=====================

2.1 EXTENDED COLOUR PALETTE
---------------------------

$ff8240 - $ff835e   rgb colour registers

colour word:

bit       11 10  9  8    7  6  5  4    3  2  1  0
meaning   R0 R3 R2 R1   G0 G3 G2 G1   B0 B3 B2 B1

Rx = Red , Gx = Green, Bx = Blue
where x = bit no.

Giving the following colour range:

intensity level  0 1 2 3 4 5 6 7 8 9 a b c d e f
4-bit nibble     0 8 1 9 2 a 3 b 4 c 5 d 6 e 7 f

2.2 SCREEN ADDRESS REGISTERS
----------------------------

$ff8201   screen base address high    (vbasehi)
$ff8203   screen base address middle  (vbasemd)
$ff820d   screen base address low     (vbaselo)

2.3 HORIZONTAL SCROLLING
------------------------

$ff820f   over-length line width      (linewid)
$ff8265   pixel scroll offset         (hscroll)

===============
3. BLITTER CHIP
===============

3.1 BLITMODE TOS CALL
---------------------

Xbios call 64 - Blitmode

          flag.w    Status
                    bit 0 - enable
                     1-14 - reserved
                       15 - 0 = clear
                            1 = get 
Blitmode  64
          trap #14  (tidy #4)

Returns d0.w:
          Bit 0 - set (Blit on)
              1 - set (If blitter present)
           2-14 - reserved
             15 - clear


3.2 BLITTER CHIP REGISTERS
--------------------------

Address   Length    Description

$ff8a00   .w        Half tone RAM 0
$ff8a02   .w        Half tone RAM 1
$ff8a04   .w        Half tone RAM 2
$ff8a06   .w        Half tone RAM 3
$ff8a08   .w        Half tone RAM 4
$ff8a0a   .w        Half tone RAM 5
$ff8a0c   .w        Half tone RAM 6
$ff8a0e   .w        Half tone RAM 7
$ff8a10   .w        Half tone RAM 8
$ff8a12   .w        Half tone RAM 9
$ff8a14   .w        Half tone RAM 10
$ff8a16   .w        Half tone RAM 11
$ff8a18   .w        Half tone RAM 12
$ff8a1a   .w        Half tone RAM 13
$ff8a1c   .w        Half tone RAM 14
$ff8a1e   .w        Half tone RAM 15

$ff8a20   .w        Source x increment
$ff8a22   .w        Source y increment
$ff8a24   .w        Source address high word
$ff8a26   .w        Source address low word

$ff8a28   .w        Endmask 1           
$ff8a2a   .w        Endmask 2
$ff8a2c   .w        Endmask 3

$ff8a2e   .w        Destination x increment
$ff8a30   .w        Destination y increment
$ff8a32   .w        Destination address high word
$ff8a34   .w        Destination address low word

$ff8a36   .w        x count
$ff8a38   .w        y count

$ff8a3a   .b        Half tone operation (HOP)
$ff8a3b   .b        Logical operation (OP)

$ff8a3c   .b        bits 0-3 - Line number
                    bit  5   - Smudge
                    bit  6   - HOG
                    bit  7   - Busy

$ff8a3d   .b        bits 0-3 - Skew
                    bit  6   - NFSR
                    bit  7   - FXSR

3.3 LOGICAL OPERATIONS 
----------------------

OP register

Value     Result

0         all 0 bits
1         source AND destination
2         source AND NOT destination
3         source
4         NOT source AND destination
5         destination
6         source XOR destination
7         source OR destination
8         NOT source AND NOT destination
9         NOT source XOR destination
10        NOT destination
11        source OR NOT destination
12        NOT source
13        NOT source OR destination
14        NOT source OR NOT destination
15        all 1 bits

3.4 HALF TONE RAM OPERATIONS
----------------------------

HOP register

value     operation

0         all 1 bits
1         half tone RAM
2         source
3         source AND half tone RAM

===================
4. CONTROLLER PORTS
===================

4.1 JOYSTICK ADAPTER
--------------------

Pin connections for two joysticks into one STE controller port.

Port A/B  Joystick 0/1  Joystick 2/3

1             1             -   
2             2             - 
3             3             -
4             4             -
5             -             -
6             6             -
7             7             7
8             -             -
9             8             8
10            -             6
11            -             1
12            -             2
13            -             3             
14            -             4
15            -             -

4.2 CONTROLLER PORT REGISTERS
-----------------------------

Port A joysticks are 0 and 2, Port B are 1 and 3
Paddles are 0 for Port A, 1 for Port B

$ff9200   xxxx xxxx xxxx 3120      Fire Buttons

$ff9202   UDLR UDLR UDLR UDLR      Joystick Direction
          Joy3 Joy2 Joy1 Joy0

$ff9210   xxxx xxxx nnnn nnnn      Paddle 0 X
$ff9212   xxxx xxxx nnnn nnnn      Paddle 0 Y
$ff9214   xxxx xxxx nnnn nnnn      Paddle 1 X
$ff9216   xxxx xxxx nnnn nnnn      Paddle 1 Y

$ff9220   xxxx xxnn nnnn nnnn      Light Pen/Gun X
$ff9222   xxxx xxnn nnnn nnnn      Light Pen/Gun Y

UDLR for joysticks 0 and 1 are bi-directional

=============
5. COOKIE JAR
=============

5.1 COOKIE POINTER
------------------

Cookie jar pointer address

$5a0  L   p_cookies      Pointer to cookie jar

5.2 COOKIE NAMES AND MEANINGS
-----------------------------
Official Atari Cookies:

Name:     _CPU
Values:   The  number here is the decimal value of the  last  two 
digits of the processor present in the machine,  indicating which 
CPU of the 68000 family it is:  00, 10, 20, 30. For instance, the 
value 30 indicates a 68030 processor.

Name:     _VDO
Values:   The  high word of this cookie contains a number from  0 
to 2 which indicates what type of video shifter is fitted:
          0 - Standard ST video shifter
          1 - STE video shifter
          2 - TT Graphic Chip
          3 - Falcon?

Name:     _SND
Values:   Here  it  is  the bits which tell us  about  the  sound 
hardware.  Bit  0  set indicates the presence of a  Yamaha  sound 
chip, bit 1 of the DMA sound chip.

Name:     _MCH
Values:    This cookie also uses the high word,  so that the  low 
word can be used for version changes, and the value describes the 
overall machine:
          0 - Standard ST
          1 - STE
          2 - Mega ST
          3 - TT


Name:     _SWI
Values:   This  cookie is used to indicate the positions  of  the 
configuration  switches on Mega STEs and TTs.  At  present  these 
switches are unused.

Name:     _FRB
Values:   This longword value will be the address of the fast RAM 
buffer,  or 0 if no fast RAM buffers are fitted.  This cookie  is 
not found on standard STs or STEs.