Macro library usage definitions
    Page 1


    
    
                                 MACRO usages
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Data placement      *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    MEM
    Developmental ORG
    
    [When developing programs that will  run in 16K, it is  advantageous to
    locate them above  DOS (typically  $4000 to $7FFF)  although they  will
    ultimately run  at around  $600 or  so. This  makes it  easier to  load
    modules to  be written  to  boot disks  etc. without  using  a separate
    utility.]
    
    During development, set OFFSET = $4000 and DEVELOP  = OFFSET. This will
    put code in high  memory and execute it  there. On the final  assembly,
    set DEVELOP = 0. This will assemble code  as though it would run in low
    memory, but write  the binary file  to load the  program image to  high
    memory.
    
    Usage:
             MEM       address
    
    Example:
             MEM       $800
    
    yields:
      given:(DEVELOP = $4000)
            (OFFSET = 0)
    
             ORG       $4800
             LOC       $800
    
    
    USEBEG
    My "USE"
    
    [The AMAC USE command simply doesn't work. This  crude kludge saves the
    current LOC and ORG counters to allow temporary  re-placement of inline
    code. This  uses the  MEM  macro to  update ORG  and  LOC according  to
    developmental variables. Also uses  local labels, so USEBEG  and USEEND
    must both reside in the same PROC module, and cannot be nested.]
    
    Usage:
             USEBEG    address
    
    Example:
             USEBEG    $3000
    
    yields:






    Macro library usage definitions
    Page 2


    
    :otmp    SET       *O
    :ltmp    SET       *L
             MEM       $3000
    
    
    USEEND
    Recovery from USEBEG
    
    Restores ORG and LOC counters after temporary resetting via USEBEG.
    
    Usage:
             USEEND    (no operand)
    
    Produces:
             ORG       :otmp
             LOC       :ltmp
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   8-bit arithmetic    *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    ADD
    Add WITHOUT carry
    
    Usage:
             ADD       #constant
             ADD       address
             ADD       address,X
             ADD       address,Y
    
    Example:
             ADD       TROGS,Y
    
    yields:
             CLC
             ADC       TROGS,Y
    
    
    SUB
    Subtract WITHOUT carry
    
    Usage:
             SUB       #constant
             SUB       address
             SUB       address,X
             SUB       address,Y
    
    Example:
             SUB       #$30
    
    yields:
             SEC






    Macro library usage definitions
    Page 3


             SBC       #$30
    
    
    DIV
    Divide A by a power of 2
    
    Usage:   DIV       power of 2
    
    Example:
             DIV       8
    
    yields:
             LSR       A
             LSR       A
             LSR       A
    
    
    MUL
    Multiply A by a power of 2
    
    Usage:   MUL       power of 2
    
    Example:
             MUL       16
    
    yields:
             ASL       A
             ASL       A
             ASL       A
             ASL       A
    
    
    BMP
    Add constant to byte at address
    
    Usage:   BMP       address,constant
             BMP       address,X,constant
             BMP       address,Y,constant
    
    Example:
             BMP       BORT,125
    
    yields:
             LDA       BORT
             CLC
             ADC       #125
             STA       BORT
    
    
    BAK
    Subtract constant from byte at address
    
    Usage:   BAK       address,constant
             BAK       address,X,constant
             BAK       address,Y,constant
    






    Macro library usage definitions
    Page 4


    Example:
             BAK       GLERX,Y,$42
    
    yields:
             LDA       GLERX,Y
             SEC
             SBC       #$42
             STA       GLERX,Y
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   16-bit arithmetic   *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    ADW
    Add two words at addresses and store at a third
    
    Usage:   ADW       address 1,address 2,dest. address
    
    Example:
             ADW       WREG,TEDUK,WREG
    
    yields:
             LDA       WREG
             CLC
             ADC       TEDUK
             STA       WREG
             LDA       WREG+1
             ADC       TEDUK+1
             STA       WREG+1
    
    
    SBW
    Subtract two words at addresses and store at a third
    
    Usage:   SBW       address 1,address 2,dest. address
    
    Example:
             SBW       VEP,QWERTY,GADS
    
    yields:
             LDA       VEP
             SEC
             SBC       QWERTY
             STA       GADS
             LDA       VEP+1
             SBC       QWERTY+1
             STA       GADS+1
    
    
    BMPW
    Add a constant to a word at address
    
    Usage:   BMPW      address,constant






    Macro library usage definitions
    Page 5


    
    Example:
             BMPW      KLUT,$4258
    
    yields:
             LDA       KLUT
             CLC
             ADC       #$58
             STA       KLUT
             LDA       KLUT+1
             ADC       #$42
             STA       KLUT+1
    
    
    BAKW
    Subtract a constant from a word at address
    
    Usage:   BAKW      address,constant
    
    Example:
             BAKW      NATHIL,HPOS
    
    yields:
             LDA       NATHIL
             SEC
             SBC       #LOW HPOS
             STA       NATHIL
             LDA       NATHIL+1
             SBC       #HIGH HPOS
             STA       NATHIL+1
    
    
    INW
    Increment a word at address
    
    Usage:   INW       address
    
    Example:
             INW       GOLD
    
    yields:
             INC       GOLD
             BNE       LABEL
             INC       GOLD+1
    LABEL    =         *
    
    
    DEW
    Decrement a word at address
    
    Usage:   DEW       address
    
    Example:
             DEW       ZUGG
    
    yields:






    Macro library usage definitions
    Page 6


             LDA       ZUGG
             BNE       LABEL
             DEC       ZUGG+1
    LABEL    DEC       ZUGG
    
    
    
                          *=*=*=*=*=*=*=*=*=*=*=*=*=*
                          *   Conditional branches  *
                          *=*=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    Usage for all branch instructions:
             XXX       address
    
    
    BGE
    Branch on Greater than or Equal to
    
    BGT
    Branch on Greater than
    
    BLE
    Branch on Less than or Equal to
    
    BLT
    Branch on Less than
    
    BNZ
    Branch on Non Zero
    
    BZ
    Branch on Zero
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Conditional jumps   *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    Usage for all jump instructions:
             XXX       address
    
    
    JMI
    Jump on Minus
    
    JPL
    Jump on Plus
    
    JCS
    Jump on Carry Set
    
    JCC
    Jump on Carry Clear






    Macro library usage definitions
    Page 7


    
    JGE
    Jump on Greater than or Equal to
    
    JGT
    Jump on Greater than
    
    JLE
    Jump on Less than or Equal to
    
    JLT
    Jump on Less than
    
    JNE
    Jump on Not Equal
    
    JNZ
    Jump on Non Zero
    
    JEQ
    Jump on Equal to
    
    JZ
    Jump on Zero
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Auto decrement and  *
                           *      branches         *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    [The sequence:
    
             LDX       #value
    LABEL    ....
             DEX
             BPL       LABEL
    
    to repeat a routine "value"  number of times is used  frequently enough
    =that it warrants  special commands. These  macros are smart  enough to
    determine whether to  branch or  jump, but not  smart enough  to branch
    forward.]
    
    
    DXPL
    Decrement X and Branch on Plus
    
    Usage:   DXPL      address
    
    Example:
             DXPL      LABEL
    
    yields:
             DEX






    Macro library usage definitions
    Page 8


             BPL       LABEL
    
    
    DYPL
    Decrement Y and Branch on Plus
    
    Usage:   DYPL      address
    
    
    DCPL
    Decrement a byte at address and Branch on Plus
    
    Usage:   DCPL      address,branch address
    
    Example:
             DCPL      SAXTRY,LABEL
    
    yields:
             DEC       SAXTRY
             BPL       LABEL
    
    
    DXNZ
    Decrement X and Branch on Non Zero
    
    Usage:   DXNZ      address
    
    
    DYNZ
    Decrement Y and Branch on Non Zero
    
    Usage:   DYNZ      address
    
    
    DCNZ
    Decrement a byte at address and Branch on Non Zero
    
    Usage:   DCNZ      address,branch address
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Comparisons         *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    CPI
    Compare a byte at address with a constant
    
    Usage:   CPI       address,constant
             CPI       address,X,constant
             CPI       address,Y,constant
    
    Example:
             CPI       FRUITY,X,$80
    






    Macro library usage definitions
    Page 9


    yields:
             LDA       FRUITY,X
             CMP       #$80
    
    
    CPB
    Compare two bytes at addresses
    
    Usage:   CPB       address 1,address 2
    
    Example:
             CPB       SWEET,SOUR
    
    yields:
             LDA       SWEET
             CMP       SOUR
    
    
    CPW
    Compare two words at addresses
    
    Usage:   CPW       address 1, address 2
    
    Example:
             CPW       LEFT,RIGHT
    
    yields:
             LDA       LEFT+1
             CMP       RIGHT+1
             BNE       LABEL
             LDA       LEFT
             CMP       RIGHT
    LABEL    =         *
    
    
    CPIW
    Compare a word at address with a 16-bit constant
    
    Usage:   CPIW      address,constant
    
    Example:
             CPIW      ZIPPER,14352
    
    yields:
             LDA       ZIPPER+1
             CMP       #HIGH 14352
             BNE       LABEL
             LDA       ZIPPER
             CMP       #LOW 14352
    LABEL    =         *
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Memory Manipulation *
                           *=*=*=*=*=*=*=*=*=*=*=*=*






    Macro library usage definitions
    Page 10


    
    
    STB
    Store a byte at an address
    
    Usage:   STB       constant,address
             STB       constant,address,X
             STB       constant,address,Y
    
    Example:
             STB       $52,ICCMD,X
    
    yields:
             LDA       #$52
             STA       ICCMD,X
    
    
    MVB
    Move a byte from one address to another
    
    Usage:   MVB       address 1,address 2
             MVB       address 1,X,address 2
             MVB       address 1,Y,address 2
             MVB       address 1,address 2,X
             MVB       address          1,address 2,Y
             MVB       address1,X,address2,X
             MVB       address1,X,address2,Y
             MVB       address1,Y,address2,X
             MVB       address1,Y,address2,Y
    
    
    Example:
             MVB       JUICE,Y,PULP
    
    yields:
             LDA       JUICE,Y
             STA       PULP
    
    
    MVW
    Move a word from one address to another
    
    Usage:   MVW       address 1,address 2
    
    Example:
             MVW       FRUM,TOO
    
    yields:
             LDA       FRUM
             STA       TOO
             LDA       FRUM+1
             STA       TOO+1
    
    
    STW
    Store a 16-bit constant at an address






    Macro library usage definitions
    Page 11


    
    Usage:   STW       constant,address
    
    Example:
             STW       DLADDR,SDLSTL
    
    yields:
             LDA       #LOW DLADDR
             STA       SDLSTL
             LDA       #HIGH DLADDR
             STA       SDLSTL+1
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *  Stack Manipulation   *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    Usage for all stack instructions:
             XXX       (no operands...)
    
    PHR / PLR
    Push (Pull) all registers
    
    [NOTE: PHX/PHY/PLX/PLY use the A  register, so make sure it's  saved or
    pushed before calling.]
    
    PHX / PLX
    Push (Pull) X register
    
    PHY / PLY
    Push (Pull) Y register
    
    
    
                           *=*=*=*=*=*=*=*=*=*=*=*=*
                           *   Miscellaneous       *
                           *=*=*=*=*=*=*=*=*=*=*=*=*
    
    
    ATTRACT
    Color-shift A register for attract mode
    
    Usage:   ATTRACT   (no operand)
    
    Produces:
             EOR       COLRSH
             AND       DRKMSK
    












    Macro library usage definitions
    Page 12


    
    
    
                              Files MACRO usages
    
    
    
    
    FCLOSE
    Closes an open  file. All that  is required is  a channel number.  If X
    already holds the proper channel,  you can specify "X" as  the channel,
    and the macro will skip the LDX part. (This is true for any of the file
    commands.)
    
    Usage:
             FCLOSE    channel
    
    Example:
             FCLOSE    6
    
    closes channel #6.
    
    SAME AS BASIC:     CLOSE #channel
    
    
    FOPEN
    Opens a device to a specified channel. "Devname"  should be the address
    of the filename in ASCII,  terminated by an EOL. Aux1  and Aux2 must be
    specified.
    
    Usage:
             FOPEN     channel,devname,aux1,aux2
    
    Example:
             FOPEN     4,RNAME,13,0
             ...
    RNAME    DB        'R2:',$9B
    
    opens R2: to channel 4 for concurrent I/O.
    
    SAME AS BASIC:     OPEN #channel,aux1,aux2,"devname"
    
    
    FGET
    Gets characters or a record from a designated channel. "Type" is either
    CHR for characters or REC  for record. "Address" is the  address of the
    buffer to receive  the data. "Length"  is optional. For  characters, it
    should equal the number of characters to fetch; for a record, it is the
    maximum number  of  characters  to  get (string  is  returned  only  on
    [RETURN].) If  "length" is  not  specified, it  is arbitrarily  set  to
    $FFFF.
    
    Usage:
             FGET      channel,type,address[,length]
    
    Example:






    Macro library usage definitions
    Page 13


             FGET      2,CHR,GETBUF,16
             ...
    GETBUF   DS        16
    
    gets 16 characters from channel #2.
    
    FGET channel,CHR,address,length
    SAME AS BASIC:     FOR NC=1 to length
                       GET #channel,var
                       address$(NC,NC)=chr$(var)
                       NEXT NC
    
    FGET channel,REC,address,length
    SAME AS BASIC:     INPUT #channel,address$
    
    
    FGET1
    A special case  of FGET  to get  1 character.  No buffer  is specified,
    because the character is returned in the Accumulator.
    
    Usage:
             FGET1     channel
    
    Example:
             FGET1     2
    
    gets 1 character in A from channel #2.
    
    SAME AS BASIC:     GET #channel,var
    
    
    FPUT
    Same as FGET, except to put characters to a channel.
    
    Usage:
             FPUT      channel,type,address[,length]
    
    Example:
             FPUT      0,REC,STRING
             ...
    STRING   DB        'HI THERE, LOUISE!',EOL
    
    puts the string "HI THERE,  LOUISE!"<cr> to the screen editor  (channel
    #0). Note: In most cases,  the screen editor is always  open to channel
    #0 and can be used in the DOS/BASIC  environment without having to OPEN
    it.
    
    FPUT channel,CHR,address,length
    SAME AS BASIC:     FOR NC=1 TO length
                       var=ASC(address$(NC,NC))
                       PUT #channel,var
                       NEXT NC
    
    FPUT channel,REC,address,length
    SAME AS BASIC:     PRINT #channel;address$
    






    Macro library usage definitions
    Page 14


    
    FPUT1
    Same as FGET1, except to put one character in the Accumulator.
    
    Usage:
             FPUT1     channel
    
    Example:
             FPUT1     4
    
    sends the value in A to channel #4.
    
    SAME AS BASIC:     PUT #channel,var
    
    
    FSPEC
    "XIO" type command. "Command" is command number. Aux1  and Aux2 must be
    specified.
    
    Usage:
             FSPEC     channel,command,devname,aux1,aux2
    
    Example:
             FSPEC     4,35,FILNAM,0,0
             ...
    FILNAM   DB        'D2:PROGRAM.BAS',$9B
    
    unlocks "PROGRAM.BAS" on disk drive 2, using channel #4.
    
    SAME AS BASIC:     XIO command,#channel,aux1,aux2,"devname"
    
    
    FSTAT
    Get channel status.  "Devname" is  optional; if specified,  it means  a
    "special" status on an un"OPEN"ed device. "OPEN"s channel, gets status,
    and then "CLOSE"s  channel automatically. In  any case, 4  status bytes
    are returned  to DVSTAT  ($2EA) to  DVSTAT+3. See  hardware manual  for
    significance.
    Usage:   FSTAT     channel[,devname]
    
    Example:
             FSTAT     4
    
    checks for status on channel #4.
    
    SAME AS BASIC:     STATUS #channel,var