-*- Text -*-

			A65 preliminary doc

[If anyone can come up with a better name than RA65, please let me
know...]

    RA65 is the assembler that goes with CC65, although it can just as
well be used by itself.  RA65 eats 6502 assembly-language source
files, and produces relocatable object files, suitable for linking
into executables with LINK65.

When you start up RA65, it wants an optional name for the output file,
optional debugging switches, and any number of input file names.  The
input files are read in order, and an output file is written.  If no
output file is specified, the output file name will be the first input
file name, with .OBJ substituted for whatever extension was there.

Ex:

RA65 foo.m65

assembles foo.m65, producing foo.obj.

RA65 -o foo.obj foo.m65

does the same thing.

RA65 -o foo.obj defs.m65 moredefs.m65 foo.m65

This form is useful when you've got some files of equates or something
that you want to assemble your code with.

Switches:

	-O	output file name, as described above.
	
	-V	verbose.  If verbose is turned on, the assembler will
		print lines to the screen as it assembles them.

Differences between RA65 and other assemblers for the Atari:

RA65 is NOT the same sort of beast as most other assemblers for Atari
8-bitters, at least all the ones I've ever seen.  The output of this
assembler is not an executable image, but a relocatable object module.

[The format of .OBJ files is described in more detail elsewhere]

These files are essentially instructions to the linker about how to
construct the real executable.  A .OBJ file contains instructions, raw
data, specialized reference codes (things like "generate a byte that's
the hi byte of the address of symbol foo") and symbol tables.  The
symbol table contains both definitions of symbols that are defined in
this module, as "symbol _BAZ is defined as 27 bytes in from the
beginning of this module" and references to symbols not defined in
this module, as "value of symbol _QUUX + 20".

There are some differences in how you use this assembler, compared to
traditional ones.

  o	No ORG or *= directive.  It's meaningless in this kind of
	assembler; as the starting address, like all other addresses,
	is determined at link time, not assemble time.

  o	Undefined symbols.  These are errors in an ordinary assembler,
	but are not necessarily errors here.  Undefined symbols are
	assumed to be references to something to be defined elsewhere.
	Note!  Since the default way to reference a symbol as a 16-bit
	quantity, addresses on page 0 must be defined properly before
	you reference them, otherwise they'll error, or at least
	generate incorrect code.

  o	No symbol for the current PC.  This is really a bug, as it's
	possible to make it work, I've just never gotten around to it.
	This means you can't say things like
	
	sym	=	*
	
	when defining symbols; you should use the 
	
	sym:
	
	form instead.

Special ops:

RA65 understands a couple of other things that aren't usually done in
traditional assemblers.  The following pseudo-ops are used by CC65, in
particular:

	ldax	#foo		This loads the AX pair with the
				constant value foo, by generating
				an lda and an ldx.  It will not
				work with non-constants.

	lbne	labl		This is a long-branch pseudo-op.
				It generates a bne if the label
				can be reached that way, otherwise
				it generates a beq *+5 followed by
				a jmp to the label.  There are similar 
				ones for lbeq, lbcc etc.

Other stuff:

RA65 understands the following pseudo-ops:

	.globl	<sym>		Define or reference a global symbol.
				used as:
				
					.globl	foo
	
	.word	<values>	Generate one or more 16-bit values.
				Values can be constants, expressions,
				symbol references etc.  Values are
				separated by commas.
	
	.byte	<values>	Generate one or more 8-bit values.
				Similar to above.

	.blkb	n		Generate n bytes of empty space.

	=			Set the value of a symbol.  Used as:

				foo = 3

[There's more; finish later]


Command lines:

Like all the members of the CC65 family, RA65 can either grok command
lines as used by Spartados and DOS XL, or prompt for its command line.
If no command line is given, or you're running something that doesn't
do command lines, RA65 will prompt, as

RA65>

You're then expected to type in the rest of the command line.  Ex:
under Spartados, if you typed

RA65 -v foo.m65

you get the same effect under DOS 2.5 by starting up RA65, then at the
RA65> prompt, typing

-v foo.m65