Sb: #Trackball InfoFm: Frank Hausman 71251,2002Atari TRAKBALL:  In TRAKBALL mode.    Here's what I've learned about thedata from TRAKBALL mode:    Bit    Function     3     Clock for vertical motion     2     Direction:  0=up, 1=down     1     Clock for horizontal motion     0     Direction:  0=left, 1=rightIt's a good idea to sample the trackball VERY FREQUENTLY to avoid missingclock transitions, and causing non-linear responses.