T R A N S K E Y 
                              BY: MICRO SOLUTIONS
                                  VERSION 1.1
                       FOR THE ATARI 400/800/XE/XL SERIES

                              - Revised 6/12/90 -



PRODUCT DESCRIPTION:


    The  main  emphasis  of  this  product  is to provide a means of utilizing a
better quality keyboard with the Atari than the one originally provided.

    Since  IBM style keyboards have become so plentiful and are made in numerous
configurations, it is the keyboard of choice. This gives the added flexibilty of
locating  the  keyboard  where  you want it, independent of the computer and its
associated  peripheral  equipment.  Also,  due  to the additional function keys,
cursor  keys,  ect.,  several  new  features  are  provided  that  could  not be
implemented  by  the  original  Atari  keyboards. One of the most interesting of
these  is  the  ability  to send out full commands (BASIC & MAC65) with a single
keypress.  This  and  many  other  features  will be covered in greater detail a
little  later  on. For now, let's look at what TRANSKEY is from a hardware point
of view and what is involved in installing it.

THE HARDWARE


    TRANSKEY  is  a microprocessor based translater board measuring aproximately
2.5  x  3.5  inches and is designed to fit underneath the RF shield on the Atari
motherboard.  The  TRANSKEY board is provided with double sided tape attached to
the  solder  side  and  is  meant  to  be  placed  in a location where it can be
sandwiched  between  the  shield  and  the  motherboard.  The location will vary
depending on what model of computer it is installed in. On the 1200XL it will be
necessary to either cut the RF shield or not use it, since there is virtually no
room underneath it.

    On  the  400/800  and  all socketed XL models, the TRANSKEY derives its main
communication  and  power  from  the  Atari  via  a  small piggy-back board that
attaches  to  TRANSKEY with a ribbon cable. This piggy-back board is designed to
be  plugged  into  the  socket  where POKEY (Atari Part# C012294) would normally
reside,  with  POKEY  then  plugged  into  the  piggy-back board to complete the
installation.  On  the  unsocketed XE series machines, the installation requires
soldering directly to the POKEY chip.

    To  fully  complete  the  installation,  assuming  that  one  wishes to have
START,SELECT,OPTION,RESET  available from the remote keyboard, the attachment of
4 jumper wires is required. Three of these wires go to a single chip called CTIA
or  GTIA  (Atari  part#  C014805)  to  tap into the option select circuitry. The
attach  point for the 4th wire for Reset varies depending on the computer model.
Generally,  to  install  these jumpers, it merely requires pulling a chip out of
its socket, inserting the bared end of the jumpers into the appropriate holes in
the socket, and then re-inserting the chip that was removed. On the XE series it
isn't possible to remove the chips, so these jumpers will have to be soldered in
place.

    With  TRANSKEY installed, all normal operations of the Atari are unimpaired,
including  the  use  of  the stock Atari keyboard. However, with TRANSKEY and an
external  IBM  style  keyboard attached, there will no longer be any need to use
the stock keyboard except for the following conditions:

    When  Cold-Booting  from  cassette  tape, it will only work by pushing START
from the stock keyboard prior to engaging power.

    On  XL/XE machines to disable Basic on Cold-Boot, it will still be necessary
to  push  OPTION  on the stock keyboard (See section 'Other Special Keys' page#3
for a way to disable basic after Disk boot-up).

    The  reason for this is that for the first couple seconds after powering up,
the  IBM  style  keyboards usually run a self-test which basically doesn't allow
for  proper recognition of a key pressed during this time. Since the Atari looks
for  these  special key presses to occur very soon after the power is turned on,
it  will  fail  to  see these with the IBM keyboard and instead just do a normal
Cold Start.

    The  IBM  keyboard is connected by means of a 5 pin DIN inline jack attached
by  a  small  ribbon cable to the TRANSKEY main board. This ribbon can be routed
through  an  existing hole or slot on the computer's case, by unplugging it from
the  Transkey  board  and  then reconnecting it when done. For those of you that
prefer  to  permanently mount this jack, it is available as a chassis style jack
with mounting hardware, requiring the drilling of 3 holes in the computer's case
(specify when ordering).

FEATURES


    With  either  an  XL  or  XE  computer, almost full use of all the extra key
functions  on  the IBM keyboard are implemented. This includes single key cursor
movement,  Home  cursor,  End  of  page  cursor, and Insert/Delete modes. Also a
special  Cursor  Left Page/Right Page is available by pressing Page Up/Page Down
respectively.  On  a  400/800  machine  the  page  movement  functions  are  not
recognized, although all others are.

    These  functions  are directly accessable from the number pad after powering
up  the  system  (default  mode).  If  you want to use the number pad for number
entry,  simply  press  the NUMLOCK key. These functions will still be available,
but  will  now  require  the  use of the Control key to initiate. If you want to
restore  the  default  condition (single keypresses), just press the NUMLOCK key
once more (pressing NUMLOCK toggles between the two modes).

    The  Home  key  has yet another use, when pressed with the Shift key it will
both  home the cursor and clear the screen. This is the same as Shift-CLEAR on a
stock  Atari  keyboard.  Pressing  the Escape key prior to this combination will
still print the curved arrow symbol like the stock system.

    The  Insert and Delete keys when pressed with Shift, will perform whole line
insertions or deletions.

    Control/Shift  (C/S)  equivalents for the arrow keys are provided by the IBM
keyboards  arrow  keys in like manner to the Atari keyboard. The C/S '>' and C/S
'<'  characters  are  produced  by the C/S INSERT and C/S DELETE keys of the IBM
keyboard (These are all available whether in a NUMLOCK or UN-NUMLOCKED state).

    If  a  101  key  Enhanced  keyboard is being used, the extra cursor control,
Insert  and  Delete  keys  will  work  exactly  the  same  as  their  number pad
counterparts.

    Perhaps,  the  nicest features are the indication of CapsLock and NumLock by
LED indicator lights on IBM style keyboards, that are so equipped.


The Function Keys:


    On an XL or XE series machine Control-F1 through Control-F5 will provide the
following special functions:

Control-F1     Disables the keyboard (both stock an
               external) and until pressed again, all
               keys will be ignored by the computer.

Control-F2     Disables DMA. Pressing this will cause
               the screen to go black until any other
               key is pressed. While the screen is
               black, processing time is accelerated
               by 30%.

Control-F3     Disables the audible keyboard click
               when a key is pressed, pressing it
               again will re-enable the click sound.

Control-F4     Toggles between International symbols
               and standard graphics symbols on the
               screen.

Control-F5     This acts as the HELP key, since there
               isn't one on most IBM keyboards.


On all other machines, 400/800's included, Control-F6 through Control-F8 provide
these additional functions:


Control-F6     This acts as the Inverse Video key.

Control-F7     Selects the BASIC macro table.

Control-F8     Selects the MAC65 macro table.


    The  last  two  keys  (Control-F7  and Control-F8) control possibly the most
interesting added feature of the new keyboard; the ability to send out an entire
string  of  characters  with one single keystroke (Macros). Built in to TRANSKEY
are  two  predefined  tables  of some commonly used commands for either BASIC or
MAC65  Assembly  languages. These are sent by pressing F1 through F8.  Depending
upon  whether Control-F7 or Control-F8 was last pressed, they will output either
the  BASIC  macro or the MAC65 macro (defaults to BASIC on power-up). Below is a
list of the supplied macro commands.


                                 --- MACROS ---

                     BASIC                           MAC65

               F1   LIST <CR>                    LIST <CR>
               F2   RUN <CR>                     ASM,#-,#D:
               F3   LOAD"D:                      LOAD#D:
               F4   SAVE"D:                      SAVE#D:
               F5   ?PEEK(                       FIND/
               F6   POKE                         REP/
               F7   SAVE"D:BACK <CR>             SAVE#D:BACK <CR>
               F8   ?FRE(0) <CR>                 SIZE <CR>


    Note:  <CR>  stands for Carriage Return. Commands with this as a suffix will
be  executed  immediately.  F7 is a way to easily save a back-up of whatever you
are working on to disk (under the name 'BACK') with a single keystroke.


    Function  keys  F9  through  F12  (F11 & F12 available on Enhanced keyboards
only) are used as option select keys.

            F9 = START     F10 = SELECT   F11 = OPTION   F12 = HELP


    The  ALTERNATE (ALT) key will also function as the OPTION key and the SYSREQ
key will also act as a HELP key (as well as Control-F5).


OTHER SPECIAL KEYS

    The  key  with  the  (~)  and  (`) symbols on it (normally on the upper left
corner)  acts  as  an  extra  Escape  key, a more comfortable location for Atari
computer  users.  Since  these  symbols are not directly available on the Atari,
this key now has a practical use.

    The  key marked PRINT SCREEN (or Shift *) when pressed will output an unused
character  on  the keyboard matrix. When PEEKing location 764, pressing this key
will produce the number 36 (HEX $24). This in itself isn't very useful, but with
a  little  ingenuity on the user's part, this key could be looked for and caused
to activate a screen printing program.

    The  Control-SCROLL key combination will actually be recognized as the Break
key  to  the Atari computer (on most 84 key keyboards this key is also labled as
break).

    If  the Control, ALT, and DELETE keys are pressed together, this will result
in  a System Reset (assuming the Reset jumper wire was installed). Releasing the
DELETE  key  first,  prior  to  Control  and  ALT, will usually result in a Disk
re-boot  with Basic disabled. Releasing the ALT key first, prior to DELETE, will
result in a normal Reset with Basic enabled.

    If  you  are  using  a BTC series keyboard, the extra key labeled MACRO will
produce  a  simultaneous  Shift-Control action in combination with any other key
pressed.  Several  programs  recognize  this as a send macro string function. Of
course, on keyboards without this key the normal Shift-Control combination would
be used instead.

    Keys not utilized are: SCROLL LOCK and the combination PAUSE/BREAK key found
only on Enhanced keyboards.


SOFTWARE COMPATABILITY

    TRANSKEY  is  an  external independent device, having it's own processor and
memory. By design it emulates a piece of hardware, the stock Atari keyboard.  To
the  Atari computer, signals coming from TRANSKEY will be indistinguishable from
signals  that  a  stock  keyboard  produces.  This  means that any software ever
written  will  be compatible with the TRANSKEY board. The only exceptions are as
follows:

    When  a  program  such  as  a wordprocessor looks at keys in an entirely new
light  and  essentially  reassigns  new  meaning to these keys, there could be a
conflict.  An  example  would  be  where  the extra symbols on the arrow keys no
longer  print  to screen, but instead are used for moving the cursor to the next
word,  or  the next line, ect.. Since these characters are on entirely different
keys on the IBM standard, it will take some getting used to in order to make the
same  things  occur  in  a  program of this kind. For instance when running from
MAC65's  DDT  menu,  to  increment  or  decrement the memory being viewed in the
display  window  requires pressing either the (-) or (=) keys on the upper right
of  the  keyboard.  If you tried pressing the up-arrow or down-arrow instead (as
the  program  instructions dictate) nothing will happen, at least not on the IBM
keyboard.  While  using  AtariWriter, the SELECT arrow key combinations will not
work  from  the IBM keyboard as they do on the Atari keyboard. Instead, you will
have  to do a SELECT _, =, +, or * for the same effect. This way of doing things
is  rather  rare, since most programs will recognize the keys in a more standard
fashion.

    Another side effect of some of the word processing programs is that they are
designed  to  put the system in lower case, when first booted up. Since there is
no  communication  of  this to the TRANSKEY board, the keyboard's CapsLock light
will indicate an upper case (or CapsLocked) condition (this is not the case when
using  a  PC/XT  keyboard,  see  next  section  for details). This can be easily
remedied by pushing the CAPSLOCK key twice, which will reinitialize the computer
to the keyboard and put the computer in upper case mode. This particular problem
can  also  occur if the CAPS key is pressed on the stock Atari keyboard, but the
same fix will also correct this problem.

    Another  minor  problem  affects  the Stock Atari keyboard and is a hardware
problem which inhibits some of its actions. With TRANSKEY installed (whether the
IBM  keyboard  is  connected  or  disconnected) the Control/Shift equivalents of
several  characters  will  no longer be produced by the Atari keyboard (although
all  will  be  available  from the IBM keyboard). This problem is due to the way
TRANSKEY  is  electrically  tied in with the Atari hardware and unfortunately is
not  resolvable  at  this  time.  However,  none  of the single SHIFT or CONTROL
combinations  or  the  standard  characters  are  affected  by  this  particular
problem.

KEYBOARDS TO USE

    TRANSKEY  was  designed  to  be as flexible as possible and because of this,
should  be  compatible  with  most  any  IBM PC/XT/AT original equipment, BTC or
KEYTRONICS keyboards. Best results will usually be obtained by selecting an 'AT'
configured (or dip switch configurable) keyboard instead of the auto-configuring
types.

    Configuring TRANSKEY to the keyboard is extremely easy. All that is required
is  to  plug  in the keyboard, with the computer off, and then simply switch the
computer on. TRANSKEY will then perform an analysis of the keyboard attached and
auto-configure  itself.  If you have a switchable PC/AT keyboard, be sure to set
its  dip  switch  to  'AT' mode. This will ensure proper setting of the CapsLock
light  on power up. When using a PC/XT keyboard, TRANSKEY will initialize itself
to  lower  case  mode  (although  the  computer  will be in upper case, unless a
boot-up program has changed the setting). The action of pressing CAPS LOCK would
then  place  the  computer  positively  in  an upper case mode and indicate this
condition  by lighting the CapsLock light. Repeated pressing of this key and the
indication  of the CapsLock light, would then correspond to the actual case mode
of the computer.

    The  reason  for  this  difference  between  an  'AT'  keyboard  and a PC/XT
keyboard,  has to do with who controls the indicator lights. On an 'AT' keyboard
the computer is solely responsible for activating or deactivating a given light.
On  a  3rd  party  XT keyboard it's the keyboard that controls the action of the
lights  (when powering-up it turns all the lights off). Since the Atari normally
powers-up  in  upper  case mode, TRANSKEY was designed not to alter this initial
setting  and,  if  at  all  possible,  to  reflect  this by turning the keyboard
CapsLock  light  on ('AT' keyboards). With a PC/XT keyboard you will still be in
upper  case  mode from the computer's point of view, but the CapsLock light will
be  off.  The  state  of  this  light  after powering-up will also act as a good
indicater as to what type of keyboard you are using, or in what way TRANSKEY has
configured itself when used with an Auto configuring keyboard.


TECHNICAL NOTES ON ALTERING MACROS

    The  following  information is provided for those people possessing an EPROM
BURNER and a thorough understanding of its operation. If you decide to undertake
this venture, please experiment on a new EPROM or EEPROM and not on the original
EEPROM.  MICRO  SOLUTIONS  will  not  be  responsible  for corrupted EEPROMs and
replacements will cost $5.00 (includes shipping).

    The  Macro  string  definitions have been pre-defined in the TRANSKEY unit's
EEPROM  (52B13)  and  are not alterable from the TRANSKEY board itself (this may
become  possible  on  a  future version). The Macros are set-up in two different
tables.  Table One holds the BASIC Command strings and Table Two holds the MAC65
Command  strings.  Along  with  these tables, there is also its associated Index
Table.  It  holds  a 1 byte pointer for the start position of each string within
the  particular  Macro  Table  (the  first  position  is always = 0). The actual
characters  in a given string are the HEX equivalents seen when PEEKing location
764  on  the  Atari  computer while pressing a given key or combination of keys.
This is the raw unprocessed keyboard scan code produced by the keyboard hardware
matrix. The first six bits are for a given key and the two most significant bits
represent  the state of the SHIFT and CONTROL keys respectively (a 1 = pressed).
The  last  character in a particular Macro string must be the number HEX $09 (an
unused character by the Atari) which serves as an End of String Flag. Also, when
two  identical  characters (this refers to the first six bits of the characters)
are to sit next to each other in a given Macro string, they must be separated by
a  HEX  $3B character (another unused character) for the Atari to know that this
is actually the same as two individual keypresses.

    The  existing  Macro  definitions sit at the very end of the 2K EEPROM space
which  is  mapped  starting  at location $1000 and ending at location $17FF. The
last  4  bytes  $17FC  -  $17FF hold the two-byte addresses of the RESET and IRQ
routines  used  by  TRANSKEY  and  absolutely  should  not  be  overwritten when
modifying  the Macro Tables. The exception to this rule is when the 2K EEPROM is
replaced  by a 4K EPROM (2732) for extra long Macros. In this case the RESET and
IRQ  address  vectors would be moved to $1FFC - $1FFF (also the J1 jumper on the
TRANSKEY board would need to be moved to its opposite position).

    Presently  the  TRANSKEY  board  is designed to send what can be called Fast
Macros. This simply means that the characters are sent at the fastest rate which
the  normal Atari keyboard handler can reliably accept data. Often times this is
too  fast a rate for replacement handlers and will result in lost characters. To
fix  this  problem there are two solutions: Number one, replace timing capacitor
C4  on  the  TRANSKEY  board with a 1uf tantalum capacitor or number two, repeat
each  character  in a given Macro string (ie: for the string TEST you would have
the Atari keyscan HEX equivalents for: TTEESSTT). The 2nd solution is the better
way  to  go  when you want to have both Fast and Slow Macro strings, although it
eats  up  twice  as  much memory and may require using a 4K EPROM instead of the
stock 2K device.

    The following is a listing of the Memory locations associated with the Macro
Routines and Tables.

$172D - $172E MACTABLE1 VECTOR  Two-Byte address (LSB,MSB)
                                start of Macro Table One.

$1736 - $1737 MACTABLE2 VECTOR  Two-Byte address (LSB,MSB)
                                start of Macro Table Two.

$176D - $1774          Present location of Index Table One

$1775 - $177C          Present location of Index Table Two

$177D - $17BB          Present location of Macro Table One

$17BC - $17FA          Present location of Macro Table Two

$17FC - $17FD          RESET VECTOR    Presently = $1190

$17FE - $17FF          IRQ VECTOR      Presently = $1223


    These  Vectors  are guaranteed to remain the same in all future revisions of
the  TRANSKEY  operating  system in the Version 1 series. However, the addresses
pointed to by these vectors are subject to change.

    When altering the Macro strings, it will be necessary to change the MACTABLE
VECTORS  in  order  to  point  to the beginning of your customized Macro Tables.
Also, the value of the 8 pointers in a given INDEX TABLE will need to be updated
to  point  at the Macros within your customized table. If you need more room and
use a 4K EPROM, don't forget to move the RESET and IRQ vectors.

                            >>>>>> DISCLAIMER <<<<<<

    The  following  list is of keyboards that have been tested with TRANSKEY and
are  known  to work reliably. Currently these are the only keyboards that we can
recommend  using  with  our  product.  If you are planning to use a keyboard not
listed  below,  you  will  hŠSƒ~;¾â�hÉ•Û W˜§yð	¥ˆ`�PŒÈÈ•
P
�
HP!(Á°ãÉ¾�Î-ÐQ-
~Ó`'à
YE
…“$Pxº VÍ¢©À�³L`ä`Õ�@Ð"EPD:UP“RPNà=›`À¥[€…°®
`"� ÀÑª@XÐ	H0˜Ý	IÀÙ�ýÖ �ÙvÝÙy�	T¡¨(e°
ƒqMî 
Ð
´��
NÌÊ¦Ìƒ
%Ð%@©@5´­
½0	+!Ð  €`Õ ÐØ,àZŒork properly with TRANSKEY.


Original IBM equipment:  PC (Type 2 only)/XT/AT
BTC  5339R-0 (Enhanced)  &  5060 (84 KEY)
KEYTRONICS  EP3435XTAT (Enhanced)  &  E03091005 (84 KEY)
MITSUMI  KPQ-E99YC (Enhanced) *SEE NOTE BELOW*
TELEVIDEO  113110 AT (84 KEY)
QUADRANT AT (84 KEY wo/lites)
EPC  SK88018-1U (Enhanced)


*Note:  This  keyboard  requires  that  a  key  (any key) be pressed while first
cold-booting the computer in order for proper initialization to occur.


ORDERING INFORMATION

    If  both  the  POKEY  and GTIA chips are socketed in your computer, than the
TK01-PB  model  will work and provide a non-soldered installation. Approximately
25%  of  the 800XL computers had these chips soldered in place. You should check
before ordering for this model.

    The  400,  800,  600XL,  and 1200XL machines are ALL socketed. The entire XE
line of computers (65XE, 130XE, and XEGS) are NOT socketed.

    The  TK01-SD  is  a  solder-in version and will fit all 8 Bit models whether
socketed or not.


--------------------------------------------------------------------------
                   * * *   O R D E R   F O R M   * * * 
                                MICRO SOLUTIONS
                 BOX 750396, Petaluma, CA 94975 (707) 763-9103

Name ____________________________ Address________________________________

City ____________________________ State ____________ Zip ________________


  _____  TK01-SD        TRANSKEY BOARD (Solder in Version)         $48.00
                      {Fits all models 400/800/XL/XE}

  _____  TK01-PB        TRANSKEY BOARD (Piggy-Back Version)        $58.00
                    {400/800/XL ONLY solderless installation}

  _____  CHASSIS MOUNTABLE JACK                        SUBTOTAL    ______

                        California residents ADD 6.25% SALES TAX   ______

                                      SHIPPING and HANDLING        $ 3.00
                                 ($5.00 for Canadian shipments)

                     MONEY ORDER or CERTIFIED CHECK enclosed for:  ______
                       (TO BE MADE OUT TO: MICRO SOLUTIONS)

           ***** Please allow 2-3 weeks for delivery *****
--------------------------------------------------------------------------
board would need to be moved to its opposite position).

    Presently  the  TRANSKEY  board  is designed to send what can be called Fast
Macros. This simply means that the characters are sent at the fastest rate which
the  normal Atari keyboard handle