This file should be LISTed to a printer with the width being›set to 80 columns.  This file is intended for use by anyone›with Percom double density drives who wishes to know more about›what is on the ROM chip.  For furthur study of how these tables›are used, see the SAMPLE program on the diskette that is sent›with each Percom first drive system.›››››››TM RFD 007                                20 SEPTEMBER 1982›››TECHNICAL MEMO›››PRODUCT: RFD DISK DRIVES›SUBJECT: OPTION TABLE›››Percom RFD disk drives for the Atari home computers use an›intelligent disk controller.  In order to properly handle its›functions, a ROM chip containing an Option Table has been›developed.  This Option Table is located in a 1K RAM chip on›the controller board, and can be accessed by request from the›computer.››Below are tables which will help the programmer in›understanding the calls on the Percom controller.  Of›particular note are the bytes which handle the density of the›controller.››The Read Option and Write Option commands pertain to the 12›byte Option Table.  There is one table set up for each drive.››To access these tables, see the SAMPLE program on the Percom›Software Support diskette that comes with Percom Double Density›drive systems (NOTE: included on this disk as "PERCOMSM.PLE").›››==============================================================›               INDIVIDUAL COMMANDS TABLE    ››FORMAT         21(hex)   FORMAT DISKETTE›RDOPT          4E        READ OPTION TABLE FOR A DRIVE (TABLE 2)   ›WROPT          4F        WRITE OPTION TABLE FOR A DRIVE (TABLE 2) ›WRSECT         50        WRITE SECTOR WITHOUT VERIFY ›               51        UNDEFINED   ›RESECT         52        READ SECTOR ›RESTCM         53        READ STATUS MESSAGE (TABLE 3)›               54        UNDEFINED ›               55        UNDEFINED ›               56        UNDEFINED ›               57        WRITE SECTOR WITH VERIFY››===============================================================››››===============================================================›           OPTION TABLE TABLE 2  ››All 2-byte values are in MSB,LSB format, unlike the 6502›practice which uses LSB,MSB format.››  BYTE(S)        OPTION›   0        Number of tracks (This is a literal value)›   1        Step Rate (Standard 17xx FDC coding)               ››               value     rate ›               -----     ---- ›                00        30 msecs.›                01        20 msecs.›                02        12 msecs.›                03        06 msecs.››   2,3      Sectors per track (This is a literal value)››   4        Number of Sides     0= 1 side›                                1= 2 sides›            any other values will cause unpredictable results›››  5         Density             00= Single Density›                                04= Double Density››            any other values will cause unpredictable results›› 6,7        Sector Size (bytes per sector.  This is a literal›            value)›› 8          Drive Present       00= Drive is not present›            any other value indicates a drive is present›› 9          ACIA      not currently implemented››Bytes 10 and 11 are reserved for future expansion››==============================================================›››==============================================================›                     DRIVE STATUS TABLE 3 ››   BYTE            USE››   0    SYSTEM STATUS OF DRIVE› ›               value     status›               -----     ------›               32(dec)   sector size     0=128  1=256›               16        motor on?›               8         write protect›               4         FDC error›               2         data frame error ›               1         cmd frame error ››   1    FDC status››   2    Timeout for format- How long to wait for response to›        format››   3    Current track where read/write head is located›››==============================================================››-END-›››