THE ATARI 130XE MEMORY UPGRADE
          
               The Atari 130XE lends itself to memory increases quite
          easily.  For those who may care the Freddie chip (Part #
          CO61991-29) has been around for a while.  Remember the 1400
          and 1450XL computers?  These machines used Freddie also.
          Freddie is used for multiplexing the address's fo th RAM
          chips and provides system timing.  The chip that does all
          of the actual work in providing for the memory management
          is the custom chip next to Freddie. (Part # CO25953)  This
          chip takes it's input's from th 6520 PIA and from Antic for
          CAS, RAS, etc.  The pin that we are concerned with is pin
          14 (CASBANK).
          
          .c
          Technical Overview
          
               Now for the good part.  If we redirect the output of
          pin 14 of the CO25953 to another bank of 64K ram chips we
          can, via software, select any one of 8 banks of 64K.  In
          this configuration one would have a maximum of 589,815
          bytes of memory.  The only disadvantage of this is the fact
          that under these constraints the hardware becomes more
          complex and the software to drive it does too.  I recommend
          that for general purposes the 130XE be upgraded to a
          maximum of 320K.  It gives the user sufficient "horsepower"
          and yet at the same time the software does not become too
          intense.  Now for the bad news.  To implement the 320K mod
          one has to remove the internal basic ROM which really isn't
          that bad because most users are using Basic XL/XE anyway.
          The reason for this is quite good.  That bit is required
          for the addressing of the extra bank(s) of memory.
          Actually one could use the Self-test bit but that requires
          additional hardware or a reburn of the O.S. ROM.  More on
          that later.
          
          .c
          The Mod
          
               What we will do is to wire up a 74LS138 to the 6520
          PIA and to pin 14 of the CO25953.  The 74138 can be best
          described as a routing switch.  The data that we want to
          re-direct is presented at pin 4 of the 138 and the data
          output is pins 15, 14, 13 and 12.  The pins that tell the
          chip to what bank to directs it's output to are pins 1, 2,
          and 3.  Now for the installation.
          
               1)  Take 24 64K x 1 RAM chips and bend out pin 15 on
          all of them.  Pin 15 is the CAS line.
          
               2)  Solder these chips onto the existing RAM chips in
          the 130.  Do not solder anything to pin 15 yet!  For ease
          of servicing and soldering I staggered these new RAM chips













          onto the existing ones.  I recommend this highly.  When you
          has completed soldering in each new bank take a piece of
          insulated wire and solder this wire to pin 15 of each new
          RAM chip.  Wire wrap wire works nicely for this.  Continue
          with this process until all 3 additional banks are wired.
          
               3)  Just to the right of Freddie is an area to solder
          in a 14 pin IC chip.  We will use this area to supply +5
          and ground to our 74138.  Take a 74LS138 and bend out all
          of the pins except pins 8 and 16.  Solder pins 8 and 16
          into the holes of the unused chip area next to Freddie.
          
               4)  Next to the RAM chips is the chip with the part #
          of CO25953.  Behind the chip are two 33 ohm resistors.
          (orange, orange, black, gold)  Unsolder the right-most lead
          of the rear resistor.  (R111)  Solder a wire from the free
          end of the resistor to PIN 15 of the 74138.  Solder another
          wire from the land where the resistor used to go to pin 4
          of the 74138.
          
               5)  Solder two wires from pins 11 and 16 of the 6520
          PIA chip (Part # CO14795-12) to pins 1 and 2 of the 74138.
          Also ground pins 3 and 5 of the 74138.
          
               6)  Solder the CAS line from each new bank of 64K to
          pins 14, 13, and 12 of the 74138.
          
               7)  Unsolder the Basic ROM chip from the board.  This
          is the 24 pin chip that is located closest to the front of
          the machine just to the left of the 555 timer IC.
          
               Thats it.
          
          .c
          Conclusion and Tech notes:
          
               To test each bank boot with DOS 2.5 with your basic
          cartridge, POKE 5439,49, set the appropriate PIA port bit,
          go to DOS and reformat D8.  Continue through all the banks
          and check your directory.  If you write a file to one bank,
          switch banks, and write another file, you will not lose
          what you wrote to the first.  The real advantage is that
          you can have your ramdisk and Basic XE too.  Around the
          bbs's here in Chicago there is a file floating around
          called RAMDISK2.  The source code is available on
          compuserve.  By re-writing the routine you can have your
          ramdisk invisible to Basic XE and/or double density.
          
               I mentioned previously about using the Self-test bit
          in the PIA port.  To use this bit you have to disconnct the
          line on the PIA that runs to the PAL MMU and connect it to
          a 556 timer that will enable the self-test input to the PAL
          for about 3-5 seconds.  Half of the timer is used for













          timing and the other half is used as an inverter.  The
          reason for using a timer is that on boot-up the OS uses
          some of the routines in the self test to check for valid
          RAM and to determine RAM size.  I have done this and then
          pulled the circuit out.  It was just too "messy" to suit
          me.
          
               One potential problem is the 555 timer used in the
          130.  This chip is used for system reset timing.  If you
          press your system reset key down and hold it there the
          system should not reset.  If it does you will notice that
          if you release it the system will reset again.  The reason
          for this is because the 555 timer is putting out a spike
          that the system sees as a valid reset.  To solve the
          problem replace the chip.  It seems about 1 in 10 are bad.
          
               That's it!  Hope you enjoy the mod.
          
          Rich Andrews
          Box 229-1 RR#7
          Lockport, Il 60441