Note to SIO2PC users:

KEYER.OBJ is a program for ham radio which took up about 2 years
of my programming time before I started SIO2PC. I'm throwing it in
just as a curiosity, to fill in disk space. If you have friends who
are ham operators, they may be interested in it.

If you want to play with it, plug a joystick
into stick #2, run KEYER.OBJ and send some Morse code.
Note: On the XL computer, boot without BASIC (hold down OPTION while
booting) before running the KEYER.




                             Instructions: The WA5BDU Keyer
         
         
         OPTION: Enter command mode.
         SELECT: Keyboard to MEMO/TRANSMIT window toggle.
         
         
                                C O M M A N D S
         
         [OPTION] plus ...

         HS: Help Screen
         HP: Help text dump to printer
         SP: Speed
         RT: Ratio, doT
         RH: Ratio, dasH
         SW: Spacing, Word (in 1/2 dot length units)
         SC: Spacing, Char (in 1/2 dot length units)
         CS: Console Speaker toggle (400/800 only)
         VO: Video Off/On toggle
         KD: Key Down (tune)
         OA: On Air/Off Air toggle
         IK: Inverse Keying (Invert output logic)
         TO: Sidetone frequency
         OM: Open message (Create or Edit; ESC to exit)
         BE: Buffer Enable (Start/Stop sending)
         TAB key: Same as above
         BC: Buffer Clear (SHIFT-CLEAR is the same thing)
         MA: Thru MZ: Send message A-Z immediately.
         Inverse A-Z: Put message A-Z in buffer to send
         PL: Parameter Load (Set up keyer the way you like it)
         PS: Save current parameters to file
         NOTE: File AUTOPARA.KEY will auto-load
         TL: Textfile Load (Load message file)
         TS: Save messages to file
         NOTE: File AUTOTEXT.KEY will auto-load.

         Messages can call each other (embed inverse A-Z in message)

         A message can call itself.  Hit any key to stop the infinite
         loop.

         Commands may be embedded within messages, "*" signals start
         of command.
         
         
         INTERFACING: Stick 2: Pin 1: Output, Pin 2: Command button
         (optional), Pin 3: Dash paddle contact, Pin 4: Dot contact,
         Pin 8: Common
         
         
         Special codes from paddle: .-... (AS) enters COMMAND mode
         (same as OPTION), .----- (EOM) exits message edit mode (same
         as ESC key).
         
         
         WA5BDU, 300 S. VANCOUVER, RUSSELLVILLE, AR 72801