The hardware

    The schematic diagram of the interface is shown in the  picture.   The
    hart  of  the interface is an Integrated Circuit of type MAX232.  This
    IC makes the ST and the XL 'understand' each other.  The modem port on
    the ST operates at a voltage level of 12 volts, and the serial port on
    the XL operates at a voltage level of 5 volts.  This IC  converts  the
    signals  from  the  12 volts level to the 5 volts level, and the other
    way round.  Don't let this confuse You if it  sounds  technical,  just
    believe  me  that  You  should  not  connect the serial port on the XL
    directly to the modem port on the ST without the  voltage  conversion.
    Getting  this  IC might be a bit hard, because it is not a very common
    type.  They are distributed by Jim-pak electronic  components.   Check
    with  Your local dealer.  I paid about $10 for this IC.  You will also
    need four electrolytic capacitors with a value of 33  micro-Farad,  at
    an  operating voltage of 16 volts or more.  They cost about 65 cents a
    piece.  Finally You will need  an  8-bit  serial  port  connector  for
    circuit  board  mounting or an old 8-bit I/O cable, and a DB-25 female
    connector to connect to the ST modem port.  All this adds up to  about
    $20.  This circuit operates on a single power supply of 5 volts, which
    is drawn from the serial port on the XL.   This  means  that  1200  XL
    owners  will  need  to  get the power from another source, unless they
    modified their machine of course.  You will  need  a  printed  circuit
    board to mount these components.  Observe the polarity when installing
    the IC and the electrolytic capacitors.

    Schematic Diagram

                  -----------
                  |         |
    Data 3      9 |         | 8      2
     in ----------|         |---------- TD
    Data 5     10 |         | 7      3
    out ----------|         |---------- RD
                  |         | 1
                  |         |----|
                  | MAX 232 |   === +
                  |         | 3 ---
                  |         |----|
                  |         | 4
        10     16 |         |----|
    +5V ----------|         |   === +
                  |         | 5 ---
                  |         |----|
                  |         |
                  |         |
                  -----------
                   | 6 |15 | 2
                  ---  |  === +
                + ===  |  ---
         4         |   |   |         7
    GND ------------------------------- GND



                                                                    Page 2


    On the IC, there is a small notch, or dot.  It is on the  top  of  the
    IC,  on  one  of  the  narrow sides.  Position the IC according to the
    drawing below.  The pin numbers will then be as shown in the  drawing.
    Note that if we are soldering the IC into the board, we are looking at
    the bottom of the IC, and this must be taken into account.

    Top View of MAX232

      1 1 1 1 1 1 1
      6 5 4 3 2 1 0 9
      XXXXXXXXXXXXXXX
      )XXXXXXXXXXXXXX
      XXXXXXXXXXXXXXX
      1 2 3 4 5 6 7 8


    If You are using a piece of prototype board, install the  IC,  or  the
    socket  for  the  IC.   If  using  a  socket, make sure to position it
    according to the notch in it, similar as with the  notch  on  the  IC.
    Solder  all  pins  to  the board.  Connect pin 15 of the IC to ground.
    Then install the rest of the components and wires.

          o  Install C1 between pins 4 and  5  of  the  IC.   Connect  the
             negative side to pin 5.
          o  Install C2 between pin 6 and ground.   Connect  the  negative
             side to pin 6.
          o  Install C3 between pins 1 and  3  of  the  IC.   Connect  the
             negative side to pin 3.
          o  Install C4 between pin 2 and ground.   Connect  the  negative
             side to ground.
          o  Connect pin 3 of the XL port or cable to pin 9 of the IC.
          o  Connect pin 5 of the XL port or cable to pin 10 of the IC.
          o  Connect pin 10 of the XL port or cable to pin 16 of the IC.
          o  Connect pins 4 and 6 of the XL port or cable to ground.
          o  Connect pin 2 of the DB25 connector to pin 8 of the IC.
          o  Connect pin 3 of the DB25 connector to pin 7 of the IC.
          o  Connect pin 7 of the DB25 connector to ground.



                          ST pin 3
               C3    C1     ST pin 2
              o   o o o   o o
              | | | | | | | |
           o  1-------------8 o
         C4   |    MAX232   |  C2
           o  16------------9 o
              | | | | | | | |
              o o         o o
             XL GND      XL XL
             10           5 3
            


    Double check all connections before trying if it works.

                                                                    Page 3


    Pin numbers of XL I/O socket for circuit board mount.
    Solder side view.

      1 1
      3 1 9 7 5 3 1
      o o o o o o o
       o o o o o o
     12 10 8 6 4 2

    Pin numbers of DB25 female connector.
    Solder side view.

                        1 1 1 1
      1 2 3 4 5 6 7 8 9 0 1 2 3
      o o o o o o o o o o o o o
       o o o o o o o o o o o o
       1 1 1 1 1 1 2 2 2 2 2 2
       4 5 6 7 8 9 0 1 2 3 4 5