›››››     ›     ›     ›     ›     ›     ›     ›     ›     ›                           MYDOS Version 4 User Guide›                                  Revision 4.50›                            for Atari Home Computers›     ›     ›             Copyright (C) 1988 by WORDMARK Systems and the authors:›     ›                               Charles Marslett›                               2705 Pinewood Dr.›                               Garland, TX 75042›                                   CIS: 73317,3662›                                   UseNet: CHASM@KILLER.DALLAS.TX.US›     ›                                        and›     ›                               Robert Puff›                               Suite 222›                               2117 Buffalo Rd.›                               Rochester, NY 14624›                                   GEnie: BOB.PUFF›     ›     ›     ›          This  software  may be freely used and distributed provided that›     this copyright notice is left intact, and provided that:›     ›     (1) The source code in machine readable form is provided with›         any binary distribution, or made available at no additional cost›         to the recipients of the binary distribution.›     ›     (2) A binary version of a derivative work may be sold for a›         reasonable distribution charge (less than $50), and the›         source code in machine readable format must be available.›     ›     (3) A derivative work may not impose and restriction on the free›         distribution of the source code.›››››››››››››     MYDOS User Manual               page 1                   Version 4.50›››››››››                           MYDOS Version 4 User Guide›                        by Charles Marslett & Robert Puff›     ›     ›     I. INTRODUCTION›     ›          The  disk  operating  system described in this manual is modeled›     after the ATARI (trademark of ATARI Corp.) disk operating system (DOS›     2),  and  may  be considered an extension of the very "user friendly"›     concepts  introduced  with  this operating system. The ATARI 810 disk›     drive  and  the ATARI 1050 disk drive are well supported by the DOS 2›     and  DOS  2.5,  but those DOSs have very limited provision for higher›     capacity  double  density  disks  (such  as  the  XF-551),  and large›     RAMdisks.›     ›     ›     II. SYSTEM REQUIREMENTS›     ›          MYDOS  4.50  is  intended to function as nearly as possible like›     ATARI  DOS  2.  This  means it occupies as little memory as possible,›     supports  all  the system calls supported by DOS 2, and in most cases›     uses  exactly  the  same  parameters  to the system calls. This means›     compatibility,  yet  MYDOS  goes  far  beyond  this.  On  a  standard›     single-sided, single density disk, MYDOS will read and write to a DOS›     2.0 or 2.5 format, and vice versa. There are a few programs that will›     not  run under MYDOS because of one or both of the following reasons:›     direct  "illegal"  calls  into  the main DOS or FMS code, and relying›     upon exact directory data (i.e., 3 digit sector counts).›     ›          MYDOS  will  run  on  any 8-bit Atari computer with at least one›     disk  drive (that is compatible with DOS 2). MYDOS 4.50 has full READ›     compatibility  with  the  DOS  2.5 format, but will only write to the›     first 720 sectors of the disk. (MYDOS has its own format for enhanced›     density  disks  that allow full access.) It is not compatible at this›     time with the OS/A+ version 4 format, or the SpartaDOS format.›     ›          Up  to eight disk drives (or nine if the ninth is a RAMdisk) may›     be  accessed,  but  only  one  is  required. The resident part of the›     operating  system  (DOS.SYS) supports all documented functions of the›     DOS 2 operating system, so MYDOS supports most available software for›     the ATARI home computers.›     ›          The memory available to a program is affected only by the number›     of  files to be open concurrently: each disk file that may be open at›     the same time requires 256 bytes of buffer space. Unlike Atari DOS 2,›     memory  requirements  are independent of the number of disk drives or›     the  sector size and density. The need for a 256 byte buffer for each›     concurrently open file means that programs that keep large numbers of›     files  open will have less memory available than under DOS 2 and as a›     result some programs (mostly older versions of compilers and language›     interpreters)  will  not  have  enough memory to run. With three file›     buffers  (which  is the default) and no resident drivers (such as for›     RS232  support), MYDOS 4.50 permits binary programs to load as low as›     $1F00.››››     MYDOS User Manual               page 2                   Version 4.50›››››››››     ›          MYDOS  4.50  also  contains a very versatile RAMdisk driver than›     can  handle  upgrades  up to 1 megabyte that follow the guidelines of›     the  expanded  memory on the 130XE, or the Axlon upgrade for the 800.›     MYDOS  also  has  a  feature  that will determine how much memory you›     have,  and set itself up for your machine (For XE-compatible upgrades›     only) automatically.›     ›     ›     III. MENU FUNCTIONS›     ›          The  menu provided by MYDOS 4.50 identifies 18 common tasks that›     might  need to be done. Rather than having to write a utility program›     (only  a few lines of BASIC would perform most of the menu functions)›     or  even  remember  the name and format of a DOS command, these tasks›     can  be  handled  by  entering a single letter. MYDOS responds with a›     question  asking  for  the details of the operation (which file, what›     density,  "are  you  sure?"  or whatever else it might need to know).›     After  you enter the remaining information, the function is performed›     and another prompt is displayed.›     ›          You  should  notice  two  interesting things about the menu: the›     second  line  on the screen identifies the disk drives present on the›     system and what they appear to MYDOS to be (single or double density,›     RAMdisk  or  high  capacity  hard  disk). The next line describes the›     current  default  directory  (that  directory  used  when  a  disk is›     referenced  by  "D:"  (without  a  unit  number  after the "D" - this›     feature  will be described later). The second thing to notice is that›     after  commands  fill  the screen, the menu "rolls" off the top: some›     DOS  programs  (e.g. Atari DOS 2) keep the menu, MYDOS does not. This›     permits  more  information  to  be  displayed when a long sequence of›     commands are done, or when many files are copied. To restore the menu›     to  the  screen,  just  type  RETURN,  and the initial screen will be›     restored.›     ›          If you wish to abort a command at any point, simply press BREAK.›     This  will  return  you to the prompt.  Pressing BREAK or RESET while›     writing  to  a  disk will not cause any damage; however, the file you›     were writing will probably not be displayed in the directory, and the›     free sector count may be incorrect.›     ›          When  entering  a  filename, the drive number should be entered,›     followed  by  a  ":", and then the rest of the filename. If the drive›     number  and  ":"  are  not entered, the default drive (and directory)›     will  be  used.  In the [C]opy file option, entering the drive number›     only  will result in copying every file on the main directory of that›     drive.  A  drive  may be specified like this: "1", "1:", or "D1:". If›     you  wish  to  specify the file or set of files to be referenced, the›     drive  format  must include a ":" or it must be omitted entirely (for›     the  default drive and directory). Examples: D1:Test.obj, 1:TEST.ASM,›     or D2TEST (really D1:D2TEST) are valid file names, but d1:Test.obj or›     1TEST.ASM are not.›     ›          The file name itself is either fully specified (referring to the››››     MYDOS User Manual               page 3                   Version 4.50›››››››››     entire  name as it is on the disk) or includes "wild card" characters›     (specifying  a set of files). A fully specified file name consists of›     one  to eight characters followed by a period (".") and zero to three›     additional "extender" characters. The characters in the file name may›     be  upper or lower case letters, numbers, the underscore ("_") or the›     character "@". The only exception is the first character - it may not›     be  a  number.  The "wild card" characters are the characters "*" and›     "?":  the  character  "*"  or  the  sequence  ".*"  end  either the 8›     character  or  the  3  character field in the file name and match all›     possible  characters.  The character "?" matches only one single file›     name  character.  Examples: "*.BAS" will match every file ending with›     .BAS.  "TEST?.*"  will  match files TEST.BAS, TEST1.OBJ, but will not›     match TESTER.BAS.›     ›          In  addition to the main directory (containing up to 64 files or›     directories),   each   MYDOS   disk   may   also  contain  additional›     subdirectories  of  64  files  each.  You may use one of two possible›     characters  to  separate  the subdirectory name(s): the ":" colon, or›     the  ">"  greater-than  sign.  If  the  main  directory contained the›     subdirectory  BAS and the file GRAPHIC1 were in the subdirectory file›     BAS,  it  could  be  referenced  with  the  filename BAS:GRAPHIC1 (or›     BAS>GRAPHIC1).  If  instead, GRAPHIC1 were in the subdirectory GR.dir›     which   in  turn  were  in  BAS,  then  the  reference  would  be  to›     BAS:GR.dir:GRAPHIC1 (and so on with as many names as needed). Because›     there  is  no  limit to the number of subdirectories on a disk (other›     than  the buffer size of programs using the directories and number of›     available  sectors  on  the  disk),  a  single  diskette  can contain›     hundreds  of files if necessary. Each subdirectory is a 8 sector file›     to  its  parent  directory.  Thus  it  is  limited  to  64  files  or›     subdirectories like the 8 sector root directory.›     ›          If  a  disk  directory  includes  the  files TEST.ASM, TEST.OBJ,›     TEST.C,   TEST.ALM,   TEASET.DOC,   TRACE.FIL,   and   BETS.LST,  the›     specification  "t*.*" will not match any file name (since "t" and "T"›     are not the same letter to MYDOS). The specification "T**" will match›     all  but "BETS.LST" (since the others all begin with the letter "T").›     The  specification  "?E??.*"  will match the first four files and the›     last  one  (since  the 8 character part of the file name must have no›     more  than  4  characters  in  it and the second character must be an›     "E").  The specification "*.?" will match only the file TEST.C (since›     it  is  the only file name with a single character in the 3 character›     field).  The  specification "????E**" will match the files TEASET.DOC›     and  TRACE.FIL  and none of the others (since the 8 character part of›     the  file  name must have at least 5 characters and the fifth must be›     an  "E").  Note  that MYDOS does not always require the "." period to›     separate  the  extender  from  the  8  character filename.  Examples:›     FILENAME.EXT  could be entered as FILENAMEEXT; TES*.* could be TES**,›     but TEST.* could NOT be entered as TEST*.›     ›     ›     IV. THE MENU COMMANDS›     ›     A. List a Directory or a Set of Files›     ››››     MYDOS User Manual               page 4                   Version 4.50›››››››››          The  "A" command will list the files on a disk with their sizes,›     followed by a line specifying the number of free sectors on the disk.›     If  the  line starts with a "*", the file has been locked and may not›     be modified or deleted without first being unlocked. A ":" before the›     file  name  marks  those  files  that are subdirectories. These files›     cannot  be  read  or  written  as  other  files  but only accessed as›     directories  or deleted (if the directory is empty). File lengths and›     the  number  of  free sectors are reported as 4 digit decimal numbers›     (most other Atari DOSs report the values as 3 digit numbers).›     ›          If  the number of free sectors on a drive exceeds 9999, the free›     sector  line  will  contain  a  5  digit number, and be one character›     longer.  If a file is longer than 9999 sectors, the blank between the›     file  extender and its sector count will contain the most significant›     digit (the line size does NOT change).›     ›          No  indication  is  made of the format of the file but ATARI DOS›     2.0,  2.5,  and  MYDOS  are  the  only  three supported file formats.›     SpartaDOS  or  OS/A+  Version  4 files must be converted to single or›     double  density  Atari  DOS  2 files first in order to be usable from›     MYDOS.  See  Section  6 for further directory information if you need›     more detail.›     ›          The  "A"  command  will  list  the  directory information to the›     screen if only one file specification is entered. If two are entered,›     the second is taken as a destination file and will be overwritten (or›     appended  to  if  the  /A  flag is used) with the directory data. Use›     "2,D1:DIR.TXT"  to  save the directory data of drive 2 to a text file›     DIR.TXT  on drive 1. The entry "1,P:" will give you a printout of the›     directory of drive 1.›     ›          To  list  the  files  in  a  subdirectory, enter the name of the›     directory  followed  by  a  ":"  colon  or ">" greater-than sign. For›     example,  "1:TEST:BAS:"  will  list the files in the subdirectory BAS›     which  in  turn  is in the subdirectory TEST in the main directory of›     the  diskette  in drive 1. Using "D1:TEST>BAS>" will achieve the same›     results.›     ›     ›     B. Run the Cartridge›     ›          The "B" command returns control to the cartridge in the left (or›     only)  cartridge  slot.  If  no  cartridge  is  present,  an error is›     displayed,   and   nothing  happens.  No  additional  information  is›     required,  so  if a cartridge is present, it is entered after loading›     MEM.SAV (if enabled) or immediately.›     ›     ›     C. Copy a File or a Set of Files›     ›          The  "C"  command  is  used  to make another copy of one or more›     files  of  data. The two file specifications asked for after entering›     the  "C"  identify  the source and the destination of the information›     being  copied.  Either  may  be fully specified disk file or a device››››     MYDOS User Manual               page 5                   Version 4.50›››››››››     specification  (such as E:, P: or one of the RS232 ports R1: to R4:).›     The  destination  may  be a set of disk files (specified with "*" and›     "?"s) only if the source specifies a file name for the destination to›     use.  The source may be a set and the destination a single disk file,›     but  unless the "/A" modifier is specified to append each copied file›     to  the end of the previously copied files, only the last source file›     will remain on the destination disk.›     ›          Note  that the "C" command always uses the full memory space for›     a copy operation (unlike ATARI DOS 2) and as a result, it will always›     invalidate  MEM.SAV  if  it  is  used.  Any pending program cannot be›     restarted after a "C" or "J" command.›     ›          There  are several options when entering files to copy.  As with›     all  filename  inputs, the default drive and directory (whatever "D:"›     is  equal  to  on  the  top  status  line) will be used if Dn: is not›     specified.  Using "/Q" at the end of the line will query you for each›     source file it finds (useful for copying certain files but specifying›     *.*)  if  you  wish to copy it. Using "/S" will copy all files EXCEPT›     those  with the first letter of the extender being "S" (will omit all›     *.S??).  This  emulates DOS 2.0's [O] copy file option, and is useful›     when you want to copy all files except .SYS files. The last option is›     the  "/X" parameter. This will prompt you for disk swaps, even if the›     source  and destination drives are not the same number. Here are some›     examples of using the [C]opy file(s) command:›     ›     "TEST.BAS"  will  copy  the  file  TEST.BAS on the default drive (and›     directory)  to  the  same  drive, but prompt you for the destination.›     (Same as the [O] command in DOS 2.0.)›     "D1:TE*.*,3"  will  copy  all  files on drive 1 starting with "TE" to›     drive 3.›     "D4:DIR>*.TXT,E:/Q" will copy all files in the DIR directory of drive›     4 ending with .TXT to the screen, but will query you before each one.›     "2:ADD,2:LIST/A"  will  append the data in the file ADD on drive 2 to›     the file LIST on drive 2.›     ›     ›     D. Delete a File or Set of Files›     ›          The  "D"  command  will  remove  all  files  that match the file›     specification  entered,  asking  for  confirmation before each one is›     removed.  The  "Delete  file  xxx?" prompts may be disabled by adding›     "/N"  to  the  filename. In this case, all the matching files will be›     removed  "quietly",  and  the only further indication you will see is›     the prompt for the next command.›     ›     ›     E. Rename a File or Set of Files›     ›          The  "E" command changes the name of the source file or files to›     match  the  specification  in  the  destination.  Unlike  other  file›     specifications,  the  destination  specification  MUST  consist  of a›     single  file  name: it must not contain any directory names or a disk›     drive  number.  For example, "D2:TEST>BASIC>NOTPNT.BAS,RANDIO.BAS" is››››     MYDOS User Manual               page 6                   Version 4.50›››››››››     the  line  entered  to  change  the name of a file in the directories›     "D2:TEST>BASIC>".  To  change  the  name  of the directory "BASIC" to›     "ATBASIC", the line would look like "D2:TEST>BASIC,ATBASIC". One word›     of  caution:  Never rename more than one file to another name without›     wildcards  in  the destination. For example, renaming "*.*" to "TEST"›     would  rename  EVERY file to "TEST", making it impossible to retrieve›     files other than the first one!›     ›     ›     F. Lock a File or Set of Files›     ›          The  "F" command limits access to the files identified. "Locked"›     files  may  not  be  deleted,  renamed, added to, or replaced without›     being  first  unlocked  with  the  "G"  command.  When a directory is›     listed, the files that have been locked will be marked with an "*" in›     the first column. The files that are locked may be read or loaded and›     executed  normally,  only  modification  or removal are prohibited. A›     locked  directory  cannot  be  deleted or renamed and no files may be›     written to it. The files already in it are not locked however.›     ›          MYDOS  will  not  ask  you  for confirmation on each file, "Lock›     xxx?" unless you specify this feature by adding "/Q" to the filename.›     ›     ›     G. Unlock a File or Set of Files›     ›          The  "G"  command removes the limitations imposed on a file when›     it  is  "locked" using the "F" command. It does not alter the file or›     otherwise  change  the  way  the  file  is accessed or used. The same›     function  may  be  performed in a program through the CIO function to›     "unlock" a file.›     ›          As   with   the  "F"  function,  MYDOS  will  not  ask  you  for›     confirmation  with  each  file to unlock, unless you specify the "/Q"›     parameter after the filename.›     ›     ›     H. Write MYDOS to a Disk›     ›          The  "H"  command is used to make a bootable copy of the current›     MYDOS  4.50  files  in memory. The two files created or rewritten are›     "DOS.SYS"  and  "DUP.SYS". "DOS.SYS" is the permanently resident file›     management  routine  accessed  through  CIO  and  the small interface›     package  that loads and saves MEM.SAV (an image of the part of memory›     used  to  hold the nonresident part (DUP.SYS) of MYDOS), and the code›     to load the menu portion of MYDOS  ("DUP.SYS"). The file "DUP.SYS" is›     a  standard  binary  load  file  containing the part of MYDOS that is›     overwritten  when  a  program is loaded into memory. Neither of these›     files  may  be  interchanged  with  any other version or type of disk›     operating  system;  both  should be treated as a single object. Never›     copy  only  DOS.SYS  or  only  DUP.SYS  to a disk without copying the›     other,  unless  you  will  never  access  the DUP.SYS menu (called by›     typing  "DOS"). The files written to the disk by the "H" command will›     reflect  the  configuration parameters currently in memory, which may››››     MYDOS User Manual               page 7                   Version 4.50›››››››››     be  different  from  the ones active if the system were rebooted from›     the  master  disk  again. (See Section IV.O., configuring the system,›     for  the  definition  of the configuration parameters provided in the›     system and how to specify a modified configuration.)›     ›     ›     I. Initialize a Diskette›     ›          The  "I"  command is used to "Format", or prepare a new disk for›     use with the MYDOS operating system, or to remove all the files on an›     old  disk.  The result of the "I" command is a completely empty disk.›     The  only  data  on  the diskette is that system provided information›     defining  the  space  available  and the empty main directory. If the›     drive  number  is followed by a "/N" parameter, the diskette will not›     be  reformatted,  but  just  "erased"  (the directory sectors will be›     rewritten).  If  a  disk  has  recently  been  formatted, this is the›     fastest way to remove all the files on a diskette, rather than to use›     the  "D" command. Use this option ONLY if you know the disk was good,›     for  this  does not verify the integrity of the disk. Due to a bug in›     some  hard  disk  interfaces,  this  "/N"  parameter may be needed to›     initially format the hard disk partitions.›     ›          A  diskette  may  also  be  formatted in the Atari 1050 enhanced›     format  by  responding  to  the  question  "(Type  [A]  to  format in›     Enhanced)  Type  [Y]  to  format  drive x:" with a "A" (presuming the›     drive  is a 1050 drive or compatible with the 1050). The diskette is,›     however,  not  compatible with the diskettes similarly created by DOS›     2.5.  The MYDOS diskette will not be readable by DOS 2.5, but DOS 2.5›     enhanced disks can be fully read by MYDOS.›     ›          An  additional note: it is a good idea to set the density of the›     drive  you  are  about  to format, unless the drive is not capable of›     double  density.  (see  the  "P"  command  for information on setting›     density.)  Otherwise,  MYDOS  will format the drive in the density of›     which it was last accessed.›     ›     ›     J. Duplicate a Diskette›     ›          The  "J" command copies all the information from one diskette to›     another.  The  information  to  be copied form the source diskette is›     determined  by  specifying a starting and an ending sector number. If›     the  range is not stated, the sectors marked as in use in the DOS bit›     map  (on the VTOC sectors) are copied. The VTOC may be constructed by›     Atari  DOS  2, any version of MYDOS or any other compatible operating›     system.›     ›          Specifying  a  sector  range  is  done  by  adding  two  numbers›     separated  by  a  dash  and enclosed in parentheses to the end of the›     drive  specification(s).  For  example, to copy sectors 19 through 54›     (tracks  1  through 3) from drive 1 to drive 3 without formatting the›     diskette  in  drive  3,  the command line could be "1,3/N(19-54)". To›     copy  the  entire  disk  from drive 1 to drive 2 after formatting the›     diskette  in  drive  2 the command could be "1,2(1-720)". This is the››››     MYDOS User Manual               page 8                   Version 4.50›››››››››     proper  way  to duplicate a non-MYDOS compatible diskette (of course,›     copies  of  "copy  protected" disks will not normally be usable after›     copying  but  data  disks  for  some word processors and games can be›     backed  up this way). Enhanced density disks may be duplicated in the›     same manner: "1,2(1-1040)".›     ›          If   the  destination  disk  is  already  a  properly  formatted›     diskette,  the "/N" modifier may be entered after either drive number›     to  skip  the  formatting  of  the  destination drive. Otherwise, the›     destination  diskette  will  be  formatted  before  the data from the›     source  is copied to it. That is, either "1/N,2" or "1,2/N" will copy›     from  drive  1  to  drive  2 without first formatting the diskette in›     drive 2.›     ›          Note  that  the  "J" command, like that in ATARI DOS 2, will use›     all of available memory to duplicate the diskette: this means that if›     memory  has  been  saved using the MEM.SAV file, it will no longer be›     valid.  Any  pending  program  cannot be restarted after a "C" or "J"›     command.›     ›     ›     K. Save Memory to Disk›     ›          The  "K"  command  builds a binary load file containing the data›     from  the  memory area specified, as well as adding an initialization›     and  a run vector address if specified. If the file is not to execute›     an  initialization routine on being loaded, the initialization vector›     should  be  omitted.  If  it  is  not to run on being loaded, the run›     vector  should also be omitted (trailing commas need not be entered).›     If  either  vector is entered as zero, that is equivalent to omitting›     it.  Note  that  the starting and ending addresses of the program and›     both  entry  points  are all specified as hex numbers. You may append›     data  to  another file by using the "/A" parameter.  This command may›     also be used for just adding a Run address to a binary file. Example:›     "D1:PROGRAM.OBJ/A,0,0,,4000"  would  add  the run address of $4000 to›     the program "PROGRAM.OBJ" on drive 1.›     ›          If  MEM.SAV  is  active  when  the  "K"  command is entered, the›     MEM.SAV file is loaded before writing the file to the disk.›     ›     ›     L. Load Memory from a File/Disable MEM.SAV›     ›          The "L" command takes a binary load file from the disk and loads›     it  into  memory.  The  load file's initialization routine(s) will be›     executed  and  the program started at its run address unless the "/N"›     parameter  is  added  to  the  file name. If the file is not a binary›     file, you will be returned with an "Error -- 180". A binary file that›     is corrupted will return an "Error -- 181".›     ›          This  command  also  disables the MEM.SAV feature before loading›     and  executing  the program. To just disable MEM.SAV, press "L", then›     [RETURN].›     ››››     MYDOS User Manual               page 9                   Version 4.50›››››››››     ›     M. Run at Address›     ›          The  "M" command is used to enter a program loaded without a run›     address,  or  to  jump into any program without the need for a return›     address.  It  may  be  used  to  restart  the  computer  (loading the›     AUTORUN.SYS  file, if any, or a new DOS, etc...) by specifying "E477"›     as  the  jump  address.  If  MEM.SAV  is active (enabled with the "N"›     command  and  not since disabled by the "L" command), the contents of›     memory  will  be  restored from MEM.SAV before jumping to the address›     specified.›     ›     ›     N. Load MEM.SAV from a File/Enable MEM.SAV›     ›          The "N" command takes a binary load file from the disk and loads›     it  into memory, just as does the "L" command. The difference is this›     command  enables  the MEM.SAV file before loading (and executing) the›     program;  and  when  control  is  returned  to MYDOS, the contents of›     memory will be saved back to MEM.SAV.›     ›          To  just  enable  MEM.SAV,  first enter this DOS menu (by typing›     "DOS" in BASIC), then press "N" and [RETURN].›     ›     ›     O. System and Drive Configuration›     ›          The "O" command is used to specify the type (at least logically)›     of  the  disk  drives  on  your  computer and is also used to specify›     several  system  configuration  parameters such as the number of file›     buffers  provided  or  whether  a  RAMdisk  is  present.  The  system›     configuration functions, which are not specific to individual drives,›     are  selected  by  pressing  [RETURN]  at the prompt "Drive number or›     RETURN:".  The  following  table  explains all the prompts for system›     configuration:›     ›     ›     Verify WRITEs?          N=do not write with verify, else do verify›     ›     Number of File Buffers? The number of disk files that can be open›                             at once (RETURN = 3)›     ›     RAM disk present?       N=no RAM disk on the system (skips the›                             next 4 questions as well), else the›                             RAMdisk is enabled, and the next questions›                             determine what kind it is.›     ›     [A]xlon or [X]E type?   A=Axlon, (RETURN)=XL or XE type. If›                             Axlon, skip the next question.›     ›     Use default config for (x)K? N=no, specify parameters. "Y" or›                             [RETURN] uses the parameters the DOS›                             generated for your type of machine. Note›                             that the "x" is replaced by the amount››››     MYDOS User Manual               page 10                  Version 4.50›››››››››                             of total memory MYDOS thinks you have.›                             Skip the next three questions if answered›                             yes.›     ›     Size(K)?                Size of the RAMdisk area in K (8 single›                             density sectors = 1K); this must be a›                             multiple of 16 (NI 256K upgrade=192 OR 128,›                             AXLON=112, default or 130XE=64).›     ›     Control Address(HEX)?   Address of the memory map control port: a›                             RETURN specifies $D301 for the 130XE. For›                             the AXLON RAMPOWER 128, enter "CFFF" here.›     ›     Page sequence?          [RETURN] if using a standard Atari 130XE›                             or equivalent RAMdisk. Other standard values›                             are (1) for the Newell industries upgrade,›                             (2) for the RAMBO from ICD, and (5) for›                             Axlon or compatible boards. The most›                             general response is to list the page›                             numbers to be used as 2 hex digits each,›                             separated by commas, and continuing if›                             necessary by ending the line with a comma.›                             The sequence is ended with a "0" if the›                             RAMdisk is 130XE compatible, and›                             with a "FF" if it is Axlon compatible.›     ›     RAM disk drive no?      Drive number used to access the RAMdisk›                             (RETURN for drive 9 or a drive number 1-9)›     ›          A  [RETURN] does not retain the current value when responding to›     these  questions;  it  changes  the setting to a generally acceptable›     default.  Even  a  BREAK  or  RESET  will not leave the configuration›     unchanged.  If  the  configuration process is aborted for any reason,›     and  you wish to retain your old configuration, you should reboot the›     computer or properly complete the configuration before doing anything›     else.›     ›          If  instead  of  a  [RETURN], a drive number had been specified,›     then  that drive would be reconfigured. The first question identifies›     whether  the  drive  is  to be included in system initialization (and›     thus be available for later use). If a non-existent disk is included,›     it does not cause any problems with the system: it simply causes that›     disk  to be examined each time the system is booted and reset (adding›     perhaps  a  second  to  the time it takes to boot MYDOS). If drive is›     excluded  from the system, no further questions are asked. Otherwise,›     the second question asks if the drive is configurable: that is, is it›     like  the  ATARI 810 drive (with a fixed configuration) or is it like›     the  PERCOM  or ATR8000 drives. If the disk is not configurable it is›     assumed   to  be  a  720  sector,  single  or  double  density  ATARI›     810/815/1050 disk drive.›     ›          The third question is whether the drive is a high capacity drive›     (does  it  use the modified configuration for non-floppy disks). This›     is  for  hard  disks.  This  should be answered "N" if the drive is a››››     MYDOS User Manual               page 11                  Version 4.50›››››››››     floppy disk drive, and "Y" if otherwise. If this question is answered›     "Y", the only remaining question is the size (in sectors, from 256 to›     65535)  of  the  drive.  Drives  up  to  16 million bytes (Megabytes)›     capacity  can  used  with  MYDOS,  and  larger  drives can usually be›     partitioned  to  appear as two or more drives of less than 16 million›     bytes  capacity.  See  your  hard disk manual for more information on›     this subject.›     ›          Drives that have not been configured can still be accessed. This›     configuration  is necessary ONLY when formatting hard disks, and when›     using  PERCOM  or ATR8000 interfaces. Other than the above, the drive›     configuration is not necessary - MYDOS will figure out by itself what›     the disk is capable of by its format.›     ›          If  the  first three answers are "N" (do not exclude the drive),›     "Y"  (it is configurable), and "N" (it is not a high capacity drive),›     the  configuration  is asked for: Is the drive double sided, how many›     tracks  are there on the each side of the disk, and at what speed can›     it  move the read/write head across the disk (what is its step rate).›     The  first question is answered with "Y" or "N" ("Y" meaning "yes" it›     is a double sided drive, and diskettes formatted on it will be double›     sided).  The  second  question  is  answered  with  35, 40, 77, or 80›     followed  by  a  [RETURN].  If you have IBM PC/AT style high capacity›     disk  drives (1.2Mb capacity) you may use 77 of the 80 tracks in high›     capacity  mode  providing  1  Mb  capacity by selecting 77 tracks. No›     other  numbers  are  accepted.  The answer to this question specifies›     both  the type of drive (8 inch/high capacity 5 1/4 inch, or standard›     5  1/4 inch) as well as the number of tracks per side. This answer is›     very important to the operation of the drive.›     ›          The  last  answer  ("Step  Rate?") is entered as a code: use the›     following  table and the drive specifications to determine the proper›     value:›     ›       Code value    8 inch rate     5 1/4 inch rate›           0         3 ms/track      6 ms/track    (XF-551)›           1         6 ms/track      12 ms/track›           2         10 ms/track     20 ms/track›           3         15 ms/track     30 ms/track›     ›     ›     P. Diskette Density Selection›     ›          The  density  used  for most MYDOS commands is determined by the›     data  written  on  the diskette and the operator need not worry about›     setting  it. The "P" command is provided to allow forcing the density›     setting  for  the  format  ("I")  command,  and to permit setting the›     density  for  disk  drives  and  systems  that  do  not automatically›     recognize  the  density  of  a  diskette  when  reading sector 1 (for›     example, Indus GT drives).›     ›          Type the drive number, followed by "S" or "D" to set the density›     of the drive. Example: "2,D".›     ››››     MYDOS User Manual               page 12                  Version 4.50›››››››››     ›     Q. Create Subdirectories›     ›          When  a  diskette  is formatted, an empty directory (the highest›     level  or  root  directory)  is created. This directory is capable of›     holding   up   to  64  files  or  other  directories.  If  additional›     directories  are  installed in this directory, each of the additional›     directories  can  contain  up  to 64 files as well. A subdirectory is›     installed  in  an  existing  directory  using  the  "Q"  command  and›     responding  with  the  filename of the new directory. For example, if›     "TEST"  and "BAS" are two subdirectories in the root directory of the›     diskette in drive 1, "1:TEST:COMM" or "1:BAS>COMM" would create a new›     directory   in   the   "TEST"   or  "BAS"  directories  respectively.›     "1:NEW:COMM"  would  not  create  a  directory,  however,  since  the›     directory  "NEW"  does  not  already  exist.  A  "Q" command with the›     response  "1:NEW"  would create it, however, and a second "Q" command›     with  the  response  "1:NEW:COMM" would then create the new directory›     called "COMM" within the directory "NEW".›     ›          Each  directory  takes  up 8 sectors, and after it is created it›     may  only be referenced as a directory (followed by a ":" or ">"), or›     deleted. It may only be deleted if it is empty (if it has no files in›     it). A directory may be emptied by using the "D" (delete) command and›     specifying  the files "*.*" or "*.*/N" to remove all the files in the›     directory. You can most safely do this by specifying the full name of›     the  directory:  D5:MSGBASE>SEPT1983>*.*/N for example. Now to delete›     the  SEPT1983 subdirectory, simply delete "D5:MSGBASE>SEPT1983" (note›     no trailing ":" or ">").›     ›     ›     R. Set the Default Directory›     ›          The  "R" command is used to select a directory to be used when a›     file is referenced without the drive number: that is, when file names›     such  as "TEST1.BAS" or "D:NEWCODE" or even ":BIGFILE" are used, they›     are  assumed to be in the default directory. Programs run under MYDOS›     can  access  the contents of the current default directory by using a›     file  name  of  the  form "D:..." without the drive number explicitly›     entered.  They  may also set the default directory by calling the CIO›     Function code 41 (set directory) routine.›     ›          The  directory  is  set  by  inserting  the  diskette  with that›     directory  on  it into the desired drive, then entering the file name›     of the directory with no trailing ":" or ">".›     ›          If the diskette in the drive containing the default directory is›     replaced,  or  if the default directory on a diskette is deleted, the›     default  should  be  redefined.  The  one exception is if the default›     directory  is  the  root  or  main  directory  on a diskette: this is›     because the root directory is at the same location on all diskettes.›     ›     ›     V. FILE MANAGER FUNCTIONS PROVIDED THROUGH CIO›     ››››     MYDOS User Manual               page 13                  Version 4.50›››››››››          This  part  of  the  documentation  is included in the technical›     notes of MYDOS, so consult those notes for details.›     ›     ›     VI. CIO FUNCTION CODES PROVIDED BY MYDOS 4.50›     ›          This  part  of  the  documentation  is included in the technical›     notes of MYDOS, so consult those notes for details.›     ›     ›     VIII. MYDOS MEMORY MAP›     ›          This  part  of  the  documentation  is included in the technical›     notes of MYDOS, so consult those notes for details.›     ›     ›     IX. CUSTOMIZING A SYSTEM DISK›     ›     ›          Much of this section is covered in the technical notes, but here›     are some things pertinent to all users.›     ›     ›     RAMdisk Configurations›     ›          The  RAMdisk  driver  included  in MYDOS 4.50 will automatically›     configure  itself  on  XE compatible memory upgrades. It is suggested›     you use this feature. If you REALLY want to set up the system to your›     specifications  (such as configuring it to NOT use the banks BASIC XE›     uses),   the  power  is  available.  This  is  necessary  when  AXLON›     compatible  upgrades  for the 800. The default page sequence uses the›     standard XE banks first.›     ›          The  file  RAMBOOT.M65, the MAC/65 assembler source code for the›     file RAMBOOT.AUT, is an AUTORUN.SYS file that simulates the operation›     of  Atari  DOS  2.5 and its RAMdisk handler. It "formats" the RAMdisk›     and  copies DUP.SYS to it, as well as setting the RAMdisk unit number›     and the unit used to access the DUP.SYS and MEM.SAV files to 8.›     ›          By modifying the code in the source file and creating a modified›     AUTORUN.SYS  file,  the  drive used to save MEM.SAV and fetch DUP.SYS›     can  be  modified, other files than just DUP.SYS can be copied to the›     RAMdisk  when  the  system is booted, or any other operation could be›     performed that you find useful.›     ›     ›     Number of Files Open at Once›     ›          The  number of files that may be simultaneously open is set with›     the  same byte as in ATARI DOS 2: location $0709 (decimal 1801). This›     byte  contains a number from 1 to 16 setting the number of disk files›     that  may  be  open  at  the  same time. Normally it is set to 3, the›     smallest  number  that  supports all the functions in the MYDOS menu.›     Specifically,  a  copy  from  one disk file to another requires three››››     MYDOS User Manual               page 14                  Version 4.50›››››››››     open  disk  files. The value in the distributed version of MYDOS 4.50›     is three; to permit more or fewer files, use the "O" command followed›     by  a  RETURN. To permanently change the maximum number of files, use›     the "H" command to write a modified MYDOS system to a disk. Each file›     that  may  be  open at one time requires the allocation of a 256 byte›     buffer, so setting this value to 7 (instead of 3) will cause MYDOS to›     be  1024 bytes longer than before, and the programs loaded must begin›     no  lower than $22E9 (instead of $1EE9). In corresponding fashion, by›     setting the value to 1, a BBS program can be loaded in with 512 bytes›     of  additional  memory if only one disk file is ever open at one time›     (commonly true of bulletin board programs).›     ›     ›     Controlling the Disk Drives Accessed by MYDOS›     ›          Like ATARI DOS 2, MYDOS automatically identifies the disk drives›     that  are  present  when  booted  up  initially  and  any  time it is›     reinitialized  (some programs do this on exiting to the DOS and it is›     always  done  if the RESET key is pressed). MYDOS 4.50 is distributed›     with  drives  1  and 2 configured, all others are omitted in order to›     speed  up  the  booting  process. To modify the maximum configuration›     MYDOS  will use, invoke the "O" command for each drive to be added to›     (or  removed  from)  the system. Pressing the RESET key will then use›     this  value  to redefine the drive. To permanently change the maximum›     drive  configuration,  use the "H" command to write out a new copy of›     MYDOS back to your system disk.›     ›     ›     Selecting or Disabling Write-with-Verify›     ›          MYDOS  4.50 is distributed with the verify disabled, to speed up›     writing. Most drives (and disks) are very reliable, and function with›     no  problems  with  the  verify  disabled. However, if you experience›     problems, or want to be 100% sure your data written will be good, use›     the  "V"  command  to  enable  verify.  As  with DOS 2.0, the byte at›     location  $0779  (1913  decimal) controls all write operations to the›     disk.  If  the  value  "poked"  into it is $57 (87 decimal), then all›     writes  will be read back to verify the action was successful. If the›     value  "poked"  into  $0779  is  $50 (80 decimal) then writes will be›     assumed successful, and will be performed in about one third the time›     taken  when verify is enabled. Note that this address is not the same›     as  in  MYDOS  4.0  and  4.1 (where it was $0770 or 1904 decimal). To›     permanently  alter the DOS, rewrite it back to the disk using the "H"›     command after changing it.›     ›     ›     X. DISK DRIVE INTERFACE (via SIO)›     ›          This information is covered in the technical notes for MYDOS.›     ›     ›     XI. RAMDISK INTERFACE›     ›          This information is also covered in the technical notes.››››     MYDOS User Manual               page 15                  Version 4.50›››››››››     ›     ›     XII. INITIAL INSTALLATION INSTRUCTIONS›     ›          The  following  checklist  is a procedure to bring up MYDOS on a›     new  hardware  configuration.  It  should be done with an un-modified›     copy  of MYDOS 4.50, and care should be taken to perform the steps in›     exactly the order specified.›     ›     HOW TO GET FROM THE DRIVEWAY TO THE FREEWAY:›     ›       1. Before turning on your computer and disk drive, make sure that›          you do not have a cartridge installed in the computer.›       2. Turn on the disk drive, and when it stops spinning, insert the›          MYDOS master diskette. Close the door.›       3. Turn on the computer (with OPTION held if using an XL or XE›          computer). After several seconds, the MYDOS menu should appear›          on the screen. A prompt "Select Item (RETURN for menu):" will›          be displayed.›       4. If you have a standard 2-drive system with single sided 40›          track drives and either no RAMdisk or the standard Atari›          130XE memory configuration, continue with step "6".›       5. Configure each of your disk drives only if they are hard›          disks or special double-sided (XF-551) or more than 40›          tracks by entering the "O" command followed by the drive›          number, and answering the questions the program asks you.›       6. If you need to run a program that requires more than 3 disk›          files active at a time or you otherwise want alter one of›          the default parameters, press the "O" key followed by the›          RETURN key and answer the system configuration questions.›          This is also where the RAMdisk configuration needs to be›          entered if it is not a standard 130XE RAMdisk. ****›       7. Now, insert a blank diskette in the disk drive and format it›          with the "I" command (remove the write protect tab if the›          diskette is write protected -- but first ask yourself why›          you put it there in the first place!). If an error message›          is displayed, insert another diskette; the first is bad.›       8. Write the system files DOS.SYS and DUP.SYS to the newly›          formatted diskette with the "H" command and skip to step›          "10" if you do not have an ATARI 130XE computer or some›          other RAMdisk usable with the MYDOS RAMdisk driver.›       9. If you have an ATARI 130XE computer or have another kind of›          RAMdisk and wish to use the MYDOS RAMdisk driver, copy›          RAMBOOT3.AUT on the master diskette to AUTORUN.SYS on the›          new diskette (use the "C" command, and if you have only one›          drive, enter the command line "RAMBOOT.AUT,AUTORUN.SYS/X"›          when MYDOS asks for the file names).**›      10. This is now your primary system backup disk: place a write›          protect tab on it, label it, and use the "J" command to›          make as many working boot disks as you need from it.›     ›     ›     NOTES:›     ››››     MYDOS User Manual               page 16                  Version 4.50›››››››››          The  RAMBOOT3  program will first format your RAMdisk, then copy›     the  files  in  a  directory  called RAMDISK on your boot disk to the›     RAMdisk  if  such  a  directory  exists.  To  take  advantage of this›     feature,  use  the  "Q"  command to create the directory and copy the›     files  you want on the RAMdisk to it. If you do not want your ramdisk›     formatted  each time you boot-up, which is not recommended, skip this›     step (step 9). Just be sure you format your ramdisk before using it.›     ›     ›      ** -- The source file for the RAM disk boot is also included; if›            you feel the urge, modify it to copy other files to the›     RAMdisk›            in addition to DUP.SYS (take out the MEM.SAV setting code,›            too, if you need the space) or perhaps add a call to change›            the default disk drive to D8:. Just remember that if you›            string together several autorun files, only the last will have›            its RUN address invoked.›     ›     **** -- NEWELL INDUSTRIES 800XL UPGRADE -- this RAMdisk can use›            page sequence 0, page sequence 1, or the default. The›            E3/E7/EB/EF pages can be reserved for BASIC/XE in›            extended mode by setting the RAMdisk size to 128K and›            the sequence to 1. Enter Size=128 (or 192 if you will›            not be using BASIC/XE often), Control address=D301, and›            Page sequence=1. In the second case this will use the area›            also used by BASIC/XE, but it will access it only after›            the first 128K are used up. By setting the size to 128K,›            BASIC/XE and the RAMdisk are fully separate and cannot›            interfere with each other.›     ›     **** -- AXLON RAMPOWER 128 for the Atari 800 computer -- MYDOS›            4.50 comes configured for the Atari 130XE -- if you are›            installing it on an 800 with an Axlon RAMPOWER board, you›            must disable the 128K mode on the RAMPOWER board until›            you have configured the MYDOS RAMdisk code by entering›            Size=112, Control address=CFFF and Page sequence=5. Then›            write the DOS back to a new diskette, copy AUTORUN.SYS›            to it, switch the RAMPOWER board back to 128K and boot›            up the new diskette.›››››››››››››››››››     MYDOS User Manual               page 17                  Version 4.50›››››››››     ›     XIII. ERROR CODES AND THEIR SOURCES›     ›       3   Last byte of file read, next read will return EOF (MYDOS)›     128   Break Abort (OS ROMs)›     129   IOCB already open (OS ROMs)›     130   No such device defined in the system (OS ROMs)›     131   Write-only IOCB, cannot read (OS ROMs)›     132   Invalid command (OS ROMs)›     133   Device or File not open (OS ROMs)›     134   Invalid IOCB reference (OS ROMs)›     135   Read-only IOCB, cannot write (OS ROMs)›     136   Attempt to read past end of file (MYDOS)›     137   Truncated record (OS ROMs)›     138   Device Timeout (OS ROMs)›     139   Device NAK (serial bus failure, OS ROMs)›     141   Cursor out of range for graphics mode (OS ROMs)›     142   Data frame overrun (serial bus failure, OS ROMs)›     143   Data frame checksum error (serial bus failure, OS ROMs)›     144   Device I/O error (in peripheral hardware, OS ROMs)›     146   Function not provided by handler (OS ROMs)›     147   Insufficient RAM for graphics mode selected (OS ROMs)›     160   Invalid Unit/Drive Number, zero or greater than 7 (both›           MYDOS and OS ROMs)›     161   No sector buffer available, too many open files (MYDOS)›     162   Disk full, cannot allocate space for output file (MYDOS)›     163*  Write protected or system error - disk is not readable (MYDOS)›     164   File number in link does not match the file's directory›           location (MYDOS)›     165   Invalid file name (MYDOS)›     166   Byte not within file, invalid POINT request (MYDOS)›     167   File locked, cannot be altered (MYDOS)›     168   Invalid IOCB (MYDOS and OS ROMs)›     169   Directory full, cannot create a 65-th entry in a directory›           -- entries may be used for "lost" as well as real files›           (MYDOS)›     170   File not in directory, cannot be opened for input (MYDOS)›     171   IOCB not open (MYDOS and OS ROMs)›     172*  File or directory of same name already exists in parent›           directory, cannot create (MYDOS)›     173   Bad diskette or drive, cannot format diskette (MYDOS)›     174*  Directory not in parent directory (MYDOS)›     175*  Directory not empty, cannot delete (MYDOS)›     180*  Not a binary file (MYDOS)›     181*  Invalid address range for binary file, END<BEGIN (MYDOS)›     ›     * -- New error codes, not present or different in Atari DOS 2.›     ›          Most  error codes are identical to those returned from ATARI DOS›     2;  the  differences  result from the expanded capabilities of MYDOS.›     Specifically,  Error  164,  indicating  a file number mis-match, only›     occurs  if  the  file is written in DOS 2.0 or DOS 2.5 format. Errors›     180  and  181 can only occur when XIO 39 (or 40) is invoked to load a›     file.  Errors  172 and 175 apply to creating and deleting directories››››     MYDOS User Manual               page 18                  Version 4.50›››››››››     and  have  no  ATARI DOS 2 equivalent; error 174 applies to accessing›     files  in  subdirectories,  so it also has no ATARI DOS 2 equivalent.›     Error code 173 serves the same function as it did in ATARI DOS 2, but›     is returned more often (to identify bad diskettes more reliably).›     ›››››››››››››››››››››››››››››››››››››››››››››››››››››     MYDOS User Manual               page 19                  Version 4.50››››