›››››     ›     ›     ›     ›     ›     ›     ›     ›     ›                      MYDOS Version 4 Technical User Guide›                                  Revision 4.50›                            for Atari Home Computers›     ›     ›             Copyright (C) 1988 by WORDMARK Systems and the authors:›     ›                               Charles Marslett›                               2705 Pinewood Dr.›                               Garland, TX 75042›                                   CIS: 73317,3662›                                   UseNet: CHASM@KILLER.DALLAS.TX.US›     ›                                        and›     ›                               Robert Puff›                               Suite 222›                               2117 Buffalo Rd.›                               Rochester, NY 14624›                                   GEnie: BOB.PUFF›     ›     ›     ›          This  software  may be freely used and distributed provided that›     this copyright notice is left intact, and provided that:›     ›     (1) The source code in machine readable form is provided with›         any binary distribution, or made available at no additional cost›         to the recipients of the binary distribution.›     ›     (2) A binary version of a derivative work may be sold for a›         reasonable distribution charge (less than $50), and the›         source code in machine readable format must be available.›     ›     (3) A derivative work may not impose and restriction on the free›         distribution of the source code.›››››››››››››     MYDOS Technical Manual          page 1                   Version 4.50›››››››››     ›     IV. THE MENU COMMANDS: The MEM.SAV feature›     ›          Whenever  the  DOS menu is entered, MYDOS will load DUP.SYS from›     drive  1.  If DUP.SYS cannot be found on drive 1, it will look for it›     on drive 2, 3, etc... until it finds it.›     ›          Loading DUP.SYS will overwrite a good chunk of lower memory, and›     will  wipe out the data in most languages. Here's where MEM.SAV comes›     into  play.  When  this  feature is enabled (by going to the menu and›     pressing  "N"  and  [RETURN], then "B" to exit back), the memory that›     DUP.SYS  would  overwrite  is  saved to the file "MEM.SAV" on drive 1›     (may  be drive 8 if you use one of the RAMBOOT programs on the disk).›     It  then  loads  the DUP.SYS. When you press "B" to return, or if you›     use the "N" command of the menu, MYDOS will load back in the MEM.SAV,›     thus  restoring  the  overwritten  memory. The result is your program›     remains intact.›     ›     ›     V. FILE MANAGER FUNCTIONS PROVIDED THROUGH CIO›     ›          MYDOS  supports all CIO calls supported by ATARI DOS 2, with the›     following  modifications to the OPEN (Function code 3) and the FORMAT›     (Function  code  254)  functions. Three additional CIO functions have›     been  added:  MAKE  DIRECTORY  (Function code 34 & 42), SET DIRECTORY›     (Function code 41) and LOAD MEMORY (Function code 39 & 40).›     ›          The  OPEN function in ATARI DOS 2 does not use the data provided›     in  the  AUX2 byte, but in MYDOS when the AUX1 byte is 8 (the file is›     opened for creation or replacement), the AUX2 byte contains two flags›     that  control  the file format, and whether it will be created locked›     or not.›     ›          If  AUX2  bit  2  is  set,  the  file will be written in MYDOS 4›     format,  and  may contain sectors beyond absolute sector 1023. Such a›     file  may not (easily) be read by DOSes other than MYDOS. This is the›     only  format used with high capacity disks. If AUX2 bit 5 is set, the›     file  will  be  written  with  the  "LOCKED" bit in the directory set›     initially.  This is provided for use by multi-tasking functions (such›     as  a  print  spooler,  sequential file pre-reading function or other›     enhancements  one  might  want  to  make  to  the  standard OS or DOS›     provided functions).›     ›          The  FORMAT  function  in  ATARI  DOS 2 does not provide for any›     variations  to  the standard disk usage: in MYDOS the contents of the›     AUX1  and AUX2 bytes are used to specify the number of sectors on the›     disk  being  formatted, and whether the disk needs to be formatted by›     the  controller as well as needing directory initialization. Bit 7 of›     AUX1  is  set  to  skip  the  physical  formatting of the entire disk›     surface when it is not required, and bits 6-0 of AUX1 and all of AUX2›     are  used  to specify the number of sectors on the disk being created›     (if  all 15 bits are zero, the disk is assumed to be the size defined›     by  the  drive configuration). This permits formatting a single sided›     diskette  on  double sided drives, for example. Be careful when using››››     MYDOS Technical Manual          page 2                   Version 4.50›››››››››     this feature.›     ›          To  load  (and  possibly execute) a program file, MYDOS provides›     the  CIO  function  39 call. CIO function 40 will do the same; it was›     included  for compatibility with programs written for SpartaDOS. From›     BASIC  you  can load and execute a program by executing the line: XIO›     39,  #3,  4, 0, "D:MYPROG.OBJ". Any inactive IOCB can be used, and if›     AUX1=4 both the INIT and the RUN entries will be executed. If AUX1=5,›     the  RUN  entry  will  be executed; if AUX1=6, the INIT entry will be›     executed;  and  if  AUX1=7, the file will be loaded without executing›     either  entry  point.  Any  other values of AUX1 will return an error›     code and do nothing.›     ›          Another  XIO call, XIO 34, has been added to create a directory.›     CIO  function  42  performs  exactly  the  same  thing,  and has been›     provided  for compatibility with programs written for SpartaDOS. When›     a  directory  is  created,  the name used must not match any existing›     file  or  directory in its parent (for example if the directory to be›     created  is  named "D1:TEST>BUGS", there can be no other directory in›     the main directory named "TEST" nor a file named "TEST" there.›     ›          From  BASIC,  the XIO 34 call is "XIO 34, #iocb, 8, 0, dirname",›     where  "iocb" is any available unit number, and "dirname" is the name›     of the new directory (it does not end with a trailing ":" or ">").›     ›          The final function added to those provided by ATARI DOS 2 is XIO›     41,  to  define  the default directory. The default directory is that›     which  will be searched for a file if the file name begins with "D:".›     In  ATARI  DOS 2 this default directory is always "D1:" but in MYDOS,›     the  default directory can be any root or subdirectory on any disk in›     the  system.  The  buffer address passed to CIO in the XIO 41 call is›     the  address  of  a  string that contains the default directory name,›     terminated with either an end of line ($9B) or a null byte ($00). The›     directory will be accessed before returning to the calling program so›     that  an  error in specifying the directory will be reported as early›     as possible.›     ›     ›     VI. CIO FUNCTION CODES PROVIDED BY MYDOS 4.50›     ›     Function code 3, OPEN›     ›          The open function uses the buffer address to point to an ATASCII›     string terminated with a non-alphanumeric character or wildcard. This›     string  is  the  name  of  the file to be accessed or created. A good›     terminator  for  this string is either a null ($00) or an end of line›     ($9B).›     ›          The  AUX1 byte defines the usage of the file: 4 for input, 6 for›     directory  data  reading,  8  for  creating/replacing  output,  9 for›     creating/appending   output   and   12   for   input/update  (without›     extension). The AUX2 byte is used when a file is replaced or created,›     and  contains two significant bits: bit 2 set causes the MYDOS format›     to  be used even if the diskette is a 40 track single sided diskette;››››     MYDOS Technical Manual          page 3                   Version 4.50›››››››››     and  bit 6 set results in the file being LOCKed initially without and›     additional  CIO  call.  For input, update or directory access AUX2 is›     ignored, and the length is always ignored. In normal use, AUX2 is set›     to zero emulating ATARI DOS 2 usage.›     ›          MYDOS  does not leave partially full sectors when appending to a›     file.  This  has two positive effects on programs which open files in›     append  mode:  the  open  will fail if the file cannot be appended to›     rather  than  the  close  (in  ATARI DOS), and the file size will not›     change  if a file appended to is copied to another disk (in ATARI DOS›     it may grow smaller).›     ›     ›     Function code 5, GET RECORD›     ›          The  get record function reads a line of data into a buffer, the›     buffer  being defined by its starting address and length. The line is›     defined  as the data bytes in the file up to an end of line character›     ($9B)  or  until the buffer is full, whichever occurs first. The line›     is  also terminated if the end of the file is read. All record I/O is›     buffered  in  MYDOS,  so record transfers are necessarily slower than›     unbuffered I/O.›     ›          No  other fields of the IOCB are referenced or needed. Note that›     the  ATARI ROM OS supports single byte I/O through the accumulator if›     the  buffer  length  is  set  to  0. In this case, GET RECORD and GET›     CHARACTERS function exactly the same way.›     ›     ›     Function code 7, GET CHARACTERS›     ›          The get characters function reads a fixed number of bytes from a›     file  into  a  buffer,  the  buffer  being defined by its address and›     length  (two  16-bit  numbers  in the IOCB). The only cases where the›     buffer is not always filled is if the end of the file is read, or the›     file  cannot  be  read  withut  error. As is the case with get record›     calls,  a single byte may be read into the accumulator by setting the›     length  field  to  zero.  A  get  character  CIO  call  will  perform›     unbuffered  I/O  if  the buffer is longer than 256 bytes (ATARI DOS 2›     sets a similar threshold at 128 bytes). For this reason a single long›     input is considerably faster than several short ones.›     ›          Only  the  buffer address and length in the IOCB are used by the›     get characters function.›     ›     ›     Function code 9, PUT RECORD›     ›          The  put  record  command  will write a single line to an output›     file:  the  line  defined  by  the starting address of the buffer and›     either  the  length  of  the buffer if no end of line ($9B) bytes are›     encountered,  or  the first end-of-line byte. Only the buffer address›     and length in the IOCB are used in this command.›     ››››     MYDOS Technical Manual          page 4                   Version 4.50›››››››››     ›     Function code 11, PUT CHARACTERS›     ›          The  put  characters command will write the contents of a buffer›     defined  by its address and length (in the IOCB) to a file opened for›     output.  Unless  an error occurs, the entire buffer is always written›     to  the file unless the write is to an output/update file and the end›     of  the file is reached or the write is to an output/append or create›     file  and  the  disk  has  filled. Only the buffer address and length›     fields  in the IOCB are used when the put character function is used.›     The  single  byte  put  character  (using  the A register as data) is›     supported by setting the length bytes to 0.›     ›     ›     Function code 12, CLOSE A FILE›     ›          To terminate use of a file (and for an output file, to write the›     incomplete  buffer  to  the  disk)  the  IOCB used to access the file›     should  be  closed.  This is done by setting the function code in the›     IOCB  to  12  and calling CIO. The close function does not use any of›     the data in the IOCB for any purpose whatsoever.›     ›     ›     Function code 13, READ STATUS›     ›          The  read status command is issued to an unopened IOCB, with the›     buffer  address  that  of  a  file  name  string.  If the file is not›     present,  that  error  condition  is  returned, if it is locked, that›     error  condition  is returned; otherwise, a normal completion code is›     returned.  Only  the function code and the buffer address in the IOCB›     are needed.›     ›     ›     Function code 32, RENAME A FILE›     ›          The  rename function is passed a character string (pointed to by›     the buffer address in the IOCB), the first part of the string being a›     file  name  identifying  the file or files to be renamed. Following a›     single  invalid  character  (one invalid in the file name, that is) a›     simple  file  name must also be present: this second file name cannot›     include  any  drive  or directory names. An example, using a comma as›     the invalid character, is "D2:TEST>PGMS>A.OUT,ZCPY" which will change›     the   string  needed  to  access  the  file  "D2:TEST>PGMS>A.OUT"  to›     "D2:TEST>PGMS>ZCPY"  --  Note  that  only  the  last  file  name  (if›     subdirectories  are  used)  can  be  changed;  to  change  "PGMS"  to›     "MLPROGS", the buffer must contain "D2:TEST>PGMS,MLPROGS".›     ›          Wild  card characters should appear only in the part of the file›     name  following  the  last  ":"  or  ">",  and  their  effect is best›     described  by  an example. The string "D2:TEST:*.*,*.XYZ" will rename›     all the files in the TEST directory, making each extension ".XYZ". If›     the  directory  had the files "ATEST.BAS", "LOG", and "REPORT.XYZ" in›     it,  the  result would be a directory with "ATEST.XYZ", "LOG.XYZ" and›     "REPORT.XYZ" in it.››››     MYDOS Technical Manual          page 5                   Version 4.50›››››››››     ›     ›     Function code 33, DELETE A FILE›     ›          The  delete  function removes any files that match the file name›     string  pointed  to  by  the buffer address in the IOCB. Files locked›     will  not  be  deleted, so must be unlocked before being removed, and›     subdirectories  that  are not empty (that have a file in them) cannot›     be deleted. If either case is attempted, the corresponding error code›     is  returned.  Otherwise,  the files are removed and their data areas›     are  returned  to  the  free  space on the disk. Files that have been›     deleted  may  be  "undeleted" by various utility programs ONLY if the›     data  has  not  been  overwritten. If you write to the disk after you›     have  just deleted a file on that disk, chances are that you will not›     be able to recover the file.›     ›     ›     Function code 34, MAKE DIRECTORY›     ›          The  make directory function will create a new subdirectory on a›     disk (it is not used to create the first directory, that is the "root›     directory" identified by the drive specification "D1:", for example).›     It  is  called  through  CIO  by  storing  the  address  of  the  new›     directory's  name  in the IOCB buffer address and setting up AUX1 and›     AUX2  as  for an open call (see Function code 3), normally AUX1=8 and›     AUX2=0. This function has no effect on the current default directory;›     and  if it is desired to make the newly created directory the default›     one,  the  program  must make a set directory call (Function code 41)›     following  the  make  directory  call  (the  order is very important,›     because  the  default  directory  cannot  be  set  to  a  nonexistent›     directory).  CIO  function  code  42  may also be used to access this›     function; the parameters are the same.›     ›     ›     Function code 35, LOCK FILE›     ›          A file can be "locked" so that it may not be modified or deleted›     inadvertently,  by  calling  CIO  with  the lock function. The buffer›     address  is  used  to point to a file name string that identifies the›     files  on  the disk to be locked. The only file modification that can›     be  performed on a locked file is to unlock it. The lock function can›     be  requested  for a file already locked, and it will return no error›     (unlike  other file modification calls to CIO), but the status of the›     file will not have been changed.›     ›     ›     Function code 36, UNLOCK FILE›     ›          The  unlock  function  is  identical to the lock function except›     that  is re-enables the modification or deletion of an unlocked file.›     A  file that is not locked can be unlocked with no error returned and›     no change in the file's status.›     ›     ››››     MYDOS Technical Manual          page 6                   Version 4.50›››››››››     Function code 37, POINT TO POSITION IN FILE›     ›          The  point  function  is  passed  the  3-byte disk address to be›     positioned to in the twelfth through fourteenth bytes of the IOCB. On›     return,  the  next  byte read from that IOCB will be the one that was›     read  or  written  next  after  the  corresponding  note function was›     executed.  A  point  call  to CIO can only be made if the file can be›     used  for  input:  that  is,  if  it  is  opened  for input or update›     processing.  The  first  two  bytes  of the disk address are a sector›     number  (in  low  byte  / high byte format) and the third is the byte›     (offset) within the sector.›     ›          If  a  file  is  being appended to (opened with AUX1=9), a point›     function  call  made before closing the file may return an unexpected›     error (this cannot happen with the note function, however).›     ›          A  problem can occur if the file being pointed to is in the last›     half  of  a 16 Megabyte disk: Atari BASICs do not allow sector number›     to  be  greater  than 32767. A solution is to use the following BASIC›     substitute  for  the POINT statement (with attention paid to the fact›     the the two AUX bytes must match the two used to open the file):›     OPEN #K,AUX1,AUX2,"D5:BIGFILE"›     . . .›     NOTE #K,SECTOR,BYTE›     . . .›     POKE 844+16*K,ASC(CHR$(SECTOR)):POKE 845+16*K,INT(SECTOR/256)›     POKE 846+16*K,BYTE: XIO 37,#K,AUX1,AUX2,"D:"›     ›     ›     Function code 38, NOTE POSITION IN FILE›     ›          The  note  function  returns  in  the twelfth through fourteenth›     bytes  of  the IOCB a 3-byte disk address that may be used at a later›     time  to  reposition  the  file  using  the  point function. The note›     function  can  be  used  on  files  open for input, output, update or›     appending.  The  three  bytes returned are the low byte of the sector›     address,  the  high byte of the sector address, and the byte (offset)›     within the sector, in that order.›     ›     ›     Function code 39, LOAD MEMORY›     ›          The load memory function takes a file formatted in the ATARI DOS›     2  executable  program  format  (generated by the "K" command, by the›     assembler/editor  cartridge,  by  AMAC or MAC65, or by any of several›     compilers  for  the  ATARI  computers),  and  loads its contents into›     memory as specified in the file. No offset control is provided and no›     part   of   memory   is  protected  from  the  loading  process.  The›     initialization  and  execution addresses (if any) can be individually›     enabled  and  disabled, to permit loading and patching a program then›     writing it back to the disk for normal use.›     ›          To  load  a  program  into  memory, the address of the file name›     string is stored into the buffer address, and a value of 4, 5, 6 or 7››››     MYDOS Technical Manual          page 7                   Version 4.50›››››››››     is  stored into the AUX1 field. If AUX1 is 4, both the initialization›     routines and the run address are executed after closing the IOCB, but›     before   returning  to  the  calling  program.  If  AUX1  is  5,  the›     initialization routines are disabled, but the program will be run. If›     AUX1  is  6, the initialization routines will be run, but the program›     execute address will be loaded and ignored. If AUX1 is 7, the text of›     the program will be loaded into memory, but no other activity will be›     performed.  CIO  function code 40 performs the exact same function as›     this (39).›     ›     ›     Function code 41, SET DEFAULT DIRECTORY›     ›          The set directory command will use the contents of the buffer as›     a  file name and open the specified file, determining if that file is›     a  valid  directory. If so, it will become the new default directory.›     File  names  of the form "D:..." will be assumed to be in the default›     directory  (which  may be on any disk in the system and may be either›     the root directory of that disk or a subdirectory).›     ›          Only  the  buffer  address and the function code are significant›     when setting the default directory.›     ›     ›     Function code 254, FORMAT A DISKETTE›     ›          The  format  function uses the contents of the buffer pointed to›     by  the  buffer address to identify the drive containing the diskette›     to  be  formatted.  If  both  AUX1  and  AUX2  are  zero, the disk is›     formatted  according to the capacity data in the system control table›     defined  using the "O" command. If AUX2 bit 7 is set to 1, the format›     operation  is  skipped  and  an  empty  file system is written to the›     diskette.  (This  assumes the disk is preformatted.) The remaining 15›     bits  of  AUX1  and  AUX2  are used as a 15 bit number to specify the›     number  of  sectors  available on the disk (permitting the use of the›     last  few  sectors of a disk outside the file system if desired). You›     may format a disk in enhanced density (MYDOS compatible - not DOS 2.5›     type format) by setting AUX1 to 1, and AUX2 to 0.›     ›     ›     VII. DISK STRUCTURES SUPPORTING MYDOS 4.50›     ›          MYDOS  uses  the first three sectors of a disk to hold some disk›     information  and  the  initial  boot  program  if  the drive contains›     DOS.SYS and DUP.SYS. Sector $168 (and sectors $167, $166, $165, etc.,›     if  the  disk  is  formatted as a higher capacity disk not compatible›     with  ATARI DOS 2) is used to hold a bit map of available sectors and›     several  flag  byte  identifying  the  default format of files on the›     disk.  Sectors  $169  through  $170 contain main disk directory data,›     identifying  the  files  on  the disk, their sizes and their starting›     sector number.›     ›          Note  that  this usage, when the diskette is a 719 sector volume›     declared to be DOS 2 compatible, is in fact exactly the same as ATARI››››     MYDOS Technical Manual          page 8                   Version 4.50›››››››››     DOS 2 would make of the disk. The default single sided format differs›     only  in  that sector 720 is not left out of the file system in MYDOS›     but  is  used to provide 708 free sectors on an empty diskette rather›     than  707.  The  only  significant change made when the high capacity›     format  is  chosen  are  that  enough  sectors before sector $168 are›     allocated to assign a bit for each sector that may be allocated for a›     file  or for use by the system (VTOC sectors). The high capacity disk›     directory  may  be read by ATARI DOS 2, but the data in the files can›     only  be  accessed  if it falls in the first 1023 sectors of the disk›     and  then only if the file number checking code in DOS 2 is disabled.›     This  format  allows MYDOS to support accessing disks of up to 65,535›     sectors of 256 bytes each (approximately 16 Mbytes).›     ›          Compatibility  with DOS 2.0 is further reduced if subdirectories›     are  used:  to ATARI DOS, the subdirectories will appear to be simple›     files  with unreadable contents. The subdirectory's files will not be›     accessible  and  the  subdirectory can be damaged if it is written to›     (even  by  appending).  For  this  reason  disks  sold to the general›     public,  exchanged  with  friends,  and  so forth, should not contain›     subdirectories  unless  there  is  reason to require that the disk be›     used  with MYDOS. A further problem with exchanging diskettes is that›     there  are many different formats are used by vendors of double sided›     disk  systems  for the ATARI. For this reason, double sided disks not›     only require both computers use MYDOS, but also require that they use›     the same disk system (PERCOM, SWP, Astra, Supra or whatever).›     ›     ›     VIII. MYDOS 4 MEMORY MAP›     ›          The  MYDOS  4.50  disk  operating  system occupies the area from›     $0700  to  $1EE9  at  all times, and when the menu is active, it also›     occupies  the  area  from  $294A  to $4331. In addition, the first 16›     bytes  of  the floating point workspace ($D4 - $E3) are used by MYDOS›     at  that  time.  Unlike  ATARI DOS 2, MYDOS utility program (DUP.SYS)›     also  calls the floating point ROM entry points. The nonresident part›     of  MYDOS 4.50 starts loading at $294A, reserving the area from $1EE9›     to  $2949 for disk buffers and drivers. Allocating three disk buffers›     leaves approximately 2500 bytes for resident drivers that will not be›     overwritten by the nonresident portion of DOS (contained in DUP.SYS).›     ›     ›     IX. CUSTOMIZING A SYSTEM DISK›     ›     RAMdisk Configurations›     ›          The  RAMdisk driver included in MYDOS 4.50 is already configured›     for  the  Atari 130XE computer and uses its banked 64K bank of memory›     for  the  RAMdisk  providing  499  free  (single  density,  128 byte)›     sectors.  The "O" command provides an easy way to alter the operation›     of  the  RAMdisk  driver for other common banked memory systems. Most›     memory  upgrades for the 800XL and 130XE use the same mapping address›     (the  PORTB pins of the PIA chip in the computer). A 128K RAMdisk can›     be used in an Atari 130XE using the last unused pin of that port with›     no  tradeoff (selecting the 64K bank is done with bit 6 of PORTB). If››››     MYDOS Technical Manual          page 9                   Version 4.50›››››››››     you  have  such  a system, enter a "2" for the page sequence, or just›     use  the  default  sequence  (answer "Y" to the question "Use default›     page sequence...").›     ›          If,  instead  of adding one or two rows of 64K memory chips, the›     enhancement  replaces the entire memory of the computer with a single›     bank  of 256K memory chips, then the banked memory is a total of 192K›     and  4 bits of the port must be used to select the memory bank. Often›     the bits used are bits 0 and 1 (as in the 130XE) along with bit 6 (as›     in  the  expansion  above)  and  bit  5 (used in the 130XE to control›     banking  screen memory). Programs that bank screen memory (a very odd›     proposition  because  of the difficulty of obtaining a useful sharing›     of  the  banked  memory  page  bits between the screen memory and the›     program)  will  not  work with this enhancement. This is the approach›     used in the Newell Industries 256K upgrade for the Atari 800XL.›     ›          If  the  enhancement is done externally or to an Atari 800 (with›     its  internal  expansion slots), a new dedicated register may be used›     to  map  the 16K pages. The Axlon RAMPOWER 128 card for the Atari 800›     works this way. In such a system, the pages are selected by writing a›     page  number  to the mapping address and no sharing of the 8 bit byte›     is  necessary.  The  address  of  the  mapping  register  is  entered›     explicitly and page sequence "5" is the proper sequence.›     ›          The page sequence table coded into MYDOS is actually one 32 byte›     sequence table of numbers to be stored in the mapping register. MYDOS›     4.50  has  a  feature  that allows you to skip all this configuration›     stuff,  if  the upgrade is XE compatible. In the configuration, MYDOS›     will  create  a  custom  page  sequence  for your memory upgrade, and›     update  its  pointers.  If you choose to enter our own page sequence,›     the  number  of  16K pages determines the number of bytes to be used.›     You  may  use  one  of the four built-in page sequences by entering a›     single sequence number:›     ›     Seq. No.    Page Values                         OR Value›         0        E3, E7, EB, EF, C3, C7, CB, CF,›                  83, 87, 8B, 8F, A3, A7, AB, AF       00›         1        C3, C7, CB, CF, 83, 87, 8B, 8F,›                  E3, E7, EB, EF, A3, A7, AB, AF       00›         2        A3, A7, AB, AF, C3, C7, CB, CF,›                  E3, E7, EB, EF, 83, 87, 8B, 8F       00›         5        00, 01, 02, 03, 04, 05, 06, 07,›                  08, 09, 0A, 0B, 0C, 0D, 0E, 0F       FF›     ›     As an example, if you want to use BASIC/XE in extended mode (or use a›     program  that  uses the standard XE banks: pages E3, E7, EB, and EF),›     and  you  have  a RAMBO XL upgrade, set your memory size to 128K, and›     use the page sequence of:›           1›           or›           C3,C7,CB,CF,83,87,8B,8F,00›     This  will  configure the RAMdisk to use only that part of the banked›     memory not used by BASIC/XE.›     ››››     MYDOS Technical Manual          page 10                  Version 4.50›››››››››          The file RAMBOOT.M65, the MAC/65 assembler source code for which›     is in the file RAMBOOT.AUT, is an AUTORUN.SYS file that simulates the›     operation  of Atari DOS 2.5 and its RAMdisk. It "formats" the RAMdisk›     and  copies DUP.SYS to it, as well as setting the RAMdisk unit number›     and the unit used to access the DUP.SYS and MEM.SAV files to 8.›     ›          By modifying the code in the source file and creating a modified›     AUTORUN.SYS  file,  the  drive used to save MEM.SAV and fetch DUP.SYS›     can  be  modified, other files than just DUP.SYS can be copied to the›     RAMdisk  when  the  system is booted, or any other operation could be›     performed that you find useful.›     ›     ›     Number of Files Open at Once›     ›          The  number of files that may be simultaneously open is set with›     the  same byte as in ATARI DOS 2: location $0709 (decimal 1801). This›     byte  contains a number from 1 to 16 setting the number of disk files›     that  may  be  open  at  the  same time. Normally it is set to 3, the›     smallest  number  that  supports all the functions in the MYDOS menu.›     Specifically,  a  copy  from  one disk file to another requires three›     open  disk  files. The value in the distributed version of MYDOS 4.50›     is  three.  To  permit  more or fewer files open, use the "O" command›     followed  by  a  RETURN.  To permanently change the maximum number of›     files,  use  the  "H"  command  to write a modified MYDOS system to a›     disk.  Each file that may be open at one time requires the allocation›     of  a  256 byte buffer so setting this value to 7 (instead of 3) will›     cause  MYDOS  to  be  1024  bytes longer than before and the programs›     loaded  must  begin  no  lower  than  $22E9  (instead  of  $1EE9). In›     corresponding  fashion,  by setting the value to 1, a BBS program can›     be  loaded  in  with  512 bytes of additional memory if only one disk›     file  is  ever  open  at  one  time  (commonly true of bulletin board›     programs).›     ›     ›     Controlling the Disk Drives Accessed by MYDOS›     ›          Like ATARI DOS 2, MYDOS automatically identifies the disk drives›     that  are  present  when  booted  up  initially  and  any  time it is›     reinitialized (some programs do this on exiting to the DOS, and it is›     always  done  if the RESET key is pressed). MYDOS 4.50 is distributed›     with  drives  1  and 2 configured, all others are omitted in order to›     speed  up  the  booting  process. To modify the maximum configuration›     MYDOS  will use, invoke the "O" command for each drive to be added to›     (or  removed  from)  the system. Pressing the RESET key will then use›     this  value  to  redefine  the  system  to configure the drive(s). To›     permanently  change  the  maximum  drive  configuration,  use the "H"›     command, writing a new copy of MYDOS back to the system disk.›     ›     ›     Selecting or Disabling Write-with-Verify›     ›          MYDOS  4.50  is distributed with the write-with-verify disabled.›     Most  drives are very reliable, and will never give you a problem. If››››     MYDOS Technical Manual          page 11                  Version 4.50›››››››››     however,  something  happens  (such  as  dust, a scratch in the oxide›     coating,  or  some  other  problem  that  may  have  arisen since the›     diskette  was  formatted), the error might not be detected. In short,›     if  you  are  working  with  something that you want to be absolutely›     positive  that is perfectly saved, enable the verify. This will cause›     the  drive to read back each sector after it has been written, taking›     about three times the time normally taken on a write without verify.›     ›          The  byte  at  location  $0779 (1913 decimal) controls all write›     operations  to  the  disk.  If  the  value "poked" into it is $57 (87›     decimal),  then all writes will be read back to verify the action was›     successful.  If the value "poked" into $0779 is $50 (80 decimal) then›     writes will be assumed successful, and will be performed in about one›     third  the  usual  time. Note that this address is not the same as in›     MYDOS  4.0 and 4.1 (where it was $0770 or 1904 decimal). This byte is›     defined,  along  with  the  count  of  the  number  of  buffers to be›     allocated  when  the  file  manager  is initialized, whenever the "O"›     command  is invoked with no drive specified (only a RETURN is entered›     in  response  to  the  drive  number query). To permanently alter it,›     rewrite  MYDOS  back to the disk using the "H" command after changing›     it.›     ›     ›     X. DISK DRIVE INTERFACE (via SIO)›     ›          The physical disk drives and diskettes are external to the ATARI›     home  computers  and  the  ones  supported  by  MYDOS  4 are normally›     attached  to  the  "serial  interface connector" on the right side or›     back  of  the  computer.  High  capacity  or "hard" disks may also be›     connected  to  the  parallel  port  of 800XL and 130XE computers. The›     software  in  the  operating  system  (OS ROMs) to access the devices›     attached  to  either connector is call the "serial I/O driver" or SIO›     for  short.  The  MYDOS  disk  operating system uses this lower level›     driver  to pass all commands and information to and from the physical›     disk  drive.  Several  commands  were defined by ATARI to communicate›     with  the  810  disk  drive and most vendors of high performance disk›     systems  for  the  Atari  have adopted a slightly extended version of›     this  set  of  commands. MYDOS will operate with any disk system that›     supports  the  original  810  set,  but  the  full set of commands is›     required  to  support  all  the  functions.  An  additional  function›     necessary  to  perform  automatic density selection is that the drive›     should  automatically  identify the density of a diskette inserted in›     it if the first operation is a read of sector 1 (this is necessary if›     the drive is to boot either a double or single density diskette).›     ›          The  minimum  set  of  disk drive functions to support MYDOS (or›     ATARI DOS 2 for that matter) are:›     ›     Device   Unit   Command  Direction   Byte Ct. Aux Bytes  Function›     $31    Drive#    $21    From Drive  128/256      0      FORMAT DISK›     $31    Drive#    $50    To Drive    128/256   1 to 720  WRITE(no vfy)›     $31    Drive#    $52    From Drive  128/256   1 to 720  READ›     $31    Drive#    $53    From Drive     4           0      READ STATUS›     $31    Drive#    $57    To Drive    128/256   1 to 720  WRITE(verify)››››     MYDOS Technical Manual          page 12                  Version 4.50›››››››››     ›     An additional command to format a disk in enhanced density is:›     ›     $31    Drive#    $22    From Drive    128          0      FORMAT DISK›     ›          The  byte count is always 128 for a single density drive, and is›     128  for  the  first  three sectors (1, 2, and 3) of a double density›     drive.  All  other  sectors  on  a double density drive are 256 bytes›     long.›     ›          The FORMAT function is always called with a sector number in the›     range  of  4 to 720. It expects 128 bytes from a single density drive›     and 256 bytes from a double density drive.›     ›          The  first  byte returned by the READ STATUS command is expected›     to  indicate  the  sector  size -- if bit 5 is a 1 (bit 7 is the sign›     bit)  then  the  sectors  are  large (256 bytes), otherwise, they are›     small (128 bytes).›     ›          The auxiliary bytes are treated as an address to a sector on the›     diskette,  and range from 1 to 720 (when in DOS 2 compatible mode) or›     from 1 to 65,535 (when accessing large capacity disk drives).›     ›          The   additional   functions   used  to  configure  disk  drives›     dynamically are:›     ›     Device   Unit   Command  Direction   Byte Ct. Aux Bytes  Function›     ›     $31    Drive#    $4E    From Drive     12       1 to 720  READ CFG.›     $31    Drive#    $4F    To Drive       12       1 to 720  WRITE CFG.›     ›          These  commands  are  used to configure the drives identified as›     configurable  when  the computer is booted: if there is a possibility›     that  a  drive does not support these functions, it should be defined›     as  not configurable (such as the Atari 810). These commands are used›     by  the  "P"  command,  permitting reconfiguration of a disk drive on›     demand  -  to format a diskette, for example. (To format a disk on an›     Indus  drive, issue the "P" command to manually change the density on›     the drive, then issue the "I" command).›     ›          The individual bytes transferred by these commands are defined›     as follows:›       byte 0: Tracks per side (40 for a standard disk drive)›       byte 1: Disk Drive Step Rate (as defined by Western Digital)›       byte 2: Sectors/Track -- high byte (usually 0)›       byte 3: Sectors/Track -- low byte(18 for standard diskettes)›       byte 4: Side Code (0=single sided, 1=double sided)›       byte 5: Disk Type Code --›               bit 2: 0=single density, 1=double density›               bit 1: 0=5 1/4 inch diskette, 1=8 inch diskette drive›       byte 6: High byte of Bytes/Sector (0 for single density)›       byte 7: Low byte of Bytes/Sector (128 for single density)›       byte 8: Translation control›               bit 7: 1=40 trk. disk I/O on an 80 trk. drive››››     MYDOS Technical Manual          page 13                  Version 4.50›››››››››               bit 6: Always 1 (to indicate drive present)›               bit 1: 1=Handle sectors 1, 2, and 3 as full size sectors›               bit 0: 1=Sectors number 0-17 (for example), not 1-18›       bytes 9-11 are not used by MYDOS (see the drive documentation as›               to how they are to be set -- usually zeroes)›     ›          MYDOS  4.50  (unlike  version  3  of MYDOS) always issues a read›     configuration  command  before writing the configuration to the drive›     and  the  contents  of  bytes  9-11  are written exactly as they were›     previously read (so they will be unchanged).›     ›          An  additional change in the usage of this command occurs when a›     high capacity drive (hard disk) is configured. The configuration data›     for  such a drive is very complex and is usually built into the drive›     controller  or  written to a "magic" location on the disk. To support›     partitioning  of  very large drives (larger than 16 Megabytes), MYDOS›     issues  a  write configuration command with the number of sectors per›     track  set  to  number  of sectors on the disk (as defined in the "O"›     command)  and  the number of tracks set to 1. All high capacity disks›     are large sector drives (using 256 byte sectors).›     ›     ›     XI. RAMDISK INTERFACE›     ›          The  driver  built  into MYDOS is intended to eliminate the need›     for  a  "driver" to use common RAMdisks. The required characteristics›     of  the  hardware  can be most easily described by explaining what is›     done to access a "sector" of information in the extended RAM.›     ›         (1) The sector number is divided by 128, and the›             remainder is then multiplied by 128 and added›             to 16384 to get the starting address of the›             sector in memory (it will be between $4000 and $7F00).›         (2) The quotient is used to index into a page table›             with one entry for each 16K that can be mapped›             into the memory area from $4000 to $7FFF.›         (3) The value from the page table is "AND"ed with the›             contents of the mapping register, and rewritten›             to the mapping register.›         (4) The data is moved to(from) the area addressed above›             from(to) the sector buffers at the high end of MYDOS.›         (5) The mapping register is restored to its›             non-mapping state by "OR"ing the restore value with›             the mapping register and rewriting the result›             to the mapping register.›     ›          Note  that  this  design forces the RAMdisk to be single density›     and  no  larger than 4 megabytes (256 pages of 16384 bytes each). Out›     of  that, MYDOS can only accommodate 1 megabyte, because its table is›     only 64 bytes long.›     ›          As  you can see, the parameters are the mapping register address›     ($CFFF  for  Axlon  boards  and $D301 for the Atari 130XE), the value›     "OR"ed  into the register to reset the system back to normal ($FF for››››     MYDOS Technical Manual          page 14                  Version 4.50›››››››››     the  Axlon  and  $00  for  the Atari 130XE types), and the actual map›     values.  These values are determined by first identifying the bits in›     the  mapping register to be left unchanged and setting them to "1" in›     each of the register values. Second, the remaining bits are filled in›     with  all  the legal combinations of mapping bits. The values for the›     Newell Industries 256K upgrade (which uses the 130XE mapping, more or›     less)  are  given here as an example -- future versions of this board›     and  other memory expansion products are not necessarily going to use›     the same design.›        Bits: 7  6  5  4  3  2  1  0›              1  x  x  x  x  x  1  1   First, set bits 7, 1 & 0›                                       in all the mapping values›              1  0  0  0  0  0  1  1   These are the 12 (of 32)›              1  0  0  0  0  1  1  1›              1  0  0  0  1  0  1  1›              1  0  0  0  1  1  1  1›              1  1  0  0  0  0  1  1›              1  1  0  0  0  1  1  1›              1  1  0  0  1  0  1  1›              1  1  0  0  1  1  1  1›              1  1  1  0  0  0  1  1›              1  1  1  0  0  1  1  1›              1  1  1  0  1  0  1  1›              1  1  1  0  1  1  1  1›     ›          Lastly,  since the mapping register at $D301 can be read as well›     as  written,  it  can  be left exactly as it was before we used it by›     "OR"ing  the  initial  value  with  zero  (leaving it unchanged). The›     sequence is then: 83, 87, 8B, 8F, C3, C7, CB, CF, E3, E7, EB, EF, 0.›››››››››››››››››››››››››››››     MYDOS Technical Manual          page 15                  Version 4.50›››››››››     ›     XIII. ERROR CODES AND THEIR SOURCES›     ›       3   Last byte of file read, next read will return EOF (MYDOS)›     128   Break Abort (OS ROMs)›     129   IOCB already open (OS ROMs)›     130   No such device defined in the system (OS ROMs)›     131   Write-only IOCB, cannot read (OS ROMs)›     132   Invalid command (OS ROMs)›     133   Device or File not open (OS ROMs)›     134   Invalid IOCB reference (OS ROMs)›     135   Read-only IOCB, cannot write (OS ROMs)›     136   Attempt to read past end of file (MYDOS)›     137   Truncated record (OS ROMs)›     138   Device Timeout (OS ROMs)›     139   Device NAK (serial bus failure, OS ROMs)›     141   Cursor out of range for graphics mode (OS ROMs)›     142   Data frame overrun (serial bus failure, OS ROMs)›     143   Data frame checksum error (serial bus failure, OS ROMs)›     144   Device I/O error (in peripheral hardware, OS ROMs)›     146   Function not provided by handler (OS ROMs)›     147   Insufficient RAM for graphics mode selected (OS ROMs)›     160   Invalid Unit/Drive Number, zero or greater than 7 (both›           MYDOS and OS ROMs)›     161   No sector buffer available, too many open files (MYDOS)›     162   Disk full, cannot allocate space for output file (MYDOS)›     163*  Write protected or system error - disk is not readable (MYDOS)›     164   File number in link does not match the file's directory›           location (MYDOS)›     165   Invalid file name (MYDOS)›     166   Byte not within file, invalid POINT request (MYDOS)›     167   File locked, cannot be altered (MYDOS)›     168   Invalid IOCB (MYDOS and OS ROMs)›     169   Directory full, cannot create a 65-th entry in a directory›           -- entries may be used for "lost" as well as real›           files (MYDOS)›     170   File not in directory, cannot be opened for input (MYDOS)›     171   IOCB not open (MYDOS and OS ROMs)›     172*  File or directory of same name already exists in parent›           directory, cannot create (MYDOS)›     173   Bad diskette or drive, cannot format diskette (MYDOS)›     174*  Directory not in parent directory (MYDOS)›     175*  Directory not empty, cannot delete (MYDOS)›     180*  Not a binary file›     181*  Invalid address range for loading a binary file, END<BEGIN›     (MYDOS)›     ›     * -- New error codes, not present or different in Atari DOS 2.›     ›          Most  error codes are identical to those returned from ATARI DOS›     2;  the  differences  result from the expanded capabilities of MYDOS.›     Specifically,  Error  164,  indicating  a file number mis-match, only›     occurs  if the file is written in DOS 2 or DOS 2.5 format. Errors 180›     and 181 can only occur when XIO 39 (or 40) is invoked to load a file.››››     MYDOS Technical Manual          page 16                  Version 4.50›››››››››     Errors  172  and  175  apply to creating and deleting directories and›     have  no ATARI DOS 2 equivalent; error 174 applies to accessing files›     in  subdirectories,  so  it also has no ATARI DOS 2 equivalent. Error›     code  173  serves  the same function as it did in ATARI DOS 2, but is›     returned more often (to identify bad diskettes more reliably).›     ››››››››››››››››››››››››››››››››››››››››››››››››››››     MYDOS Technical Manual          page 17                  Version 4.50››››