*******************************************************************************
                                     Piasw
*******************************************************************************

CUPL            2.15b Serial# 6-00001-421
Device          p16l8  Library DLIB-h-24-8
Created         Sat Feb 04 11:36:46 1995
Name            Piasw
Partno          TBD
Revision        01
Date            03/02/95
Designer        Peter
Company         N/A
Assembly        Atari800
Location        Q101

===============================================================================
                            Expanded Product Terms
===============================================================================

CB2_out =>
    !CB2_a & !CB2_b
  # !CB2_b & !os800
  # !CB2_a & os800

PIA1_cs =>
    !A2 & os800 & piaCS
  # A0 & A2 & !os800 & piaCS
  # !A0 & !A2 & !os800 & piaCS

PIA2_cs =>
    A2 & os800 & piaCS
  # A0 & !A2 & !os800 & piaCS
  # !A0 & A2 & !os800 & piaCS

CB2_out.oe  =>
    1 

PIA1_cs.oe  =>
    1 

PIA2_cs.oe  =>
    1 



===============================================================================
                                 Symbol Table
===============================================================================

Pin Variable                                    Pterms   Max     Min    
Pol   Name              Ext     Pin     Type     Used   Pterms  Level   
--- --------            ---     ---     ----    ------  ------  -----   

    A0                          3        V        -       -       -     
    A2                          2        V        -       -       -     
    CB2_a                       4        V        -       -       -     
    CB2_b                       5        V        -       -       -     
    CB2_out                     15       V        3       7       1     
 !  PIA1_cs                     13       V        3       7       1     
 !  PIA2_cs                     14       V        3       7       1     
 !  os800                       6        V        -       -       -     
 !  piaCS                       1        V        -       -       -     
    CB2_out             oe      15       D        1       1       0     
    PIA1_cs             oe      13       D        1       1       0     
    PIA2_cs             oe      14       D        1       1       0     


LEGEND    F : field      D : default variable        M : extended node
          N : node       I : intermediate variable   T : function
          V : variable   X : extended variable       U : undefined



===============================================================================
                                   Fuse Plot
===============================================================================

Pin #19 
 0000 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0032 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0064 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0096 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0128 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0160 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0192 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0224 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #18 
 0256 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0288 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0320 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0352 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0384 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0416 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0448 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0480 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #17 
 0512 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0544 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0576 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0608 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0640 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0672 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0704 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0736 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #16 
 0768 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0800 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0832 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0864 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0896 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0928 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0960 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 0992 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #15 
 1024 -------------------------------- 
 1056 ---------x---x------------------ 
 1088 -------------x--x--------------- 
 1120 ---------x-------x-------------- 
 1152 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1184 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1216 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1248 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #14 
 1280 -------------------------------- 
 1312 x--x-------------x-------------- 
 1344 -x-xx-----------x--------------- 
 1376 x--x-x----------x--------------- 
 1408 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1440 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1472 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1504 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #13 
 1536 -------------------------------- 
 1568 -x-x-------------x-------------- 
 1600 x--xx-----------x--------------- 
 1632 -x-x-x----------x--------------- 
 1664 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1696 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1728 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1760 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
Pin #12 
 1792 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1824 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1856 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1888 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1920 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1952 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 1984 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 
 2016 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx 


LEGEND    X : fuse not blown 
          - : fuse blown 


===============================================================================
                                 Chip Diagram
===============================================================================

                               ______________
                              |    Piasw     |
                   !piaCS x---|1           20|---x Vcc                      
                       A2 x---|2           19|---x                          
                       A0 x---|3           18|---x                          
                    CB2_a x---|4           17|---x                          
                    CB2_b x---|5           16|---x                          
                   !os800 x---|6           15|---x CB2_out                  
                          x---|7           14|---x !PIA2_cs                 
                          x---|8           13|---x !PIA1_cs                 
                          x---|9           12|---x                          
                      GND x---|10          11|---x                          
                              |______________|