;***********************************************************
;***********************************************************
;
; FILES REQUIRED:     C32.EXE
;                 C32DEMO.BAT
;                 C32DEMO.DOC
;                 C32DEMO.TBL
;
;         TO RUN: Copy all files to a directory
;                 C32DEMO <CR>
;
;***********************************************************
;
;       Cross-32 Meta-Assembler Version 2.0
;
;       The Cross-32 Meta-Assembler from Universal Cross-
;       Assemblers is a table based macro cross-assembler
;       that compiles programs for numerous different
;       target processors on any MS-DOS computer.  For
;       the purposes of this demo, only a table for the
;       Intel 8051 processor is provided.  The assembler
;       will write the value 0DDH in all data locations
;       of the hex output file, but is otherwise fully
;       functional.
;
;       By using a flexible instruction table structure,
;       Cross-32 assembles source code for many microprocessors,
;       microcontrollers and digital signal processors,
;       written in the original manufacturer's mnemonics.
;       Cross-32 reads the assembly language source file
;       and a corresponding assembler instruction table,
;       and writes a list file and an absolute hexadecimal
;       machine file in the binary, Intel or Motorola
;       formats.  This hexadecimal file can then be down-
;       loaded to most EPROM programmers, EPROM emulators
;       and in circuit emulators.
;
;       Cross-32 saves the cost of purchasing many
;       individual assemblers, and reduces the time needed
;       to learn numerous different products.  It can be
;       difficult enough to grasp the intricacies of
;       different processors, without having to master new
;       tools.  To further simplify the learning process,
;       Cross-32 uses features of the C programming
;       language wherever possible.
;
;       The Cross-32 User's Manual includes full
;       directions for writing new processor tables, and
;       modifying those supplied.  Since many new
;       processor's assembly language instruction sets are
;       merely supersets of one of the processors included
;       with Cross-32, this can be as simple as adding
;       several lines to an existing table.  Therefore, as
;       new processors are introduced, the assembler does
;       not become obsolete, and your investment is
;       protected.
;
;       Processor Families Included:
;            1802/5/6
;            37700
;            3870/F8
;            4004/40
;            50740/37450
;            64180
;            6502/C02
;            65816
;            6800/1/2/3/8/6301/3
;            6805/HC05
;            6809
;            68HC11
;            68HC16
;            68000/8/10/302
;            8041
;            8048/49
;            8051/52
;            8085/80
;            8086/88/186/188
;            8096/C196KC
;            80166
;            COP400
;            COP800
;            H8/300
;            H8/500
;            NEC7500
;            NEC781x
;            PIC165x
;            PIC1742
;            SUPER8
;            TMS3201x
;            TMS3202x
;            TMS34010
;            TMS370
;            TMS7000
;            TMS9900/95
;            Z8
;            Z80
;            Z180
;            Z280
;            Z8002/4
;            Call regarding others...
;
;       Assembler Directives
;            ;         Comment
;            CPU       Processor
;            DFB       Define byte or string
;            DFS       Define data storage
;            DWM       Define word
;            DWL       Define inverted word
;            DFL       Define long word
;            ELSE      Alternate conditional
;            END       End of assembly
;            ENDI      End of IF block
;            ENDM      End of MACRO block
;            EQU       Equate label to value
;            HEX       Switch hex file on or off
;            HOF       Select hexadecimal format
;            IF        Conditional assembly
;            INCL      Include file into source
;            LIST      Switch list file on or off
;            MACRO     Define macro
;            ORG       Program counter origin
;            PAGE      Listing Page length and eject
;            SETL      Alterable equate label
;            TITL      Title starting listing pages
;            WDLN      Size of processor word
;
;       Labels
;            -unlimited length
;            -all characters significant
;            -must start with A-Z,_,., or ?
;            character
;            -may include A-Z, 0-9,_.,
;            and ? characters
;            -must end with colon :
;
;       Numeric Constants
;            32-bit signed integers
;            ANSI C: 0xnn, 0nn, nn
;            Trailing character:
;            nnB,nnO,nnQ,nnD,nnH
;            $ sign: $nn
;            Decimal is default base
;            Range -2,147,483,648 to
;            2,147,483,647
;
;       Operators
;            Arithmetic and logical
;            Similar to ANSI C
;            {}   script parentheses
;            !    logical complement
;            ~    arithmetic complement
;            +    unary addition
;            -    unary subtraction
;            INV  invert byte order
;            *    multiplication
;            /    division
;            %    modulus
;            +    addition
;            -    subtraction
;            <<   left shift
;            >>   right shift
;            <    less than
;            <=   less than or equal to
;            >    greater than
;            >=   greater than or equal to
;            ==   equal to
;            !=   not equal to
;            &    arithmetic AND
;            ^    arithmetic XOR
;            |    arithmetic OR
;            &&   logical AND
;            ||   logical    OR
;            ,    multiple expressions
;
;       Other Special Symbols
;            $    value of program counter
;            "    character "string"
;
;       Editor
;            Use your favorite ASCII editor
;            or word-processor in non-document
;            mode
;            Error output compatible with many
;            programming editors
;
;       Error Output
;            file(row,column): message
;            sent to screen and listing
;            compatible with many programming
;            text editors giving an integrated
;            programming environment
;
;       Command Line
;            C32 filename -L listname -H hexname
;
;       Hexadecimal Output
;            User chooses format using
;            HOF directive from:
;                 Binary
;                 Intel Hex and Extended Hex
;                 Motorola S records:
;                      S19, S28, or S37
;
;       Processor Instruction Tables
;            Tables for ALL processors listed above are
;            included.
;            Tables are ASCII files that may be printed
;            and edited.
;            Tables have a four part structure defining
;            registers; operands and their ranges; addressing
;            modes; and mnemonics.
;            Creating a new table requires 3 to 30 hours
;            of work, depending on the processor's complexity.
;
;       Benchmark
;            Assembles 6000 lines per minute of 6801
;            source code on a 12 MHz 80286 computer.
;
;       Documentation
;            User's manual
;            Table of contents
;            Index
;            Numerous examples
;            Instructions for creating processor tables
;            Example source file for each processor on disk
;
;       Support
;            Call the above number anytime
;            Will talk to registered users for as long as
;            they wish
;
;       System Requirements
;            MS-DOS 2.0 or later
;            256 kilobytes RAM
;            3.5" 720k or 5.25" 1.2M floppy drive
;
;       License
;            Each unit of Cross-32 may be used on only one
;            keyboard of one computer at any given time.
;            Unauthorized use, duplication or distribution
;            is strictly prohibited.
;
;       Other Features
;            Case insensitive
;            Two pass assembler with third pass if a phase
;            error occurs.
;            Program counter range: 0 to 4,294,967,295
;            Binary checksum displayed on screen
;            Not copy protected.
;
;       Available from:
;            Universal Cross-Assemblers
;            P.O. Box 6158
;            Saint John, NB, Canada
;            E2L 4R6
;            Tel/Fax: (506)847-0681
;
;       For only US$199.00!!!
;            American Express, Mastercard and VISA accepted!
;            Free planet wide airmail shipping!


;******************************************************
;	8051 TEST FILE

	CPU	"C32DEMO.TBL"
	HOF	"INT8"
        PAGE    56           ;PAGE LENGTH
        TITL    "8051 DEMO"  ;TITLE
        PAGE                 ;PAGE EJECT

;******************************************************
;MCS-51 INTERNAL REGISTERS
;
B:        EQU       0F0H      ;B REGISTER
ACC:      EQU       0E0H      ;ACCUMULATOR
PSW:      EQU       0D0H      ;PROGRAM STATUS WORD
IPC:      EQU       0B8H      ;INTERRUPT PRIORITY
P3:       EQU       0B0H      ;PORT 3
IEC:      EQU       0A8H      ;INTERRUPT ENABLE
P2:       EQU       0A0H      ;PORT 2
SBUF:     EQU       99H       ;SEND BUFFER
SCON:     EQU       98H       ;SERIAL CONTROL
P1:       EQU       90H       ;PORT 1
TH1:      EQU       8DH       ;TIMER 1 HIGH
TH0:      EQU       8CH       ;TIMER 0 HIGH
TL1:      EQU       8BH       ;TIMER 1 LOW
TL0:      EQU       8AH       ;TIMER 0 LOW
TMOD:     EQU       89H       ;TIMER MODE
TCON:     EQU       88H       ;TIMER CONTROL
PCON:     EQU       87H       ;POWER CONTROL REGISTER
DPH:      EQU       83H       ;DATA POINTER HIGH
DPL:      EQU       82H       ;DATA POINTER LOW
SP:       EQU       81H       ;STACK POINTER
P0:       EQU       80H       ;PORT 0
;
;MCS-51 INTERNAL BIT ADDRESSES
;
CY:       EQU       0D7H      ;CARRY FLAG
AC:       EQU       0D6H      ;AUXILIARY-CARRY FLAG
F0:       EQU       0D5H      ;USER FLAG 0
RS1:      EQU       0D4H      ;REGISTER SELECT MSB
RS0:      EQU       0D3H      ;REGISTER SELECT LSB
OV:       EQU       0D2H      ;OVERFLOW FLAG
P:        EQU       0D0H      ;PARITY FLAG
PS:       EQU       0BCH      ;PRIORITY SERIAL PORT
PT1:      EQU       0BBH      ;PRIORITY TIMER 1
PX1:      EQU       0BAH      ;PRIORITY EXTERNAL 1
PT0:      EQU       0B9H      ;PRIORITY TIMER 0
PX0:      EQU       0B8H      ;PRIORITY EXTERNAL 0
EA:       EQU       0AFH      ;ENABLE ALL INTERRUPT
ES:       EQU       0ACH      ;ENABLE SERIAL INTERRUPT
ET1:      EQU       0ABH      ;ENABLE TIMER 1 INTERRUPT
EX1:      EQU       0AAH      ;ENABLE EXTERNAL 1 INTERR
ET0:      EQU       0A9H      ;ENABLE TIMER 0 INTERRUPT
EX0:      EQU       0A8H      ;ENABLE EXTERNAL 0 INTERR
SM0:      EQU       09FH      ;SERIAL MODE 0
SM1:      EQU       09EH      ;SERIAL MODE 1
SM2:      EQU       09DH      ;SERIAL MODE 2
REN:      EQU       09CH      ;SERIAL RECEPTION ENABLE
TB8:      EQU       09BH      ;TRANSMITT BIT 8
RB8:      EQU       09AH      ;RECEIVE BIT 8
TI:       EQU       099H      ;TRANSMIT INTERRUPT FLAG
RI:       EQU       098H      ;RECEIVE INTERRUPT FLAG
TF1:      EQU       08FH      ;TIMER 1 OVERFLOW FLAG
TR1:      EQU       08EH      ;TIMER 1 RUN CONTROL BIT
TF0:      EQU       08DH      ;TIMER 0 OVERFLOW FLAG
TR0:      EQU       08CH      ;TIMER 0 RUN CONTROL BIT
IE1:      EQU       08BH      ;EXT INTERR. 1 EDGE FLAG
IT1:      EQU       08AH      ;EXT INTERR. 1 TYPE FLAG
IE0:      EQU       089H      ;EXT INTERR. 0 EDGE FLAG
IT0:      EQU       088H      ;EXT INTERR. 0 TYPE FLAG

	ORG	0200H
;
	ACALL	ABSOL		;B180

LADD:	ADD	A,R0		;28
	ADD	A,R1		;29
	ADD	A,R2		;2A
	ADD	A,R3		;2B
	ADD	A,R4		;2C
	ADD	A,R5		;2D
L0:	ADD	A,R6		;2E
L2:	ADD	A,DIRECT	;2580
L1:	ADD	A,R7		;2F
;L3:	ADD	A,@R0		;26
;L4:	ADD	A,@R1		;27
;L5:	ADD	A,#IMM8		;24F0

LADDC:	ADDC	A,R0		;38
	ADDC	A,R1		;39
	ADDC	A,R2		;3A
	ADDC	A,R3		;3B
	ADDC	A,R4		;3C
	ADDC	A,R5		;3D
	ADDC	A,R6		;3E
	ADDC	A,R7		;3F
	ADDC	A,DIRECT	;3580
	ADDC	A,@R0		;36
	ADDC	A,@R1		;37
	ADDC	A,#IMM8		;34F0

	AJMP	ABSOL		;A180

	ANL	A,R0		;58
	ANL	A,R1		;59
	ANL	A,R2		;5A
	ANL	A,R3		;5B
	ANL	A,R4		;5C
	ANL	A,R5		;5D
	ANL	A,R6		;5E
	ANL	A,R7		;5F
	ANL	A,DIRECT	;5580
	ANL	A,@R0		;56
	ANL	A,@R1		;57
	ANL	A,#IMM8		;54F0
	ANL	DIRECT,A	;5280
	ANL	DIRECT,#IMM8	;5380F0
	ANL	C,CY		;82D7
	ANL	C,2AH.6		;8256
	ANL	C,P0.5		;8285
	ANL	C,/CY		;B0D7
	ANL	C,/PSW.7	;B0D7
	ANL	C,/2AH.6	;B056

	CJNE	A,DIRECT,$+42H	;B5803F
	CJNE	A,#IMM8,$+42H	;B4F03F
	CJNE	R0,#IMM8,$+42H	;B8F03F
	CJNE	R1,#IMM8,$+42H	;B9F03F
	CJNE	R2,#IMM8,$+42H	;BAF03F
	CJNE	R3,#IMM8,$+42H	;BBF03F
	CJNE	R4,#IMM8,$+42H	;BCF03F
	CJNE	R5,#IMM8,$+42H	;BDF03F
	CJNE	R6,#IMM8,$+42H	;BEF03F
	CJNE	R7,#IMM8,$+42H	;BFF03F
	CJNE	@R0,#IMM8,$+42H	;B6F03F
	CJNE	@R1,#IMM8,$+42H	;B7F03F

	CLR	A		;E4
	CLR	C		;C3
	CLR	CY		;C2D7
	CLR	PSW.7		;C2D7
	CLR	2AH.6		;C256

	CPL	A		;F4
	CPL	C		;B3
	CPL	CY		;B2D7
	CPL	PSW.7		;B2D7
	CPL	2AH.6		;B256

	DAA			;D4
	DA	A		;D4

LDEC:	DEC	A		;14
	DEC	R0		;18
	DEC	R1		;19
	DEC	R2		;1A
	DEC	R3		;1B
	DEC	R4		;1C
	DEC	R5		;1D
	DEC	R6		;1E
	DEC	R7		;1F
	DEC	DIRECT		;1580
	DEC	@R0		;16
	DEC	@R1		;17

	DIV	AB		;84

	DJNZ	R0,$+42H	;D840
	DJNZ	R1,$+42H	;D940
	DJNZ	R2,$+42H	;DA40
	DJNZ	R3,$+42H	;DB40
	DJNZ	R4,$+42H	;DC40
	DJNZ	R5,$+42H	;DD40
	DJNZ	R6,$+42H	;DE40
	DJNZ	R7,$+42H	;DF40

	DJNZ	DIRECT,$+42H	;D5803F

	INC	A		;04
	INC	R0		;08
	INC	R1		;09
	INC	R2		;0A
	INC	R3		;0B
	INC	R4		;0C
	INC	R5		;0D
	INC	R6		;0E
	INC	R7		;0F
	INC	DIRECT		;0580
	INC	@R0		;06
	INC	@R1		;07
	INC	DPTR		;A3

	JB	2AH.6,$+42H	;20563F
	JB	PSW.7,$+42H	;20D73F
	JB	CY,$+42H	;20D73F

	JBC	2AH.6,$+42H	;10563F
	JBC	PSW.7,$+42H	;10D73F
	JBC	CY,$+42H	;10D73F

	JC	$+42H		;4040

	JMP	@A+DPTR		;73

	JNB	2AH.6,$+42H	;30563F
	JNB	PSW.7,$+42H	;30D73F
	JNB	CY,$+42H	;30D73F

	JNC	$+42H		;5040

	JNZ	$+42H		;7040

	JZ	$+42H		;6040

	LCALL	LONG		;121234
	LJMP	LONG		;021234

LMOV:	MOV	A,R0		;E8
	MOV	A,R1		;E9
	MOV	A,R2		;EA
	MOV	A,R3		;EB
	MOV	A,R4		;EC
	MOV	A,R5		;ED
	MOV	A,R6		;EE
	MOV	A,R7		;EF
	MOV	A,DIRECT	;E580
	MOV	A,@R0		;E6
	MOV	A,@R1		;E7
	MOV	A,#IMM8		;74F0
	MOV	R0,A		;F8
	MOV	R1,A		;F9
	MOV	R2,A		;FA
	MOV	R3,A		;FB
	MOV	R4,A		;FC
	MOV	R5,A		;FD
	MOV	R6,A		;FE
	MOV	R7,A		;FF
	MOV	R0,DIRECT	;A880
	MOV	R1,DIRECT	;A980
	MOV	R2,DIRECT	;AA80
	MOV	R3,DIRECT	;AB80
	MOV	R4,DIRECT	;AC80
	MOV	R5,DIRECT	;AD80
	MOV	R6,DIRECT	;AE80
	MOV	R7,DIRECT	;AF80
	MOV	R0,#IMM8	;78F0
	MOV	R1,#IMM8	;79F0
	MOV	R2,#IMM8	;7AF0
	MOV	R3,#IMM8	;7BF0
	MOV	R4,#IMM8	;7CF0
	MOV	R5,#IMM8	;7DF0
	MOV	R6,#IMM8	;7EF0
	MOV	R7,#IMM8	;7FF0
	MOV	DIRECT,A	;F580
	MOV	DIRECT,R0	;8880
	MOV	DIRECT,R1	;8980
	MOV	DIRECT,R2	;8A80
	MOV	DIRECT,R3	;8B80
	MOV	DIRECT,R4	;8C80
	MOV	DIRECT,R5	;8D80
	MOV	DIRECT,R6	;8E80
	MOV	DIRECT,R7	;8F80
	MOV	DIRECT,DIRECT	;858080
	MOV	DIRECT,@R0	;8680
	MOV	DIRECT,@R1	;8780
	MOV	DIRECT,#IMM8	;7580F0
	MOV	@R0,A		;F6
	MOV	@R1,A		;F7
	MOV	@R0,DIRECT	;A680
	MOV	@R1,DIRECT	;A780
	MOV	@R0,#IMM8	;76F0
	MOV	@R1,#IMM8	;77F0
	MOV	C,2AH.6		;A256
	MOV	C,CY		;A2D7
	MOV	C,PSW.7		;A2D7
	MOV	2AH.6,C		;9256
	MOV	CY,C		;92D7
	MOV	PSW.7,C		;92D7
	MOV	DPTR,#IMM16	;90FC00

	MOVC	A,@A+DPTR	;93
	MOVC	A,@A+PC		;83

	MOVX	A,@R0		;E2
	MOVX	A,@R1		;E3
	MOVX	A,@DPTR		;E0
	MOVX	@R0,A		;F2
	MOVX	@R1,A		;F3
	MOVX	@DPTR,A		;F0

	NOP			;00

	MUL	AB		;A4

	ORL	A,R0		;48
	ORL	A,R1		;49
	ORL	A,R2		;4A
	ORL	A,R3		;4B
	ORL	A,R4		;4C
	ORL	A,R5		;4D
	ORL	A,R6		;4E
	ORL	A,R7		;4F
	ORL	A,DIRECT	;4580
	ORL	A,@R0		;46
	ORL	A,@R1		;47
	ORL	A,#IMM8		;44F0
	ORL	DIRECT,A	;4280
	ORL	DIRECT,#IMM8	;4380F0
	ORL	C,2AH.6		;7256
	ORL	C,PSW.7		;72D7
	ORL	C,CY		;72D7
	ORL	C,/2AH.6	;A056
	ORL	C,/PSW.7	;A0D7
	ORL	C,/CY		;A0D7

	POP	DIRECT		;D080
	PUSH	DIRECT		;C080

	RET			;22
	RETI			;32

	RL	A		;23
	RLC	A		;33

	RR	A		;03
	RRC	A		;13

	SETB	C		;D3
	SETB	2AH.6		;D256
	SETB	PSW.7		;D2D7
	SETB	CY		;D2D7

	SJMP	$+42H		;8040

	SUBB	A,R0		;98
	SUBB	A,R1		;99
	SUBB	A,R2		;9A
	SUBB	A,R3		;9B
	SUBB	A,R4		;9C
	SUBB	A,R5		;9D
	SUBB	A,R6		;9E
	SUBB	A,R7		;9F
	SUBB	A,DIRECT	;9580
	SUBB	A,@R0		;96
	SUBB	A,@R1		;97
	SUBB	A,#IMM8		;94F0

	SWAP	A		;C4

	XCH	A,R0		;C8
	XCH	A,R1		;C9
	XCH	A,R2		;CA
	XCH	A,R3		;CB
	XCH	A,R4		;CC
	XCH	A,R5		;CD
	XCH	A,R6		;CE
	XCH	A,R7		;CF
	XCH	A,DIRECT	;C580
	XCH	A,@R0		;C6
	XCH	A,@R1		;C7

	XCHD	A,@R0		;D6
	XCHD	A,@R1		;D7

	XRL	A,R0		;68
	XRL	A,R1		;69
	XRL	A,R2		;6A
	XRL	A,R3		;6B
	XRL	A,R4		;6C
	XRL	A,R5		;6D
	XRL	A,R6		;6E
	XRL	A,R7		;6F
	XRL	A,DIRECT	;6580
	XRL	A,@R0		;66
	XRL	A,@R1		;67
	XRL	A,#IMM8		;64F0
	XRL	DIRECT,A	;6280
	XRL	DIRECT,#IMM8	;6380F0

ABSOL:	EQU	0580H
IMM8:	EQU	-16
IMM16:	EQU	-1024
DIRECT:	EQU	80H
LONG:	EQU	1234H
BIT.56:	EQU	56H

ZZZ:
         PAGE    0            ;STOP PAGING
         TITL    ""           ;STOP TITLE

         END                  ;END OF PROGRAM