MACRO CROSS ASSEMBLERS

                                      Series I

                                    USER'S MANUAL


                         for the following microprocessors:

                                        8044
                                        8048
                                       8051/52
                                        8080
                                        8085
                                        8096
                                         Z80
























                                                    MICEPT INSTRUMENTS INC.



          Macro Cross Assembler - Series I                               ii
















                               MACRO CROSS ASSEMBLERS

                                      Series I

                                    USER'S MANUAL
























          Edition 2




          MICEPT INSTRUMENTS INC.
          377 Julien St.
          Cap De La Madeleine, PQ
          Canada  G8T 6W6

          e-mail: jveillet@aei.ca



          Macro Cross Assemblers - Series I                             iii

















          NOTICE

          This version of  the software is  distributed as shareware.  This
          version may  be  freely  copied and  distributed  for  evaluation
          purposes as  long  as  NO  FEE IS  CHARGE  FOR  USE,  COPYING  OR
          DISTRIBUTION (EXCEPT FOR A NOMINAL DISTRIBUTION FEE) and as  long
          as THE SOFTWARE PACKAGE IS NOT MODIFIED IN ANY WAY.

          USE OF  THIS  SOFTWARE  BEYOND  A  REASONABLE  EVALUATION  PERIOD
          REQUIRES REGISTRATION.

          The  entire   package,   consisting   of   the   main   programs,
          documentation file and  various utility files  are all  copyright
          (C) 1991-1996 by Micept Instruments Inc. All rights reserved.


          DISCLAIMER

          Micept Instruments  Inc.  disclaims  all warranties  as  to  this
          software and  the  documentation,  whether  express  or  implied,
          including,  without   limitation,  any   implied  warranties   of
          merchantability  and   of  fitness   for  any   purpose.   Micept
          Instruments Inc.  assumes no  liability  for damages,  direct  or
          consequential, which may results from the use of this software or
          the documentation.

          Information in this document is subject to change without notice.


          TRADEMARKS

          Intel is a registered trademark of Intel Corporation.
          Zilog and Z80 are registered trademarks of Zilog Inc.
          MS-DOS is a trademark of Microsoft Corporation.
          IBM, PC, XT, AT are trademarks of International Business Machines
          Corporation.
          All  brand  and  product  names  are  trademarks  or   registered
          trademarks of their respective companies.







          TABLE OF CONTENTS



          TABLE OF CONTENTS..............................................iv


          1. INTRODUCTION.................................................1

          1.1 ABOUT THIS MANUAL...........................................1
          1.2 OVERVIEW....................................................1
          1.3 SPECIFICATIONS..............................................1
          1.4 NOTATIONAL CONVENTIONS......................................2
          1.5 LEARNING MORE ABOUT THE MICROPROCESSORS.....................2

          2. GETTING STARTED..............................................3

          2.1 INSTALLATION................................................3
          2.2 SYSTEM REQUIREMENTS.........................................3
          2.3 DISK CONTENTS...............................................3
          2.4 SETTING UP THE ENVIRONMENT..................................3

          3. ASSEMBLING...................................................4

          3.1 RUNNING THE ASSEMBLER.......................................4
          3.2 OPTIONS IN MORE DETAILS.....................................4
          3.3 ERROR CODES RETURNED TO DOS.................................6
          3.4 OBJECT CODE FILE FORMATS....................................6

          4. ASSEMBLER LANGUAGE...........................................7

          4.1 SOURCE LINE FORMAT..........................................7
          4.2 EXPRESSIONS IN THE OPERAND FIELD............................8
           4.2.1 Symbols .................................................8
           4.2.2 Constants ...............................................8
           4.2.3 Operators ...............................................9
           4.2.4 How expressions are evaluated ...........................9
          4.3 ASSEMBLER DIRECTIVES.......................................11
           ACLIST .......................................................13
           DB ...........................................................13
           DW ...........................................................13
           ELSE .........................................................13
           END ..........................................................13
           ENDIF ........................................................14
           ENDM .........................................................14
           EQU ..........................................................14
           EXITM ........................................................14
           EXPAND .......................................................14
           FAIL .........................................................15
           FLIST ........................................................15
           FNOLIST ......................................................15
           IF ...........................................................15
           IFC ..........................................................15



          Macro Cross Assemblers - Series I                               v


           IFN ..........................................................16
           IFNC .........................................................16
           INCLUDE ......................................................16
           LIST .........................................................16
           LLEN .........................................................17
           MACRO ........................................................17
           NOACLIST .....................................................17
           NOEXPAND .....................................................17
           NOLIST .......................................................17
           ORG ..........................................................18
           PAGE .........................................................18
           PLEN .........................................................18
           REDEF ........................................................18
           RSB ..........................................................18
           RSW ..........................................................19
           SET ..........................................................19
           TITLE ........................................................19
          4.4 CONDITIONAL ASSEMBLY.......................................19
          4.5 MACRO ASSEMBLY.............................................20

          5. ERROR MESSAGES..............................................23

          5.1 COMMON ERRORS..............................................23
          5.2 WARNINGS...................................................29
          5.3 FATAL ERRORS...............................................30

          6. SPECIAL SECTION ON THE MICROS...............................31

          6.1 INTEL 8044.................................................31
          6.2 INTEL 8048.................................................34
          6.3 INTEL 8051/52..............................................35
          6.4 INTEL 8080.................................................39
          6.5 INTEL 8085.................................................39
          6.6 INTEL 8096.................................................39
          6.7 ZILOG Z80..................................................40

          7. BUG REPORTING PROCEDURE.....................................41


          8. ORDERING INFORMATION........................................42


          INDEX..........................................................45








          1. INTRODUCTION



          1.1  About this manual

          This manual  provides  the  necessary  technical  information  to
          install and use the Macro Cross Assemblers in the series I. It is
          written for  the individual  end user  but a  certain measure  of
          experience in the operation of MS-DOS has been assumed. A certain
          knowledge of the assembly language of each microprocessor is also
          assumed.

          Most of this manual  is intended for  the registered versions  of
          the  software  and  therefore  not  everything  in  it  will   be
          applicable to  the  unregistered  versions.  Macros,  conditional
          assembly and included files are not supported in the unregistered
          versions.


          1.2  Overview

          This software are  high quality  Macro Cross  Assemblers for  the
          Intel 8044, 8048, 8051/52,  8080, 8085, 8096,  and the Zilog  Z80
          microprocessors. This  software  are  basic  two-pass  assemblers
          which supports macros, conditional assembly and included files.

          These powerful Macro  Cross Assemblers for  the MS-DOS  operating
          system support the complete instruction set and a complete set of
          directives. They also  support  the  8051/52  and  8044  special
          function registers and their assigned bit names. These assemblers
          can produce formatted listing files and  object code in both  the
          Intel Hex and the Motorola Hex formats.

          The supported assembler directives are the same as the ones  used
          by the microprocessor manufacturers, but you can customised  them
          to your liking using the REDEF directive.


          1.3  Specifications

          The Macro Cross Assemblers supports:

             up to 16 nested include files
             up to 16 nested conditional assembly sections
             up to 16 nested macros
             unlimited number of include files
             unlimited number of macros (only limited by memory)



          Macro Cross Assembler - Series I                                2



          1.4  Notational conventions

          The following rules are used in this manual:

            1. Words in capital letters are keywords and must be entered as
               shown.  They  may  be  entered  in  uppercase  or  lowercase
               characters.

            2. Items in square brackets ([]) are optional.

            3. Symbolic fields are enclosed in < >.

            4. An ellipsis (...) indicates that an item may be repeated  as
               many time as you wish.

            5. All punctuation, except  the one mentioned  before, must  be
               included where shown.

            6. xxx is  a two  or three  character string  representing  the
               microprocessor identification.
               This string is:

                   44   : for the Intel 8044 microprocessor
                   48   : for the Intel 8048 microprocessor
                   51   : for the Intel 8051/52 microprocessor
                   80   : for the Intel 8080 microprocessor
                   85   : for the Intel 8085 microprocessor
                   96   : for the Intel 8096 microprocessor
                   Z80  : for the Zilog Z80 microprocessor


          1.5  Learning more about the microprocessors

          You may want  to get more  familiar with  the microprocessor  you
          plan to  be  using  by reading  assembly  language  books,  other
          handbooks and data books.







          2. GETTING STARTED



          2.1  Installation

          Make a working  copy of  your disk,  using the  COPY or  DISKCOPY
          utility supplied with MS-DOS. Save the original disk for backup.

          No particular installation  is required except  that you have  to
          copy the executable files to the disk you are going to use.


          2.2  System requirements

             IBM PC/XT/AT or compatible computer
             DOS 2.0 or later
             256K of RAM required  (more for bigger  symbol table or  many
             macros)


          2.3  Disk contents

          Each assembler package (one for each microprocessor) will contain
          the following files:

               MAxxx.EXE     The  executable  file  of  the  corresponding
                             Macro Cross Assembler
               EXAMPLEn.xxx  An example of a source file
               README.xxx    An  optional   file  containing   the  latest
                             information


          2.4  Setting up the environment

          Each assembler environment  can be customised  by the  use of  an
          environment variable.  The variable,  if  set, will  specify  the
          default command  line  options.  The options  specified  in  that
          variable will  not  replace but  will  be added  to  the  options
          invoked in the command  line. Options are  specified in the  same
          manner as if they were invoked  in the command line. The  setting
          of this variable can be automatically done if the set command  is
          placed in the AUTOEXEC.BAT file.

          The variable is called MAxxxOPT and  can be set by the  following
          command:

              SET MAxxxOPT=-l -m -r10h

          That command would invoked the l,  m and r options each time  the
          assembler is invoked.







          3. ASSEMBLING



          3.1  Running the assembler

          The assembler can be invoked as follow:

          MAxxx [<options>] <sourcefile> [<objfile> [<listfile>]]

          Where <options> can be one or more of the following separated by
          spaces:

             -l      Produce a listing file
             -o      Produce NO object file
             -t      Produce NO symbol table in the listing
             -m      Produce object in Motorola Hex
             -q      Quiet mode
             -s      Display software license
             -p<n>   Set listing page length (in lines per page)
             -w<n>   Set listing width (in characters per line)
             -r<n>   Set object record size (in bytes)
             -e      Expand macros in the listing
             -f      Do not list false conditions
             -x      Use special function register set for the 8052
             -c      Produce complete object in listing for long constants

             <sourcefile>  Source file name. Default extension is ".xxx".
             <objfile>     Object file name. Default extension is ".OBJ".
             <listfile>    Listing file name. Default extension is ".LST".

             If the  assembler is  invoked with  an error  in the  command
             line, a help screen is displayed on the console.

             For  <objfile> and <listfile>, if no  name is specified,  the
             source file name with the default extensions will be used and
             the files will be created in the current directory.


          3.2  Options in more details

            c  Complete object code in listing for long constants. This  is
               used to see  all object codes  generated by long  constants,
               like strings  and series  of data.  A source  line may  then
               generate more than one  line in the  listing because only  a
               few object codes can be written on one line of listing.

            e  Expand macros in the listing. This option lists the complete
               macro text when that macro is invoked. Even when this option
               is invoked, the expansion of macros in the listing file will
               still be controlled by the EXPAND and NOEXPAND directives.



          Macro Cross Assembler - Series I                                5


            f  False  conditional   sections   not  listed.   This   option
               suppresses the listing of conditional sections that evaluate
               as false. Even when this option  is invoked, the listing  of
               conditional section  that evaluate  as false  will still  be
               controlled by the FLIST and FNOLIST directives.

            l  Listing file. This  option enables the  output to a  listing
               file. The  listing produced  has  page headers  and  footers
               inserted at appropriate intervals.  Even when the option  is
               invoked, the  output  to  the listing  file  will  still  be
               controlled by the LIST and NOLIST directives.

            m  Motorola Hex format. This option  causes the object file  to
               be produced  in  the Motorola  Hex  format rather  than  the
               default Intel Hex format.

            o  Object file disabled. This  option suppresses the output  to
               an object file.

            p  Page length. This option sets the  number of lines per  page
               in the listing file. When a listing file is produced,  since
               page headers  and footers  are inserted,  a page  length  is
               required. If this option, immediately followed by a  numeric
               constant, is invoked, the  page length will  be set to  that
               value. The value must  be between 20 and  120 or it will  be
               ignored. Even when this option  is invoked, the page  length
               may be set again anywhere in the file by the PLEN directive.
               The default page length is 66 lines.

            q  Quiet mode.  This  option  turns off  the  display  of  line
               numbers  during   assembly.   Normally  a   running   count,
               incremented by 50s, of the numbers of lines being  assembled
               is displayed on the console.

            r  Record size in the object file. This option sets the number
               of bytes in each object file record. The number selected  is
               the number  of counted  bytes in  the selected  format.  The
               number must be between 8 and  255 or it will be ignored.  If
               the m option is invoked, the  r option must appear after  it
               in the command line to have  any effect. The default  record
               size in Intel Hex is 24. The default record size in Motorola
               Hex is 27.

            s  Software license. This option displays an information screen
               on the software license.

            t  Table of symbols suppressed in the listing file. This option
               suppresses the output  of the  symbol table  in the  listing
               file. Of course if output to the listing file is disabled at
               the end of the listing, the symbol table will not appear  at
               the end of the listing file anyway.

            w  Width of the listing  file. This option  sets the number  of
               characters per line  in the  listing file.  If this  option,



          Macro Cross Assembler - Series I                                6



               immediately followed by a numeric constant, is invoked,  the
               line length will  be set to  that value. The  value must  be
               between 60 and  132 or it  will be ignored.  Even when  this
               option is invoked, the line length may be set again anywhere
               in the file by the LLEN  directive. The default line  length
               is 80 characters.

            x  Use the extended function register  set for the 8052.  (only
               for the 8051 assembler)

          Note: Each option must be preceded by a  dash (-) in the command
                line, to distinguish it from a file name.


          3.3  Error codes returned to DOS

              Condition                                    Error code
              Normal completion, without errors            0
              Normal completion, with assembly errors      1
              Abnormal completion, insufficient memory     2
              Abnormal completion, file access error       3


          3.4  Object code file formats

              This assembler supports two object file formats:

               1.  Intel Hex
               2.  Motorola Hex (S1-S9)







          4. ASSEMBLER LANGUAGE



          4.1  Source line format

          Lines in  the  source file  consist  of  up to  four  fields,  as
          follows:

              [Label] [Opcode] [Operand] [Comment]

          Each line  of the  file may  be  up to  256 characters  long.  An
          arbitrary number of  white space (spaces  or tabs) must  separate
          each field.


          Label

          Labels are symbols and follow the  same rules. If a label  starts
          in the first  column, it  must be  terminated with  at least  one
          white space (space  or tab) or  the end of  the line  but it  may
          follow the rules of  a label starting in  any other column. If  a
          label starts in any  other column, it must  be terminated with  a
          colon (:) followed with at least  one white space (space or  tab)
          or the end of  the line. The  ending colon is  never part of  the
          symbol.

          A line may consist  of a label alone.  With a normal  instruction
          mnemonic, the assembler assigns a value to the label equal to the
          current location counter.


          Opcode

          The operand  field  contains  the  instruction  mnemonic  or  the
          assembler directive that is to be performed. This field must  not
          start in the first column.


          Operand

          The operand field may  or may not be  required, depending on  the
          opcode or directive being assembled. If present, this field  will
          contain a certain number of operands, separated by commas.  There
          must not  be  any  white  space  (space  or  tab)  between  these
          operands.


          Comment

          The optional comment field is used for annotation purposes.  This
          field is  ignored  by  the assembler,  but  is  included  in  the
          listing. No character is necessary  to designate a comment  which



          Macro Cross Assembler - Series I                                8



          does not begin in  the first column. A semicolon (;) is  used by
          the assembler to designate the beginning of a comment and it  can
          be used anywhere in the line, including in the first column for a
          stand-alone comment.


          4.2  Expressions in the operand field

          Expressions are combinations of constants, symbols, operators and
          parentheses that are evaluated as an integer value.


          4.2.1 Symbols

          Symbols are strings of characters  that contain letters (A-Z,  a-
          z), numbers (0-9),  points(.) and underscores  (_) but they  must
          begin with a letter. A symbol may be of any length, but only  the
          first 8  characters are  significant and  will be  listed in  the
          symbol table. Since  all lowercase  letter will  be converted  to
          uppercase, symbols which are capitalised differently will be  the
          same. A symbol can not be a reserved word.

          examples:LOOP
                   loop_2
                   key.buffer

          The reserved words are the ones representing:

             the mnemonics and assembler directives.
             the microprocessor's registers.


          4.2.2 Constants


          Numeric constants

          Numeric constants must  always begin  with a  decimal digit.  The
          radix is determine by a  letter immediately following the  number
          according to the following table:

              Format         Suffix
              Binary         B
              Octal          O or Q
              Decimal        D or nothing
              Hexadecimal    H

              examples: 10010001b
                        7774Q
                        18d
                        255
                        6fh
                        0FEH



          Macro Cross Assembler - Series I                                9





          Character constants

          A character constant consists  of one ASCII character  surrounded
          by single quote marks (').

          Note: To put a single quote mark  into a character constant, two
                consecutive single  quotes may  be used  to  represent one
                such character.

          examples:'a'
                   '*'
                   ''''


          The location counter

          The current  value of  the location  counter can  be used  in  an
          expression. It is represented by the dollar sign ($).


          4.2.3 Operators

          The operators allowed in expressions are shown, in the  following
          table, in descending order of precedence:

          Order Operator  Type            Description
          ----- --------  --------------  -----------
          1.    ()        expression      parentheses
          2.    -         unary           unary negative
                ~                         one's complement
          3.    &         binary          bitwise AND
                !                         bitwise OR
                ^                         bitwise EXCLUSIVE OR
          4.    *         multiplicative  multiplication
                /                         division
                %                         remainder
          5.    +         additive        addition
                -                         subtraction
          6.    <<        shift           shift left
                >>                        shift right
          7.    =         relational      equal
                <                         less than
                >                         greater than
                <=                        less than or equal
                >=                        greater than or equal


          4.2.4 How expressions are evaluated

          In an expression parenthetical  expressions are evaluated  first,
          the innermost parentheses before the outer ones. Next, operations



          Macro Cross Assembler - Series I                               10



          involving higher  precedence  operators  are  done  first.  Where
          several operators  have the  same precedence  they are  evaluated
          from left to right except for unary operators which are evaluated
          from right to left.  All intermediate values  are truncated to  a
          16-bit integer value. The result of the expression is also a  16-
          bit integer value.



          Macro Cross Assembler - Series I                               11



          4.3  Assembler directives


          Assembly Control
          ----------------
          ORG       Set assembly origin
          END       End of source
          REDEF     Redefine an assembler directive

          Symbol Definition
          -----------------
          EQU       Equate symbol value
          SET       Set symbol value (temporary)

          Memory Allocation
          -----------------
          DB        Define constant byte(s)
          DW        Define constant word(s)
          RSB       Reserve storage for byte(s)
          RSW       Reserve storage for word(s)

          Listing Control
          ---------------
          TITLE     Set title of page(s)
          LLEN      Set line length (characters per line)
          PLEN      Set page length (lines per page)
          PAGE      Advance to top of next page
          LIST      List the assembly
          NOLIST    Do not list the assembly
          ACLIST    List all object codes for long constants
          NOACLIST  Do not list all object codes for long constants
          FLIST     List sections that evaluate as false
          FNOLIST   Do not list sections that evaluate as false
          EXPAND    Expand macros
          NOEXPAND  Do not expand macros

          Conditional Assembly
          --------------------
          IF        Assemble if not equal to zero
          IFN       Assemble if equal to zero
          IFC       Assemble if string1 equals string2
          IFNC      Assemble if string1 not equal to string2
          ELSE      Reverse condition
          ENDIF     End of conditional assembly
          FAIL      Print error message

          Include files
          -------------
          INCLUDE   Include file



          Macro Cross Assembler - Series I                               12



          Macro Directives
          ----------------
          MACRO     Define a macro
          ENDM      End of macro definition
          EXITM     Skip to the end of a macro definition



          Macro Cross Assembler - Series I                               13



          ACLIST

          Purpose:  This directive  restores the  listing of  the  complete
                    object code  for long  constants. If  the object  codes
                    generated by the line  do not fit on  a single line  of
                    listing, they will be listed on the following lines.

          Format:   ACLIST

          Remarks:  NOACLIST is the complementary directive.


          DB

          Purpose:  This directive allocates  and initialises  one or  more
                    bytes.

          Format:   [<label>] DB <expression>[,<expression>]...

          Remarks:  <expression> must be an 8-bit integer value or a string
                    surrounded by single quote marks (').


          DW

          Purpose:  This directive allocates  and initialises  one or  more
                    words.

          Format:   [<label>] DW <expression>[,<expression>]...

          Remarks:  <expression> must be a 16-bit integer value.


          ELSE

          Purpose:  This directive allows the alternate section of code  to
                    be assembled when  the opposite condition  exists in  a
                    conditional section.

          Format:   ELSE


          END

          Purpose:  This directive designates the end of the source file.

          Format:   END

          Remarks:  No line  in the  source file  will be  read after  this
                    directive.



          Macro Cross Assembler - Series I                               14



          ENDIF

          Purpose:  This directive  designates  the end  of  a  conditional
                    section in the code.

          Format:   ENDIF

          Remarks:  Each conditional  assembly  section must  end  with  an
                    ENDIF directive.


          ENDM

          Purpose:  This  directive   designates  the   end  of   a   macro
                    definition.

          Format:   ENDM

          Remarks:  Each macro definition must end with an ENDM directive.


          EQU

          Purpose:  This directive  assigns the  value of  <expression> to
                    <label>.

          Format:   <label> EQU <expression>

          Remarks:  The <label> entry can not be redefined.


          EXITM

          Purpose:  This directive is used  to skip to the  end of a  macro
                    definition. When  this  directive is  encountered,  the
                    expansion  is  exited  immediately  and  any  remaining
                    statement in the macro is not generated.

          Format:   EXITM

          Remarks:  An ENDM directive  is still required  when an EXITM  is
                    encountered.


          EXPAND

          Purpose:  This directive lists  the complete macro  text for  all
                    expansions.

          Format:   EXPAND

          Remarks:  NOEXPAND is the complementary directive.



          Macro Cross Assembler - Series I                               15



          FAIL

          Purpose:  This  directive  sends  the  <message>  string  to  the
                    console and writes it in the listing file.

          Format:   FAIL <message>


          FLIST

          Purpose:  This directive  restores  the  listing  of  conditional
                    section that evaluate as false.

          Format:   FLIST

          Remarks:  FLIST  is  the  default   condition.  FNOLIST  is   the
                    complementary directive.


          FNOLIST

          Purpose:  This directive  suppresses the  listing of  conditional
                    section that evaluate as false.

          Format:   FNOLIST

          Remarks:  FLIST is the complementary directive.


          IF

          Purpose:  This directive designates  the start  of a  conditional
                    section. The conditional section will only be assembled
                    if <expression> is not equal to zero.

          Format:   IF <expression>


          IFC

          Purpose:  This directive designates  the start  of a  conditional
                    section. The conditional section will only be assembled
                    if <string1> is identical to <string2>.

          Format:   IFC <string1>,<string2>



          Macro Cross Assembler - Series I                               16



          IFN

          Purpose:  This directive designates  the start  of a  conditional
                    section. The conditional section will only be assembled
                    if <expression> is equal to zero.

          Format:   IFN <expression>


          IFNC

          Purpose:  This directive designates  the start  of a  conditional
                    section. The conditional section will only be assembled
                    if <string1> is not identical to <string2>.

          Format:   IFNC <string1>,<string2>


          INCLUDE

          Purpose:  This directive assembles the source statements from the
                    <pathname> file into the current source file.

          Format:   INCLUDE <pathname>

          Remarks:  The  <pathname>  entry   can   be   any   valid   file
                    specification  as  determined  by  the  Disk  Operating
                    System. The  file  is  opened and  assembled  into  the
                    current source file  immediately following the  INCLUDE
                    statement. When the end-of-file  is reached, or an  END
                    directive is  encountered,  assembly resumes  with  the
                    statement following the INCLUDE. There may be up to  16
                    nested  INCLUDE  directives.  The  maximum  length   of
                    <pathname> is 60 characters.


          LIST

          Purpose:  This directive restores the output in the listing.

          Format:   LIST

          Remarks:  If a listing  is not  being made,  this directive  will
                    start one. NOLIST is the complementary directive.



          Macro Cross Assembler - Series I                               17



          LLEN

          Purpose:  This directive sets the number of characters per  line,
                    in the listing, to the value of <expression>.

          Format:   LLEN <expression>

          Remarks:  The number of  characters per line  must be between  60
                    and 132. The default is 80 characters per line.


          MACRO

          Purpose:  This directive defines a macro called <label>. A macro
                    is a sequence  of statements that  can be generated  in
                    various places in the program.

          Format:   <label> MACRO


          NOACLIST

          Purpose:  This directive suppresses the  listing of the  complete
                    object code  for long  constants. If  the object  codes
                    generated by the line  do not fit on  a single line  of
                    listing, they will not all be listed.

          Format:   NOACLIST

          Remarks:  NOACLIST  is  the  default  condition.  ACLIST  is  the
                    complementary directive.


          NOEXPAND

          Purpose:  This directive suppresses listing of the complete macro
                    text for all expansions.

          Format:   NOEXPAND

          Remarks:  NOEXPAND  is  the  default  condition.  EXPAND  is  the
                    complementary directive.


          NOLIST

          Purpose:  This directive suppresses the output in the listing.

          Format:   NOLIST

          Remarks:  NOLIST  is   the  default   condition.  LIST   is   the
                    complementary directive.



          Macro Cross Assembler - Series I                               18



          ORG

          Purpose:  This directive sets the  location counter to the value
                    of <expression>.

          Format:   ORG <expression>

          Remarks:  <expression> must not involved any forward references.


          PAGE

          Purpose:  This directive starts a new page in the listing.

          Format:   PAGE


          PLEN

          Purpose:  This directive sets  the number of  lines per page,  in
                    the listing, to the value of <expression>.

          Format:   PLEN <expression>

          Remarks:  The number of  lines per page  must be  between 20  and
                    120. The default is 66 characters per line. The first 3
                    lines and the last 3 lines of the page are left  blank.
                    The fourth and fifth line are  used for the date,  page
                    number and page title.


          REDEF

          Purpose:  This  directive  redefines  the  <directive>  assembler
                    directive to the <directive2> directive.

          Format:   REDEF <directive>,<directive2>

          Remarks:  This allows you to  change the name  of each and  every
                    directive to satisfy your particular source file needs.
                    You can also use it to  make your own set of  universal
                    directives.


          RSB

          Purpose:  This directive reserves a block of <expression> byte(s)
                    for storage.

          Format:   [<label>] RSB <expression>

          Remarks:  The number  of bytes  reserved must  be between  1  and
                    32767.



          Macro Cross Assembler - Series I                               19



          RSW

          Purpose:  This directive reserves a block of <expression> word(s)
                    for storage.

          Format:   [<label>] RSW <expression>

          Remarks:  The number  of words  reserved must  be between  1  and
                    16383.


          SET

          Purpose:  This  directive  temporarily   assigns  the  value   of
                    <expression> to <label>.

          Format:   <label> SET <expression>

          Remarks:  The <label> entry can be redefined.


          TITLE

          Purpose:  This directive  sets  the  title  of  the  current  and
                    following page(s) to the <text> string.

          Format:   TITLE <text>

          Remarks:  <text> is truncated to the first 60 characters.


          4.4  Conditional assembly

          All conditional section of code uses the following format:

              IFxx argument
              .
              .
              .
              [ELSE]
              .
              .
              .
              ENDIF

          Note: There may  be up  to 16  nested conditional  sections. Any
                argument to a conditional must be known in pass 1.



          Macro Cross Assembler - Series I                               20



          4.5  Macro assembly

          A macro is a collection of  assembler statements that may  appear
          several times in a program with some optional modifications  each
          time it is used.

          To properly use a macro you must:

            1. Define  the  macro  using  the  MACRO  and  ENDM   assembler
               directives.

            2. Invoke the macro by using the  name of the macro just as  if
               it were a microprocessor mnemonic. (in the opcode field)

          The invocation must be done  after the definition. When  invoked,
          the statements in the macro are inserted, starting on the current
          line, and assembled.

          A macro may contain up to 9 parameters. In the macro  definition,
          parameters are called dummy parameters and are represented by two
          characters. The  dummy parameter  is formed  of a  backslash  (\)
          followed by the parameter identification number (1-9).

          In the macro invocation, actual  parameters are specified in  the
          operand  field  of  the  invoking  line.  These  parameters   are
          separated by commas and  will replaced their corresponding  dummy
          parameters when the macro is invoked.


          Example:

          macro definition

              message   MACRO
                        LDA       #\2       ;dummy parameter no 2
                        JSR       SET_Y
                        LDA       #\1       ;dummy parameter no 1
                        JSR       SET_X
                        LDX       #\3       ;dummy parameter no 3
                        JSR       TEXT
                        ENDM


          macro invocation

                        message   12,5,mssg1     ;print mssg1 at 12,5

          In this  example, the  first actual  parameter  is 12  and  would
          replace the first dummy parameter \1. The second actual parameter
          is 5 and would replace the  second dummy parameter \2. The  third
          actual parameter is mssg1 and  would replace the dummy  parameter
          \3. The actual parameters are all  strings that will replace  the
          dummy parameters.



          Macro Cross Assembler - Series I                               21



          The code assembled would become:

                        LDA       #5
                        JSR       SET_Y
                        LDA       #12
                        JSR       SET_X
                        LDX       #mssg1
                        JSR       TEXT

          Since labels  may  be  required in  a  macro  and  since  macros,
          generally, will be invoked more than once, there must be a way to
          generate distinct labels each time the macro is invoked. This  is
          required to eliminated  multiply defined  symbols. These  symbols
          require a special syntax to be  recognise by the assembler.  This
          syntax is only recognised in macro definitions.

          These symbols must end by an underscore (_) followed by a  dollar
          sign ($). Only the  first 4 characters of  these symbols will  be
          used and a three character number (in hexadecimal) preceded by an
          underscore will follow these 4 characters to make the symbol.

          Example:

          macro definition

              count     MACRO
                        DECA
              wait_$:   BNE       wait_$
                        DECB
                        BNE       wait_$
                        ENDM


          code generated the first time the macro is invoked:

                        DECA
              wait_001: BNE       wait_001
                        DECB
                        BNE       wait_001


          code generated the second time the macro is invoked:

                        DECA
              wait_002: BNE       wait_002
                        DECB
                        BNE       wait_002








          5. ERROR MESSAGES



          5.1  Common errors

          These errors are reported with the name of the source file  where
          they are detected, and the line number.


          Bit number out of range

             This occurs  when the  bit number  specified  is too  big  or
             negative.


          Branch out of range

             This occurs when the  relative branch required is  not within
             the range -128  +127 of the current instruction.


          Branch out of the 2Kbytes page

             This occurs when  the branch  required is out  of the  2Kbyte
             page.


          Data is not an 8-bit value

             This occurs when the data is not an 8-bit integer value.


          Different size registers

             This occurs when two or  more of the specified  registers are
             of different sizes when they have to be of the same size.


          Directive is reserved word

             This occurs on a try to redefine a directive with  a reserved
             word.


          Division by zero attempted

             This occurs  when  a division  by  zero  is attempted  in  an
             expression.



          Macro Cross Assembler - Series I                               24



          Embedded macro not allowed

             This occurs  on  an attempt  to  define  a macro  within  the
             definition of another macro.


          End of conditional assembly section missing

             This occurs when a conditional assembly section does  not end
             with an ENDIF directive.


          End of macro missing

             This occurs when a macro definition does not end with an ENDM
             directive.


          File name too long

             This occurs when the specified file path name is more than 60
             characters long.


          Forward reference is illegal

             This occurs when the expression could not be evaluated in the
             first pass of the assembly.


          Illegal addressing mode

             This occurs  when  the addressing  mode  does not  match  any
             admissible addressing mode for the current opcode.


          Illegal bit addressable location

             This occurs  when the  bit addressed  location is  not a  bit
             addressable special function  register or a  byte of the  bit
             addressable segment of the 8051 microprocessor.


          Illegal bit location

             This occurs  when  the  accessed location  is  not  a  direct
             addressed bit in the internal data RAM or a  special function
             register bit.



          Macro Cross Assembler - Series I                               25



          Illegal block length

             This occurs when the  specified length for a  reserved memory
             block is out of the specified range.


          Illegal character in expression

             This occurs when  an illegal character  is encountered in  an
             expression constant.


          Illegal direct location

             This occurs when  the accessed  location is not  part of  the
             internal data RAM of the 8051 microprocessor.


          Illegal forward macro call

             This occurs on an attempt to  invoke a macro that  is forward
             defined. All macros must be backward defined.


          Illegal interrupt mode

             This occurs when an illegal interrupt mode is specified.


          Illegal label

             This occurs when  an illegal  character is  encountered in  a
             label.


          Illegal listing line length

             This occurs when the specified listing line length is  out of
             the allowed range.


          Illegal listing page length

             This occurs when the specified listing page length is  out of
             the allowed range.


          Illegal opcode

             This occurs when the opcode in  the statement is not  a valid
             mnemonic or a valid assembler directive.



          Macro Cross Assembler - Series I                               26



          Illegal port

             This occurs when an illegal port name or number is specified.


          Illegal register for indirect access

             This occurs when the specified register number is not 0  or 1
             in an indirect access.


          Illegal shift count

             This occurs when the shift count is not between 0 and 15.


          Illegal starting address

             This occurs when an illegal starting address is specified. It
             is either too big or negative.


          Illegal word register

             This occurs  when  the  specified  register  is  not  a  word
             register.


          Immediate data is not a 3-bit value

             This occurs when the specified immediate data is not  a 3-bit
             value. It is probably too big.


          Immediate data is not an 8-bit value

             This occurs when an  immediate data is  not an 8-bit  integer
             value.


          Label is reserved word

             This occurs when the specified label is a reserved  word. The
             mnemonics,  special  function  registers,   special  function
             register bits  and registers  of the  microprocessor are  all
             reserved words.


          Label required with this directive

             This occurs when  the directive in  the statement requires  a
             label and none is present.



          Macro Cross Assembler - Series I                               27



          Line too long

             This occurs if the line is more than 256 characters long.


          Macro already defined

             This occurs on an attempt to redefine a macro.


          Macro name is reserved word

             This occurs when the specified macro name is a reserved word.
             The mnemonics, special  function registers, special  function
             register bits  and registers  of the  microprocessor are  all
             reserved words.


          Missing argument in invoked macro

             This occurs when  an argument  required in the  macro is  not
             present in the invoking line.


          Missing file or bad file

             This occurs on  an attempt to  include a  file that does  not
             exist in the specified directory.


          Missing operand

             This occurs when the  opcode or assembler directive  requires
             an operand and none is present.


          Not a byte register

             This occurs  when  the  specified  register  is  not  a  byte
             register.


          Not a long word register

             This occurs when the  specified register is  not a long  word
             register.


          Not a word register

               This occurs  when  the  specified register  is  not  a  word
               register.



          Macro Cross Assembler - Series I                               28



          Not aligned at a multiple of 4 boundary

               This occurs when the specified address  is not aligned at  a
               multiple of 4 boundary.


          Not aligned at an even byte boundary

             This occurs when the specified  address is not aligned  at an
             even byte boundary.


          Not an even byte address for a word

             This occurs when  the specified  address do not  point to  an
             even byte.


          Not in conditional section

          This occurs  when  an ELSE  or  ENDIF is  encountered  without  a
          previous conditional assembly directive active.


          Not in macro definition

             This occurs when an  EXITM or ENDM  is encountered without  a
             previous macro definition active.


          Offset is not an 8-bit value

             This occurs when the specified offset is not an 8-bit value.


          Phase error

             This occurs when a label value in the second pass of assembly
             differs from its value in the first pass.


          Same register specified twice

             This occurs when the same register is specified more than one
             in a list or registers.


          Symbol multiply defined

             This occurs on an attempt to  redefine a symbol that  can not
             be redefined.



          Macro Cross Assembler - Series I                               29



          Syntax error

             This occurs when the syntax  of the statement does  not match
             any recognisable syntax.


          Too many nested conditional assembly sections

             This occurs  on  an  attempt  to  insert  a  new  conditional
             assembly section  within  one  while the  maximum  number  of
             nested conditional assembly sections has been reached.


          Too many nested files

             This occurs on an attempt to include a file within  one while
             the maximum number of nested include has been reached.


          Too many nested macros

             This occurs on an attempt to invoked a macro within one while
             the maximum number of nested macros has been reached.


          U register and S register together

             This occurs  when  the  two  stack pointers  (U  and  S)  are
             specified in the push or pull operation.


          Undefined symbol

             This occurs when a symbol encountered is not defined.


          Unknown directive

             This occurs when a specified directive is unknown. An unknown
             directive can not be redefined.


          5.2  Warnings

          These warnings are  generated with the  name of  the source  file
          where they are detected, and the line number.


          Ascii constant is not an 8-bit value

             This occurs when an ascii constant is more than one character
             long.



          Macro Cross Assembler - Series I                               30



          End directive missing

             This occurs when a source file ends without an END directive.


          Label ignored

             This occurs when the definition of a label is  attempted with
             a directive which does not require (and allow) one.


          Numeric constant is not an 16-bit value

             This occurs when a numeric  constant is not a  16-bit integer
             value.



          5.3  Fatal errors

          When one of these errors occur, the assembler sends a message  to
          the console and aborts, returning and error code to DOS.


              Error closing input file:  "error message"
              Error closing listing file:  "error message"
              Error closing object file:  "error message"
              Error opening input file:  "error message"
              Error opening listing file:  "error message"
              Error opening object file:  "error message"
              Error reading input file:  "error message"
              Error writing to listing file:  "error message"
              Error writing to object file:  "error message"

              Out of memory for the symbol table
              Out of memory for the macro table







          6. SPECIAL SECTION ON THE MICROS



          6.1  Intel 8044

          The reserved words in this assembler are:
          A, AB, C, DPTR, R0, R1, R2, R3, R4, R5, R6, R7


          Special Function Registers:

          The 8044  has Special  Function  Registers. These  constants  are
          words representing the 8044 registers accessible through the  use
          of their addresses in the on-chip RAM.

          These are predefined in this assembler:
          ACC, B, PSW, SP, DPL,  DPH, P0, P1, P2,  P3, IP, IE, TMOD,  TCON,
          TH0, TL0, TH1, TL1,  FIFO, TBS, TBL, TCB,  NSNR, STAD, RFL,  RBS,
          RBL, RCB, SMD, STS, SMD


          Special Function Register Bits:

          These Special  Function Registers  have bits  which are  directly
          accessible. These  constants  are  words  representing  the  8044
          microprocessor register bits accessible through the use of  their
          addresses in the on-chip RAM.

          These are predefined in the assembler:

          SFR bit  Description
          P        PSW bit 0
          OV       PSW bit 2
          RS0      PSW bit 3
          RS1      PSW bit 4
          F0       PSW bit 5
          AC       PSW bit 6
          CY       PSW bit 7
          EX0      IE bit 0
          ET0      IE bit 1
          EX1      IE bit 2
          ET1      IE bit 3
          ES       IE bit 4
          ET2      IE bit 5
          EA       IE bit 7
          PX0      IP bit 0
          PT0      IP bit 1
          PX1      IP bit 2
          PT1      IP bit 3
          PS       IP bit 4
          PT2      IP bit 5
          IT0      TCON bit 0



          Macro Cross Assembler - Series I                               32



          IE0      TCON bit 1
          IT1      TCON bit 2
          IE1      TCON bit 3
          TR0      TCON bit 4
          TF0      TCON bit 5
          TR1      TCON bit 6
          TF1      TCON bit 7
          ACC.0    Accumulator bit 0
          ACC.1    Accumulator bit 1
          ACC.2    Accumulator bit 2
          ACC.3    Accumulator bit 3
          ACC.4    Accumulator bit 4
          ACC.5    Accumulator bit 5
          ACC.6    Accumulator bit 6
          ACC.7    Accumulator bit 7
          B.0      Register B bit 0
          B.1      Register B bit 1
          B.2      Register B bit 2
          B.3      Register B bit 3
          B.4      Register B bit 4
          B.5      Register B bit 5
          B.6      Register B bit 6
          B.7      Register B bit 7
          PSW.0    PSW bit 0
          PSW.1    PSW bit 1
          PSW.2    PSW bit 2
          PSW.3    PSW bit 3
          PSW.4    PSW bit 4
          PSW.5    PSW bit 5
          PSW.6    PSW bit 6
          PSW.7    PSW bit 7
          P0.0     Port 0 bit 0
          P0.1     Port 0 bit 1
          P0.2     Port 0 bit 2
          P0.3     Port 0 bit 3
          P0.4     Port 0 bit 4
          P0.5     Port 0 bit 5
          P0.6     Port 0 bit 6
          P0.7     Port 0 bit 7
          P1.0     Port 1 bit 0
          P1.1     Port 1 bit 1
          P1.2     Port 1 bit 2
          P1.3     Port 1 bit 3
          P1.4     Port 1 bit 4
          P1.5     Port 1 bit 5
          P1.6     Port 1 bit 6
          P1.7     Port 1 bit 7
          P2.0     Port 2 bit 0
          P2.1     Port 2 bit 1
          P2.2     Port 2 bit 2
          P2.3     Port 2 bit 3
          P2.4     Port 2 bit 4
          P2.5     Port 2 bit 5



          Macro Cross Assembler - Series I                               33



          P2.6     Port 2 bit 6
          P2.7     Port 2 bit 7
          P3.0     Port 3 bit 0
          P3.1     Port 3 bit 1
          P3.2     Port 3 bit 2
          P3.3     Port 3 bit 3
          P3.4     Port 3 bit 4
          P3.5     Port 3 bit 5
          P3.6     Port 3 bit 6
          P3.7     Port 3 bit 7
          IP.0     IP bit 0
          IP.1     IP bit 1
          IP.2     IP bit 2
          IP.3     IP bit 3
          IP.4     IP bit 4
          IP.5     IP bit 5
          IP.6     IP bit 6
          IP.7     IP bit 7
          IE.0     IE bit 0
          IE.1     IE bit 1
          IE.2     IE bit 2
          IE.3     IE bit 3
          IE.4     IE bit 4
          IE.5     IE bit 5
          IE.6     IE bit 6
          IE.7     IE bit 7
          TCON.0   TCON bit 0
          TCON.1   TCON bit 1
          TCON.2   TCON bit 2
          TCON.3   TCON bit 3
          TCON.4   TCON bit 4
          TCON.5   TCON bit 5
          TCON.6   TCON bit 6
          TCON.7   TCON bit 7
          RBP      STS bit 0
          AM       STS bit 1
          CPB      STS bit 2
          BV       STS bit 3
          SI       STS bit 4
          RTS      STS bit 5
          RE       STS bit 6
          TBF      STS bit 7
          SER      NSNR bit 0
          NR0      NSNR bit 1
          NR1      NSNR bit 2
          NR2      NSNR bit 3
          SES      NSNR bit 4
          NS0      NSNR bit 5
          NS1      NSNR bit 6
          NS2      NSNR bit 7
          STS.0    STS bit 0
          STS.1    STS bit 1
          STS.2    STS bit 2



          Macro Cross Assembler - Series I                               34



          STS.3    STS bit 3
          STS.4    STS bit 4
          STS.5    STS bit 5
          STS.6    STS bit 6
          STS.7    STS bit 7
          NSNR.0   NSNR bit 0
          NSNR.1   NSNR bit 1
          NSNR.2   NSNR bit 2
          NSNR.3   NSNR bit 3
          NSNR.4   NSNR bit 4
          NSNR.5   NSNR bit 5
          NSNR.6   NSNR bit 6
          NSNR.7   NSNR bit 7

          Note: Consult  a   data   book   on   the  8044   microprocessor
                architecture for  more  details  on  the special  function
                registers.


          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          DATA     instead of EQU
          ORG
          END
          DB
          DW
          SET
          DS       instead of RSB
          DSW      instead of RSW


          6.2  Intel 8048

          The reserved words in this assembler are:
          A, R0, R1, R2, R3, R4, R5, R6, R7, @R0, @R1, BUS, P1, P2, P4, P5,
          P6, P7, C, F0, F1, I, TCNTI, CLK, @A, PSW, T, MB0, MB1, RB0, RB1,
          TCNT, CNT


          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          DATA     instead of EQU
          ORG
          END
          DB
          DW
          SET



          Macro Cross Assembler - Series I                               35



          DS       instead of RSB
          RSW      is not supported, because it is not necessary


          6.3  Intel 8051/52

          The reserved words in this assembler are:
          A, AB, C, DPTR, R0, R1, R2, R3, R4, R5, R6, R7


          Special Function Registers:

          The 8051  has Special  Function  Registers. These  constants  are
          words representing the  8051 microprocessor registers  accessible
          through the use of their addresses in the on-chip RAM.


          These are predefined in this assembler:
          ACC, B, PSW, SP, DPL,  DPH, P0, P1, P2,  P3, IP, IE, TMOD,  TCON,
          TH0, TL0, TH1, TL1, SCON, SBUF, PCON

          If the extended special function  register set option is  invoked
          (x option), the 8052  microprocessor additional special  function
          registers are also predefined in the assembler.

          These are:
          T2CON, TH2, TL2, RCAP2H, RCAP2L


          Special Function Register Bits:

          These Special  Function Registers  have bits  which are  directly
          accessible. These  constants  are  words  representing  the  8051
          microprocessor register bits accessible through the use of  their
          addresses in the on-chip RAM.


          These are predefined in the assembler:

          SFR bit  Description
          P        PSW bit 0
          OV       PSW bit 2
          RS0      PSW bit 3
          RS1      PSW bit 4
          F0       PSW bit 5
          AC       PSW bit 6
          CY       PSW bit 7
          EX0      IE bit 0
          ET0      IE bit 1
          EX1      IE bit 2
          ET1      IE bit 3
          ES       IE bit 4
          ET2      IE bit 5



          Macro Cross Assembler - Series I                               36



          EA       IE bit 7
          PX0      IP bit 0
          PT0      IP bit 1
          PX1      IP bit 2
          PT1      IP bit 3
          PS       IP bit 4
          PT2      IP bit 5
          IT0      TCON bit 0
          IE0      TCON bit 1
          IT1      TCON bit 2
          IE1      TCON bit 3
          TR0      TCON bit 4
          TF0      TCON bit 5
          TR1      TCON bit 6
          TF1      TCON bit 7
          RI       SCON bit 0
          TI       SCON bit 1
          RB8      SCON bit 2
          TB8      SCON bit 3
          REN      SCON bit 4
          SM2      SCON bit 5
          SM1      SCON bit 6
          SM0      SCON bit 7
          RXD      Port 3 bit 0
          TXD      Port 3 bit 1
          INT0     Port 3 bit 2
          INT1     Port 3 bit 3
          T0       Port 3 bit 4
          T1       Port 3 bit 5
          WR       Port 3 bit 6
          RD       Port 3 bit 7
          ACC.0    Accumulator bit 0
          ACC.1    Accumulator bit 1
          ACC.2    Accumulator bit 2
          ACC.3    Accumulator bit 3
          ACC.4    Accumulator bit 4
          ACC.5    Accumulator bit 5
          ACC.6    Accumulator bit 6
          ACC.7    Accumulator bit 7
          B.0      Register B bit 0
          B.1      Register B bit 1
          B.2      Register B bit 2
          B.3      Register B bit 3
          B.4      Register B bit 4
          B.5      Register B bit 5
          B.6      Register B bit 6
          B.7      Register B bit 7
          PSW.0    PSW bit 0
          PSW.1    PSW bit 1
          PSW.2    PSW bit 2
          PSW.3    PSW bit 3
          PSW.4    PSW bit 4
          PSW.5    PSW bit 5



          Macro Cross Assembler - Series I                               37



          PSW.6    PSW bit 6
          PSW.7    PSW bit 7
          P0.0     Port 0 bit 0
          P0.1     Port 0 bit 1
          P0.2     Port 0 bit 2
          P0.3     Port 0 bit 3
          P0.4     Port 0 bit 4
          P0.5     Port 0 bit 5
          P0.6     Port 0 bit 6
          P0.7     Port 0 bit 7
          P1.0     Port 1 bit 0
          P1.1     Port 1 bit 1
          P1.2     Port 1 bit 2
          P1.3     Port 1 bit 3
          P1.4     Port 1 bit 4
          P1.5     Port 1 bit 5
          P1.6     Port 1 bit 6
          P1.7     Port 1 bit 7
          P2.0     Port 2 bit 0
          P2.1     Port 2 bit 1
          P2.2     Port 2 bit 2
          P2.3     Port 2 bit 3
          P2.4     Port 2 bit 4
          P2.5     Port 2 bit 5
          P2.6     Port 2 bit 6
          P2.7     Port 2 bit 7
          P3.0     Port 3 bit 0
          P3.1     Port 3 bit 1
          P3.2     Port 3 bit 2
          P3.3     Port 3 bit 3
          P3.4     Port 3 bit 4
          P3.5     Port 3 bit 5
          P3.6     Port 3 bit 6
          P3.7     Port 3 bit 7
          IP.0     IP bit 0
          IP.1     IP bit 1
          IP.2     IP bit 2
          IP.3     IP bit 3
          IP.4     IP bit 4
          IP.5     IP bit 5
          IP.6     IP bit 6
          IP.7     IP bit 7
          IE.0     IE bit 0
          IE.1     IE bit 1
          IE.2     IE bit 2
          IE.3     IE bit 3
          IE.4     IE bit 4
          IE.5     IE bit 5
          IE.6     IE bit 6
          IE.7     IE bit 7
          TCON.0   TCON bit 0
          TCON.1   TCON bit 1
          TCON.2   TCON bit 2



          Macro Cross Assembler - Series I                               38



          TCON.3   TCON bit 3
          TCON.4   TCON bit 4
          TCON.5   TCON bit 5
          TCON.6   TCON bit 6
          TCON.7   TCON bit 7
          SCON.0   SCON bit 0
          SCON.1   SCON bit 1
          SCON.2   SCON bit 2
          SCON.3   SCON bit 3
          SCON.4   SCON bit 4
          SCON.5   SCON bit 5
          SCON.6   SCON bit 6
          SCON.7   SCON bit 7

          If the extended special function  register set option is  invoked
          (x option), the 8052  microprocessor additional special  function
          register bits are also predefined in the assembler.

          These are:

          SFR bit  Description
          CPRL2    T2CON bit 0
          CT2      T2CON bit 1
          TR2      T2CON bit 2
          EXEN2    T2CON bit 3
          TCLK     T2CON bit 4
          RCLK     T2CON bit 5
          EXF2     T2CON bit 6
          TF2      T2CON bit 7
          T2CON.0  T2CON bit 0
          T2CON.1  T2CON bit 1
          T2CON.2  T2CON bit 2
          T2CON.3  T2CON bit 3
          T2CON.4  T2CON bit 4
          T2CON.5  T2CON bit 5
          T2CON.6  T2CON bit 6
          T2CON.7  T2CON bit 7

          Note: Consult a  data  book  on  the  8051, 8052  microprocessor
                architectures for  more  details on  the  special function
                registers.


          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          DATA     instead of EQU
          ORG
          END
          DB
          DW



          Macro Cross Assembler - Series I                               39



          SET
          DS       instead of RSB
          DSW      instead of RSW


          6.4  Intel 8080

          The reserved words in this assembler are:
          A, B, C, D, E, H, L, M, BC, DE, HL, SP


          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          EQU
          ORG
          END
          DB
          DW
          SET
          DS       instead of RSB
          RSW      is not supported, because it is not necessary


          6.5  Intel 8085

          The reserved words in this assembler are:
          A, B, C, D, E, H, L, M, BC, DE, HL, SP


          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          EQU
          ORG
          END
          DB
          DW
          SET
          DS     instead of RSB
          RSW    is not supported, because it is not necessary


          6.6  Intel 8096

          There are no reserved words in this assembler.



          Macro Cross Assembler - Series I                               40



          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          EQU
          ORG
          END
          DCB      instead of DB
          DCW      instead of DW
          SET
          DSB      instead of RSB
          DSW      instead of RSW


          6.7  Zilog Z80

          The reserved words in this assembler are:
          A, B, C, D, E, H, L, BC, DE, HL, SP, IX, IY, M, NC, NZ, Z, P, PE,
          PO, AF, I, R

          Assembler directives:

          For this microprocessor, the  standard assembler directives  have
          been predefined as follows:

          EQU
          ORG
          END
          DEFB     instead of DB
          DEFW     instead of DW
          DEFL     instead of SET
          DEFS     instead of RSB
          RSW      is not supported, because it is not necessary







          7. BUG REPORTING PROCEDURE


          Although each software is extensively tested prior to release, no
          software is  perfect  and may  contain  a  few bugs.  It  is  the
          intention of  Micept  Instruments  Inc. to  correct  any  genuine
          problem that  will be  considered as  a problem  by the  company,
          although this  is  not  a  warranty  that  any  problem  will  be
          corrected.

          If you have any comments or suggestions, please send them to  the
          following address or e-mail them to us.

          If you think you have found  a bug in this software, please  take
          the time to report it. Any report will be helpful, but you should
          follow these directions:

            1. Provide the name and version of the software.

            2. Provide a brief  description of  the problem  and provide  a
               copy or listing of  the problem source  file. Please try  to
               isolate the problem area in the source and only provide that
               part of the source file.

            3. Send it to:  Micept Instruments Inc.
                            377 Julien St.
                            Cap De La Madeleine, PQ
                            Canada  G8T 6W6
                            e-mail: jveillet@aei.ca







          8. ORDERING INFORMATION


          To register please use the order form.

          The registration fee will licence one  copy of the software  that
          you will receive, for use on any one computer at any one time.



          Macro Cross Assembler - Series I                               43



                                      Series I

          Cat.  Description                                  License
          No.                                                Fee
          ----------------------------------------------------------
          MA44  Macro Cross Assembler for the Intel 8044     $20.00
          MA48  Macro Cross Assembler for the Intel 8048     $20.00
          MA51  Macro Cross Assembler for the Intel 8051/52  $20.00
          MA80  Macro Cross Assembler for the Intel 8080     $20.00
          MA85  Macro Cross Assembler for the Intel 8085     $20.00
          MA96  Macro Cross Assembler for the Intel 8096     $20.00
          MAZ80 Macro Cross Assembler for the Zilog Z80      $20.00

          SERIES-I Complete series containing the Macro      $99.00
                   Cross Assemblers for the Intel 8044,
                   8048, 8051/52, 8080, 8085, 8096 and
                   the Zilog Z80 (manual on disk)


                                      Series II

          Cat.  Description                                  License
          No.                                                Fee
          ----------------------------------------------------------
          MA03  Macro Cross Assembler for the Motorola 6803  $20.00
          MA05  Macro Cross Assembler for the Motorola 6805  $20.00
          MA09  Macro Cross Assembler for the Motorola 6809  $20.00
          MA65  Macro Cross Assembler for the Rockwell 6502  $20.00
          MA65C Macro Cross Assembler for the Rockwell 65C02 $20.00
          MA68  Macro Cross Assembler for the Motorola 6800  $20.00

          SERIES-IIComplete series containing the Macro      $79.00
                   Cross Assemblers for the Motorola 6800,
                   6803, 6805, 6809 and the Rockwell 6502
                   and 65C02 (manual on disk)


                                  Complete Package

          Cat.    Description                                License
          No.                                                Fee
          ----------------------------------------------------------
          MICRO-8 Package containing all the Macro Cross     $139.00
                  Assemblers of the series I and II
                  (Both manuals on disk)



          Macro Cross Assembler - Series I                               44



                                     ORDER FORM


          Date: ___________________                   #96-MC224-000

          Qty  Cat. No. Description           Unit Price      Price
          ---  -------- --------------------- ----------  ---------

          ___  ________ _____________________ $____.___   $____.___

          ___  ________ _____________________ $____.___   $____.___

                                               Subtotal  $_____.___

                          Add $6.00 Shipping + handling  $_____.___
                     (Outside North America Add $10.00)
                                               Subtotal  $_____.___

                               Canada residents Add GST  $_____.___

                                               Subtotal  $_____.___

              Quebec residents Add Provincial Sales Tax  $_____.___

                                     Total U.S. dollars  $_____.___

          Canadian Dollar Exchange Rate______

          Payments in Canadian Dollars $_____.__

          Please Specify Disk Format: ___ 5 1/4''                                                 or ___ 3 1/2''

          Send your check or money order to:

          Micept Instruments Inc.
          377 Julien St.
          Cap De La Madeleine, PQ
          Canada  G8T 6W6

          Name:    _______________________________________

          Company: _______________________________________

          Address: _______________________________________

                   _______________________________________

                   _______________________________________


          * Prices are in U.S. dollars. We accept only U.S. and
            Canadian funds.  All other will be refused. Prices
            are subject to change without notice.







          INDEX


                                            INCLUDE                      16
          8044                        31    Installation                  3
          8048                        34    Intel 8044                   31
          8051/52                     35    Intel 8048                   34
          8080                        39    Intel 8051/52                35
          8085                        39    Intel 8080                   39
          8096                        39    Intel 8085                   39
                                            Intel 8096                   39
          ACLIST                      13    Introduction                  1
          Assembler directives        11
          Assembler language           7    Label                         7
          Assembling                   4    LIST                         16
                                            LLEN                         17
          Bug reporting procedure     41    Location counter              9

          Character constants          9    MACRO                        17
          Comment                      7    Macro assembly               20
          Common errors               23    Manual                        1
          Conditional assembly        19    Microprocessors           2; 31
          Constants                    8
          Conventions                  2    NOACLIST                     17
                                            NOEXPAND                     17
          DB                          13    NOLIST                       17
          Disclaimer                 iii    Notice                      iii
          Disk contents                3    Numeric constants             8
          DW                          13
                                            Opcode                        7
          ELSE                        13    Operand                       7
          END                         13    Operators                     9
          ENDIF                       14    Options                       4
          ENDM                        14    Ordering information         42
          EQU                         14    ORG                          18
          Error codes                  6    Overview                      1
          Error messages              23
          EXITM                       14    PAGE                         18
          EXPAND                      14    PLEN                         18
          Expressions               8; 9
                                            REDEF                        18
          FAIL                        15    RSB                          18
          Fatal errors                30    RSW                          19
          File formats                 6    Running the assembler         4
          FLIST                       15
          FNOLIST                     15    SET                          19
                                            Setting up the environment    3
          Getting started              3    Source line format            7
                                            Specifications                1
          IF                          15    Symbols                       8
          IFC                         15    System requirements           3
          IFN                         16
          IFNC                        16    Table of contents            iv



          Macro Cross Assembler - Series I                               46



          TITLE                       19
          Trademarks                 iii

          Warnings                    29

          Z80                         40
          Zilog Z80                   40






                                        Notes






                                        Notes