NEWELL 256k to RAMBO XL Switch
                      By Craig Goranson
                  Version 1.0  October 17,1990
                  Version 1.1  May 7,1991

  This is instructions on how to install a switch, with some 
hardware, to give you Newell Industries memory expansion board 
100% RAMBOXL compatibility.


I.     Why I built it.  (this is just some background)


     When I decided to upgrade my 800XL to 256k I chose the Newell 
Industries upgrade.  It is a very well thought out upgrade and I 
have been happy with it and its performance.  Unfortunately the 
Newell upgrade and the popular Rambo XL/CLause Bucholz upgrades 
are incompatible.  They use different bank selection technics and 
locations that means software written for the Rambo XL will not 
run on the Newell upgrade.   The two main differences between the 
upgrades is the fact that the Newell does not allow you to bank 
select the main memory while the Rambo does, and the fact that 
they went with different memory maps of the banks.  Because of this 
I could not run such fine programs as SNAPSHOT and MTOS3.  There 
has been a modification out for some time that added a switch that 
rectified the bank switching incompatibilities so the Newell could 
use the same bank select sequence as the rambo XL, but it did not 
fix the problem that the Newell does not allow you to select the 
main banks.   So I decided to sit down and fix it so the Newell 
could be switched to 100% Rambo compatible mode.  The next section 
is how the upgrade works.  You can skip it if you just want to get 
down to the nitty gritty.

II.      How it works


     The problem arises with how the two upgrades handles bits 5 
and 6 of PORTB.  Bits 5 & 6 can equal from 0 to 3 and select one of 
the 4, 64k segments of the 256k chips.  Bits 2 & 3 of PORTB then 
select 1 of the 4, 16k banks of the 64K subdivision. 
(4*16k=64K,64K*4=256k)  The following is a table of the values for 
bits 5 & 6 on the Newell and Rambo boards and which 64k bank they 
select.

                |-----------------------------------------|
                |B|B| Newell Board      | Rambo Board     |
                |5|6|  64k bank         |  64k bank       |
                |-|-|-------------------|-----------------|
                |0|0| enhanced bank     | main 64k bank   |
          *     |1|0| protected         | enhanced bank   |
                |0|1| enhanced bank     | enhanced bank   |
          *     |1|1| enhanced bank     | enhanced bank   |
                |-----------------------------------------|













      In the above table you will notice the "protected" bank in 
the Newell table.  This is the number that would select the main 
banks of memory if they were not blocked out.  Instead of the 
Newell switching in the main banks of memory it just switches in 
the same banks as if bits 5 & 6 were both 1's.   If you ran a 
program that expected to be using a machine with a RamboXL 
upgrade, it will seem to work but the mirror effect of the one 
bank being switched in as two different banks will destroy data.  
(The RD.COM file from Sparta Dos takes advantage of this fact to 
tell if you have a RAMBO or not.)
     A simple fix to this problem is to invert the BIT 5 before it 
reaches the Newell board.  This is the fix that was given to us by 
Wess Newell.  This fixes the mirror bank problem, and 
RD.COM and other software will run, the bit inversion juggles the 
banks so they are in the right place.  But the Newell upgrade 
still protects the main bank of memory.  SO software written for 
the Rambo that needs to access the main banks through the $4000-
$8000 window still will not work. (Major Crash!!)
     My solution is fairly simple to build it you are good will a 
soldering iron and are fairly patient.  What my modification 
basically does is invert bit 5, bypass a NOR gate, and invert a 
bit that was going through the NOR gate.  It to lengthy to explain 
the nitty gritty so I will leave it up to you to figure it out if 
you really want to.  You don't need to understand how it works to 
install it, the main thing is that it works.   Anyway after this 
modification is installed you will have a switch to change between 
100% Rambo mode and 100% Newell mode.  The best of both worlds.


III.     Building the Newell/RAMBO switch

          Parts list.
1   74ls14 inverter (or 7414,7404,74ls04, doesn't matter.)
1   DPDT switch for mounting on case
a fairly good amount of wire

     You will also need a soldering iron, solder, a small awl or 
screw driver to pry up a pin, and a steady hand.  (and prayer if 
you are religious.)  And a desoldering device such as a suction 
device or de-soldering braid.


       Assembling it:

     1.   remove the top, and shielding from you computer to you 
are looking down at the Newell board.  ( I hope you know how to do 
that.)
     2.   Locate the 7402 or 74ls02 chip on you Newell Board.  It 
should be on the left side, second from the bottom.  It is 
labeled U5 on my board.
     3.   Locate pin 1 of the U5 chip and desolder it.
     4.   Carefully bend up pin one and clip it off leaving enough 
room to solder a wire on to it.  
     5.   Clean up the solder pad that pin one was pried out of, 












then solder one end of a wire to it.
     6.  Orient the DPDT switch so you are looking at the back of 
it.  I will refer to the pins by the letters as follows in the 
diagram below.  The "*" sign designates a pin on the back of the 
switch.

                  a*  d*

                  b*  e*

                  c*  f*

     7.  Solder the other end of the wire, that is attached to the 
solder pad, to pin "b" of the switch.
     8.  Now desolder the wire that goes from the Newell board to 
pin 15 of the PIA chip, from the PIA. (the pia chip is labeled U23 on the 
computer board)  Then attach the end of the wire to pin "e" of the 
switch.  (This allows the re-routing of the BIT 5 of PORTB)
     9.  Now solder a wire from pin 1 of the U5 chip to pin "a" of 
the switch.  (pin one is the one you bent up earlier.)
     10.  Now get you 74ls14 (or equivalent) and trim all the pins 
except 3,8,16.  Leaving enough room to tack solder wires on to the 
trimmed pins.
     11.  Next solder a wire from pin 4 of the 74ls14 to pin "c" 
of the switch.
     12.  Solder a wire from pin 1 of the 74ls14 to pin"d" of the 
switch
     13.  Now carefully place the 74ls14 chip over U5 (74ls02) on 
your newell board.   Then solder pins 3,8,16 to the corresponding 
pins on U5.  The chip should piggy back nicely on the U5 chip and 
the only pins of the 74ls14 chip that should touch pins on the 
74ls02(U5) is 3,8,16.
     14.  Desolder the wires (from the pia) that go from the 
Newell upgrade board to pins 12 & 13 of the PIA chip.  Then solder 
the wire that went to pin 12 to pin 13.  And solder the wire that 
went to pin 13 to pin 12.  (you are just swapping the wires to put 
the banks in the right order)
     15.  Last but not least solder a wire from pin 15 of the PIA 
to pin"d" on the switch.  (there should now be two connections on 
pin "d" of the switch)
     16.  Congrats!!!  You made it.

     You now have a switch that can be mounted were you want, that 
gives you full RamboXL compatibility at a flip of the switch and 
allows you to switch back to Newell mode.  I also recommend that 
you install the switch described in you newell instalation manual 
that allows the Antic chip to follow bank selecting.  This will 
give full compatibility with about every program.   Any input is 
welcome, as I can be reached on by BBS or genie.  This is the 
first revision of this modifications so I would appreciate any 
notifications of errors in this document.  (except grammar and 
spelling)














      Starship Voyager II BBS  8-bit\ST  (509-783-8740)
          24 hours a day\7days a week\ 300\1200\2400 baud
       Run by A2D2, (Atari Association of Desert Dwellers)

On Genie:  R.GORANSON2


Revisions:
v. 1.0   The document as I originally wrote in back when I made 
the modifications to my computer.
v. 1.1   revised on may 6, 1991.  I had left out step #14 in which 
you swap the wires going to pins 12 & 13.