06601030301800
6L....T....T....T....T....T....T....T....T....T....T....T....T....R
€              The 65XE/320K upgrade, by Scott Peterson.
              Copyright (C) July 1987, released to the public.

 The following text file will explain how-to upgrade your 65XE to 320K total
ram, 64K standard and 256K page mapped. It is 100% compatible with my older
130XE/320K-mod-and-about-99%-compatible-with-a-unmodified 130XE, you will, as
usual, lose the "video Enhanced" memory option that is rarely used on the
130XE. There is very little de-soldering in this upgrade,there is quite a
bit of piggy-backing and jumpers however.

TOOLS NEEDED;
Low wattage(15-25) soldering iron.
Vacuum de-soldering tool(Radio Shack PN#64-2098)
#2 Philip head screwdriver.
Small flat blade screwdriver and fine tip needle-nose pliers(Optional)

PARTS AND SUPPLIES;
Z1     74LS158
Z2     CO25953(Atari custom chip, stocked by Best Electronics)
Z3-Z10 41256(150ns.) 256K Ram Chips.
R1-R2  33 ohm resistor.
Also some 30 gauge wire(Radio Shack PN#278-501) and 1/8 inch heat shrink tubing
 
Remove the 65XE case and metal RF shield to get down to the mother board,set
it aside for the moment. Take your 8 256K ram chips(Z3-Z10) and bend up pin 15
on all of them, trim them back so only the "fat" part is left. Take the 65XE
mother board and locate the 8 64K ram chips that run along the left side of
the mother board(U9-U16). Solder Z3 thru Z10 on top of U8 thru U15, make sure
you get the little notches on the same end,things get a bit tight between U9
and U16 so be-careful. When you get done take a piece of wire and solder a
jumper to all the pin 15's on Z3 thru Z10, you should have no excess. Flip
over the motherboard and solder a jumper to all the pin one's of U9 thru U16,
and leave about 1 foot of extra wire attached to pin one of U12. Next take
Z1(74LS158) and bend up all pins except 8 and 16, trim them back till just
the "fat" part is left. Locate U24(front right) on the 65XE mother board and
piggy back Z1 on top of it. Solder pin 1-of Z1 to pin 1 of U24, and solder pin
16 of Z1 to pin 16 of U24. Now, take Z2(CO25953) and bend up all pin except 8
and 16, again trim back the rest so that just the fat part is left. Locate
U2(center) on the motherboard and piggyback Z2 on top of it, solder pin 1 of
Z2 to pin 1 of U2, and pin 16 of Z2 to pin 16 of U2. Take a 33 ohm resistor
and trim the leads back to about 1/4in. Bend one end at a 90 degree angle and
solder it to Z3,pin 15.Its the 256K ram chip piggy backed on-top of U12.
 Solder a wire to the other end of the resistor, run it to Z2,pin 10. Take
another 33 ohm resistor and trim the leads to 1/4 inch and bend one end at 90
degree's and solder it to Z1,pin 4. Take the excess wire you left attached to
U12,pin 1 and snake it thru a hole in the mother board. Attach it to the other
end of the resistor you just soldered to Z1,pin 4. Locate R108(front,left) on
the mother board and desolder the end closest to the front of the computer.
 Trim the end you desoldered back to about 1/4 inch, solder a wire to it and
use a piece of heat shrink tubing or tape to keep it from touching anything.
 Run the wire over to Z2, and solder it to pin 11. Next locate U6(front,
center), and desolder pins 23 and 24. Carefully, with a sharp pointed object,
bend up pins 23 and 24 of U6, wiggling them with a pair of needle nose pliers
first helps to free them from the mother board, trim them back so that only
the fat part remains(NOTE:-If-you-are-not-sure-you-can-bend-up-the-pins-without
damaging-U6,-use-a-40-pin-socket-and-completely-desolder-U6-from-the-motherboard).
 Solder a wire into the hole that pin 23 just came from,-connect it to Z2 pin 1.
-Solder another wire into the hole that pin 24 came-from and connect it to 
Z2 pin 2. What follows is a list of solder connections-to be made between chips.



chip/pin     chip/pin
---------------------
Z1/1    to   U17/30
Z1/2    to   U23/15
Z1/3    to   U23/16
Z1/15   to   Z1/8
Z2/6    to   U6/35
Z2/7    to   Z2/8
Z2/9    to   U17/26
Z2/12   to   U6/23
Z2/13   to   U6/24
Z2/14   to   Z2/16
Z2/15   to   U6/5
U23/12  to   Z2/3
U23/13  to   Z2/4
U23/14  to   Z2/5
----------------------

The control number's for location 54017(PORTB)
----------------------------------------------
BANK#       CONTROL#    HEX#
----------------------------------------------
BANK 1  -----------131 |83
BANK 2  -----------135 |87
BANK 3  -----------139 |8B
BANK 4  -----------143 |8F
BANK 5  -----------163 |A3
BANK 6  -----------167 |A7
BANK 7  -----------171 |AB
BANK 8  -----------175 |AF
BANK 9  -----------195 |C3
BANK 10 -----------199 |C7
BANK 11 -----------203 |CB
BANK 12 -----------207 |CF
BANK 13 -----------227 |E3<-----\
BANK 14 -----------231 |E7       \
BANK 15 -----------235 |EB       / 130XE BANKS.
BANK 16 -----------239 |EF<-----/
--------------------------------------------- 

Well, that about does it for now, I hope you enjoy your 320K 65XE. As far as
support software goes, I recommend Spartados 3.2D, it's one of the easier-to
use DOS's for the upgrade. Also, MYDOS 4.1 or higher and Topdos 1.5+ supports
the 320K upgrades. All-the-software-written-for-the-130/320K-mod-will-run
on-this-mod.(the-testers,Scopy-program's,ect.).-If you have a problem, drop me
a line on GENIE(S.PETERSON)-or contact-Best Electronic's at 408-243-6950 for 
some help.
                               Good Luck
            -                Scott Peterson