A65 (A very simple 6502 assembler)

The A65 assembler is modeled after the Atari MACRO Assembler (AMAC) that
was distributed by APX along with the MEDIT editor and the DDT debugger.
The most significant thing about it is that the source files cannot contain
line numbers (so editors that use line numbers must be able to write an
unnumbered output file).  A second characteristic is that it is a disk-to-
disk assembler (the source must be in a disk (or cassette) file and the
object cannot be inserted directly into memory.

The assembler is run from the DOS menu using the 'L' command, and prompts
you for the source file name, the object file name and the listing file
name:  a RETURN in response to the object and listing prompts will cause
the assembler to generate files on the same drive with extensions '.OBJ'
and '.LST' using the same file name as the source file.  If no '.' appears
in the source file name, '.ASM' is its assumed extension.  A listing can
be printed directly by specifying 'P:' as the list file or dumped to the
screen by specifying 'E:'.  A '-' should cause the listing to be omitted,
and it does, but it also results in the object file being garbled(???).

Some of the 65C02 opcodes are implemented, but they have not been tested
very thouroughly.  Otherwise, the machine instructions are as any other
standard 6502 assembler would expect.  Expressions can include +, -, *
and / operators as well as HI[] and LO[] functions to extract the high and
low bytes of 16-bit numbers.  Brackets, [ and ], may be used to group terms
in an expression if necessary.  Symbols may have up to 8 characters.

The assembler directives are:

DB      defines a byte, in decimal (12), hex ($0C), octal (@14) or binary
        (%00001100) and may also be a character string (enclosed in quotes)
DC      defines a byte, as above, but with the high bit set (if defining a
        string, only on the last byte of the string has the high bit set)
DW      defines a word, low byte first, as if an indirect pointer
DS      allocates a number of bytes without storing any data in them
END     terminates the program and specifies INIT and RUN addresses
EQU     defines a symbol to have a specific value
=       same as EQU
INCLUDE causes the file specified to be inserted at this point in the
        assembly (cannot be nested)
ORG     sets the location counter to a fixed address
*=      same as ORG
PAGE    causes the assembler to go to the top of th next listing page
SUBTTL  allows entering a second title line
TITLE   specifies the first title line
LIST    specifies listing control (several options are controlled by the
        operands of the LIST pseudo-op)

Octal numbers, EQU, *=, LIST and the INIT and RUN addresses may have bugs
in them -- good luck.  Most of the rest has been debugged reasonably well.

The END statement can have the following forms:

        END             no RUN or INIT vectors generated at all
        END  ADDR       ADDR is the RUN entry point
        END  ADDR,      ADDR is the INIT entry point (no RUN vector)
        END  INIT,RUN   both vectors specified

The possible options for the LIST command are:

     -- not implemented yet (the LIST command is ignored completely) --

(This is what I call minimum documentation, I may add to it as questions
are asked)

                        Charles Marslett
                        8/21/85