››           DISASSEMBLER 6502››             Copyright 1983›            By Gary C. Crider›                 For the›    North Texas Atari Computer Team.›››     DISASSEMBLER 6502 was written›for the hardcore assembler language›programmer who is seldom happy with› existing piece of software.  When›no source code is available,›modifying machine language programs›can be extremely difficult.›     DISASSEMBLER 6502 creates source›code from machine language that can›be modified, reassembled, and›executed.››SYSTEM REQUIREMENTS:››MEMORY: 24k minimum and 48k›        desirable.››INPUT DEVICES: Keyboard and one or›        more disk drives.››OUTPUT DEVICES: Screen and one disk›        drive.  A second disk drive›        or cassette drive is needed›        for machine-readable output›        of disk boot files or large›        disassemblies. Double density›        can be very beneficial.››SOFTWARE: An assembler/editor is›        required if you wish to›        reassemble the output.›        DISASSEMBLER 6502 output›        has been tested on the›        ATARI ASSEMBLER/EDITOR›        cartridge and MAC/65 from›        Optimized Systems Software.›››INPUT:››     Input to the disassembler can be›from the following sources:››     MEMORY - Any range of memory›addresses from 0 to $FFFF can be›disassembled.  Addresses can be›entered in either decimal or hex›(e.g. 100 or $64).››››     DISK SECTORS - Any range of›sector numbers from 1 to 720 can be›disassembled.  Sector numbers may›be entered in either decimal or hex.›The last three bytes of a DOS format›sector are control bytes.  They›contain the directory entry number,›next sector number and number of›bytes used in the sector.  Options›are available to disassemble›sectors including or excluding these›control bytes.››     DISK BOOT FILES - By simply›placing the disk in the specified›drive after disk boot option›selection, any boot file on that disk›will be disassembled.  This does›not work on double density disks. The›ATARI operating system initialization›code only supports double density›disk boot in half sectors. Caution-›Many times the disk boot file is›simply a loader to load the remainder›of the program.  Use the sector›disassembly option to disassemble the›remainder of the program once it has›been determined what sectors are›being loaded.››     BINARY LOAD FILES - DISASSEMBLER›6502 will disassemble any DOS 2.0 or›OS/A+ Version 2 format binary load›file.  Compound structures are also›supported.›››OUTPUT:››     There are four output options›available for DISASSEMBLER 6502.  Any›one or more in combination can be›used. You may continue to select›options until the <RETURN> key is›pressed.  At that time remaining›information may be obtained and›disassembly begun.››     SCREEN - Output is directed to›the screen editor.  A line of output›includes the hex machine instruction,›the 6502 assembler language›instruction, and the hex address of›the instruction.››››     PRINTER - Output is directed to›the printer.  You will be prompted›for an optional page heading to be›printed at the top of each page.  A›line of output includes the hex›instruction, the line sequence number›(as it would appear on a disk output›file), the assembler instruction and›the hex address of the instruction.››     DISK - Output is directed to a›specified disk file.  The output is›in LIST format and includes a line›sequence number, assembler›instruction, and hex address.  The›file can be ENTERed into the›assembler/editor for modification and›reassembly.  Since most assemblers›can only assemble about 1800-2100›lines of instructions, the output is›put into multiple files of 1600 lines›or less.  This allows room for›modifications. An extender of X01 -›Xnn is appended to the file name. All›of the output files can be›reassembled as a unit by using the›.INCLUDE facility and/or disk›assembly facility which are available›in many good assemblers.  They can›also be assembled separately and›combined using the binary save›feature of DUP.SYS.  A 1600 line file›will use from 120 to 150 single›density disk sectors. Thus an empty›disk can hold two files.  Double›density disks have double the›capacity.››     CASSETTE - Output is directed to›a cassette recorder in the same format›as that directed to disk.  The files›are also split into 1600 line files.›This will require most of one side of›a sixty minute cassette.›››UNRECOGNIZED INSTRUCTIONS:››     If an opcode is encountered that›is not recognized as a valid 6502›opcode, a .BYTE instruction is›generated.  Up to three unrecog-›nizable characters will be included›in a single .BYTE record.  A BRK›instruction ($00) most often occurs›as a data byte rather than an›instruction.  The disassembler treats›binary zeros as a .BYTE character.›››››     Since data bytes that are valid›opcodes cannot be distinguished by a›disassembler as data bytes, they will›be interpreted as instructions.  The›logic flow of the program should›indicate which of these instructions›are actually data bytes.  This mis-›interpretation of data bytes will not›prevent the reassembled program from›looking just like the original.››