›  ----------------------------------››  From: Chuck Steinman / DataQue›  Acct: GEnie: DataQue.1›  Date: May 16, 1990›  Subj: Misc CBPP Information››  File: CBPPINFO.DOC››  ----------------------------------››  Some information is derived from›  information contained in documents›  received from ChalkBoard, Inc.››  ----------------------------------››  ----------------------------------›  pad resolution (total):››  x-axis:  120›  y-axis:  120››  ----------------------------------›  pad numric orientation (x,y):››   ---------------------›   | 120,000   000,000 |›  ||                   |›  ||                   |›  ||                   |›   | 120,120   000,120 |›   ---------------------››  ----------------------------------›  DB-9 connector pinout:››  pin  function            pia›  ---  -----------------  -----›   1   data from pad      bit-0›   2   clear to pad       bit-1›   3   clock to pad       bit-2›   4   sense from pad     bit-3›   5   n/c›   6   n/c›   7   +5v supply to pad›   8   ground to pad ›   9   n/c› ››  ----------------------------------›  DB-9 plug (from pad) orientation:››      5   4   3   2   1›    ---------------------›    \ o   o   o   o   o /›     \  o   o   o   o  /›      -----------------›       9   8   7   6›››  ----------------------------------›  Also included in this archive are›  two BASIC files which show how›  you can access the PowerPad with›  BASIC.  ››  CBPPPRG1.LST››  an 'all BASIC' file which shows›  the currently contacted X:Y›  coordinate on the pad.››  CBPPPRG2.LST››  basically the same file only›  with machine language USR calls›  to do the port manipulations.››  Both files are written in simple›  BASIC routines.  Yes, there are›  a multitude of ways the code ›  could be improved, but I dont›  think it would make the examples›  that much cleared.››  Anyway... have fun!  If you ›  write an application using ›  this information, I (and others)›  would appreciate it being uploaded›  so we can all enjoy it!››  Thanks,›    Chuck›  ----------------------------------››