Very briefly, this file is simply a›driver that installs a device M: into›the IOCB block and bumps memlo up to›$2580 under Spartados 3.2D. Open by:›OPEN #1,12,0,"M:" in basic with a GR0›screen. Get #1 for input, Put #1 to›change the mouse color. When you Get,›read Peek(84) and (85) for the last›location of the mouse when the button›was pressed. It uses some ram at $600›to $606 for temporary storage. The ›driver starts at $1B00 and unlike the›original Antic mouse of a few years›past, allows Disk I/O as well! Of ›course you have to "Close" the mouse›first. You'll find this one a bit›smoother in operation as well, when›you "Get" from the mouse.››G.Filion #26-249 Kitchener Cresc.›         Kamloops, B.C., Canada›         V2B 1B9›         For more info and/or the›         source code listing.››-------------------------------------››