Flick80.COM ver 1.0››FLICK80L.COM - flickering 80 column handler loads into low memory (8192)›FLICK80H.COM - version that loads into high memory (45056)›FLICK80.DOC -  this file››                               Intro››Flick80 gives you 80 columns at a cost of 4K of memory, only about 3K more›than the normal atari screen editor.  Flick80's pricipal is similiar to that›of FlickerTerm, except horizonal scrolling registers is changed each›vertical blank as apposed to character sets, saving 1K of memory required›by a second character set.  Every line is shifted 2 color clocks (4 graphics›8 sized pixels) right one vertical blank, and back the next, etc.  Also›screens are swapped (actually display lists are swapped.)  This requires›each line pointer in the display list be set 4 bytes lower, and HSCROLL is›alternately changed from 0 to 2 each vbi.  Because each screen is swapped›with an alternate screen every 1/60th second the screen will flicker.  Use›in a dimly lit room with careful adjustment of contrast and brightness›controls may improve the picture somewhat.  I used the font from flickerterm›since characters are 4 pixels wide instead of the 3 pixel wide characters›I used in earlier version.››                               Usage››Enough technical babble.  Here is how to use this handler.  Two versions are›present in this distribution.  FLICK80L loads into low memory for use with›BASIC, cartridges, and programs that load into high memory.  FLICK80H loads›into high memory and is for use with programs that load into low memory›like KEDIT (my editor) or DOS. You can also BLOAD FLICK80H into turbo BASIC XL.›Flick80 is basically an output device, this version supports no cursor or›Editing.  If you attempt a line input via Flick80, any editing functions will›be returned within the string.  FLICK80L loads at 8192 ($2000) and uses›4K of memory.  Place it as an AUTORUN.SYS file with MYDOS or Atari Dos and›boot to BASIC or cartridge.  Going to DOS with any DOS using memory above›8192 will cause a crash.  It also loads some code temporaily at 12288 that›is not needed after the handler has been installed.  FLICK80H loads at 40960›($A000) to 49151 ($BFFF) but only remains resident at 45056 ($B000). ››                            Using with KDIT››To use Flick80 with KEDIT version 1.51.  Copy KEDIT to a copy of the handler›and copy DUMMY.SYS to EHANDLER.SYS and be sure it is in the default path (D:)›when you load KEDIT.  Be sure to use the FLICK80H handler not FLICK80L.›Flick80 will not work correctly if it is renamed EHANDLER.SYS and loaded by›KEDIT and I am not sure why.  With KEDIT, the cursor will appear to be wider›than it should be, the left half of the cursor block is the actual cursor.››                               Comments››This is a bare bones handler that I scrunched into 4K.  Inverse video looks›bad because inverse characters will interfere with adjacent characters.›Bold characters could be used instead like on flickerterm by using Player-›Missile graphics (I think thats how flicker-term does it) at a cost of speed›and memory.  Or, inverse characters could be represented by colors.›Hopefully someone will find this version useful.  I welcome any comments›or requests for other versions.  If you don't find the flickering display›distracting, try FlickerTerm VT100 terminal emulator.  If text upload/capture›and some transfer protocols are added it would be a great program.››Ken Siders›cp576@cleveland.freenet.edu››P.S.›A graphics 8 type 80 column handler and a fast 40 column hander are available›with KEDIT and may be freely distributed.  The graphics 8 type handler uses›almost 12.5 K of RAM where FLICK80 uses only 4K.›››