OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     This release of OmniCom features a limited but quite functional  VT100 
     emulation, XMODEM, Kermit, capture mode, and screen dump.  We plan  to 
     continually improve this package as time goes on.  You can always  get 
     the latest version by sending us $10.00. 
      
     Every attempt has been made to make OmniCom compatible  with  850-like 
     and 835/1030 devices.  For there to  be  any  hope  that  it  will  be 
     compatible with other incompatible devices  (MPP,  in  particular)  we 
     will need technical data on the device.  Feedback on whether it  works 
     with these and other devices is requested: 
      
                                 CDY Consulting 
                                   421 Hanbee 
                              Richardson, TX 75080 
                                  (214)235-2146 
      
     The OMNIVIEW has been updated to support the  entire  ASCII  character 
     set.  In particular, the characters for left and right  braces,  grave 
     accent,   and  tilde  have  been  substituted  for  the  corresponding 
     (worthless) characters in the ATARI character set.  If you bought your 
     OMNIVIEW before these changes you can update to the latest version  by 
     sending us the old chip with $10.00. 
      
                             Getting OmniCom to run 
      
     ATARISRS.232 is an RS232 handler for the 850,  835,  and  1030  and  I 
     believe it originated from Russ Wetmore.  It provides an  'R:'  device 
     that will work with any of these ATARI modems.  If you have an 835  or 
     1030 you should probably use this as your RS232 handler.  If  you  are 
     using a P:R:Connection you will want to use the handler supplied  with 
     that device. 
      
     To get this program into an executable form you will  need  to  append 
     OC.OBJ    to   your  RS232  handler.    For  example,  if  you  choose 
     ATARISRS.232, then you should make a copy of it to a file called 'OC'. 
     From DOS this is done as follows: 
      
                     'C (RETURN) ATARISRS.232,OC (RETURN)'. 
      
     Then append 'OC.OBJ' with the following command: 
      
                       'C (RETURN) OC.OBJ,OC/A (RETURN)'. 
      
     Now you can load and execute 'OC' with the 'L' option of DOS: 
      
                            'L (RETURN) OC (RETURN)'. 
      
                              Operation of OmniCom 
      
     First of all I must give credit to David Bailey and others who  worked 
     on the public domain version of  VT10SQ,  a  simple  80  column  VT100 
     emulator.  Their work resulted in a minimal VT100 emulation  that  was 
     satisfactory for many applications.  It was used as an early model for 




                                     page 1 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     OmniCom, which has much improved screen and keyboard processing, along 
     with  file  transfer  protocols  and  the  ability  to  customize  the 
     communication parameters. 
      
     The operation of OmniCom was designed to be simple and  yet  flexible. 
     If you are running a 300 baud modem then you can  just  start  typing. 
     If you are running a 1200 baud modem then you will want to change  the 
     baud rate.  This and other parameters are changed via the  OPTION  key 
     under the '(P)arameters' selection.  Using the  OPTION  key  you  will 
     also find other goodies: a BREAK generator, capture mode, an  835/1030 
     dialer, file transfer, dumb ATASCII or smart VT100 terminal selection, 
     and the ability to quit to DOS.  Feel free to  experiment.    You  can 
     answer any question with a RETURN without having any effect. 
      
     Although OmniCom should be able to keep up with 1200 baud most of  the 
     time, it may have trouble keeping up if several screens of  continuous 
     data are received, especially if the lines  are  short,  resulting  in 
     lots of scrolling.  In this case it will  use  XON/XOFF  to  keep  the 
     input buffer from overflowing.    You  will  know  this  is  happening 
     because the screen border will blink everytime an XOFF is  sent.    If 
     you want to avoid missing any characters on the screen, be  sure  that 
     the computer at the other end has XON/XOFF activated.  It is even more 
     critical that XON/XOFF be activated  during  capture  mode  since  the 
     capture buffer is quite small (256  bytes).    If  the  host  you  are 
     communicating with cannot be made to recognize XON/XOFF  then  capture 
     mode will work very poorly. 
      
     The keys to generate the characters for left and right  braces,  grave 
     accent, and tilde (which ATARI left out of  their  character  set  for 
     some dumb reason) are as follows: 
      
                    Left brace  : control-9 
                    Right brace : control-0 
                    Grave accent: control-7 
                    Tilde       : ATARI key (lower right corner) 
      
     The other thing you should be aware of is the simulation  of  the  DEC 
     VT100 keypad.  It is accessed by holding down  the  SELECT  key  while 
     typing the following keys: 
      
     Mapping of VT100 Keypad to ATARI Keyboard  
      
                        +-------+-------+-------+-------+ 
                        | PF1/1 | PF2/2 | PF3/3 | PF4/4 | 
                        +-------+-------+-------+-------+ 
                        |  7/Q  |  8/W  |  9/E  |  -/R  | 
                        +-------+-------+-------+-------+ 
                        |  4/A  |  5/S  |  6/D  |  ,/F  | 
                        +-------+-------+-------+-------+ 
                        |  1/Z  |  2/X  |  3/C  |       | 
                        +-------+-------+-------+ENTER/V| 
                        |      0/B      |  ./N  |       | 
                        +-------+-------+-------+-------+ 




                                     page 2 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


      
     If you do not like this mapping you are free to redo it to  suit  your 
     tastes.  Read about that in  the  next  section  on  customizing  your 
     keyboard. 
      
                        ATARI     VT100 keypad         Xmitted 
                                                      Sequence 
                                              (application)(numeric) 
                      <SELECT ->     UP ARROW   <ESC O A>  <ESC [ A> 
                      <SELECT =>   DOWN ARROW   <ESC O B>  <ESC [ B> 
                      <SELECT *>  RIGHT ARROW   <ESC O C>  <ESC [ C> 
                      <SELECT +>   LEFT ARROW   <ESC O D>  <ESC [ D> 
                      <SELECT 1>        PF1     <ESC O P>   (same) 
                      <SELECT 2>        PF2     <ESC O Q>   (same) 
                      <SELECT 3>        PF3     <ESC O R>   (same) 
                      <SELECT 4>        PF4     <ESC O S>   (same) 
                      <SELECT Q>        7       <ESC O w>   (same) 
                      <SELECT W>        8       <ESC O x>   (same) 
                      <SELECT E>        9       <ESC O y>   (same) 
                      <SELECT R>        -       <ESC O m>   (same) 
                      <SELECT A>        4       <ESC O t>   (same) 
                      <SELECT S>        5       <ESC O u>   (same) 
                      <SELECT D>        6       <ESC O v>   (same) 
                      <SELECT F>        ,       <ESC O l>   (same) 
                      <SELECT Z>        1       <ESC O q>   (same) 
                      <SELECT X>        2       <ESC O r>   (same) 
                      <SELECT C>        3       <ESC O s>   (same) 
                      <SELECT V>        ENTER   <ESC O M>   (same) 
                      <SELECT B>        0       <ESC O p>   (same) 
                      <SELECT N>        .       <ESC O n>   (same) 
      
                             ATASCII/VT100 Selection 
      
     If you wish to communicate with an ATARI BBS system, you may  want  to 
     do so in ATASCII mode to take advantage  of  the  ATARI  line  drawing 
     graphics and editing functions.  Some ATARI BBS's  use  this  mode  to 
     draw pretty boxes and do animation.  The other characteristic of  this 
     mode is that all CR characters ($0D) are translated to $9B.   However, 
     a Hayes compatible modem will only recognize CR to terminate commands. 
     Thus, when you are talking directly to a Hayes  compatible  modem,  as 
     when you are dialing (ATDT...), you must be in VT100 mode.  Switch  to 
     dumb ATASCII mode after you get  the  "CONNECT"  indication  from  the 
     modem but before typing anything else (the  BBS  will  use  the  first 
     RETURN character to determine whether you  are  in  ATASCII  or  ASCII 
     mode).  You do so by pressing OPTION and typing "T2". 
      
                                  Sending BREAK 
      
     Some systems require the remote terminal to send a BREAK in  order  to 
     set communication parameters.  This can be done by pressing OPTION and 
     then typing 'B'. 






                                     page 3 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


                                  Capture Mode 
      
     IMPORTANT: The computer you  are  communicating  with  must  recognize 
     XON/XOFF in order for this feature to work!  XON  and  XOFF  are  what 
     OmniCom uses to control the speed at which the other computer sends it 
     data in order to prevent it from overflowing the capture buffer. 
      
     Capture mode allows you to save everything that is being sent  to  you 
     from the other computer to any output device.  Usually you  will  want 
     to capture the data to a disk file or to the printer.  This is done by 
     pressing OPTION and typing 'C'.  You can supply a  file  specification 
     or just hit RETURN if you want the output to go to  a  printer.    You 
     terminate capture mode by pressing OPTION and typing 'C' again.   This 
     will cause the output file to be closed.  Using 'Q'  to  quit  OmniCom 
     will also close the file. 
      
     It is important to note that capture mode is designed to be used  only 
     with ASCII data.  The reason for this is that it is not reliable  like 
     the file  transfer  protocols  XMODEM  and  Kermit.    Also,  it  will 
     translate all incoming CR characters ($0D) to  $9B  and  discard  LF's 
     ($0A).  It is most useful for grabbing mail or documentation where  an 
     occasional missing or garbled character is not critical. 
      
     If you are capturing to a printer attached  to  an  ATR8000  you  will 
     notice that the printing will be sporadic and appear not  to  keep  up 
     with the screen.  This is because the ATR8000  is  also  used  as  the 
     modem interface and cannot print while  serial  I/O  is  active.    To 
     deactivate serial I/O press OPTION.  This will  take  OmniCom  offline 
     and allow the data stored in the ATR's printer buffer to  flow  freely 
     to the printer.  This should only be done when you expect no new  data 
     from the remote computer since it will be lost until  you  hit  RETURN 
     again to take OmniCom back online. 
      
                                   Screen Dump 
      
     You can make an exact copy of the screen to the printer at any time by 
     holding down SELECT and then  pressing  OPTION.    Any  data  arriving 
     during the interval that the screen is being  copied  to  the  printer 
     will be lost.  If you own an ATR8000 then you will also want  to  read 
     the last paragraph under Capture Mode. 
      
                            Customizing your Keyboard 
      
     If you type OPTION and 'P', you will be asked if you want to edit  the 
     key mapping.  Answering 'N' to this question  (or  just  RETURN)  will 
     take you into the  section  to  adjust  the  communication  parameters 
     (explained in the next section).  If you do  want  to  customize  your 
     keyboard then answer 'Y'. 
      
     Now you are free to assign one or more characters (up to 17)  to  each 
     key or key in combination with CONTROL, SHIFT,  or  both  CONTROL  and 
     SHIFT.  Do that by typing the desired key when prompted.  Now you will 
     be asked for the code(s) that you wish that key to produce.   You  can 




                                     page 4 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     do that in hex if it is to produce only one byte.  Otherwise  you  can 
     delete the hex byte and hit RETURN to specify a sequence of characters 
     up to 17 bytes long.  When specifying the character sequence  you  are 
     free to use the normal ATARI editing controls.  If you want to  insert 
     a  CONTROL  character  (like  CR)  hold  down  CONTROL  and  type  the 
     corresponding letter of the alpahbet.  For example,  if  you  want  to 
     insert a CR ($0D), type CONTROL-M.  One key many people will  need  to 
     change is DELETE/BACKSPACE.  As it comes, OmniCom produces a DEL ($7F) 
     when this key is  pressed  and  a  BS  ($08)  when  control-DEL/BS  is 
     pressed. You may want to reverse these definitions. 
      
     An entirely different set of key codes are accessed when you hold down 
     SELECT while typing a key.  SELECT activates the keypad mode.  In this 
     mode a VT100 generates a particular sequence of characters everytime a 
     key is pressed.  This sequence  is  ESC-'O'-code  where  the  code  is 
     different for every key of the keypad.  You can edit these codes also, 
     but you are only allowed to enter one byte in hex. 
      
     As you customize your keyboard you will want to save these changes  to 
     disk so that your keyboard will always act the same when  you  execute 
     OmniCom.     To  save  your  customized  keyboard  (along  with  other 
     parameters you may have changed, like screen color)  just  hit  RETURN 
     when prompted for the next key to edit.  Now you  will  be  given  the 
     opportunity to either save the changes you just made  or  restore  the 
     previous parameters, negating any recent changes.    These  parameters 
     are stored in a file called OC.OPT.  This file must be on drive 1 when 
     OC is loaded for your options to be in effect. 
      
     Using these techniques you can even alter the keyboard  for  use  with 
     PROFS on an IBM mainframe.  This has been done for you and is  on  the 
     disk under PROFS.OPT.  Rename this file to OC.OPT  and  your  keyboard 
     will act according to the following mapping (thanks  to  David  Bailey 
     for coming up with this convention): 
























                                     page 5 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


                Yale Protocol        ATARI     VT100 keypad   Xmitted 
                   Converter                                  Sequence 
      
                      PF1          <SELECT 1>        PF1     <ESC O P> 
                      PF2          <SELECT 2>        PF2     <ESC O Q> 
                      PF3          <SELECT 3>        PF3     <ESC O R> 
                      PF4          <SELECT 4>        7       <ESC O w> 
                      PF5          <SELECT 5>        8       <ESC O x> 
                      PF6          <SELECT 6>        9       <ESC O y> 
                      PF7          <SELECT 7>        4       <ESC O t> 
                      PF8          <SELECT 8>        5       <ESC O u> 
                      PF9          <SELECT 9>        6       <ESC O v> 
                      PF10         <SELECT 0>        1       <ESC O q> 
                      PF11         <SELECT CLEAR>    2       <ESC O r> 
                      PF12         <SELECT INSERT>   3       <ESC O s> 
                      PA1          <SELECT Q>        PF4     <ESC O S> 
                      PA2          <SELECT W>        -       <ESC O m> 
                      PA3          <SELECT E>        ,       <ESC O l> 
                      NA           <SELECT R>        0       <ESC O p> 
                       
                      NEWLINE        <RETURN>        RETURN  <^M> 
                      ENTER          <ATARI> (Logo)  LF      <^J> 
                      CLEAR          <CONTROL-CLEAR> ENTER   <ESC O M> 
                      FIELD TAB      <TAB>                   <^I> 
                      DELETE         <DELETE/BACK S>         <DEL> ($7F) 
                      ERASE EOF      <CONTROL-DELETE/BACK S> <ESC DEL> 
                      TOGGLE INSERT  <CONTROL-INSERT>.       <ESC O n> 
                      HOME           <CONTROL-H>             <^H> 
                      RE-DISPLAY     <CONTROL-V>             <^V> 
                                      <CTL-7>   Grave Accent <$60> 
                                      <CTL-8>        Tilde   <$7E> 
                                      <CTL-9>     Left Brace <$7B> 
                                      <CTL-0>    Right Brace <$7D> 
      
                        Changing Communication Parameters 
      
     If you press OPTION and then answer 'P' and 'N', you will be given  an 
     opportunity to adjust some communication parameters,  set  the  screen 
     colors, cause  local  echo,  and  then  save  your  changes  to  disk. 
     Remember, if you want to leave a parameter the way  it  is,  just  hit 
     RETURN. 
      
     In selecting the baud rate,  you  can  either  choose  300,  1200,  or 
     customize.  If you choose to customize then you can specify the values 
     for AUX1 and AUX2 during the XIO 36 and XIO 34 when the modem  channel 
     is opened.  These two XIO commands control the  baud  rate,  the  word 
     size, the number of stop  bits,  carrier  detect,  and  other  control 
     lines.  Refer to your interface manual to  find  out  which  of  these 
     parameters are recognized by your interface: 
      
     XIO 36: AUX1: bits 0-3 - baud rate ($0A=1200, $08=300, $0E=9600) 
                   bits 4-5 - word size (8 to 5 bits  -> 0 = 8 bits) 
                   bit  7   - 1 or 2 stop bits (0 = 1 stop bit) 




                                     page 6 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


      
             AUX2: bit  0   - monitor CRX  * Interface will return an    * 
                   bit  1   - monitor CTS  * error if one of these lines * 
                   bit  2   - monitor DSR  * is selected but not on.     * 
      
     XIO 34: AUX1: bits 0-1 - 0 -> do not change XMIT 
                              2 -> set XMIT to SPACE (0) 
                              3 -> set XMIT to MARK (1) 
                   bits 4-5 - 0 -> do not change RTS 
                              2 -> turn RTS off 
                              3 -> turn RTS on 
                   bits 6-7 - 0 -> do not change RTS 
                              2 -> turn DTR off 
                              3 -> turn DTR on 
      
     In selecting the parity you can either  choose  none,  even,  odd,  or 
     custom.  If you choose to customize then you will be able  to  specify 
     the AUX1 and AUX2 to be used during the XIO 38 when the modem  channel 
     is opened.  This XIO command controls parity, translation and linefeed 
     options: 
      
     XIO 38: AUX1: bits 0-1 - 0 -> do not change parity bit 
                              1 -> set output parity odd 
                              2 -> set output parity even 
                              3 -> set output parity to 1 
                   bits 2-3 - 0 -> ignore and do not change parity bit 
                              1 -> check for odd parity, clear parity bit 
                              2 -> check for even parity, clear parity bit 
                              3 -> do not check parity, clear parity bit 
                   bits 4-5 - 0 -> light ATASCII/ASCII translation 
                              1 -> heavy ATASCII/ASCII translation 
                              2 -> no translation 
                   bit  6   - 0 -> do not append LF 
                              1 -> append LF after CR 
      
     After setting the modem parameters you  can  set  the  screen  colors. 
     These values are stored in the color  registers  at  $2C5,  $2C6,  and 
     $2C8.  You may have to experiment to find the  best  colors  for  your 
     tastes.  You can also activate local echo if the computer at the other 
     end is not echoing your typing. 
      
                           Use of XMODEM File Transfer 
      
     XMODEM is a simple, fairly  reliable  way  of  transferring  files  to 
     (upload) and  from  (download)  other  computers  and  bulletin  board 
     systems.  It uses a very simple handshaking mechanism for transferring 
     the file in 128 byte blocks whereby each  block  that  is  transmitted 
     must be acknowledged by the receiving computer with a single byte ACK. 
     If noise on the line causes the block to arrive  corrupted  then  this 
     will usually be detected by a checksum that is appended to the  block, 
     in which case a NAK is returned instead so  that  the  block  will  be 
     retransmitted.  A sequence number is also part of the block to  insure 
     that everything arrives in order and that no block is lost. 




                                     page 7 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


      
     To start the transfer you must get the remote computer started  first. 
     For example, if you wish to download a file (from the remote  computer 
     to yours) you must tell it  that  you  wish  to  download.    It  will 
     probably ask you for the filename and then after a short interval tell 
     you that it is ready.  At that point you can go to the OPTION menu and 
     choose (F)ile-xfer and then  (D)ownload.    You  must  then  supply  a 
     filename, which can be different from the  filename  supplied  to  the 
     remote computer.  After that your computer will  send  a  NAK  to  get 
     things started and you should see  the  transmit  and  receive  lights 
     blinking, assuming that your modem has status lamps.   You  will  also 
     see a number representing the  retransmission  count  printed  to  the 
     screen for every block transferred.  When the transfer is complete the 
     file transfer menu will appear again and you can (Q)uit or hit  RETURN 
     to go back to the terminal mode. 
      
     Before an upload or download is  attempted  you  should  first  decide 
     which mode to do the transfer in,  ASCII  or  ATASCII,  and  make  the 
     appropriate choice under the (O)ptions selection  in  the  (F)ile-xfer 
     menu.  ATASCII will transfer the file as is, without any  translation. 
     It is mainly used for transferring programs and other non-text  files. 
     In ASCII mode during upload, all $9B bytes are converted to two bytes: 
     $0D $0A (CR LF).  In ASCII mode during download, all  $0D  (CR)  bytes 
     are converted to $9B and all $0A (LF) bytes are thrown  away.    ASCII 
     mode is used for transferring text, especially if the remote  computer 
     is not an ATARI. If you are unsure  which  mode  to  use,  ATASCII  is 
     probably the safest, especially if you are communicating with an ATARI 
     computer. 
      
     Another option concerns the method in which the XMODEM  at  the  other 
     end handles the end-of-file.  OmniCom defaults to using the byte count 
     of the last block to pad the last block (which seems to  be  the  most 
     popular technique in the ATARI world).  However, many systems pad  the 
     last block with ctrl-Z ($1A).  If you know this to be the case  or  if 
     you discover extraneous ctrl-Z characters at the end  of  a  file  you 
     downloaded, be sure to enable this option. 
      
     Under the same (O)ptions selection in the  (F)ile-xfer  menu  you  can 
     also make a couple of other choices.  If you would like  you  can  put 
     OmniCom in debug mode so that all XMODEM transactions are  printed  to 
     the screen. You may find this interesting but it is not good to  leave 
     it in this mode all the time as it will slow down your file transfers. 
     Another option is the default disk drive when you  do  not  supply  it 
     with the filename at the beginning of a transfer.  Once you have these 
     options set the way you like them you will probably want to save  them 
     to disk under the (P)arameters selection in the OPTION menu. 
      
                                Kermit Operation 
      
     For file transfer over a packet switched network like  the  ARPANET  a 
     more robust protocol like Kermit is usually preferred, even though  it 
     is slower than XMODEM.  The Kermit in OmniCom is  particularly  robust 
     because it will not only retry individual packets but, if a particular 




                                     page 8 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     file fails for any reason, it will keep retrying that file until it is 
     finally successful.  If the remote computer is in server mode then you 
     can be fairly certain that your transfer will be successful,  even  if 
     left unattended.  If you want to abort a transfer you  can  do  so  by 
     holdng down START/SELECT/OPTION for one packet time.    You  can  also 
     cause a premature timeout or retransmission by typing any key. 
      
     A complete description of Kermit operation is beyond the scope of this 
     manual.  However, for most cases you can put the  remote  computer  in 
     server mode by starting the remote Kermit and typing "server".    Then 
     you can control things  from  your  end  by  using  either  (S)end  or 
     (R)eceive.  When prompted for a filename wildcards are  allowed  (this 
     is the one big advantage over XMODEM). Use  the  (F)inish  command  to 
     take the remote computer out of server mode.  You can  also  send  and 
     receive files one at a time by starting the operation at each end  for 
     every file.  Notice that the filename is part of the  transfer  so  it 
     does not do any good to specify the filename on the receive end. 
      
     The Kermit protocol is more elaborate than that of  XMODEM,  involving 
     the exchange of communication parameters and the filename in  addition 
     to the user data.  It also uses a quote character ('#')  to  transform 
     all control characters (<$20) into printable ASCII characters  because 
     some communications  media  and  networks  are  sensitive  to  control 
     characters.  There are also provisions for quoting bytes with the  8th 
     bit on and for repeat counts but these options are not yet implemented 
     in OmniCom.  If you are curious, you can activate the debug mode under 
     the 'Options' selection to see the protocol in action.   However,  you 
     should not always run in  this  mode  because  it  slows  things  down 
     considerably and may cause unneeded retransmissions. 
      
     A couple of other things may be of help.  To transfer binary files  or 
     other files where the 8th bit of the characters  is  necessary,    you 
     will need to use the '(O)ptions' selection to tell Kermit to pass  all 
     8 bits.  Also, you must not have parity enabled (under 'Parameters' in 
     the VT100 OPTION menu) if you want your modem to pass all  eight  bits 
     intact.  Likewise, you may have to do something special to  your  host 
     to make it store 8 bit files.  For example,  if you are going  through 
     a TAC onto a host on the ARPANET, you will need to make the  TAC  pass 
     all   8  bits  with  the  following  commands:  '@b  o  s(RETURN)@b  i 
     s(RETURN)'.  On a TOPS-20 operating system the  command  to  make  the 
     Kermit store 8 bit files is: 'SET FILE 8-BIT'. 
      
     Also under the (O)ptions selection  you  will  find  that  the  Kermit 
     timeout between retransmissions can be set.  If you are  communicating 
     over a network with large  delays  (possibly  because  of  congestion) 
     resulting in many timeouts you may want to lengthen this parameter. 
      
            Responses To Characters Received By the Terminal Emulator 
      
     Unknown  escape  sequences  of the form "ESC char" are absorbed by the 
     emulator without further effect. 
      
     Escape Seq     Mnemonic       Description of Action 




                                     page 9 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     ESC D          IND            Index, cursor down 1 line, can scroll 
     ESC E          NEL            Cursor start of line below, can scroll 
     ESC H          HTS            Set one tab at current position 
     ESC M          RI             Rev Index, cursor up 1 line, can scroll 
     ESC Z          DECID          Indentify term (response is ESC[?1;0c) 
     ESC 7          DECSC          Save cursor position and attributes 
     ESC 8          DECRC          Restore cursor from saved position 
      
     ESC [ Pn A     CUU            Cursor up Pn lines, does not scroll 
     ESC [ Pn B     CUD            Cursor down Pn lines, does not scroll 
     ESC [ Pn C     CUF            Cursor forward, stays on same line 
     ESC [ Pn D     CUB            Cursor backward, stays on same line 
     ESC [ Pn; Pn H CUP            Set cursor to row, column (same as HVP) 
     ESC [ Ps J     ED             Erase in display: 
                                   0= cursor to end of screen, inclusive 
                                   1= start of screen to cursor, inclusive 
                                   2= entire screen, cursor does not move. 
     ESC [ Ps K     EL             Erase in line: 
                                   0= cursor to end of line, inclusive 
                                   1= start of line to cursor, inclusive 
                                   2= entire line 
     ESC [ Pn; Pn R CPR            Cursor report (row, col), sent by term 
                                   Example: home position yields ESC[1;1R 
     ESC [ Pn c     DA             Device attributes (reports ESC [?1;0c) 
     ESC [ Pn; Pn f HVP            Set cursor to row, col (same as CUP) 
     ESC [ Ps g     TBC            Tabs clear, 0 = here, 3 = all 
     ESC [ 20 h     LNM            Set newline mode (lf = cr/lf) 
     ESC [ 20 l     LNM            Reset newline mode (lf = lf) 
     ESC [ ? Ps;...;Ps h  SM       Set mode, see table below 
     ESC [ ? Ps;...;Ps l  RM       Reset mode, see table below 
             Ps     mnemonic       mode           set            reset 
             1      DECCKM         cursor keys    application    numeric 
             3      DECCOLM        Columns         clear  screen      clear 
     screen 
             5      DECSCNM        Screen         reverse video  normal 
             7      DECAWM         Autowrap       on             off 
     ESC [ Ps;...;Ps m  SGR        Select graphic rendition 
                                    0 = reverse video off 
                                    7 = reverse video 
     ESC [ Ps n     DSR            Device Status Report. 
                                   Response from VT100: 0 = ready. 
                                   To VT100: 5 = report status with DSR, 
                                   6 = report cursor position using CPR 
     ESC [ Pn; Pn r DECSTBM        Set top and bottom scrolling margins 
      
     ESC ( A  or  ESC ( B          G0 points to ASCII symbols 
     ESC ( 0 or ESC ( 1 or ESC ( 2 G0 points to line drawing graphics 
     ESC ) A  or  ESC ) B          G1 points to ASCII symbols 
     ESC ) 0 or ESC ) 1 or ESC ) 2 G1 points to line drawing graphics 
      
     ^G             BELL           Beep and blink border color 
     ^H             BS             Backspace, cursor left one character 
     ^I             HT             Horizontal tab, cursor to next tabstop 




                                     page 10 





               OmniCom: VT100 Emulator/Kermit/XMODEM for OMNIVIEW 


     ^J             LF             Linefeed, move cursor down one line 
     ^L             FF             Formfeed, treated as a line feed 
     ^M             CR             Carriage return, move cursor to col 1 
     ^N             SO             Invoke G1 character set 
     ^O             SI             Invoke G0 character set 
      
                                                       David Young 04/01/87 


















































                                     page 11