››SMARTT.COM - by Joe Hitchens July 86››(This version compiled at $2400,›which seems to work with K65›Kermit/VT100 emulator)››SMARTT is a smart-modem emulating›handler for the Atari 1030 modem.››Its commands may seem awkward, com-›pared to the handlers for the Atari›modems.  But bear in mind it is pre-›tending to be a hardware box outside›your computer.  If you have actually›used a smart-modem these commands will›be familiar.››Most programs expecting the 850 or›similar device handlers should work›with this handler.  For serial I/O›do close R: and reopen R: when finished›like the 850.››The first time your program tries to›open R:, you should see the SMARTT:›prompt.  At other times, it may be›necessary to hit the "+" key 3 times›quickly to raise the prompt.  When›at the SMARTT: prompt, the following›Hayes smart-modem commands are›accepted.›››SMART T command summary:››atdt - pulse dial a number, for example›       ATDT7296046<return> dials›       and connects to NCAUG.››atdp - pulse dial, like atdt is tone›       dial.››ato  - if you are at the SMARTT: prompt›       but you just want to go back›       online, get connected by saying›       ATO››atb  - send a .5 second break signal››ata  - put modem into Answer mode, to›       pick up the phone››ath  - hang up the phone››atf  - set full/half duplex toggle›››That is the limited set of smartmodem›commands supported by SMARTT.  In›practice, SMARTT does not seem to›work with some programs.  However, it›does work with some R: telecom›programs when R.BIN doesn't.›