›I thought I had posted this last week, but we have had a queue problem...›(I wondered why I never saw these docs come up in the group!)  So here›they are again:››here are the docs for the pd vt100 emulator for the 8-bits...›i debated about posting this as is rather than 'compress'ing it on our›Unix system, and then uuencoding it there..., but i figured that›some of you may not have 'compress' and 'uudecode' on your unix systems,›so here it is.››it would be good to get some idea about how many of us in the 8bit›group have :››1) uuencode & decode on our:›a) unix systems›b) 8bits›2) arc & arc11 for the 8bits›  (which i posted recently)›3) compress & uncompress on our unix systems›4) are NOT on a Unix system...››if you all would like to send me mail telling me about your net›access environment, I would be willing to compile this info, and›post a summary to the group. (i hope it's not going to overflow my›mailbox!)››brad banko›cleveland, ohio›...!decvax!cwruecmp!ncoast!btb››››            *******************************************************›         ›                 VT-10-Squared Terminal Emulator Instructions›         ›            *******************************************************›         ›         Version 0.7 adds some VT-100 features and corrects some bugs›         in order to facilitate operation with UNIX and the vi editor.›         It also adds a capability to transmit even or odd parity.›         ›         This version of VT-10-Squared operates at either 300 or 1200›         baud, and will also operate with the ATARI 835 and 1050›         modems (thanks to the Russ Wetmore/Joe Miller R.BIN, and some›         consulting from Russ) as well as with the 850 interface›         module.›         ›         VT-10-Squared emulates a limited, but basic, set of VT-100›         functions. It provides a full 80-column screen by use of a›         software handler which uses a 3-pixel-wide character set.›         While the characters are not perfect, you will find them›         quite readable on a crisp monitor or black-and-white TV.›         ›         VT-10-Squared requires:›         ›              Atari 400/800 with 24 K (requires the translator disk›         when used with the XL's).›              DOS 2.0-compatible disk drive›              850 interface module and 300- or 1200-baud modem›                         OR›              835 or 1030 modem›                         OR›              A (compatibile) non-Atari handler--requires a special›         VT-10-Squared file called VT10NH.XMO›              A 'good' monitor›         ›         Two different keypad layouts are provided; one is patterned›         after the normal DEC VT-100 keypad, and the other is tailored›         for use with IBM's PROFS office automation software. You will›         probably want to use the DEC keyboard, but read the›         descriptions and decide for yourself!›         ›         VT-10-Squared does not support all VT-100 capability,›         particularly special graphics characters, special character›         sizes, and 132-column screen. As a result, it will not work›         properly with some DEC products.›         ›         GENERATING A WORKING DISK FOR ATARI 850, 835, or 1030.›         Download the file VT10SQ.XMO using Xmodem transfer protocol.›         This file should be renamed AUTORUN.SYS. DOS 2.0 must be on›         the same disk. This single file contains two handlers (for›         comm. and for the 80-column screen) as well as the main›         communication program.›         ››››››››››››››         ›         GENERATING A WORKING DISK FOR NON-ATARI HANDLERS.›         Download the file VT10NH.XMO using Xmodem transfer protocol.›         This file *does not* have any comm. handler, but only the›         80-column handler and the main communication program. With›         some non-Atari handlers, the next step is to name *your*›         comm. handler AUTORUN.SYS. Then append the VT10NH.XMO to the›         AUTORUN.SYS file (C - copy - VT10NH.XMO to AUTORUN.SYS/A›         using DOS 2.0). If this works, great. If not, you're on your›         own!›         ›         LOADING AND STARTUP.›         The disk produced above is self-booting. DOS 2.0 loads the›         three pieces (comm. handler, 80-col. handler, and emulator),›         and install the two handlers. After the program is booted, a›         title screen appears, followed by a setup menu. The setup›         menu permits choice of 300- or 1200-baud (not available for›         835/1030), choice of parity (none, even, or odd), and choice›         of the DEC or PROFS keypad layout (see description below).›         ›         When the setup is satisfactory, pressing <START> begins›         communication. If you're using the 850, start typing! (Setup›         your modem, or whatever.) If you're using an 835 or 1030, a›         new screen will appear so that you can type in the number to›         be dialed. All non-numerical entries are ignored (spaces,›         hyphens, etc.). Pressing <SELECT> will abort dialing.›         Pressing <SELECT> will also hang up the phone when you are›         finished.›         ›         Don't forget to have your 850, 835, or 1030 or non-Atari›         device turned on *before* booting VT-10-Squared. There are no›         error messages!›         ›         If you run across any problems, let me know.›         ›                                            -Dave Bailey [71635,1034]›         ››››››››››››››››››››››››››››››         ›         ›         ›                                  **********›         ›                    VT-10-Squared DEC keypad configuration›         ›                                  **********›         The 'DEC' keyboard functions are shown below. This keyboard›         arrangement is intended to bear a reasonable similarity to›         the VT100 layout, so that keypad functions can be translated›         with a minimum of pain.›         ›         Entries on the DEC keypad are made using a <ESC><char>›         sequence, where <char> is shown below in the right-hand cell›         of the VT100 keypad illustration. As an alternative, the›         keypad entry may be made using the <START> key as a shift›         key.›         ›         Of course, these two-character sequences apply only when the›         keypad is in 'Keypad Application Mode', and not for normal›         numeric entry.›         ›                                  VT100/ATARI›         ›                      ___________________________________›                     |        |        |        |        |›                     | PF1/1  | PF2/2  | PF3/3  | PF4/4  |›                     |________|________|________|________|›                     |        |        |        |        |›                     |  7 /Q  |  8 /W  |  9 /E  |  - /R  |›                     |________|________|________|________|›                     |        |        |        |        |›                     |  4 /A  |  5 /S  |  6 /D  |  , /F  |›                     |________|________|________|________|›                     |        |        |        |  E     |›                     |  1 /Z  |  2 /X  |  3 /C  |  N     |›                     |________|________|________|  T /V  |›                     |                 |        |  E     |›                     |      0 /B       |  . /N  |  R     |›                     |_________________|________|________|›         ›         ››››››››››››››››››››››››         ›         Additional VT100 keyboard entries are as follows:›         ›                 VT100              ATARI›         ›               Backspace         <DELETE/BS>›         ›                 Delete        <SHIFT-DELETE/BS>›         ›                 Escape          <ESC><ESC>›         ›               Line Feed        <ATARI>(Logo)›         ›              Grave Accent         <CTL-7>›         ›                 Tilde             <CTL-8>›         ›               Left Brace          <CTL-9>›         ›              Right Brace          <CTL-0>›         ›         Cursor control is the normal ATARI <CTL-arrow>.›         ››››››››››››››››››››››››››››››››››››››››››››         ›         ›         ›         ›                                  **********›         ›                   VT-10-Squared PROFS keypad configuration›         ›                                  **********›         ›         Note: PROFS is an Office Automation program which runs on IBM›         mainframes under VM/CMS. It is designed to work with an IBM›         3270 terminal. There is a protocol converter which runs on a›         IBM Series 1 minicomputer connected as a front-end to the›         mainframe which allows VT100 terminals (among others) to use›         PROFS. Since this protocol converters was first developed at›         Yale University, it is known by that name.›         ›         The following ATARI key sequences are used to represent the›         equivalent VT100/3270 keys:›         ›             Yale Protocol       ATARI      VT100 keypad   Xmitted›                Converter                                  Sequence›         ›                 PF1             <ESC><1>        PF1     <ESC><O><P>›                 PF2             <ESC><2>        PF2     <ESC><O><Q>›                 PF3             <ESC><3>        PF3     <ESC><O><R>›                 PF4             <ESC><4>        7       <ESC><O><w>›                 PF5             <ESC><5>        8       <ESC><O><x>›                 PF6             <ESC><6>        9       <ESC><O><y>›                 PF7             <ESC><7>        4       <ESC><O><t>›                 PF8             <ESC><8>        5       <ESC><O><u>›                 PF9             <ESC><9>        6       <ESC><O><v>›                 PF10            <ESC><0>        1       <ESC><O><q>›                 PF11            <ESC><CLEAR>    2       <ESC><O><r>›                 PF12            <ESC><INSERT>   3       <ESC><O><s>›                 PA1             <ESC><Q>        PF4     <ESC><O><S>›                 PA2             <ESC><W>        -       <ESC><O><m>›                 PA3             <ESC><E>        ,       <ESC><O><l>›                 NA              <ESC><R>        0       <ESC><O><p>›                 ›                 NEWLINE         <RETURN>        RETURN  <^M>›                 ENTER           <ATARI> (Logo)  LF      <^J>›                 CLEAR           <CONTROL-CLEAR> ENTER   <ESC><O><M>›                 FIELD TAB       <TAB>                   <^I>›                 DELETE          <DELETE/BACK S>         <DEL> ($7F)›                 ERASE EOF       <CONTROL-DELETE/BACK S> <ESC><DEL>›                 TOGGLE INSERT   <CONTROL-INSERT>.       <ESC><O><n>›                 HOME            <CONTROL-H>             <^H>›                 RE-DISPLAY      <CONTROL-V>             <^V>›                                 <ESC><ESC>      Escape  <ESC>›                                  <CTL-7>   Grave Accent <$60>›                                  <CTL-8>        Tilde   <$7E>›                                  <CTL-9>     Left Brace <$7B>›                                  <CTL-0>    Right Brace <$7D>›         ›         ›         As an alternative, all of the two-key sequences beginning›››››››››         with <ESC> can also be accomplished by using the <START> key›         as a shift key. (E. g., depressing <1> while holding down the›         <START> key will transmit the equivalent of PF1.›         ›         ›                                     -end-››Brad Banko›Cleveland, Ohio...!decvax!cwruecmp!ncoast!btb››