› CHARACTER FONT - Character Set Editor››The screen is divided into 3 windows:››  1. At the top is the Drawing/Edit›Window. The small white marks at screen›top show each character's boundary.››  2. In the middle the Selecting Window›displays the entire character set. Use›Joystick #1 to move the cursor to any›desired character; press FIRE to move›the character into the Edit Window.››  3. The bottom window displays your›character in any chosen graphics mode.›The pink line indicates the vertical›position of the drawing cursor.›››COMMANDS:››  [H or ?] - displays the HELP screens.››  [E]DIT - Toggles cursor between the›Drawing/Edit and the Selecting Windows.››  [B]LANK - Changes a series of chars.›into blank spaces. Use joystick/FIRE to›select starting & ending characters.››  [R]ESTORE - Changes a series of chars›back into their original forms. Works›in the same way as the BLANK command.››  [C]OPY - Makes multiply copies of a›single character. Use joystick/FIRE to›select, then move to the character to›be replaced & FIRE. ESCape exits mode.››  [F]LIP - Changes chars in the Edit›Window into their "mirror-images".››  [I]NVERT - Inverts EDIT characters.››  [INVERSE] - Changes the current Edit›display into inverse video.››  [M]ODES - Select Graphics Mode:›Graphics 0, 1, 2 or Antic modes 4 & 5.››  [P]UT SET - Displays your char. set›in the chosen graphics mode.››  [S]ELECT SET - Toggles the built-in›char. set with the set being worked on.››  [U]NDO - Restores original characters››  [>] UPDATE UNDO - Update characters›to the current data.››  [K]OLOR - Adjust color of characters›(Antic 4/5): Press 1-5 to select color›register; then move joystick left-right›to adjust color, up-down for luminance.›Press FIRE for next color register.››  [G]RID - Choose the size of the Edit›Window grid. Input 2 numbers. 6 x 6 is›max (only 2 lines can be displayed at›once). For Gr.2 or Antic 5 the grid›should be no bigger than 6 x 4.››  [A] TOP - Moves cursor to the top of›the EDIT grid.››  [Z] BOTTOM - Moves cursor to the›bottom of the Edit grid.››  [X] SWITCH - Alternates between two›characters. Press ESCape to exit.››Shift the characters in the Edit grid›one position - with "wrap-around":›   [-] SHIFT UP     [=] SHIFT DOWN›   [+] SHIFT LEFT   [*] SHIFT RIGHT››Adjust the speed of the Drawing cursor:›   [1] SLOW         [2] FAST››  [W]RITE DATA - Scans for redefined›characters, then writes then to Disk,›Tape, Printer, or Screen. If Disk or›Tape then either BASIC DATA or Assembly›.BYTE statements are options - you must›input the starting line nbr & filename.››  [D] INPUT DATA - Lets you type in the›numbers to form a character instead of›drawing it with a joystick. Choose the›first character, enter 8 numbers, and›press RETURN. Press RETURN only to skip›any subsequent char. ESCape exits mode.››  [OPTION] - Displays the directory of›any selected disk drive.››  [SELECT] - Loads a character set.››  [START] - Saves current character set›and the five color registers.››