THE XF SPEEDY REVIEWED
          ----------------------
          
          By FM and TML
          
          
          Supplier   : Klaus Peters
          Price      : DM 179,-
          
          It is almost unbelievable, but there are still new hardware kits
          designed and produced for the Atari 8-bit. The latest product of
          the German company 'Klaus Peters Elektronik + Software' is an
          upgrade-kit for the XF-551 disk-drive.
          
          This kit allows you to upgrade a standard Atari XF-551 to load
          and write in Ultraspeed. This means that all your disks will
          load approximately 6 times faster than a normal XF-551. Klaus
          Peters already made such an upgrade for the 1050 a few years
          ago. That upgrade was called a speedy, so he calls this upgrade
          the XF speedy.
          
          The kit consists of two printed boards, which are quite big, and
          a small switch. The printed boards replaces the CPU of the
          disk-drive. Because the CPU is soldered into the board of the
          drive, you have to solder it out and replace it with a socket.
          After that you also have to remove the ROM of the XF-551 drive
          and a small wire, which was not included, must be connected to
          one of the pins of the I/O socket. Last but not least, the small
          switch must be glued into the drive-mechanism. TML of
          ANG-software fitted this upgrade into my drive and he thinks
          that fitting this upgrade into the drive is far too difficult
          for people without soldering-experience.
          
          The manufacturer claims that the XF speedy is 100% compatible
          with the 1050 speedy. So lets take a look.
          
          I tested the speedy with several disks. All programmes which
          switch to Ultraspeed automatically are loading much faster than
          normally. When you own the Q-meg operating system the fun really
          starts. All disks will load and save in Ultraspeed. Also the
          disks which were made with standard drives. There is only one
          little problem: the density. A standard 1050 checks the density
          of the inserted disk when you close the drive latch. The XF does
          not have that feature. That is why you have to glue a switch
          into the drive mechanism. This switch will take care of this
          problem. Now when you close the drive latch the XF will also
          check the density. The only drawback of this solution is that I
          wonder if the switch will stay at its place.
          
          Back to the compatibility. There are several programmes
          available for the 1050 speedy to copy protected software.
          Examples of these programmes are Ultra Copier and MS copy. Klaus
          Peters has informed ANG that MS copy will be updated to work
          with the XF speedy. So I already knew that MS copy would not
          work so I tried to run Ultra Copier. The disk loaded perfectly,
          but when I tried to copy a disk the XF speedy crashed
          completely. The drive-busy light stayed on while the motor was
          not running. The only way to get the XF speedy running again was
          to switch the drive off. So Ultra Copier didn't run either.
          
          Together with the 1050 speedy you'll receive a disk with copiers
          and utilities which will work with the speedy. The disk loaded
          perfectly but that cannot be said of the programmes. One of the
          three copiers, namely Backup, does not work with the XF speedy.
          Fortunately the other two copiers, HSS copy and Copy 2000, work
          perfectly. It is the same story with the utlities. The utilities
          which test the speedy are working fine, but the utility to slow
          down the speedy will crash the speedy. Everything seems to work
          perfectly but when you load a disk the first sectors are read
          and then a very strange sound comes out of the drive. The drive
          will not load any further. But why slow down the drive? Some
          protected disks will not load in Ultraspeed. When you slow down
          the drive, the drive will simulate a standard drive and load all
          protected disks.
          
          An explanation of these problems might be that the disk, which
          you receive with the 1050 speedy, is specially made for the 1050
          speedy. The XF speedy does not come with any disk because the
          necessary programmes are stored in ROM. When you boot your
          system with the drive latch open you will automatically see a
          menu. In this menu you can slow down the drive and load a copier
          (copy 2000). Also a DOS is included in ROM, namely Bibodos. The
          slow down option in this menu works perfectly. All protected
          disks will load and run, but there is one exception: the
          original Polish version of Operation Blood (the ANG-version
          loads perfectly).
          
          After some while it was clear to me that the XF speedy simulates
          a 1050 drive. The XF drive was always very quiet, but now the
          drive makes the same noise as the 1050 when the read/write head
          is moving. An advantage of this is that the drive now runs disks
          which did not run on a standard XF-551. Examples are Boulderdash
          2 and the original Polish version of Inside. Also the problems
          of the index hole have been dissappeared. The disk can now be
          formatted at both sides without the need of a second index hole.
          
          According to the manual the XF speedy can also read and write in
          quad density format (360K). This is a feature of the standard
          XF-551 drive. I still have not managed to format a disk in quad
          density with the XF-speedy, but the speedy does recognize the
          format. It is strange that the built-in DOS, Bibodos, does not
          have the option to format in quad density. I had expected that
          such option was provided.
          
          The conclusion of TML is that this upgrade is far from
          perfection. The kit is very big and is not very stabil. Also the
          price of DM 179, which is about 65-70 pounds, is very high and
          the upgrade can not be fitted by a unexperienced solderer. The
          upgrade is also NOT 100% compatible with the 1050 speedy. I
          agree with him. This kit gives mainly the advantage of reading
          and writing at a much higher speed. It will make your drive more
          compatible but the price which must be paid for these advantages
          is very high.