This is a plaintext dump of the HTML version available at
 http://www.nacs.net/~classics.   The resulting format is sometimes hard
 to read.  For a well formatted and illustrated version see the URL above.

----------------------------------------------------------------------------


                         THE ATARI PERIPHERAL EMULATOR
                                  USERS GUIDE

                             -----------------


                                _Version 1.18_


    To make sure you have the _NEWEST_ version of APE, check the APE HOME
                   PAGE at _http://www.nacs.net/~classics/_


   Also see the ProSystem Users Manual and the APE Warp+ OS InfoPage for
                            current information!


   July 30, 1998





   _Steven J Tucker
   3978 Brookside Blvd
   Cleveland, Ohio 44111
   _U.S.A



   Written by Steven J Tucker

   Copyright (c) 1998 by Steven J Tucker




                           ---------------------

    The Atari Peripheral Emulator (APE) is a advanced serial application
                          that emulates an entire
   subsystem of atari 8 bit peripherals using your existing or purchased
                                 APE cable.

    APE has been created in the idea that _anything_ a real, physical SIO
                               device can do,
       APE can do better, faster, and at _far less cost_ than the real
                                peripheral!

     __________________________________________________________________

                            ORDERING INFORMATION

   For additional information on licensing the Atari Peripheral Emulator,
                       see the end of this document,
     the Ape Online Order Form, ORDER.DOC (included in the APExxxD.ZIP
                         distribution), or contact:

                              _Steven J Tucker_
                            Voice (216) 688-0001
                            3978 Brookside Blvd
                         Cleveland, Ohio 44111 USA

                            Electronic Mail to:
                             _classics@nacs.net _
               (if mail to this address fails, please e-mail
                         _ai123@freenet.carleton.ca_)


      _______________________________________________________________

                APE DISTRIBUTION AND SOFTWARE LICENSE TERMS

    _The Atari Peripheral Emulator, the Ape Pro System program and image
                                  format,
      this document and all other portions of the APE archive not the
                                property of
       third parties are the copyrighted property of Steven J Tucker_.

     Distribution of registered versions of this product is a violation
     of copyright law. You may use the unregistered version of this
     program for a 30 day free trial period. If after 30 days you wish
     to continue using APE you MUST purchase it or remove all copies of
     the software from your system.

     The author makes no representations or warranties with respect to
     the contents hereof and specifically disclaims any implied
     warranties of merchantability or fitness for any particular
     purpose. Further, the author reserves the right to revise this
     publication and to make changes from time to time in the content
     hereof without obligation of the author to notify any person or
     organization of such revision or changes.

                            PROGRAM DISTRIBUTION

     Without my written permission, no version of APE, past or present,
     may be included on any CDROM or other software compilation that is
     intended for sale, with or without profit to the seller. The
     shareware version of APE may not be sold for any amount, except a
     media charge not to exceed $5 US, without my written permission.
     The registered version may never be distributed in any form, and
     any licences received are non-transferable.

     Written permission can be obtained only by submitting your request
     along with your product content listing, and sale price to:

     Steven Tucker
     3978 Brookside Blvd
     Cleveland, Ohio 44111

     The shareware version of APE may continue to be freely distributed
     between private parties without charge (including personal web
     pages), and by online archives and BBS systems, without charge.

      _______________________________________________________________


                                WHAT IS APE?

    Thank you for trying the Atari Peripheral Emulator! You've taken the
     first step to making your Atari 8 Bit computer more enjoyable and
                                  useful!

    APE is an advanced serial application capable of emulating an entire
              subsystem of devices on the Atari 8 Bit SIO bus.



                        ---------------------------

                         WHAT HARDWARE IS REQUIRED?

   APE talks to the SIO bus of your Atari 8 bit home computer using the
   Ape Interface Cable (or SIO2PC cable). This serial device provides the
   hardware required to convert the voltage levels present on the Atari
   SIO bus to levels compatible with the PC serial port.

   This device hooks _directly to the SIO port of your atari computer_,
   and to the serial port of your PC compatible computer. No interface or
   other additional hardware is required!

   Plans for building this device yourself are found at the end of this
   document. The 2 chip version requires $20-25 of parts, some not
   commonly available. The newer _one chip_ version of this device
   requires only commonly available parts and can cost between $10-20,
   depending again on the cost of parts in your area.

   Assembly and testing of this device takes 2-3 hours. If you have no
   soldering experience I suggest you pick up a book on electronics and
   practice before attempting final construction.

   If you do not wish to make the interface yourself, I can provide a
   completely assembled and pre-tested serial unit for you. See ORDER.DOC
   for details, or ORDERING INFORMATION at the end of this document.
   Also, anyone purchasing the hardware from me will receive a _$5
   discount_ on the more robust REGISTERED version of this software.

                            PC Hardware Required

   APE is compiled using 808x compatible instructions, and will run on
   most any machine from an _XT to a Pentium II_ with a serial port and
   at least 200k of free DOS memory. A 286+ class machine with a hard
   drive and disk caching software (Norton Speed Drive, MS Smart Drive,
   etc) are recommended to get the very best performance. You should have
   WRITE BEHIND CACHING turned ON when using APE w/ disk cache software.

      _______________________________________________________________

                          CAN APE BE MULTITASKED?

   APE is designed to operate under MSDOS or MSDOS compatible operating
   systems that allow _exclusive control of the system by a single task
   _. APE requires very precise timing for its serial core functions, and
   may fail to function if operated under 'time sharing' operating
   systems such as Desqview, Windows 95, etc. Some users however have
   reported success under these operating systems with high end pentium
   class machines.

   _This is not a shortcoming in APE_. The Atari SIO bus was designed to
   talk to devices that were always ready to respond, and to respond
   within a strict time frame. When you system takes time away from APE
   for other applications, the time critical handshaking operations
   between APE and your Atari become desynced, and IO operations may
   fail.

   Even systems like Windows 95, which claim to give 'idle sensitive'
   control of the system to DOS applications can still fail. This is
   because the OS layer of these applications continues to slice time
   away from APE for its own housekeeping functions.

   If you wish to try running APE under Windows95, first run APE under a
   clean dos boot to see it work _properly._ After seeing how it should
   work, you will have better luck evaluating your success under windows.

   To boot to a real dos session with Win95 installed, press F8 _BEFORE_
   your system boots and select _Command Prompt Only_. When you do try
   running APE in a Win95 dos box, set _idle sensitivity_ under
   _Properties_ to its _lowest setting_, and _window type_ to Full
   Screen.

   _APE can also be run under Linux DOSEMU._

     _Instructions for running APE under dosemu 0.60:_


    1. In the dosemu-60.x/serial directory, edit the file ser_defs.h and
       change the following values:
    2. The line #RX_READ_FREQ. Change the value shown to 19L.
    3. The line #MS_MIN_FREQ. Change the value shown to 19L.
    4. This will change how often dosemu updates the serial port status
       registers for your dos box. We need FAST updates.
    5. In /etc/dosemu.conf, emulate ONLY ONE SERIAL PORT. Comment all the
       other ports out. If you enable 2 or more ports things get choppy
       as it takes longer to update the serial registers.
    6. (Re)compile dosemu and install it, run it, and run APE.


     APE should work OK for you. I have /dev/ttyS0 emulated, with
     'sillyint' set to off. Setting sillyint to the IRQ of your serial
     port might yield some improvement if you still have trouble. The
     higher the priority you give 'dos', the WORSE ape runs. If you set
     the priority with renice to say '14' then APE runs so good even
     APE+ 56kbps 3X ultraspeed works.

      _______________________________________________________________

       WHAT _SOFTWARE SERVICE_S & _HARDWARE EMULATION_ DOES APE PROVIDE?

    _APE emulates the following devices, commands and addressing modes. _

     * Up-To 8 Hard Drives & Floppy Drives
     * ANY DENSITY: Single, Double, Quad, and 1050 Enhanced Density for
       ANY floppy drive.
     * Disk images of up to 16 megabytes in size, up to 8 hard drives at
       once!
     * SpartaDOS ULTRASPEED I/O, or APE+ 3X SIO in any drive & density
       combination!
     * Full cooperation with REAL sio devices, such as disk drives,
       modems, printers, etc.

     * PC-MIRROR's new _ApeLoader_ software allows you to load EXE files
       directly from your PC Hard Drive!
       _Don't waste your time with boot loaders, ATR images, or menu
       programs anymore! _

     * Special _APE+ 3x SIO mode!_
       APE+ Ultraspeed is 1.5x faster than Happy Warp Speed, and 3X
       FASTER THAN STANDARD DISK I/O!
       _Functions transparently under Spartados, or ANY dos with the APE
       Warp+ OS. No patch or loader required!_

     * _PC MIRROR drive gives access to files on your PC hard drive &
       MSDOS filesystem with any dos and at all SIO speeds, including
       APE+ 3X SIO! _

     * REGISTERED users may now WRITE files, as well as read them from
       the PC mirror, making file transfers to your PC as easy as using
       the _Copy_ command of your favorite Atari DOS.

     * As of version 1.09, APE can emulate _ALL FORMS OF COPY PROTECTION
       _using images created using the AMAZING NEW APE PRO SYSTEM!

       APE can emulate even the most complex, heavily protected disks by
       companies such as Electronic Arts, Datasoft, Broderbund, etc!

       Ape's ProSystem can easily copy disks protected with so-called
       'impossible to copy' schemes such as the Electronic Arts
       super-track games (Realm of Impossibility, Archon II, etc),
       Synapse super-track, etc.

       _All using a STANDARD 1050 DISK DRIVE w/ ProSystem cable and
       software. No expensive Archiver/Happy hardware required!_

     * All your valuable copy protected diskettes can easily be converted
       to the new .PRO format using a stock 1050 (or 100% compatible)
       disk drive, using the powerful _APE ProSystem_ software!

     * FULL Emulation of the Atari 850 interface, allowing you to use
       your PC modem and printer _from any atari application_ that can
       use the 850 interface.

     * _100%_ 850 stage 1 compliant, allowing loading of the Atari R:
       handler from any communications program!

     * _Hardware flow control for the PC modem using the R: device. _
       A feature offered in NO OTHER ATARI 8 BIT SOFTWARE OR HARDWARE
       INTERFACE!

   _Basic SIO Commands Supported_
     * Read Sector
     * Write Sector
     * Put Sector
     * Disk Drive Status
     * Controller Format Diskette
     * Controller Format Enhanced Density Diskette
     * Read Percom Extended drive configuration block
     * Write Percom Extended drive configuration block
     * Get 'Speed Byte'
     * Ultraspeed HS I/O Sector Skew Format Diskette
     * Happy HS I/O Skewed Sector Format Diskette
     * Print to 850 interface
     * Initialize 850 R: Interface and download custom R: handler
     * Custom Stage 2 and 3 R: 850 Interface download code
     * XF551/Speedy High Speed Read Sector
     * XF551/Speedy High Speed Put Sector
     * XF551/Speedy High Speed Write Sector
     * XF551/Speedy HS Format Diskette
     * All Spartados 3.2X flavors of the above XF551 commands
     * Archiver Read Track (Beta)
     * Archiver Write/Format Track (Beta)
     * Happy Warp Speed Read Sector
     * Happy Warp Speed Put Sector
     * Happy Warp Speed Write Sector
     * Happy 'Are You Happy?' Command
     * Happy Read Status Command
     * Happy Format Diskette
     * Happy Init Controller
     * Happy Reset Drive
     * Happy Set Unhappy Command
     * Happy Set Fast Write
     * Happy Force Protect
     * Happy Force Write
     * Download Happy Tracer Data
     * Happy Controller Option RAM Load/Unload
     * Happy Drive Program Area RAM Load/Unload
     * REMOTE.COM download disk name
     * REMOTE.COM upload keystrokes
     * And many more...

      _______________________________________________________________

                                WHY USE APE?

     _Buying or building this interface, and purchasing the REGISTERED
     version of APE will be one of the the best investments you can
     possibly make in your Atari computer._

     APE is an investment in your Atari 8 bit, securing your data and
     ability to make use of it for years to come. APE provides
     extraordinary hardware emulation at a SMALL FRACTION of the cost of
     real hardware devices!

      _______________________________________________________________

                              THE PRICE FACTOR

     _For less than the price of a SINGLE 'refurbished' 1050 disk drive
   from one of the few remaining atari 8 bit dealers you will receive all
                               the following:_

     * Emulation of 8 disk drives, each of which may hold a disk image of
       up to 16 MEGABYTES.
       _Thats 128 megabytes of information and programs at your
       fingertips at all times!_

     * Each emulated disk drive is also capable of emulating the
       Spartados US Doubler ULTRASPEED (2x), XF551 Warp Speed I/O (2x),
       Happy Warp Speed I/O (2x), APE+ Warp Speed I/O (3x) [Under ANY
       DOS!]
       This enables your disk access to be more than _three times_ as
       fast as a standard 1050 disk drive using Spartados, Happy Warp
       Speed Dos, Mydos, and other high speed operating/dos systems and
       copy programs or just ANY dos using the Happy Warp Speed OS patch.
       New!: As of 1.10, Ape fully supports the Ape Warp+ OS Upgrade! You
       can now experience 3x SIO at all times, under any OS, and even in
       games! Check out the Ape Warp+ OS InfoPage for information and
       benchmarks.

     * Using APE is like having a hard drive equal to that of your PC on
       your Atari, and for a _SMALL FRACTION_ of what a similar system
       would cost for your 8 bit.

     * APE _preserves_ the value of your existing PC hardware by making
       it available to use on your Atari also.

     _Ape does ** NOT ** erase and reuse your PC hard disks, it stores
     data in 'disk images'. Disk images are regular PC files (like this
     one) that mimic the size and format of a real Atari disk. They may
     be as small as 90k, the size of a Single Sided/Single Density 810
     disk. And as large 16 megabytes, 65,535 DOUBLE DENSITY SECTORS._

     * If you previously used the software 'SIO2PC', your old SIO2PC disk
       images are 100% compatible with APE.
       APE itself creates images that are backward compatible with the
       SIO2PC .ATR format.

     * _Transparent access to your PC printer_ from any atari 8 bit
       application, without the use of any special atari software. APE
       can redirect the P: printer output of all Atari applications and
       send it directly to your PC Printer, or even to a file on your PC!
       APE also is capable of performing translations of this data on the
       fly to match the exact specifications of your PC printer!

     * _Direct access to any file on your pc hard drive, from your Atari
       using the powerful PC MIRROR function. _
       _Transfer files to and from your MSDOS filesystem, including hard
       drives, CD-ROM's, Floppy Disks, ZIP Drives and MORE using only the
       Atari DOS copy function! No other software can offer this
       revolutionary new feature!
       You can even download small separate executable (EXE) files from
       the major archives and run them right from the PC Mirror, without
       even copying them into ATR images! _

     * _Transparent access to your PC MODEM_ from most any Atari terminal
       program that is compatible with the Atari 850 interface!
       APE responds to stage 1 calls for the 850 interface R: (modem)
       handler, making it 100% compatible with terminal programs like
       _BobTerm _that use the device independent stage 1 loader!.

     * APE continues to provide access to your disk drives even when
       running in concurrent i/o.
       This allows you to do things such as run a BBS, download files,
       etc all without having ANY real atari disk drives or modems
       attached to your computer! (or wallet :)
       Note: _Concurrent I/O _is the special serial bus mode the atari
       uses to communicate with the 850 interface, modems and other
       streaming serial devices.

     * The _registered_ version of APE provides automatic _HARDWARE_ flow
       control, allowing you to access modems transmitting data faster
       that 19.2k. No other Atari 8 Bit Hardware or software product can
       provide this service!

     * _Advanced copy protection emulation!_
       _APE can emulate even the most complex copy protection schemes,
       making the archival of your valuable copy-protected originals
       possible._
       APE can emulate even the _most complex_ forms of floppy disk
       protection, such as '_Phantom Sector_' and '_Fuzzy Sector_'
       schemes.
       APEs _.PRO format_ has been able to archive even the most
       notorious of the late issue titles, such as:_ Alternate Reality_,
       _All Electronic Arts titles_, _Lucasfilm titles_, _First Star
       titles _(Spy vs Spy), _Broderbund_ titles, and others.
       The APE ProSystem is included in this distribution. It allows you
       to create .PRO images of even the most complex copy protected
       disks and use them with APE.
       All _PHANTOM EMULATION_ modes are not available to _unregistered_
       users. Modes 1,3,4,5,6,7,8, and 9 are reserved for users who
       support the future development of APE by _REGISTERING_.

     * _Reliability_. You will never fear your data being lost to a bad
       floppy disk. Your files and data will rest in file on your PC hard
       drive, and can be backed up to a more reliable storage medium such
       as CD-ROM, tape streamer, etc.
       We all know how difficult it can be to find good, working
       replacement hardware for our atari computers at reasonable prices.
       APE is designed to _eliminate_ these worries, providing you with a_
       flexible software system_ that will continue to grow and become
       more useful over time as the software is improved and upgraded.
       _
    And MUCH MORE! Read on to discover all the powerful features of APE.
          ____________________________________________________________

                              ABOUT SHAREWARE

     The user supported software concept (also known as "Shareware") is
     an attempt to provide quality software at low cost.

     Both the user and author benefit from this plan. The user will
     benefit by being able to "_test drive_" software thoroughly before
     purchasing it. The author benefits by being able to enter the
     commercial software market while avoiding the high cost of
     commercial distribution.

     This concept helps many independent authors and small companies
     that otherwise would be discouraged from developing and promoting
     their ideas. It can only work with your support. If you obtain a
     user supported program from a friend and are still using it after a
     few weeks, then it is obviously worth something to you, and a
     registration fee should be paid. _

     This software is distributed under the user supported software
     concept. Though APE is copyrighted, you are encouraged to copy and
     distribute the ** UNREGISTERED ** package to others. You may only
     distribute the unregistered software package in its original
     unaltered ZIP form.

     Please do not steal APE, it is the product of THOUSANDS of hours of
     coding and debugging. It also represents something quite rare at
     this time, new software development for the Atari 8.

     IF YOU USE APE LONGER THAN 30 DAYS YOU *MUST* REGISTER IT_

      _______________________________________________________________


            UNREGISTERED RESTRICTIONS AND REGISTRATION BENEFITS

    _Unregistered_ evaluation users have ALL of APEs powerful features at
    their disposal except the follow, which are available to _REGISTERED_
                                users only.

    1. _UNREGISTERED_ users may not bypass the startup screen. Registered
       users may bypass this screen by setting a configuration switch.
    2. _UNREGISTERED_ users are allowed _complete working access_ to the
       powerful _APELOADER_ software. UNREGISTERED users will see a
       registration reminder, and a small delay before loading an EXE
       file from the menu.
    3. _UNREGISTERED_ users are allowed _*FULL ACCESS*_ to read files in
       the _PC MIRROR_ drive. Only _registered_ users may WRITE files to
       the _PC MIRROR_.
    4. _UNREGISTERED_ users are allowed _FULL ACCESS_ to APE's advanced
       _Pro System_, and can create .PRO images of even the most complex
       copy protected diskettes. Only _REGISTERED_ users receive full
       access to all _PHANTOM EMULATION_ modes in APE.
    5. _UNREGISTERED_ users may not use sticky sessions.
    6. _UNREGISTERED_ users will see a short delay when using the
       APETIME.COM time downloader for the first time each session.
    7. _UNREGISTERED_ users will see a short delay when mounting images
       located with the [F]ind Image function.
    8. Registered users are granted _full access_ to APE's powerful
       ATR-FAST system. Once registered you will be able to see the
       contents of an ATR image _as you browse them_ in the file
       selector! A terrific time saving feature!
    9. Only 1 F-Key macro. _REGISTERED_ users may define 10 custom F-Key
       macros that allow any series of keystrokes to be entered
       _automatically_.
   10. Block Configurations. _REGISTERED_ users may create special _Block
       Configurations_ that allow up to 8 disk images to be loaded with a
       _single keystroke_. See later in this document for more
       information on block configurations.
   11. All of APE's enhanced SIO read modes are available to
       _unregistered_ users. You may read your diskettes at any speed,
       including the enhanced _3X APE+ SIO_ mode. Only _registered_ users
       may perform disk WRITES at the following speeds: Happy 2x Warp,
       APE+ 3x Warp, APE+ 3x Sparta.
       _Unregistered_ users may still read AND write at the US DOUBLER
       Spartados warp speed, and normal SIO speeds. The disk image
       _453_WARP.ATR_ is included as a demonstration of Happy 2x Warp SIO
       in MyDOS, and APE+ 3x SIO in MyDos. No special software or loaders
       are required to use these enhanced speeds under Spartados.
   12. _Unregistered_ users _ARE_ permitted to use APE's POWERFUL R:
       _Atari Modem emulator_, but only at speeds up to 2400 baud.
       _Registered_ users receive access to the concurrent i/o R:
       emulator at 38.4K and above! Speeds of up to _56k bps_ are
       possible using the enhanced _registered_ version of APE.
   13. _Registered_ Users may start the ATASCII/ASCII/UNIX text browser
       from the command line. _Unregistered_ users still have full access
       to this powerful feature, but must start it from within APE.
   14. _Unregistered_ users are limited to 2 command line switches. There
       are no limitations (except as imposed by the DOS operating system)
       on _registered_ users.
   15. APE's startup screen may be bypassed by _registered_ users, and
       there are no nag screens or timed waits.
   16. Unlimited usage. You may use the _unregistered_ version of this
       software for _only a 30 day trial period_. If you wish to continue
       using APE after that time you _must_ pay for it. The program will
       not eat itself or stop working after 30 days, I'm depending on
       your honesty as a fellow atari 8 bit computer user to do your
       part.
   17. Limited tech support. _Registered_ users will receive priority
       with regard to technical support issues, custom versions, and bug
       fixes.
   18. _Registered_ users will receive upgrades to the next revision of
       the program (os specific) free or at a substantial discount. (so
       far all upgrades have been free)
   19. Future registered versions will include:
          + The ability to save browsed text in ibm, unix, or atascii
            format.
          + Direct manipulation of files inside ATR images
          + Additional _PHANTOM EMULATION_ modes, as required.
          + _User Suggestions._ Over 50% of the new features in APE since
            Beta 4 are the direct result of suggestions submitted by _APE
            users._ Your comments, complaints, and suggestions are _very_
            important to me. Please feel free to contact me for even the
            smallest suggestion!

      _______________________________________________________________

                        INSTALLING AND STARTING APE

      The _SHAREWARE_ APE package is distributed as a ZIP'ed collection
     under the filename APExxxD.ZIP Where 'xxx' represents the version
     number of that archive. The archive contains the following files:

     APExxx.EXE The Main APE Executable
     PROxxx.EXE The FULL OPERATIONAL APE Pro System!
     SIGNATR.EXE Tool to sign & authenticate ATR Archives

     ORDER.DOC APE Registration and Order Form
     APExxx.DOC The APE Users Manual in ASCII Form
     PROxxx.DOC The ProSystem Users Manual

     APE_F32G.ATR APE version of the Spartados 3.2g distribution
      w/ APETIME.COM and REMOTE.COM

     APE_WARP.ATR APE version of the Mydos 4.53 distribution
      w/ REMOTE.COM, APE+ OS Patch and High Speed Sector Copier

     *.PRO Any Example .PRO Protected Disk Images
     *.CAS Any Example .CAS Digital Cassette Images

    To install APE, change to the directory on your hard disk where you
        wish to place APE and unzip the ZIP file by typing '_PKUNZIP
                                APExxxD.ZIP_'

     _HINT_: The first thing you should do when you start APE is to go to
     the _[Z]_ Configuration Menu and choose option _[D]_ to configure your
                                 Com Ports.

    This will allow APE to function if your computer uses a non standard
                    IRQ/BASE address for its comm ports.

      _______________________________________________________________

                                Starting Ape

      Once you have successfully installed APE, its time to start and
                      configure it for your hardware.

      Typing 'APE /?' will give you a listing of command line options:

                          _APE Command Line Options_

   Specifying any of these options on the command line will override any
    settings you might store in your startup _APE.CFG_ configuration file.

        These are all shortcuts for commands available in the main &
   configuration menus. Their complete functions are covered in detail in
                              those sections.

    _After processing of any command line options you may have specified
    the emulator will start. You will then be presented with the status
                                  screen._

     Use of the '/?' switch will immediately return you to DOS without
                           starting the emulator.

      _______________________________________________________________

                             The Status Screen

                             APE Status Screen


   This is the main status screen you will see during all disk operations
    with the Atari. All commands are carried out using the PC keyboard.

   The status screen displays a wealth of information about the state of
     your emulated peripheral system. The screen is as you would see it
       with various disk images loaded, and the emulator _is ready_ to
                  accepts commands from you or the Atari.

   The status line for bay 1 shows you have loaded 'DUNGEON1.PRO' and the
   following information:

     * _Sio Command_ - This field will display the last SIO COMMAND
       issued by the Atari to this drive.

     * _Sector_ - The sector number that was read

     * _Total_ - The total number of sectors in this image.
       In this case the image is that of a PROTECTED disk that contains
       more sectors than a normal 720 sector diskette.

     * _'P' - PRO System Emulation Mode_. '-' Indicates this image is
       _NOT A PRO IMAGE_. Any other symbol indicates the _PRO SYSTEM_
       copy protection emulation mode shown is currently active for that
       image.

     * _Dns_ - Represents the number of bytes per sector in this image,
       also called its _Density_. Single density sectors contain 128
       bytes, Double density sectors contain 256 bytes.

     * _Protect_ - Indicates if APE will or will not protect your disk
       image from writes by the atari. When you 'write protect' and disk
       image, _no_ harmful action can be taken on it by the atari

     * _Image Fname_: The real filename of the image as it resides on the
       PC hard drive.

     * '_Ultraspeed: APE+_' shows that the last command received on the
       serial bus was answered using the incredible _APE+ 3X SIO!_

     * '_Emulation: SMART_' shows that the emulator is currently handling
       disk images in its 'SMART' mode. More information on this feature
       is given in the KEYSTROKE COMMANDS section of this manual.

     * Any drive that is currently tied to the _PC mirror _function will
       have its drive number in inverse/red text as with drive 8.

     * Any disk images currently running in the _Pro System Emulation_
       mode (i.e. a .PRO file was loaded) will have the corresponding
       drive number _highlighted in inverse purple_. Disk 1 above is a
       copy protected disk image. The number listed indicates the current
       _Pro System Copy Protection_ emulation mode.

      _______________________________________________________________

                             Keystroke Commands

      Pressing _'H' _from the main menu will display the following menu:

                              Ape Help Screen

                                Help Screen

     * _[F1 - F10]_ - Execute Quick Macro. These keys will execute the
       quick macro assigned, just as if the command had been typed at the
       PC keyboard.

     * _! _- Spawn your default shell. This command will launch a _DOS
       shell _using the program specified in your _COMSPEC_ dos variable.
       If _COMSPEC_ is not set, it will attempt to spawn_ C:\COMMAND.COM_
       or _C:\DOS\COMMAND.COM_. You can set APE to swap itself to EMS or
       DISK using the configuration menu [Z]. By default APE will try EMS
       if it is available.

     * _@_ - You can _force the program into its concurrent i/o emulation
       mode_ with this command. This is only useful if while in your
       terminal program you are forced to abort concurrent i/o on the PC
       side to mount a new disk image, etc. More on modems, RS232
       emulation and concurrent i/o later in this document.

     * _1-8_ - You can use these keys to _swap disk images_ around in
       their bays. Lets say for example you have _ENCHANT1.ATR_ loaded in
       bay 1, and _ENCHANT2.ATR_ loaded in bay 2. After you load side one
       of Enchanter (which is stored in _ENCHANT1.ATR_) it tells you to
       please 'turn the disk over'. You can move_ ENCHANT2.ATR_ into bay
       1 _by simply pressing '12' on your keyboard._

     * _A_ - _DCM & XFD -> ATR Conversion_. Before you can use _Xformer
       (.XFD) and Diskcomm3 (.DCM)_ images with APE, they need to be
       converted from their format into a better ATR '_disk image_' thats
       available for random access, and has a descriptive header.
       When you select [A], you will be prompted for a filename or
       filemask for the image to convert. If your specify no filename, a_
       file selector will appear_ so you can pick a single XFD/DCM image
       to convert.
       If you sucessfully convert an image, you will then be asked if you
       would like to mount the new ATR image automatically!
       If you specify _wildcards_ (i.e. _C:\TEL\DOWN\*.DCM_) _all _the
       files matching your filespec will be coverted in automatic _BATCH
       mode._

     * _B_ : _Block Configurations Menu_. Block configurations are files
       that store the current state of all 8 bays of the disk emulator.
       This can be a _TERRIFIC time saver_ if you often need to load
       specific sets of disk images, for games, utilities, etc. With just
       a single command you can mount 8 disk images and be ready to go!
       To create your own block configuration file, use the 'L' command
       to load your disk images into the drive configuration you want to
       save. Then select the 'B' option. You will be asked if you want to
       _Load or Save_ a block configuration. Press 'S' for save. You can
       then choose a name for your block configuration, after which it
       will be saved to disk for future use.
       _Loading your newly created block configuration is now a breeze!
       _Just press 'B' then 'L' for load, choose your configuration from
       the menu and _all the images you specified previously will be
       automatically mounted!_

     * _C_ - _Create ATR Image_. This is possibly one of the most complex
       (and often confusing to the newcomer) part of using emulated
       disks.
       As previously explained, _your new atari disks are not real floppy
       disks at all_, but MSDOS files that match the storage capacity of
       the _real physical media._
       When you press 'C' to create a disk image, you will first be
       prompted to choose the _'disk size'_ for your image.


       _A number of pre-defined sizes are provided for your convenience.
       _These sizes are _exact_ matches for real physical disks/drives
       that are commonly used on the Atari 8 bit.
       Even though you may want small disk images for copying your real
       physical disks to (_for a perfect size match_), you can create
       disks as large as _16 *MEGABYTES* _each!
       Using advanced DOS systems like _MyDOS_ and _SpartaDOS_ you can
       format and utilize disks up to the Atari addressing limit of 16
       megabytes (_65,535 double density sectors_).
       If you are using a early dos, such as atari dos 2, 2.5, or other
       non-enhanced dos you should stick with the smaller sizes until you
       are more familiar with the creation of images.
       Once you have chosen a size for your disk image (_choose #1 if
       this is your first time_) we have to pick out a_ name_ for your
       'disk image' file on your PC.
       I recommend you use a filename that describes the contents of the
       disk image well, such as '_MYDOS.ATR_' for your MYDOS master disk,
       etc.
       If you wish to overwrite an existing disk image, you can simply
       press RETURN at the filename prompt and_ a file selector box will
       appear_. You may use this file selector to quickly pick the ATR
       you want to overwrite.
       _CAUTION: IF YOU OVERWRITE A DISK IMAGE USING THIS FUNCTION IT CAN
       NEVER BE RECOVERED, USE EXTREME CAUTION WHEN ERASING OLD DISK
       IMAGES! IF IN DOUBT CHOOSE A UNIQUE NAME FOR YOUR DISK._
       Once you have selected a filename you will be prompted one last
       time for final confirmation. You will also be shown various
       information about the image that will be created, such as real
       msdos file size, if the file exists, and its full pathname.
       Pressing 'Yes' when prompted will begin the creation of the disk
       image.


       This is _very_ dependent on speed of your machine, its disk
       caching, and your hard drive throughput. _A bar graph will display
       the progress of the creation._
       Small disk images are created very quickly, where as very very
       large disk images such as 16 megabytes can take a few minutes
       (_though this is rare, it takes 15 seconds on my 486/100_).
       Installing a disk cache with '_write caching_' activated will
       greatly increase the speed of this function, and also improve the
       performance of the emulator greatly.
       Once successfully created you will be asked if you wish to mount
       the image you just created. A great time saver over having to
       manually load the image after creation.
       FORMATTING YOUR DISK IMAGE
       Note also that a newly created 'disk image' is the same as a blank
       diskette you would bring home from the supply shop. _Its totally
       blank and must be 'formatted' using your favorite atari DOS before
       it can be used._
       _FORMATTING WITH ATARI DOS 2.x_
       If you disk is a standard size, such as 720 sectors & single
       density it can be formatted with any standard atari DOS. If you
       are using Atari DOS 2.0, you may only use disks of 720
       sectors/single density. Atari DOS 2.0 is rather stupid, and
       refuses to believe that any other size disk might exist.
       If you are using dos 2.5, you may create images of 1040 single
       density sectors (called _ENHANCED DENSITY_) You may then format
       them with Dos 2.5's '_I_' command.
       To make use of _VERY large_ disks (virtual atari hard drives you
       might say :) you will need an advanced DOS system such as
       _SpartaDOS _or _MyDOS_. _I recommend if you use your atari more
       than very infrequently that you get one of the DOSes_. They are
       not only capable of using standard sizes (720, 1040, etc sectors),
       they can manage images of _ANY_ size up to 16 megabytes.
       Both of these fine products are _SHAREWARE,_ and can be downloaded
       from gopher://gopherblue.umich.edu in the Software
       Archives/Atari/8Bit/Os directory. If you use them please register
       them. MyDos 4.53 is included in this APE distribution on the disk
       image Warp_453.Atr
       Lets assume you created the grand daddy of disk images, the 16 meg
       monster :) Formatting procedures for both DOS systems are as
       follows:
       _FORMATTING WITH MYDOS 4.5x_
       Boot MYDOS and mount your _mega disk image_ in bay 2. APE will
       show the image as having 65535 DD sectors.
       Choose option '_O_' from the _Mydos_ main menu, configure drive.
       We need to tell MYDOS that the disk in 'drive' one is bigger than
       your average disk (heh).
       _Steps for getting MyDos ready for a LARGE disk image_
          + Enter 'O' at the main menu for Configure Drive.
          + Enter '2' for the drive number.
          + Enter 'Y' for 'is drive configurable'
          + Enter 'Y' for 'is drive a HIGH CAPACITY drive'
          + Enter '65535' for number of sectors
       You should now be back at the main menu. Notice at the top of the
       screen that it says '_2H_'. Mydos now understands drive 2 is a
       _high capacity_ drive.
       We now need to FORMAT the 'disk' to make it ready for DOS use.
       Press '_I_' at the MYDOS main menu and format the disk (do _not_
       use the ENHANCED density option).
       To verify the disk was formatted Ok press '2' at the MYDOS main
       menu for a listing of files on drive 2. It should read _well over
       65,000 free sectors_.
       Now choose option 'H' and write the MYDOS disk operating system to
       your image. _Once completed you are ready to boot off your virtual
       hard drive! Yeah!_
       _FORMATTING WITH SPARTADOS 3.2g_
       Boot SpartaDOS and mount your _mega disk_ image in bay 3. APE will
       show the image as having 65535 DD sectors.
       _Spartados_ is a modular DOS system, its utility functions stored
       in separate executable files on the main system disk. To
       initialize a disk image this large, you will require the Spartados
       utility '_HDINIT_' (_Hard Disk Init_)
       _Run HDINIT_. It will ask you which hard disk you want to
       initialize, 3 or 4. The program apparently only thinks disks this
       big would be on those drive numbers, so for now its important your
       image be loaded in bay 3. (or 4)
       It will ask you if you're sure, and once confirmed will proceed to
       format and write the SpartaDOS FAT to your disk image.
       Now that the basic format of the disk has been established, you
       need to copy a dos file to the image so it can be booted directly.
       Copy your favorite Spartados DOS file (the *.DOS file, like
       X32G.DOS) from an existing disk (or disk image) to your new image.
       Type 'BOOT X32G.DOS' where X32G.DOS is replaced by the name of the
       DOS file you just copied onto the disk. Spartados will now
       configure the boot sectors of your hard disk image to self boot
       using the new DOS file!

     * _F_ - _Find Image_.

                             _Find Image Screen_

                             Find Image Screen
       The find image command will allow you to search any set of drives
       specified, including CDROM drives, floppy drives, etc.
       To specify which drives to search, use command [D]rives, and edit
       the drive listing.
       To speficy which files to search for, use the [F]ilespec command,
       and edit the search filespec.
       To start a search, just press [F]ind, and APE will start a quick
       search for up to 10 images that match your request.

                            _Find Search Results_

                                Find Results
       The screen above displays the results of a search for MyDOS
       related images, using the search filespec "MYD*.*" across drives
       A-G.
       As shown above, oncce you have the results of your search, loading
       the images into APE is easy!
       Just press [F1 - F10] to select the image you want to mount, and
       press [1 - 8] to select the APE bay you want to mount the image
       in!
       You can repeat the search / mount process as many times as you
       need to.
       While in the Find section, you can also perform some basic APE
       utility commands, such as [S]wap drives, and [R]elease Image.

     * _H_ - _Help_. Displays the quick keystroke reference chart.

     * _L_ - _Load Image_.

                      Ape 1.12 Enhanced File Selector
                      Ape 1.12 Enhanced File Selector

       This function is used to select an already created ATR image file
       and mount it in the drive '_bay_' of your choice.
       You will first be prompted to select the bay # for the image your
       going to load. _If an image in already using that bay you will be
       prompted to confirm before displacing it._
       Once you have selected the drive bay, you will then be asked for
       the filename of your disk image. If you know the filename and want
       to type it in you may, or you can just _press RETURN for an easy
       to use file selector with which you may browse your ATR images._
       After you select the name of your image, APE will take care of
       everything else such as reading the image configuration, etc, and
       mount it for you in your selected bay.
       If your image contains an Authentication Signature, it will be
       evaluated and if the CRC does not match you will be notified.

       PROTECTED DISK SOFTWARE
       _APE can now emulate ALL copy protection, even the most complex
       'Phantom' sector schemes._
       Using a special program to read your protected disks, APE can
       create _.PRO disk images_. _This is a new form of disk image,
       incorporating timing, error and other information critical to
       emulating the copy protection present on the orignal diskette._
       APE can currently emulate defective sectors and the resultant
       contents of the FD1771 status register when reading them._ APE can
       also emulate protection schemes that do not produce controller
       errors, such as the Phantom Sector protection used on Electronic
       Arts titles._
       APE has been tested with the following software originals and has
       performed _perfectly_.
       These PRO images are not '_cracked_' copies of games, but contain
       information representing the _real copy protection_ on the
       original diskette:
          + Alternate Reality, The City (Phantom Sector Protection)
          + Alternate Reality, The Dungeon (Fuzzy Sector Protection)
          + Realm Of Impossibility (EA 'Super Track' Protection)
          + Archon (Phantom Sector Protection)
          + Archon II: Adept (EA 'Super Track' Protection)
          + 7 Cities Of Gold (Phantom Sector Protection)
          + Agent USA (Standard Protection)
          + Spy vs Spy: Artic Antics (Phantom Sector Protection)
          + Ultima ][ (Standard Protection)
          + Jumpman (Phantom Sector Protection)
          + Koronis Rift (Phantom Sector Protection)
          + Apple Bandits (Standard Protection)
          + The Edilon (Phantom Sector Protection)
          + Spy vs Spy (Standard Protection)
          + Gumball (Standard Protection)
          + Karateka (Phantom Sector Protection)
       As other images are reported to work by registered users, they
       will be added to this list. _Based on the complexity of the copy
       protection used by the above companies, I am confident that APE
       can emulate 100% of existing software._

     * _P_ - _Change Pro Emulation Mode_. Changes the current ProSystem
       copy protection emulation mode for any currently loaded .PRO
       image.

       This function is available to _REGISTERED_ users only. You can now
       change ProSystem modes easily from within APE to allow you to find
       the best mode for your new .PRO images as quick as possible!

     * _Q_ - _Quit program_. Unmounts all images/drives and exits to your
       operating system.

     * _R_ - _Release Image_. This function will unmount your ATR image
       from the bay (drive) you select and make that slot then available
       for other disk images.

     * _S_ - _Set the PC MIRROR drive_.
       _The PC MIRROR is by far one of the most powerful features
       available to you in APE. _When you mount at drive as a 'PC MIRROR'
       that drive acts like a window to the files that actually reside on
       the MSDOS portion of your PC hard drive.
       Where before it was very difficult to get files from your PC to
       your Atari, using null modem cables, modems, terminal software,
       etc; _You can now access these files DIRECTLY!!_
       The new _APELOADER_ Software of the PC-MIRROR provides the
       _ULTIMATE_ bootloader, by giving you access to all your EXE files
       directly from the Atari keyboard, using a simple and functional
       menu interface.
       _You can access the APELOADER at any time by simply booting
       directly from your PC-MIRROR drive!_
       Lets try an example of using some PC-MIRROR services!

                             ApeLoader Services
               _________________________________________________

               _________________________________________________


   To boot the APELOADER, set the PC-MIRROR drive to drive #1, then boot
   your Atari from the PC-MIRROR as you would normally boot, depending on
                          if you want BASIC, etc.

   _The ApeLoader will work with or without BASIC, on any machine type._
                           __________________________

   ApeLoader KeyStroke Commands

   (all commands are used directly from the Atari keyboard)
                           __________________________

          + _A-Z and 0-9_: These keys select files or directories,
            depending on what is displayed on the screen.
            If you select a directory, the ApeLoader will change the
            directory on the PC, and automatically display the new
            listing of files!
            If you select an Atari executable file (EXE, COM, etc), APE
            will verify it to be a valid Atari binary file, and load it
            automatically!
            The memory footprint of the ApeLoader in Atari memory is
            _less than 128 bytes_! This makes the ApeLoader the _most
            powerful and flexable binary boot loader EVER MADE_ for the
            Atari. It can load _ANY_ file that does not REQUIRE dos.
            Even if the binary file overwrites the ApeLoader, _Ape can
            STILL LOAD THE FILE_, becuase the ApeLoader can be relocated
            in memory!
            The ApeLoader is also intellegent, and will try to start
            binary files even if they have had extra data appended to
            them via old style XMODEM transfers, etc!
          + _[Up Arrow]/[Down Arrow]_: Press these WITHOUT shift (easier
            that way :-). These keys cause the menu to scroll to the
            next/previous page of files. The ApeLoader can display up to
            3000 (yes, thats really _three THOUSAND_) files per
            directory.
          + _[Shift + Letter]_: Pressing SHIFT + any keyboard LETTER will
            cause the ApeLoader to instantly ZOOM to the first file that
            starts with that letter! This is a great timesaver, and even
            if you have 1000 EXE files in a single directory, you can
            file any one with just 2-3 simple keystrokes!
          + _[Control + Letter]_: Pressing CONTROL + any keyboard LETTER
            fill cause the ApeLoader to change your PC DIRECTORY to the
            drive letter you selected. e.g. press CONTROL+C for drive C:,
            or CONTROL+E for drive E:.
          + _[TAB]_: This option will change the BASE ADDRESS of the
            ApeLoader boot program.
            The BASE ADDRESS is the area of memory inside the Atari
            Computer used to hold the ApeLoader Boot Code.
            If your game/program tries to overwrite the ApeLoader while
            loading, just change the base address using this option and
            you can still load your program!
            Ape can relocate its loader to page 4 ($400) or to the high
            stack ($110).
               _________________________________________________

   _PC-MIRROR File Services_
               _________________________________________________


       Let's try the PC-MIRROR's powerful file services!
       Boot MYDOS 4.5x and once at the main menu choose APE option 'S'
       and mount your PC mirror drive in bay 2.
       Now, press '2' on the atari keyboard, you will get an atari
       directory of the files in the root directory of your PC hard
       drive! _APE takes the information from your PC files and makes
       your atari THINK they are on a real atari disk!_
       Lets try and copy one of your _MSDOS_ files to the atari. For this
       example we will use _AUTOEXEC.BAT_ since most anyone with MSDOS
       will have this file.
       Choose MYDOS option 'C' (_Copy file_) and then enter
       '2:AUTOEXEC.BAT,1'. This will tell MYDOS to copy file
       'AUTOEXEC.BAT' off drive 2, and put it on drive 1.
       _Its just that easy! The entire contents of your PC hard drive are
       now at your fingertips!_
       _Note: Files on the pc mirror are sequential access only! If you
       wish random access to a file on the PC MIRROR for editing, etc,
       simply copy it to an ATR drive._
       NAVIGATING PC DIRECTORIES IN THE PC MIRROR
       Getting a directory listing of the PC MIRROR directory of your PC
       will show not only the files there, but also the _subdirectories_
       on your hard drive.
       One of my main goals when creating APE was to make it _DOS
       independent_.
       _SpartaDOS, MYDOS, etc all use separate methods for storing
       information in subdirectories, but APE will work with them all._
       _To change to a subdirectory on your PC MIRROR drive, all you have
       to do is to make the atari access that 'file' somehow. Its just
       that easy._
       If you using_ MYDOS_, use the _'L'_ command and 'load' the
       directory. You will receive an error, which is _*NORMAL* and
       expected._ _APE is telling MYDOS that it cant load that file and
       mydos goes back to its main menu. _Now press '2' once again. _WOW!_
       APE has changed directories and your now looking at the
       subdirectory you selected on your PC hard disk.
       If your using _SPARTADOS_ all you need to do is type the name of
       the directory _(you may need to add a '.' to the end of the name
       if there is not extension, i.e. 'DOS.')_ and _APE will do the
       rest_. After you receive the error message, type 'DIR' once again
       and you will see APE has changed directories for you! :)
       Also note that the subdirectory you are in contains a directory
       called _'UP'_. _'L'oading or otherwise accessing this directory
       will cause the PC MIRROR to go UP the MSDOS directory tree to the
       parent directory. This is equivilant to the MSDOS command 'CD ..' _
       WRITING FILES TO THE PC MIRROR
       _Registered _users may now _WRITE_ files directly to the PC mirror
       using MyDOS. To transfer a file to the current PC MIRROR directory
       from your Atari all you need to do is use the MyDOS (C)opy command
       and copy your file to the PC MIRROR drive.
       _NO SPECIAL SOFTWARE OR DRIVER is required for this function! APE
       takes care of EVERYTHING for you, once the copy operation is
       complete, a file of the same name and size will exist on your PC
       hard drive! :)_
       This advanced feature will make file transfer problems between
       your PC and atari a thing of the past!

     * _T - Toggle Emulation. _This command switches APE between its
       _'SMART'_ mode of emulation, and its _'STUPID'_ mode.
       This toggle is useful for booting some programs that refuse to run
       on _'enhanced' _drives. This switch may be obsolete since the
       addition of full support for Happy Warp Speed I/O. It was really
       only useful with SUPERDOS which now works perfectly in Happy Warp
       Speed Mode.
       SMART MODE
       APE operates at full tilt, all _heuristics are enabled_ and APE
       will respond to all special and enhanced forms of disk
       communication it understands.
       STUPID MODE
       All Ultraspeed SIO _heuristics are disabled _and APE will refuse
       any request to switch into an enhanced drive emulation mode. _APE
       is most like a stock 1050 disk drive when used in this mode._

     * _U - Ultraspeed Toggle._ This command will _FORCE _APE to switch
       the method it uses to talk on the SIO bus. Normally APE uses
       advanced heuristic methods to _automatically_ determine what speed
       devices on the SIO bus are talking at, but if you encounter a
       problem with SpartaDOS desyncing you can use this command to force
       the switch.
       This command is left over from the early beta test versions of the
       program, and since I installed the new syncro code and switching
       logic I've never had to use it again.

     * _V - View Atascii/Ascii/Unix Text File. _You can browse any text
       file with this command, _even native ATASCII text!_
       Its is a completely integrated version of my Multitype file
       browser. Once you select the file to view, APE will determine what
       type of text is it automatically (atascii, etc). If APE fails to
       correctly display your text you can toggle the format manually
       with the _[F] _command inside the browser.
       You may browse _multiple files_ once the browser has been started
       by selecting the _[N]_ew filespec option. _Press ESC to exit the
       browser._
       _Registered users _may start the browser program from the command
       line, as a stand alone program within APE.

     * _W - Write Protect Image. _This function marks your ATR image as
       write protected, and affords it the protection offered by real
       physical write protection on floppies. Once write protected, any
       writes to the image will be totally ignored. _The Atari cannot
       damage or write to the image in any way._
       Write protect is a toggle, and your images may be _unprotected_ by
       using 'W' on them again.
       NOTE: This does not protect your images from being damaged by the
       MSDOS operating system, only by APE. As always, keep appropriate
       backups of your data.

     * _Y - Playback Cassette. _
       APE now includes full support for _Ernest Schreurs_ excellent
       digital cassette format. To obtain more information, and the
       program used to create .CAS files, you currently need to contact
       Ernest, as there is no public FTP site yet.
       This feature is unrestricted and free for all users. An example
       .CAS cassette file is included with APE.
       Playing files is a simple process, simply enter the filename (or
       use the lightbar selector to locate it), and APE will prompt you
       to press return to start.
       Boot your Atari the normal way you would load the cassette, and
       press return at APE and the Atari at the same time. The cassette
       will then playback.

     * _Z - Configuration Menu. _

   This is used to setup APE for proper operation with your system, and
   to setup your quick Function Key macros.

      _______________________________________________________________

   General Configuration Menu

   This screen controls the operation of most serial core functions, the
   hardware flow control for concurrent i/o, the sio command window, the
   verbose command monitor, sio command monitor filters, and registered
   user keystroke definitions.

     * _1 - Sio2PC device type_. This tells APE what kind of serial
       conversion cable you are using. Older versions of the cable use a
       2 IC setup which requires manual control over the serial bus
       tri-state.
       _Its very important you set this correctly._ If you have a 2 chip
       device and you set it to 1 chip, it will fail to function
       correctly or will cause interference with other, real SIO
       peripherals.

     * _2 - APE device port. _This is the Com port to which your serial
       conversion device is attached. Com Port _IRQ/Base Address_ may be
       set under configuration menu Z/C.

     * _3 - Framing Threshold._ This is used by the heuristic ultraspeed
       switching routines to decide how quickly to change modes when new
       speeds are detected on the SIO bus. Normally you will not change
       this setting.
       If APE switches to ultraspeed when it should not, you may have the
       framing threshold set _too low_. A setting of below 8 may cause
       this.
       If APE fails to switch into ultraspeed when using mixed speeds,
       and you get command timeouts or drive errors, you may have the
       framing threshold set _too high_.
       This will depend _greatly_ on the speed of your machine. I
       recommend a setting of 8 for most machines, but if this causes
       problems you will need to experiment with this setting. Framing
       thresholds of below 4 or above 15 are of no use and are not
       allowed.

     * _4 - Extra Safety Margin_. This setting should not be changed
       unless you are having serious timing problems due to your machine
       being _too fast_. Setting to other than '1' on machines which run
       APE fine will result in a decrease in performance.

     * _5 - Serial Control_. When building the standard APE Interface,
       you will use the RI line on the serial port. Some people have
       reported better performance under windows using the DSR line and
       requested an option to support it, so here it is. If you set this
       to DSR with a standard APE (RI) cable the system will not work.
       CTS is also available at the request of MAC users.

     * _% - Command filters_. Command filters are used to eliminate the
       display of commands you dont wish to see from the scrolling SIO
       command monitor. I.E. you may wish to filter out the read sector
       command _[$52] _to be able to see the more unusual SIO commands
       only.
       All other switches in this field control the HEX value of the
       filters you wish to use.

     * _F - SIO Command monitor._ This switch controls the scrolling SIO
       Command Monitor at the _bottom_ of the Status screen. _If your
       machine is slow, turning this OFF will help increase the speed of
       the emulator._

     * _G - Verbose command monitor._ This switch controls the display of
       the command names/sector numbers for each SIO command received.
       _Turning it off can help speed up the emulator on very slow
       machines._

     * _H - File Selector._ As of APE 1.12 a new, better file selector is
       available. It supports a number of new features: Atr-Fast Window
          + _Full Support for Windows 95 Long Filenames _(Only available
            in the Windows 95 Dos Box, see notes on multitasking)
          + _Warp-to-Key._ Pressing the first letter of a file will warp
            to it, and the next with the same letter if the key is
            pressed again.
          + _ATR-Fast_. Pressing SHIFT will display a window with the
            root directory of your Spartados/Atari DOS image. ATASCII is
            supported.
          + _Fast drive switch_. Pressing Ctrl-Drive to quickly change
            drives. i.e. Ctrl-D for drive D.
          + Extended use of Page Up/Down and Home/End keys.

       You can change to the old file selector if you dont like the new
       one using this option.

     * _I - ATR-FAST Mode_. When using the old file selector, you can
       control the method used to make the ATR-Fast window appear
       (registered users only). Options are:
         1. Never - The ATR-FAST window is disabled.
         2. Shift-Driven - Pressing any SHIFT key brings up the window.
         3. Always - The ATR-FAST window is always present.
       Because the new file selector needs the whole screen for Win95
       support, the ATR-FAST mode is always Shift-Driven when using the
       new selector, regardless of this setting.

     * _J - Swap out on Shell_. When spawning your default DOS shell with
       the '_!_' command, APE can swap itself out to EMS or DISK. You can
       set the default swap method here. If you don't want APE to ever
       swap out, select 'NEVER'.

     * _M - Happy/Syncromesh Detect Enable_. With some special
       applications, like some games and Spartados X, you might want to
       disable the detection of the Happy Enhancement and Syncromesh. You
       can do so by selecting 'RESTRICT'.

     * _N - ApeLoader Base Address_. With this option you can set the
       _default_ base address for the ApeLoader Boot Code. This option
       can be changed on the fly from the ApeLoader menu of course. See
       the PC-MIRROR section for more details on the Apeloader.

     * _O - Hard Write Protect_. As of 1.15, APE can use 2 different
       methods of emulating diskette write protect.
          + Old (_SOFT_) Method: No error is reported to the Atari when
            it tries to write to a protected ATR, yet the ATR remains
            unchanged.
          + New (_HARD_) Method: Atari receives en error when trying to
            write to a write protected ATR image. This mode operates
            exactly as if a real write protected diskette were in a real
            disk drive.

     * _P - Persistent Sessions_. Persistent sessions allow registered
       users to keep their current APE setup intact between sessions.
       For example, with persistent sessions turned ON:
          + You have 'C:\MYDISK.ATR' loaded in drive 1, and the PC-MIRROR
            set in drive 2.
          + You press 'Q' and quit APE.
          + You restart APE sometime later.
          + Your 'C:\MYDISK.ATR' is still loaded in drive 1, and the
            PC-MIRROR is still in drive 2 at the same path.
       With Persistent Sessions turned off, APE will start each session
       with 8 empty drive bays.
       This feature is not available to unregistered users.

     * _Q - Bypass Startup Screen_. This switch allows registered users
       to bypass the startup copyright and information screen.
       This feature is not available to unregistered users.

     * _T - FAT32 Long Filenames_. If you experience any problems with
       APE attempting to obtain long filenames, such are garbage in the
       file selector, you can manually disable the use of long filenames
       using this setting.

     * _U - Allow Large PC-MIRROR_. In APE 1.16, the PC-MIRROR has been
       expanded to allow files as large as 7 megabytes to be written
       directly to it. This change requires the PC-MIRROR to appear to
       the Atari to be a large hard disk formatted w/ Atari DOS.
       Spartados X for example, is not capable of reading from Atari DOS
       formatted hard disks due to a problem in the ATARIDOS.SYS driver.
       If you experience any problems reading or writing to the new
       PC-MIRROR, you may set this option to 'NO' to force APE to use the
       old, smaller, PC-MIRROR.
       A rom patch for Spartados X is available.

     * _L - Load APE Configuration_. Loads the configuration stored in
       APExxx.CFG, in the path which you launched APE from. If APExxx.CFG
       (where xxx is the version number) does not exist you can create
       one with the _[S]_ save function. This file is automatically
       loaded when you start APE.

     * _R - Restore system defaults. _This loads the default parameters
       that are _hard coded_ into APE. This should be used only if you
       damage your configuration and connot figure out how to reset it.

     * _S - Save APE Configuration_. Saves the configuration you have set
       in _ALL APE MENUS_ to the file called _APE.CFG_ in the path from
       which you launched APE.

      _______________________________________________________________

   _A_ - Printer Configuration

   This screen controls the operation of the _Atari Printer Emulation_.
   All commands sent from the atari to the_ P:_ printer device will
   handled by APE or passed on to your Atari printer depending on your
   configuration.

   Values set in this section can be saved to APExxx.CFG.

     * _A. Print Destination_. Select PRINTER to pass Atari print
       commands directly to your PC Printer, FILE to save the print data
       to a file, or NOWHERE to allow a real Atari Printer to answer the
       request.

     * _B. Printer Port_. If PRINTER is selected in option A, this option
       controls the PC Printer port used

     * _C. EOL Conversion_. When the atari prints data, it terminates
       each line with the _ATASCII_ (Atari Ascii) EOL character which is
       155. The PC terminates each line diffrently, with a _CR/LF_ pair.
       Even though this is the standard for PC text, some printers
       require_ only _the CR part be sent.
       If your printer requires line feeds (such as the_ HP deskjet_
       series) then select _YES_. If your printouts are all on one line,
       text overlapping text then your printer requires line feeds and
       CR/LF should be _selected_.

     * _D. Atascii TAB conversion_. The Atascii character set uses a
       different value for _TAB_ than the PC and PC printers. Enabling
       this will _automatically_ convert these characters to PC
       compatible ones.

     * _E. Global conversions_. Enabling this will strip the high bit
       from all characters sent to the printer. Useful with some printers
       that may react badly to _ATASCII_ graphic characters, etc.

     * _F. Printer data drive and filespec_. Specify in this box the file
       in which you want printer data sent from the Atari stored in, if
       you selected 'FILE' in option A.

     * _G. Append or Overwrite_. Selecting APPEND will cause the file
       selected in option F to be added to each time APE prints, if you
       select OVERWRITE, the file will be replaced each time APE starts

      _______________________________________________________________

   _B_ - Modem (_R:_) Setup & Emulation

     * _A. PC Modem Com-Port_. Com-Port of the PC MODEM to use when
       emulating the R: modem/interface device on the Atari 8-bit.

     * _B. PC Modem Baud Rate_. Baud rate at which the PC will
       communicate with the PC-Modem. By default this is 57.6k BPS.

     * _C. PC Modem DTR Line_. Setting of the DTR line when communicating
       with your PC-Modem. Consult your modem manual for the proper
       setting.

     * _D. PC Modem RTS Line_. Setting of the RTS line when communicating
       with your PC-Modem. Consult your modem manual for the proper
       setting.

     * _E. Hardware Flow Control Window_. Unlike all other serial
       adapters and products, APE can provide real _HARDWARE FLOW CONTROL_
       for your Atari.
       This option sets the overflow queue size after which hardware flow
       control will be used.
       A setting of 700 is default.

     * _F. Disable R: Emulation_. Disabling R: emulation will stop APE
       from doing the following things.
          + Opening or reading from the specified com port.
          + Responding to requests for the 850 interface handler.
          + Doing any modem emulation.
       It is reccomended that you use this switch if you do not have a
       modem attached to your PC.

          ________________________________________________________

   _C_ - APE Path, Macro, and Find System Configuration
   Path Configuration Screen

   This screen allows you to set the APE Search Paths for locating
   images, the _PC-MIRROR_ path and filespec, the Find system defaults,
   and the Quick Macros.

   Values set in this screen may be saved to APExxx.CFG.

     * _[1 - 0] - Define APE Quick Search Path._
       The APE Quick Search Paths are a tool for convienent access to
       your disk images.
       Specify upto 10 locations on any device attached to your PC, and
       APE will automatically look in those directories each time you
       specify an image that is not located in the current directory.
       For example: you press [L] to load an image, and type MYDOS.ATR in
       the quick load box. If MYDOS.ATR is not found in the current DOS
       directory, APE will look in all the paths specified here for it
       automatically.

     * _[F1-F10] - Define Quick Macro._ The quick macro feature of APE
       can be a _very powerful _time saver. By allowing you to enter a
       series of keystrokes to be executed on the function key of your
       choice, most any feature of APE (_and even into the DOS shell!_)
       can be automated!
       All characters entered in your macro will be executed _EXACTLY_ as
       if you had typed them from the PC keyboard. The only exception to
       this is the '|' character which is used for a embedded carriage
       return.
       Any function that requires a _RETURN_ when done should be trailed
       by the '|' character since APE will not press return for you be
       default.
       This feature can also execute functions _OUTSIDE APE!_ You can use
       the '!' function to shell to DOS inside your macro and any
       remaining keystrokes will be executed by your dos shell. (i.e.
       '!EDIT AUTOEXEC.BAT|' would cause APE to shell to DOS and execute
       _EDIT AUTOEXEC.BAT_)
       _Example_: Setting F1 to the string '!C:|CD C:\TASM|MAKE|EXIT|'
       and then pressing F1 at the APE main screen will:
         1. Cause APE to shell out (command !)
         2. Change to drive C (C: typed at the command prompt)
         3. Change to directory 'C:\TASM\' (CD C:\TASM typed at the
            command prompt)
         4. Execute the program or batch file called 'MAKE' (MAKE typed
            at the command prompt)
         5. Exit back to APE (EXIT typed at the command prompt)
       All quick macros are executed from the main status screen only. To
       access deeper functions simply add them to your macro. (i.e.
       'L1C:\TEST.ATR|' to tell APE you want to load an image, then in
       Drive 1, then the filename and RETURN to load it)

     * _D - Find Image Drives. _This is the _default_ list of drives that
       will be presented to you each time you use the [F]ind Images
       command. You may add or remove any drives you desire.

     * _F - Find Image Filespec. _This is the _default_ filespec that
       will be presented to you each time you use the [F]ind Images
       command.

     * _P - Default PC Mirror Path. _This is the _default_ path APE will
       use for the PC-MIRROR each time APE is started.

     * _M - Default Mirror Filespec. _This is the _default_ filespec that
       will be used for the PC-MIRROR each time APE starts.

     * _R - Remember last path used. _If this is set to YES, APE will
       remember the last PC-MIRROR path and filespec you used between
       sessions, and restore it each time APE is started.
       For example: if you last accessed a file via the PC-MIRROR in
       C:\MYFILES\ then APE would start in that directory next session.
       If this is set to NO, APE will use the values entered here as the
       default pathname, and filespec each time it starts.

      _______________________________________________________________

   _D - Com IRQ & Base Address

   _This menu will allow you to confure APE to function with the
   _IRQ/BASE address_ settings used on your computer. APE is pre
   configured with the 'standard' AT values for these ports, so _you
   should only need to use this function if APE fails to perform properly
   for you._

   To find the IRQ/BASE address of your com port use the_ MSD.EXE_
   utility provided with MSDOS v5 and above, or consult your users
   manual.


   You may totally disable any Com ports you wont be using by setting its
   BASE ADDRESS to_ $0000_. This is normally NOT required, but may help
   if you are running TSR comm software, etc.

      _______________________________________________________________

   E - Configure Ultraspeed

   The above menu will allow you to tell APE what speed it should operate
   at with Spartados and other programs that use the US Doubler enhanced
   warp speed mode.

   _This option effects ONLY the operation of US DOUBLER type I/O and has
   NO EFFECT on the operation of other high speed systems such as Happy
   Warp Speed or XF551 mode._

     * _1 - Force 1x SIO operation in Ultraspeed mode._ This will force
       APE to *NEVER* switch into 2x or 3x ultraspeed mode, even when
       asked to. _This option should NEVER be used unless you have very
       serious problems with Ultraspeed I/O._ (Please contact me if you
       do!)

     * _2 - Set 2x SIO Ultraspeed operation._ This is the normal _US
       DOUBLER ultraspeed mode_, and operates at 2x the standard SIO
       rate. This is the speed you normally see with enhanced disk
       peripherals such as the _USdoubler, Happy Enhancment_, etc.

     * _3 - Set 3x APE+ Ultraspeed. _APE+ 3X SIO operation is a feature_
       NEVER BEFORE_ available on the atari computer. It allows your
       Atari computer to commuicate with APE at 3x the normal SIO rate.
       _Thats 1.5x faster than Happy, XF551, and USDoubler drives, and 3x
       the speed of a stock 1050!_
       No special software or patch is required to use APE+ Ultraspeed.
       Spartados 3.2g will _AUTOMATICALLY_ switch to this mode at bootup
       when APE instructs it to.
       _APE+ IO pushes Spartados to its serial speed limits. _You should
       use_ FTE's Spartados 3.2g _(earlier versions may not be fast
       enough) and have KEY turned OFF. Having KEY turned on slows the
       Atari to the point it cannot keep up w/ APE+ 3X SIO.
       To get the very most from APE and 3x SIO, check out the Ape Warp+
       OS Upgrade.

   USING YOUR PC MODEM WITH APE

   Having your inexpensive PC modem do double duty on your your atari is
   now possible!

   _You may use any program that is compatible with the Atari 850
   interface. No additional software or hardware is required!_

   For this example we will use_ BOBTERM_. If you already have bobterm
   make sure you use the bare version of the program that _does NOT_ have
   an R: handler appended to it.

   Load BOBTERM using your favorite DOS. Upon loading, BOBTERM will
   'call' for the 850 interface handler. _APE will download its own
   resident handler and bobterm will finish loading._

   _Notice your APE screen now says 'Concurrent I/O running', it has been
   commanded by BOBTERM to start talking to your PC modem!_

   Make sure BOBTERM is set for 19.2k bps and then go ahead and enter
   terminal mode. You should be able to type commands to your PC modem
   just as if it was attached through an 850 interface!

   If you cant seem to talk to your PC modem go back to the configuration
   section and review the instructions for setting up your modem with
   APE. Also, make sure bobterm is set for 19.2k bps.

   _Unregistered Users Note: You also should set your terminal rate to
   19.2k bps but your actual throughput will be restricted to 2400 bps
   until you register._

      _______________________________________________________________

                       USING YOUR PC PRINTER WITH APE

      _First review the above configuration section on setting up your
      printer for use with APE._ Once set up properly all commands sent
    through the atari P: (printer) device will be intercepted by APE and
                  sent to the destination of yourc choice!

      _______________________________________________________________

                        COMMON QUESTIONS AND ANSWERS

     * Q: _How can I use ultraspeed and Ape Warp+ 3x SIO in games?_
       A: While some dos systems, such as Spartados have native support
       for speed-enhanced peripherals, no games or other software by
       default support it. To get Ape Warp+ 3x sio at ALL times, even in
       games, check out the Ape Warp+ OS InfoPage.

     * Q: _What is the difference between the APE and ProSystem Cables?_
       A: The APE Cable is designed to allow the PC to emulate Atari
       peripherals. Using it, your PC pretends to be a wide range of 100%
       SIO compliant Atari 8 Bit peripherals.
       A: The _PRO System_ cable is designed to to allow Atari
       PERIPHERALS such as the 1050 disk drive to be attached directly to
       the PC. Using a special software package I have developed, called
       the Pro System, you can use this system to create .PRO images of
       even the most complex copy protected diskettes using only a stock
       1050 disk drive. Or just ATR images at high speed if you choose.
       A: The PRO Cable does _NOT_ perform the functions of the APE
       cable. Once the .PRO images have been created, you can use your
       REGISTERED Ape software to load the images and emulate the
       peripheral behavior using the APE Cable.
       A: Remember! The .PRO cable is used ONLY to _CREATE_ disk images.

     * Q: _I can't find any documentation for the Prosystem!_
       A: For the illustrated HTML version, check here. For a plaintext
       version check PROSYS.DOC in the APE distribution.

     * Q: _Why is APE 'crippled'?_
       A: APE is provided in its current form for your evaluation. Even
       in its UNREGISTERED form, it provides unmatched power, speed and
       flexibility. You are given free of charge the ability to 'try
       before you buy' all of APE's powerful features, such as the PC
       MIRROR, Copy Protection Emulation, R: Modem emulation, 3X SIO
       operation, unmatched hruristic Ultraspeed speed switching,
       Diskcomm3 compatibility, and much more!

     * Q: _I created a .PRO image of 'Game X' using the Pro System and it
       will not run under APE._
       A: If you are a registered user, and cannot get your title to run
       under APE using all the available emulation modes, it it possible
       I can add a new emulation mode that can deal with this new scheme.
       Please send the original or 100% functional copy to me at the
       address listed in REGISTER.DOC and I will do my best to make it
       part of the next APE release.

     * Q: _When I create disk images with APE, dos shows them all as
       having 000 sectors free!_
       A: When you create a 'disk image', it is the same as a real floppy
       disk you bring home from the store. Its totally blank and needs to
       be FORMATTED with your favorite DOS before it can be used. See the
       above section on creating disk images for more assistance.

     * Q: _How can I boot my Atari if I dont have a real disk drive?_
       A: With the serial conversion device attached to the SIO port of
       your Atari computer, the atari cannot tell APE from a real Atari
       disk drive. If you mount an image in drive 1 and turn on the Atari
       it will boot from that 'disk' just as if it were a real drive.
       Ever better because APE is faster than a real disk drive.

     * Q: _Will APE overwrite or format my PC hard drive?_
       A: NO. Ape stores all its data and disk images in regular PC files
       like every other MSDOS application and will not harm, alter or
       otherwise interfere with the normal operation of your filesystem.

     * Q: _Can I use real hardware in combination with APE?_
       A: APE can cooperate fully with your existing SIO hardware such as
       disk drives, cassette drives, etc. Just make sure you dont assign
       an APE drive to the drive number of a REAL disk drive that is
       turned on. If both APE *AND* the real disk drive try to answer on
       the SIO bus at the same time it will confuse the atari and cause
       an error. Your serial conversion cable should be the last device
       on your SIO chain.
       If you are using a 1 chip cable and are having interdevice
       interference problems, consider upgrading to a 2-chip cable with a
       manual tri-state. It may help alleviate problems w/ an
       ultra-sensitive devices.

     * Q: _All my data is on floppy disks, how can I convert them to ATR
       images?_
       A: If you wish to move your data to faster more reliable ATR
       images all you need is a floppy drive capable of reading your
       disks.
          + Set up your REAL floppy disk drive as Drive 1.
          + Create a new ATR image that matches the physical size and
            density of your real disk using the 'C' function of APE.
            Mount this image in bay #2.
          + Using a SECTOR COPIER program such as MYCOPIER, DISK WIZARD
            or FASTCOPY copy the REAL diskette in drive 1 to the emulated
            diskette in drive 2. (I suggest you use MYCOPIER since it
            supports ULTRASPEED high speed I/O)
       The disk image in bay #2 is now an exact copy of the real physical
       disk in drive 1. You may use it in the same manner (except you
       cant play Frisbee with it anymore :)
       This can obviously be a time consuming process. Future updates to
       the ProSystem software will allow the Pro cable to be used to
       create .ATR images in a fraction of the time this requires, and at
       a fraction of the time required to create the complex .PRO images.

     * Q: _When I try to access drives higher than #2 I get error 160._
       A: Atari DOS 2.0 and other early dos systems were not by default
       capable of addressing disk drives higher than 2. (At $1000 each
       who had more than 2 disk drives back then anyway? :) You can
       attempt to patch your DOS.SYS file using the instructions
       available on many BBS's, or you can switch to a superior dos
       system. I suggest MYDOS because it is DOS 2 compatible.

     * Q:_ After using the '!' command to exit to DOS, I cant run APE
       again. I get an error message!_
       A: When you use the '!' command to shell out to DOS, APE does not
       actually terminate. APE places itself into the background and
       launches a new copy of your command shell. To return to APE after
       using the '!' command, type 'EXIT' then return.

     * Q: _Do I need to save my disk images before I leave APE?_
       A: No. Any time the Atari writes to a disk 'image' APE updates
       that file automatically.

     * Q: _Can I use my copy protected software on APE?_
       A: Yes! _All copy protected software can now be emulated
       successfully with APE! _Using the Pro System included and a stock
       1050 (or 100% compatible) drive, you can create .PRO images of
       even the _most complex_ diskettes.
       See 'PROTECTED DISK EMULATION' in the APE users manual for
       complete information on .PRO images.

      _______________________________________________________________

                             TECHNICAL SUPPORT

    Though technical support is not restricted to registered users, they
   will be given top priority. Please review the documentation and common
                          questions sections also.

      Internet E-mail: _classics@nacs.net_ [this is the preferred addr]
               _dh395@cleveland.freenet.edu_ [emergency backup]

                          Telephone: _216-688-0001_.
   Anytime you can catch me at home is pretty much ok. Just try and call
                              _before_ 11pm EST.

                                Snail Express
                               Steven J Tucker
                             3978 Brookside Blvd
                            Cleveland, Ohio 44111
                                    USA_

      _______________________________________________________________

                            PROGRAM DISTRIBUTION

                           _APE is user supported.

     _This means that you may copy UNREGISTERED VERSIONS freely and give
   the copies away to anyone you wish. They are in turn requested to send
               in the registration if they decide to use it.

    You can help me distribute APE to others who might find it useful by
    uploading it local BBSs and by giving copies of it to friends, user
                      groups, and business associates.

       _Thank you for supporting the Atari Peripheral Emulator and the
                             Shareware concept.

      ________________________________________________________________

                        NEW FEATURES/PROGRAM HISTORY

       _This version of APE has many new features not available in the
                  previous beta test and public releases._

   7/30/98 1.17. Added or improved since 1.16
     *         o ProSystem emulation mode added for special Mindscape games
               o Programs updated to run on fast machines (RTE 200 Bug)
               o Incorrectly formed ATR's could cause program abort.  Fixed.
               o Colors restored correctly upon program exit.

   1/30/98 1.16. Added or improved since 1.15.

     * _Summary of main program changes._
          + _APETIME.COM_ now included free with APE.
               o Included on image APE_F32G.ATR
               o Source code available.
               o Downloads the PC time to the Atari and updates the
                 Spartados clock.
               o Compatible w/ both Spartados and Spartados X.
               o Atari 800 and XL/XE compatible.
          + _REMOTE.COM_ now included free with APE.
               o Included on both APE_F32G.ATR and APE_WARP.ATR
               o Allows user to perform all APE functions from the Atari
                 keyboard.
               o Atari 800 and XL/XE compatible.
               o Compatible w/ all DOS systems.
               o See users manual for a complete description.
          + _Feature [F]ind Image_ implemented.
            Can recursively search an entire set of drives for any
            image(s)
          + Path configuration now supports 10 'spider' paths.
          + Configuration Option [_5_].
            Cables using the CTS line now supported.
          + Configuration Option [_P_].
            Registered users can now use persistent sessions.
          + Configuration Option [_Q_].
            Registered users can now bypass the startup screen
            permanently.
          + Configuration Option [_T_].
            Attempts to use Windows95 long filenames can be manually
            disabled.
          + Configuration Option [_U_].
            Force use of old smaller PC-MIRROR. (Spartados X)
          + Configuration Option [_B/F_].
            R: Atari Modem emulation can be manually disabled.
          + Configuration Option [_C/1-0_].
            Spider path settings.
          + Configuration Option [_C/D_].
            Default search drive list for find and REMOTE.COM
          + Configuration Option [_C/F_].
            Default filespec for find function.
          + Configuration Option [_C/R_].
            Persistent PC-MIRROR path switch.

     * _Summary of PC-Mirror changes._
          + Maximum file write size is now 7,864,320 bytes.
            Old limit was 93,000 bytes.
          + Maximum read size is now unlimited.
          + Configuration Setting allows switch back to old small image
            method.
          + Special SpartadosX 4.20 rom patch available on request.
          + Mirror can now be swapped like any other image, using keys
            1-8.
          + Mirror path and filespec are now separate items.

     * _Summary of APELOADER changes._
          + Now moves up a directory when _backspace_ is pressed.
          + Now executes APE macros on PC when Shift 1-0 pressed.
          + Complete loader rewrite, now totally relocatable anywhere in
            memory.

     * _Bugs Fixed in APE_
          + Screen color corruption in menu Z/C fixed.
          + DCM Decompression code fixed.
            Thanks to Ernest Schreurs (see IMAGIC.DOC).
          + Faster, more consistent, serial I/O routines written.
          + Keyboard buffer expansion code rewritten.
            Problem with an international keyboard driver.
          + Work around for faults in Microsoft's Win95 serial interrupt
            processing.
            Could cause APE to stop responding when Win95 drops an
            interrupt.

   5/13/97 1.15. Added or improved since 1.11b/1.12b
     * When a DOS shell is launched (Key _!_),
       APE will now try and swap itself out to EMS or disk.
     * Free's up about 300k of memory for shell usage.
     * New Config Opt: Default swap method.
          + EMS
          + DISK
          + NEVER
     * Various Screen Update Bugs Fixed
     * Fixed READ-ONLY File Problem w/ PC-MIRROR
     * New Printer Options
          + Print to file now supported
          + Print to any printer port supported
          + Turn off printer (allows real Atari printer to talk)
          + Print to file supports APPEND or OVERWRITE
          + (Next version will support multiple emulated printers e.g.
            P2,etc)
     * New Config Opt: Disable Happy/Syncromesh Detect
     * Patch available for Spartados X 4.20 for Ape Warp+ (request)
     * Added HARD Write protect, acts like a real drive (error returned).
     * New Config Opt: Hard/Soft Write Protect (Soft allows old method)
     * _APELOADER Software Created_
     * APELOADER Added via direct boot from PC-MIRROR drive.
     * (see Ape User's Manual for all the features!)
     * APELOADER updated to run even broken EXE files
     * APELOADER menu updated, allow base address switch from Atari
       keyboard
     * New Config Opt: Default APELOADER base address
     * Full support for .CAS digital cassette images added (key _Y_)
     * (see Ape User's Manual for all the features!)
     * New PC modem configuration interface
     * New configuration manager interface

   2/7/97 1.12. Added or improved since APE 1.10
     * APE now works 100% will all monochrome cards.
     * Lockup bug fixed.
     * Indus GT Syncromesh is now supported
     * Many internal changes
     * Crashes caused by file access violations are fixed.
     * Printer emulation reworked. APE now supports many new printer
       options.
     * PC Mirror could be crashed by unexpected file permissions, fixed.

   11/11/96 1.10. Added or improved since APE 1.09:

     * Added initial ATR-FAST code.
     * Buffers are allocated earlier in the initialization for computer
       with low memory.
     * ATR FAST system now supports multiple call methods and keystroke
       activation
     * Setting the framing threshold sometimes caused an infinite loop,
       fixed.
     * The TILDE character used in Windows95 long filenames caused
       filenames in the PC MIRROR to be garbled. Files now use the
       underscore character for long filename translation
     * While writes to the PC mirror under spartados are not supported,
       trying to do it caused a crash instead of a warning. Fixed.
     * SpartaDOS X cartridge support for floppy formatting added
     * SpartaDOS X cartridge support for PC Mirror added
     * SpartaDOS X cartridge now sees the PC mirror and can read it.
     * SDX COPY command now compatible with PC Mirror.
     * Problem with last path used in ATR file selection fixed
     * Ultraspeed and Ape Warp+ 3x SIO now compatible with more software,
       Top Mag, Superdos, etc
     * ATR FAST now displays ATASCII comments properly
     * ATR FAST system now responds to shift driven option
     * Extra SIO commands added for more support of the 1050 Speedy
       upgrade. Bibocopy 1.5 now works at 56k
     * Some functions optimized to allow faster performance with the APE
       Warp+ OS
     * Configuration menu totally revamped
     * New configuration options: Safety Margin, Sio Control Method, file
       selector choice.
     * Cursor was sometimes left visible after a pick box was displayed.
       Fixed.
     * More robust configuration file checking installed
     * Many new features added to the Win95 file selector
     * APE sometimes left stray characters at the right margin. Fixed.
     * Write protect no longer clobbers byte 15 of ATR header
     * APE fully supports CRC32 ATR Authentication. ATR Authentication
       standard and documentation available at the APE Home Page.
     * Warp_453 from 1.09 now obsolete due to new driver in APE_WARP.ATR.
       3x SIO patch for MyDOS/Atari DOS now much more reliable.
     * New versions of MyCopier included on the APE_WARP.ATR. Old version
       was also corrupted.

   5/22/96 1.09. Added or improved since APE 1.07:

     * Distribution Change: FTED32F.ATR contains the Shareware version of
       Spartados 3.2f. Spartados is an advanced _high speed_ DOS system
       from Fine Tooned Engineering.
     * Distribution Change: 453_WARP.ATR contains MyDos 4.53, as well as
       2x Happy High Speed I/O Patch, 3x APE+ Warp Speed Patch (modified
       Happy patch), and MyCopier ultra high speed sector copier that is
       compatible with APE+ 3x SIO.
     * Ape 1.09 and ProSystem 1.50 now support images of enhanced density
       and a extension of the .PRO format was changed to help this along.


       You _must_ convert your old v2 .PRO images to v3 .PRO images or
       they cannot be used with Ape 1.09. A fast and automated program,
       PRO2TO3.EXE is included to convert all your old images. You can
       give it a wildcard filespec so you should be able to convert all
       your .PRO images in one pass :)
     * Executable file now smaller because of internal changes in
       allocation of dynamic memory vs. the old static method.
     * Executable now uses overlays for routines that are not time
       critical, freeing page space for more features in the main
       program.
     * 850 Emulation Fixed - A problem in 1.07 caused a 6502 vector in
       the stage 3 handler to point to a BRK instruction (OOPS!).
     * 850 Emulation Fixed - Problem with concurrent I/O dropping out the
       instant it starts cured.
     * Fixed DCM code to allow decompression of double density images,
       bug has been in the DCM code since its was written.
     * PC Mirror: Files written to the PC mirror would fail with a DISK
       FULL message after about 400 sectors, fixed. Mirror now supports
       capture of files up to 8 Megs.
     * PC Mirror: Writing to a file that already existed in the PC Mirror
       drive would cause the program to fail with a device timeout.
       Mirror now supports writes to any file, even if it exists.
     * PC Mirror: Files written to the PC Mirror would on rare occasions
       be truncated to 125 byte intervals, or have an extra 125 bytes
       appended. Fixed.
     * Pc Mirror: Files written to the PC Mirror would appear in the
       default DOS path instead of the current PC Mirror path. Fixed.
     * Ape and ProSystem now be more monochrome friendly. If MDA adapters
       are detected all screens are displayed in white on black _only_.
     * Ape 1.07 could be crashed about 10 ways with runtime error 203.
       This sloppy memory problem has been fixed and wont happen anymore.
     * Spartados 3.2x (XF551 version) is now fully supported. Thanks to
       the user who sent 3.2x for testing. Problems included failure to
       format any disk floppy or HD). Unknown if this will effect the X
       cart situation.
     * When ATR images were created, they could then be mounted on the
       same drive as the PC Mirror, caused some interesting effects but
       is fixed.
     * When creating ATR images they would appear in the default DOS path
       if no path was specified, they now appear in the default ATR/PRO
       path.
     * APE ProSystem emulation code rewritten and streamlined, added 5
       extra emulation modes (more coming). ProSystem now _requires_
       version 3 format images. See the above instructions for converting
       your existing .PRO images.
     * Many improvements to file selector including better path handling,
       type highlighting, drive change entries, visible marker (mono
       friendly) and internal changes.
     * Ape now includes an XFD conversion utility in addition to an
       improved and hopefully now complete DCM conversion utility. Image
       conversion is available to all users and is invoked with the 'A'
       keystroke.
     * Many users asked for APE to handle commands sent by Nick Kennedy's
       program REMOTE.OBJ. Ape now handles these requests, but obviously
       you must use APE keystrokes. Keystrokes accepted for registered
       users only.
     * REMOTE.OBJ was created by and is the property of another software
       author and is therefore not included in this software package. I'm
       not aware of any restrictions on its use, but if it requires some
       type of payment for use of course please register it.
     * You can now select a new ProSystem emulation mode for any image
       directly from within APE as of 1.09. This _greatly_ speeds up the
       PRO image testing process. Registered users only.
     * Sometimes the screen was left 'dirty' from previous menus, little
       dots at the right edge, etc. Fixed.
     * The shareware version of APE could crash in the Atascii/Ascii
       viewer. Fixed.
     * The file selector has again changed and you should note a
       significant change to the usage of the 'Additional Extension'
       option of configuration menu 3. This option used to specify the
       extension of the files to be displayed in the file browser.

       This setting _no longer_ performs this function. It now specified
       an _extra_ extension to be displayed in the file browser. ATR and
       PRO extensions are now automatically displayed at the proper
       times. If you have this option set to '*' I suggest you clear it
       so you do not have to wade through tons of useless files to get to
       your disk images.

   11/20/95 1.07. Added or improved since APE 1.06:

     * Most of the changes I had noted were lost when I had a file
       corruption problem. So anything new thats not listed here... :)
     * Screen blanker was causing many systems to crash after loading
       APE. It has been removed. Other more stable freeware screen
       blankers are available anyway.
     * Old .PRO format totally scrapped. Old .PRO riders are no longer
       compatible with APE and will not be supported in the future.
     * New .PRO v2 image format created.
     * Coded or re-coded about 1000 lines of code to install full dual
       ATR/PRO compatibility. First public release in 1.07.
     * Bug causing ignored writes to disk images for many users has
       hopefully been eliminated.
     * Beta .PRO image creator coded and made available to registered
       users.
     * APE now 100% functional in dual ATR/PRO mode.
     * Added multiple compatibility modes for PRO images, now allows all
       my copy protected software to run!!! :)
     * Added compatibility timing to PRO v2 format. Disks which require
       reads at normal 1050 speed (300 rpm) can now be emulated.
     * Added sector overrides for all .PRO functions. Each sector can now
       be modified individually (if desired) to bypass any of the global
       .PRO settings.
     * Minor improvments/bugfixes for the file selector
     * Minor improvments/bugfixes for the text browser
     * Misc improvements to the core routines
     * Pro System 1.02b now available to the public.
     * Plans for the PRO CABLE added to APE.DOC

   9/2/95 Added or improved since APE 1.04:

     * Titles added to file selector
     * TAB can now be used to edit file selector path/filespec
     * Misc HELP screen fixes
     * Found memory leak in load disk image routine, fixed.
     * Added first Diskcomm3 -> ATR conversion code
     * DCM -> ATR converter now part of APE program, option [A]
     * DCM -> ATR converter can now handle batch processing using
       wildcards
     * DCM -> ATR converter now asks if you want to mount the image you
       just converted (if you convert only 1 image).
     * Integrated new COMM routines, speed and reliability improved
     * Verified HAPPY HS I/O w/ Diskcomm3, ok.
     * Verified Ultraspeed I/O w/ Bitter Reality Demo, ok.
     * APE now rejects corrupt/invalid ATR files
     * HAPPY SECTOR COPY from the Happy System Disk verified to work ok.
     * Bug in Happy write routine found and fixed.
     * Bug in computation of high sector numbers found and squashed.
       Nobody complained about this, anyone out there? :)
     * Added UART/COMM configuration screen and code, now available in
       [Z] Configuration, [4] Option 4.
     * UART/COM settings now saved in APE.CFG
     * Eliminated '.' from file selector, useless entry and its now
       easier to navigate using the browser.
     * Added '>' and ' PC Mirror updated to work a 2x speed w/ Happy HS
       I/O
     * * PC Mirror now compatible with Spartados. Can now copy files of
       any size from the PC mirror into spartados using COPY, XCOPY, etc.
       Spartados still has a bug in its i/o routine but i found a way
       around it.
     * Happy HS I/O writes were still causing jumps to ultraspeed on
       occasion. Found a problem in the timing code and its now a very
       solid routine.
     * XF551 high speed I/O didn't work most of the time, again nobody
       reported this monster bug. Fixed and verified with XFTOOLS.ZIP.
     * Much of APE recoded and optimized. Many sections were in the
       original beta 'just make it work' form and were real electronic
       elephants. A few sections of non time-critical repetitive code
       centralized. Code and data segment sizes reduced significantly and
       program speed increased.
     * Started recoding I/O routines for 3x SIO.
     * Recoding of 3x SIO routines finished.
     * Patched WARP.COM to allow 3x SIO speed, now renamed to
       APE_WARP.COM to avoid confusion. Verified reads and writes with
       MyDOS 4.53.
     * * Added support for 3x SIO speed using Spartados 3.2g with NO
       DRIVER REQUIRED. Spartados now boots in APE+ (3x SIO) mode
       automatically.
     * 'Force' in the help screed was spelled 'Forse', duh.
     * Added Spartados Configuration Menu (Cfg [Z] Option [5]) to allow
       selection of default Spartados speed for very slow PC machines
       that cannot handle 3x SIO.
     * 3x SIO verified NOT to work with Spartados versions 3.2d and
       earlier. Spartados SIO routines in these versions cannot keep up
       with APE+ SIO and get choppy.
     * Cursor turned off, guess it annoyed some folks just sitting there
       and blinking.
     * Added 'APE+' display to indicate 3x sio running.
     * APE+ SIO (3x) verified to work w/ 3.2g in single and double
       density.
     * APE+ SIO (3x) verified to work at 3x speed w/ bitter reality demo.
       Any program that follows the Spartados model should work w/ APE+
       IO.
     * APE+ SIO (3x) verified to work with MyCOPIER at 3x SIO speed.
     * APE+ SIO (3x) verified to work w/ Diskcomm3
     * * Added support for 'simple' PROTECTED DISK images. Protection
       information is stored in a 1k file of the same name with the
       extension '.PRO'.
       Sample Images
       APPLE.ATR/PRO - Apple Bandits protected version SPY.ATR/PRO - Spy
       vs Spy protected version
     * Fixed a bug in the DCM->ATR conversion code, leftover junk from
       the standalone version eliminated.
     * Unregistered users restricted to only 2 command line switches.
     * Fixed PC MIRROR to allow APE+ (3x) sio access.
     * [The following code is complete, but is not included in APE 1.06
       because without the ability to use the READ/WRITE TRACK commands
       properly, they are not really useful except for show. When I get a
       Happy/Archiver drive to test with, these may be included]
     * Happy Controller Ram emulated.
     * HAPPY System Disk now recognizes APE as HAPPY w/ Controller Option
       installed.
     * Happy Tracer Buffer emulated. HAPPY system disk now recognizes its
       presence and displays it contents.
     * Happy code buffer emulated and high speed transfers working. Able
       to completely load 'BACKUP ANY DISK' and accept drive programming.
     * Happy move head command recognized
     * Archiver READ TRACK command recognized, only response figured out
       so far indicates a totally empty track.
     * Archiver FORMAT TRACK command accepted.
     * Screen blanker added, now blanks screen after 2 minutes of
       keyboard and SIO inactivity.
     * Ultraspeed timing tightened, better performance.

   Added or improved since public beta 8:

     * Bugfix for 1050 formatting and status routines
     * Happy high speed reads now supported
     * New syncro code added, great improvement!
     * Better swapping method, you no longer have to press the existing
       image first, either is fine.
     * Happy high speed write support added
     * Some extended Happy commands now supported
     * Write protection of images now effective
     * Command line options added
     * User now asked to mount image after creation
     * 850 Interface serial emulation now working at 9600 baud
     * Scrapped 850 interface code and starting rewriting some public
       domain R: code.
     * Automatic switching between command and concurrent i/o mode now
       working
     * PC MIRROR directories are now built on the fly
     * Support for 43/50 line screens installed
     * 850 Interface R: emulation now working at 19.2k bps
     * Added General/Serial configuration screen
     * Added command filters
     * Added slow machine display options
     * Added user definable framing value
     * New streamlined core serial i/o routines. Much faster now.
     * Now recognizes many more extended happy commands
     * Added hardware flow control for PC modem, now works automatically.
     * Added user definable flow control threshold
     * Added the ability to load and save block configurations
     * Added enhanced command line help and registered CL features
     * Added Path/Macro configuration screen
     * Added support for default paths and file extensions
     * Added support for quick macros, and editing code
     * New consolidated configuration menu, 'I' function for printer
       configuration now in this menu.
     * Improved and incorporated my multi-type text browser into APE. Can
       also be called from the command line. (reg)
     * Improved file selector, now has title and user can enter own
       path/filespec using the TAB key.


----------------------------------------------------------------------------



 REGISTRATION AND ORDER FORM

  Send orders to:       Steven Tucker
                        3978 Brookside Blvd
                        Cleveland, Ohio  44111 USA

  Program information:  Telephone:      216-688-0001

                        E-Mail:         classics@nacs.net (primary address)
                                        ai123@freenet.carleton.ca



  -----------------   Single Computer Licenses Includes   ----------------

    1. Enhanced & Registered versions!
    2. Priority Tech Support (E-Mail, Phone, Mail)
    3. Notice of Major Upgrades

  ------------------------------------------------------------------------

    Item Description                                  Price     Quantity

    _Atari Peripheral Emulator_

    Registered & Enhanced Version of APE              $39.99      [  ]

    _Ape WARP+ OS Upgrade Option for XL/XE Computers

    APE Warp+ XL/XE OS_ w/ Installation Kit           $49.99      [  ]
    APE Warp+ XL/XE OS_ Installed (see shipping note) $79.99      [  ]

    _Preassembled Interface Cables_

    APE 1489 Serial Interface Cable                   $59.99      [  ]
    ProSystem .PRO Imaging Cable                      $59.99      [  ]

    _Imagic_

    Imagic-95 Registered and Enhanced                 $10.00      [  ]
    Imagic-DOS Registered and Enhanced                $10.00      [  ]
    (GET BOTH IMAGIC-DOS and IMAGIC-95 for only $15)              [  ]

    _Shipping_

    Shipping ($5 USA, $6 Canada, $9 Abroad)           [    ]

    Subtract Discount                                 [    ]
    ($5 discount _per interface cable_ purchased)

    _Total + Shipping (less any discount)_            [              ]

   -----------------------------------------------------------------------

     _Shipping_: flat-rate, regardless of the size of your order. If you
      choose to get the APE Warp+ OS upgrade with installation, return
    shipping of your computer is FREE within the contential USA. Please
       contact me for return shipping rates outside the USA. For more
              shipping details see the Ape WARP+ OS Info Page.

     Note on payment: Canadian and overseas users must pay by check or
     money order _PAID IN US DOLLARS AND DRAWN DIRECTLY ON A US BANK._ In
         Canada, a postal money order in US DOLLARS is acceptable.

     Contact: ________________________________________________________

      Company ________________________________________________________

      Address ________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

       Phone _________________________ FAX _________________________

                  How did you get your copy of APE/IMAGIC?

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

                          Suggestions or Comments:

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________

     _________________________________________________________________


       _______________________________________________________________

                  The APE 1489 Serial Conversion Interface

                      Click Image for large schematic

           _How to construct the 1489 version of the APE interface_

   Sio Orange (Sio Pin 3) -> Diode Clear End & Diode Band End -> 1489 Pin
                                     #8
                  Sio Lt Blue (Sio Pin 10) -> 1489 Pin #14
                    Sio Black (Sio Pin 4) -> 1489 Pin #7
                   Sio Purple (Sio Pin 7) -> 1489 Pin #4
                    Sio Green (Sio Pin 5) -> 1489 Pin #1

              PC Signal Ground (9p #5) (25p #7) -> 1489 Pin #7
             PC Ring Indicator (9p #9) (25p #22) -> 1489 Pin #6
                   PC RXD (9p #2) (25p #3) -> 1489 Pin #3
                  PC TXD (9p #3) (25p #2) -> 1489 Pin #10

      _______________________________________________________________