WriteAtr V0.92 (c) 2002 by HiassofT

This program allows you to transfer double density (256 bytes per
sector) ATR-images directly from/to Atari-8bit floppy disks with your PC!
All you need is a PC running MSDOS and a 5.25" or 3.5" floppy
disk drive in your PC!

You are allowed to use, copy, and distribute this program for free.

If you like this program, or if you have suggestions for new features,
feel free to contact me:

   HiassofT
   Matthias Reichl
   Wolfgangerstr. 26
   A-4820 Bad Ischl
   Austria

   e-mail: hias@horus.com
   WWW: http://www.horus.com/~hias/atari/

1. Installation:
   There should be 3 files in the zip-file:
   writeatr.exe - the executable
   writeatr.doc - this file
   change.log   - ChangeLog of WriteAtr

   To install the program, simply copy the file writeatr.exe
   into any directory (eg c:\tools).


2. Using the program:

   WriteAtr does not have a graphical user interface. Instead of that,
   you have to pass commandline options to WriteAtr to tell it what
   it should do. Don't be afraid - there are only very few options
   and you will know them all in 2 minutes.

   If you start WriteAtr without any options, it will print out an
   overview of the available options. It should look like this:

   Usage: writeatr [-b] [-d] [-fX] [-l] [-n] [-r] filename.atr

   options:
       -b : use drive B
       -fX : set atari floppy drive type (X=0..8)
             0=180k/5.25" (this is the default)
             1=360k/5.25"        2=720k/3.5"        3=1.44M/3.5"
             4=360k/5.25"/head   5=720k/3.5"/head   6=1.44M/3.5"/head
             7=360k/5.25"/XF551  8=720k/3.5"/XF551
       -r : read disk (create ATR-image of disk)
       -l : create long ATR-image (extra 384 zero-bytes at the end)
       -d : increase debug level by 1
       -n : no verify when writing (DANGEROUS!)

   The only mandatory item in the commandline is the filename of the
   ATR file. You can combine several options, although some combinations
   will have no effect (eg: "no verify writes" makes no sense when reading
   a disk).

   By default, WriteAtr will assume your drive is a 5.25" disk drive
   and the floppy disk should be formatted in the standard 180k
   double density format (720 sectors of 256 bytes each).
   If you want to use higher capacity formats (up to 1.44MB) please
   have a look into section 6.


3. Writing ATR-images to floppy disk:

   By default, if you don't specify any other options, WriteAtr
   will read the given ATR-File and write it to the disk in
   your first floppy drive (drive A). The disk does not need to be
   formatted, it will be formatted on the fly.

   For example:
   writeatr d:\hias\xl\dos\mydos.atr

   If you want to use drive "B", you have to add the option "-b".

   For example:
   writeatr -b d:\hias\xl\source\disk42.atr

   By default WriteAtr verifies the sectors after writing. Of course
   this takes a little time, but you can be sure that everything got
   written correctly.

   If you like doing risky things and want to save a little bit
   time, you might consider disabling the write-verify by using
   the "-n" option. I don't recommend this, so do it at your
   own risk!

   For example:
   writeatr -b -n d:\hias\xl\games\coolgame.atr


4. Creating an ATR-image from a floppy disk:

   Creating an image is as easy as writing images: Simply use the
   option "-r". WriteAtr will then read the floppy disk and store
   an ATR-image in the given file. NOTE: If the file already
   exists, it will be overwritten!

   For example:
   writeatr -r pics.atr
   or:
   writeatr -b -r basic.atr

   If you use the option "-l" when creating an ATR-image, WriteAtr
   will create a (NumberOfSectors*256+16) bytes long ATR-file. By
   default, WriteAtr creates a 384 bytes smaller ATR-files. The only
   difference between these two types of images is that the larger
   image is padded with 384 zero-bytes at the end of the file.

   The main purpose of this option was for debugging. If you dump
   an ATR-image to disk, and then read it back, it should (of course)
   be exactly the same as the original image (except maybe some bits
   in the header). With the "-l" option you can create an image that
   has the same size as the original image, so that a file-compare
   (eg.: "fc /b orig.atr new.atr") will work. Such (longer) images
   are created by SIO2PC (at least in the versions I used), but in
   99 percent of the cases you won't need this option at all.

   For example:
   writeatr -b -l -r new.atr
   will create a long ATR-image from drive B.


5. Error handling

   Whenever an operation (formatting a track, reading/writing/verifying
   a sector) fails, the exact position and the exact BIOS error code
   are reported and you have the possibility to abort, retry, or ignore
   the failed operation. Whenever a sector-IO operation fails, WriteAtr
   reports both the (PC-style) sector/track/head position, and the
   position translated into an (Atari-style) sector number.

   If you choose "abort" the program will stop immediately,
   "retry" will try the same operation again, and "ignore" will
   skip the current operation and proceed to the next.

   Please note: Ignoring errors is generally a very bad idea!
   In most cases errors are caused by bad floppy disks. So if you
   experience an error while writing an image to a disk, please try
   using another disk.

   On the other hand, if you are getting read errors while creating
   an image from a disk, there is a high possibility that your floppy
   disk is starting to "fade away". In this case, you should retry the
   failed operation until it succeeds. If you just ignore the error,
   you will be creating a broken image! So use this at your own risk!


6. Higher capacity formats

   You can select the type of your Atari floppy drive by using the
   "-fX" command line option. Substitute 'X' with a value from
   0 to 8. The different values have the following meaning:

   -f0 : single sided, double density, 5.25", 180k drive (eg a 1050).
         256 bytes per sector, 18 sectors per track, 40 tracks per side.
         This is also the default that is used if you don't specify
         the "-fX" option (so this option is pretty useless :-)

   -f1 : double sided, double density, 5.25", 360k drive (default mapping)
         256 bytes per sector, 18 sectors per track, 40 tracks per side.

   -f2 : double sided, double density, 3.5", 720k drive (default mapping)
         256 bytes per sector, 18 sectors per track, 80 tracks per side.

   -f3 : double sided, high density, 3.5", 1.44M drive (default mapping)
         256 bytes per sector, 36 sectors per track, 80 tracks per side.

   -f4 : double sided, double density, 5.25", 360k drive, head first
         256 bytes per sector, 18 sectors per track, 40 tracks per side.

   -f5 : double sided, double density, 3.5", 720k drive, head first
         256 bytes per sector, 18 sectors per track, 80 tracks per side.

   -f6 : double sided, high density, 3.5", 1.44M drive, head first
         256 bytes per sector, 36 sectors per track, 80 tracks per side.

   -f7 : double sided, double density, 5.25", 360k Atari XF551 drive
         256 bytes per sector, 18 sectors per track, 40 tracks per side.

   -f8 : double sided, double density, 3.5", 720k drive built into XF551
         256 bytes per sector, 18 sectors per track, 80 tracks per side.


   Short Explanation of the various mapping-types:

   * Most double sided Atari disk drives (like the HDI or the ATR8000)
     first fill tracks 0-39 (or 0-79) on the first side, then switch
     over to side 2 and again fill tracks 0-39 (0-79 for 3.5" disks).
     If you have got such a drive, use one of the options
     "-f1", "-f2", or "-f3".

   * If -f1/-f2/-f3 didn't work for you, please try one of the
     options "-f4", "-f5", or "-f6". This mapping is not too common
     for Atari disk drives, the only drive I know of that uses this
     mapping is the "Karin Maxi".
     If your Atari disk drive uses this mapping, it first fills
     track 0 on side 1, then track 0 on side 2, then seeks to track 1,
     again first fills track 1 / side 1, then track 1 / side 2,
     and so on, until it finishes with track 39 (79) / side 2.
     I called this mapping 'head first' (or short: head), because
     the drives switches the heads (sides) first before switching
     the track.

   * If you have got a XF551, use options "-f7" or "-f8".
     The XF551 first fills track 0 on the first side. Then it
     fills track 1, then track 2, ... up to track 39 (on a 5.25" disk)
     or 79 (on a 3.5" disk). Then it switches to side 2 and fills
     the disk in reverse order (starting at track 39/79, then 38/78,
     ... til it has reached the end of the disk at track 0).

   If you've got a drive other than the Atari XF551, please tell me
   which mapping (default or "head first") worked for you. Email me the
   manufacturer and the name of your drive, so I can build a list of
   the known drives and mappings and include it in future versions
   of WriteAtr.
   Thanks!

   Long explanation of the different mapping types:
   (you may skip it if you are already familiar with the concept
   of SIO and disk drives).

   The OS of the Atari accesses the sectors of a disk in a linear,
   block oriented, way. It does not care if you've got a single
   or double sided floppy drive, if it's a 3.5" or a 5.25" drive
   or if you connected your Atari to something that's only pretending
   to be a floppy drive (eg your PC running SIO2PC or APE).

   In other words: if the Atari wants to write to a disk it simply
   tells the drive "hey, drive, here's some data. please be so
   kind and write it to sector 528". When, later, the Atari tells
   the drive to read back sector 528, the drive should return the
   same data that the Atari sent to the drive when writing
   (otherwise we have kind of serious troubles :-)

   On the other hand, the drive has of course to know much more
   about the floppy disk that it's going to access. Usually a
   floppy disk is accessed by specifying the HEAD (eg: a double sided
   floppy disk drive has two heads, head "0" acessing the first side,
   and head "1" accessing the second side), the TRACK (usually disks
   have 40 or 80 tracks), and the SECTOR-number within this track,
   on the specified side (head).

   And that's the point where the troubles begin.

   It's the job of the disk drive to translate each sector-number
   (as received from the Atari) into a unique sector/track/head-triple.

   Let's start with the simplest case - a single sided/double density 1050:
   A 1050 can store 720 sectors of 256 bytes each on a disk. Actually,
   such a disk consists of 40 tracks of 18 sectors:

   Sectors 1-18 are stored in sectors 1-18 of track 0.
   Sectors 19-36 are stored in sectors 1-18 of track 1.
   ...
   Sectors 703-720 are stored in sectors 1-18 of track 39.

   Simple, wasn't it?

   Now let's move to the complicated part - double sided disks.

   I would like to show you the difference between the various
   mappings on a simple example: a double sided, double density,
   360k 5.25" disk, formatted with 40 tracks of 18 sectors each.
   This means we have a total of 1440 sectors of 256 bytes.

   * The default mapping:

     This mapping stores the first 720 sectors on the first side in
     tracks 0-39, like the 1050 or the XF551.
     When finished with the first side, the drive switches to the second
     side and starts again at sector 1 of track 0. This means:

     Sector 721 is stored in sector 1 of track 0 on side 1.
     Sector 722 is stored in sector 2 of track 0 on side 1.
     ...
     Sector 738 is stored in sector 18 of track 0 on side 1.
     Sector 739 is stored in sector 1 of track 1 on side 1.
     ...
     Sector 1440 is stored in sector 18 of track 39 on side 1.

   * The head-first mapping:

     This mapping is identically to the way the PC stores data on
     a floppy disk. First the drive fills track 0 on side 0. Then
     it switches to side 1 and fills track 0. When it's finished
     with that, it seeks forward to track 1. There it again first
     fills the track on side 0, then on side 1.

     Sector 1 is stored in sector 1 of track 0 on side 0.
     Sector 2 is stored in sector 2 of track 0 on side 0.
     ...
     Sector 18 is stored in sector 18 of track 0 on side 0.
     Sector 19 is stored in sector 1 of track 0 on side 1.
     ...
     Sector 36 is stored in sector 18 of track 0 on side 1.
     ....
     Sector 1405 is stored in sector 1 of track 39 on side 0.
     ...
     Sector 1422 is stored in sector 18 of track 39 on side 0.
     Sector 1423 is stored in sector 1 of track 39 on side 1.
     ...
     Sector 1440 is stored in sector 18 of track 39 on side 1.

   * The XF551 mapping:

     This mapping is really strange :-)
     I just can't imagine that someone thought this was a good idea.
     And even more unrealistic than that, someone actually used it
     in a floppy disk drive - the XF551.

     Older (single sided) drives, like the 1050, should be able to access
     at least the first half of the disk. Therefore sectors 1-720 are
     stored on the first side, in the same way as the 1050 would do it:

     Sectors 1-18 in sectors 1-18 of track 0 on side 0.
     ...
     Sectors 703-720 in sectors 1-18 of track 39 on side 0.

     When finished with the first side, the XF551 switches over to side 2.
     But it does not start again at track 0, no, it starts at the last
     track. And that's not enough, even the sector numbers within each
     track are reversed! This means:

     Sector 721 is stored in sector 18 of track 39 on side 1.
     Sector 722 is stored in sector 17 of track 39 on side 1.
     ...
     Sector 738 is stored in sector 1 of track 39 on side 1.
     Sector 739 is stored in sector 18 of track 38 on side 1.
     ...
     Sector 1439 is stored in sector 2 of track 0 on side 1.
     Sector 1440 is stored in sector 1 of track 0 on side 1.


7. Debugging:

   If you include the option "-d", WriteAtr will print out some
   debug info when reading/writing images.

   If you specify the option "-d" twice (eg: "writeatr -d -d test.atr")
   you will get even more debugging info.

   If you have problems using WriteAtr, please use this option and
   email the output of WriteAtr to me. Since the output will usually
   be quite long, use output redirection to save the output into a file.
   For example:
   writeatr -d -d test.atr > debug.log

   Here are some hints how you can test if WriteAtr works.

   * Format a disk on your Atari using MyDOS and copy some large
     files onto the disk, so that at least more than half of the
     sectors of the disk are used.

     Then read this disk with WriteAtr on your PC and either
       - use SIO2PC with the ATR-image or
       - load the ATR-image into an emulator
     and check if you can access all of the files.

     If you chose the wrong mapping, or if there's a bug in WriteAtr
     MyDos will give you an error message concerning incorrect sector
     chaining. If none of the mappings offered by WriteAtr work for
     you, please contact me by email and, if possible, send me the
     ATR-image and some information about the disk drive connected
     to your Atari.

   * If you've got some known good ATR-images (eg. images that work
     with SIO2PC or an emulator), try to write them to an Atari
     floppy using WriteAtr and then try reading them with your
     Atari disk drive.


8. Features / known bugs:

   WriteAtr only supports double density (256 bytes per sector)
   ATR-images. This limitation is caused by the floppy disk controller
   used in most PCs: the controller simply cannot cope with 128
   bytes-per-sector formats.

   If the size of the ATR-file does not match the size of the
   selected disk type, WriteAtr will issue a warning but still do
   what you told it to do. It is therefore possible to write
   the first part of a larger ATR-file to a smaller disk, or
   to write a smaller ATR-file to a larger disk. In the second
   case, WriteAtr will fill the remaining sectors with zero bytes.

   WriteAtr only works in plain MSDOS, because it needs direct access
   to the PC-hardware. Using WriteAtr inside a Windows-DOS-box
   might work (I had success using it in a Win95 and WinME DOS-box,
   and also got several emails from people who had success), but
   I can't guarantee that it will work on all PCs.

   It is not possible to use this program without a harddisk, because
   it has to reprogram the disk controller to read Atari disks and
   the controller is no longer able to read PC-disks (at the end
   of the program the controller is reset so that you can read PC-
   disks again).

   It is not possible to access side 2 of Atari-disks by flipping them,
   because all PC disk drives use the index-hole on the disk
   (eg the 1050 doesn't). The only way would be to cut a second index-hole
   in your disk (a similar problem exists with the XF551-drive
   because this drive also uses the index-hole).

   If the specified disk format does not match the floppy disk inserted
   into your PC disk drive (eg. if you insert a 3.5" 1.44M HD disk and
   tell WriteAtr it is a 3.5" 720k DD disk) the floppy controller may
   get confused, and further operations (even with the right format
   specification) might fail. If this happens to you, simply take the
   disk out of the drive and insert it again.
   I'm not sure what's actually going wrong, but re-inserting the disk
   always helped for me...


9. Credits

   I would like to thank a lot of people who helped me develop WriteAtr
   (by providing me important information, helped me testing, etc.).

   Many, many thanks go to (in no particular order):

   Lee Barnes
   Erhard Puetz
   Marco Antonio Checa Funcke
   Mr.Bacardi
   Ron Fucci
   Larry White
   HatMouse
   Piotr Fusik

   If I forgot _you_ and you should be on this list, just send me an email!

   Thank you!