››››                                   APACVIEW ›                                  Version 2.4›                   Copyright (c)November 1992 by Jeff Potter›     ›          "The Graphics Interchange Format (c) is the Copyright property of›          CompuServe Incorporated. GIF(sm) is a Service Mark property of›          CompuServe Incorporated."›          ›          ›     INTRODUCTION›     ›     This is APACVIEW, the advanced graphics decoder/viewer for the Atari›     8-bit computer.  With this program you can view Graphics Interchange›     Format (GIF) files in monochrome (black and white), in 256 color APAC›     mode, or you can create color separation files for viewing GIF files›     in spectacular 4096-color Colorview mode (viewable only with the›     separate COLRVIEW program).›     ›     ›     SYSTEM REQUIREMENTS›     ›     This program will execute on all Atari 8-bit computers with at least›     48K of RAM and one or more disk drives.  A joystick is optional.›     ›     ›     QUICK-START PROCEDURE›     ›     Load APACVIEW.OBJ from DOS with no cartridges installed.  The file›     RGBTABL8.OBJ should be on the default disk (normally D1:) when you›     load APACVIEW.  Adjust the hue and brightness of your monitor for a›     pure, bright yellow.  Press L to load a GIF file.  Enter the filename,›     (device name of D: is assumed if not entered), including›     subdirectories, if used (32 character limit on total filename length).›     The header from the file will be loaded, and the resolution and number›     of colors will be displayed.  APACVIEW will automatically select width›     and height dividers based on the header information.  Press return›     when prompted, and the conversion process will start.  The screen will›     normally clear to a default color, then gradually fill up.  A›     monochrome image will be displayed until the last line (of the GIF›     file) has been interpreted.  The full color rendition will then "pop"›     on.  Press START to return to the menu screen (picture will not be›     erased).›     ›     ›     FEATURES›     ›     The following menu items are available:›     ›        [A] LOAD .APC›            Loads an APAC mode file, such as one created with the S option›            below.  Also loads caption.›            ›››››››››››                                                  APACVIEW V2.4 Docs page 2››››        [B] TOGGLE BLANKING›            This allows you to load files up to 30% faster by turning ANTIC›            off during the decoding process.  The border of the menu screen›            will change to gray to indicate this option is active.  Press B›            again to disable.›            ›        [D] VIEW DIRECTORY›            You will be prompted for the search specification.  Enter disk›            number (if desired), and subdirectories, or simply *.* to›            search the default disk.›            ›        [I] LOAD .ILC›            Loads an interlaced APAC file.  See below about how to create›            such a file.›            ›        [L] LOAD GIF›            Load a new GIF file, as explained above.  Usually this resets›            the settings of width, height, and bias.›            ›        [M] SELECT MODE›            This allows you to select between APAC or several other modes›            of monochrome viewing/saving.  When "GR.9" is selected (and the›            screen color changes to gray), the program will load files in›            graphics 9 with 16 colors.  Resolution will be 80H x 192V. ›            Note that the "true" gray scale value is calculated by›            interpreting all three color components.  When "GR.11" is›            selected (and the screen color changes to turquoise), the›            program can decode a GIF file into its color components,›            without respect to the intensity of the pixels.  This is›            necessary to create interlaced APAC and Pryzm mode files.  When›            one of "Red9", "Green9", "Blue9", "Red15", "Green15", or›            "Blue15" is selected, the program loads files in graphics 9 or›            15, and only interprets the appropriate color selected.  These›            modes are specifically for creating files viewable with the›            COLRVIEW program.  Note that the image will appear in shades of›            gray, and not the color selected.›            ›        [P] LOAD .PZM›            Loads Pryzm files.  These can be created with Darryl Yong's›            Pryzm artist program, or see below about how to create these›            from GIF files.›            ›        [S] SAVE CURRENT PICTURE›            This option allows you to save the current picture file as a›            .APC file (viewable with APACSHOW.OBJ).  You will be prompted›            for the filename (default D:).  You will also be prompted for a›            38-letter caption which will be saved in the file.  I suggest›            you enter this centered at the bottom of the screen.  Avoid›            typing off the right hand side, or the use of the vertical›            arrow keys, as your caption may be lost.  Press return to save›            the caption and your picture file.  Note:  if you are saving a›            monochrome picture, you cannot enter a caption.  The file will›            be the standard 62-sector .GR9 format which you can load and››››››››››                                                  APACVIEW V2.4 Docs page 3››››            view with other graphics 9 loaders or slide shows.  APACVIEW›            checks the filename you have entered, and if it already exists,›            asks you to confirm that you want to overwrite it or append to›            it.  Answer by pressing "O" or "A".›            ›        [V] VIEW CURRENT PICTURE›            This pops you back to the APAC mode screen.›            ›        [Z] EXIT TO DOS›            This allows you to return to DOS, assuming it is on the default›            disk drive.  You will be prompted to confirm this before it›            exits.›            ›        [!] UNJAM XF551›            This sends the correct control codes to restore an Atari XF551›            disk drive to DSDD operation.  This is to correct for the bug›            in the XF551 operating system, where it refuses to return to›            DSDD operation after you let it read a single density disk.›            ›        [@] SHAREWARE NOTE›            This displays a short notice reminding you that this copy is an›            unregistered shareware version of APACVIEW.  It also gives you›            my mailing address.›            ›            ›     KEYPAD OPTIONS›               ›       OPTION: Press this (either while the file is loading, or after) to›               enter joystick mode.  In joystick mode, two cursors will be›               activated to show the upper left and lower right boundaries›               of the screen.  A joystick (or trackball) plugged into jack›               1 can be used to move the cursors within the screen›               boundaries.  Pressing W or H will adjust the cursors for›               different Width and Height dividers (8, 4, 2, or 1).  Move›               the cursors to select an area of the picture to view, and›               press the joystick button.  The original file will be›               reloaded with new settings for width, height, horizontal,›               and vertical bias (offset).  This can be done recursively,›               but you must reload (press START to exit and use the L›               command) in order to see all of the picture again.  The›               cursors will not stray very far off the screen, and are›               clamped to the picture's boundaries.  Also note that you›               cannot select width or height dividers less than 1.›               ›       SELECT: Press this while a file is loading to stop the loading›               process and switch to color display.  This is useful to skip›               areas of the file which do not show up on the screen, or if›               you are merely impatient.›               ›       START:  Press to return to the menu screen.›               ›               ›››››››››››                                                  APACVIEW V2.4 Docs page 4››››     A LITTLE ABOUT APAC›     ›     APAC mode (Any Point, Any Color) was first described (to my knowledge)›     by Thomas Tanida in ANALOG Computing, Issue 60, May 1988 (pp. 64-71). ›     It is an 80H x 96V display mode which simulates 256 different colors. ›     It performs this feat by displaying pixels in graphics 11 (16 colors)›     followed by pixels in graphics 9 (16 intensities) in the line directly›     below them.  From a reasonable distance, the illusion of full color is›     complete.  Although it produces 256 colors, only the hue and intensity›     can be controlled.  The saturation of the color is constant.  For this›     reason, the best pictures can be viewed from GIF files with fairly›     saturated colors.  My monitor display (a Magnavox Color Monitor 40,›     Aug. 86) looks best when the comb filter is enabled (COMB DEFEAT›     switch in the out position).  Some monitors do not produce a›     full-color display, and some experimentation is necessary.  Other›     users have found that a regular television set does display true›     colors.  Monitors with split video inputs (such as the Commodore 1702)›     will display APAC mode best when you are not using the separate›     luma/chroma inputs.›     ›     ›     ABOUT INTERLACED APAC›     ›     Interlaced APAC mode was suggested to me by Charles Blaquiere.  It›     allows APAC mode to increase its resolution to 80H x 192V.  Basically›     it involves two fields of information (15,360 bytes of screen memory›     total).  One field/screen contains the color/intensity information of›     the even numbered lines, the other contains the odd lines.  You may›     have noticed that originally APAC displays had distracting black lines›     in the picture.  Page-flipping between two screens/fields of picture›     eliminates these lines, at the expense of generating a small amount of›     image flicker.  For those users with monitors that can display APAC,›     this mode presents the highest resolution, best color images I have›     seen on an unmodified Atari 8-bit.›     ›     ›     ABOUT PRYZM›     ›     Pryzm mode was (to my knowledge) developed by Darryl Yong.  He has›     released a slide show program and a drawing program.  This mode works›     by displaying a monochrome (GR.9) image for 1/60th second, followed by›     an "all color" (GR.11) image for 1/60th second by page-flipping.  The›     images resulting from this mode are in 80H x 192V resolution, with 256›     possible colors.  I could never get his demonstration programs to look›     as good as APAC on my system, but I did notice that Pryzm appeared to›     display better on some monitors that could not display APAC.›     ›     ›››››››››››››››                                                  APACVIEW V2.4 Docs page 5››››     ABOUT THE PROGRAM›     ›     This program was written entirely in 6502 Assembly Language, using the›     Atari Macro Assembler (AMAC) for optimal speed.  The decoding of GIF›     format was adapted from the program "gif2ras.c" Copyright (c) 1988,›     1989 by Patrick J. Naughton.  All pixels are converted from the source›     file, and are averaged (yes, averaged; eight bits each of red, green,›     and blue) from one to 32 pixels of source per pixel displayed.  The›     resulting color is looked up in a table of 4096 colors (RGBTABL8.OBJ)›     to speed the conversion to Atari chroma/luma format (GR.11/GR.9).›     ›     ›     This version (2.4) has the following limitations/enhancements:›          ›         -Skips over GIF extension blocks (such as those created by a›          program called "GIFLITE").  These were popping up on newer GIF›          files.›          ›         -Skips over the 128-byte header present in MacIntosh GIF files›          (this wouldn't have been necessary if the guys at Apple had›          abided by the GIF specification).›          ›         -Handles GIF files of any width and height.  Note that if your›          file is larger than 640H x 384V, you cannot display all of it on›          screen at once.  You can, however, use the joystick to select›          areas to view.›          ›         -More accurately guesses the correct width and height divisors›          when first loading a GIF file.  Will even accurately display GIF›          files created by my GIFNCODE program.›          ›         -No longer displays ugly color bars when displaying GIF files in›          APAC mode immediately after running certain other programs.  Some›          users wrote me saying they had to press [M] several times to›          cycle through all modes until APAC came around again.  It turned›          out I had not initialized a certain variable (sigh).›          ›         -Signals user during Save if file already exists, asks if you wish›          to overwrite or append (put stuff at the end of the existing›          file).›          ›         -Allows user to create R/G/B color separations for use by COLRVIEW›          (see section called "COLRVIEW Compatibility").  These may be›          created in graphics 9 or 15.›          ›         -Displays in "APAC Interlace mode", which suppresses the annoying›          black lines that appeared in previous APAC displays.  Some›          shimmering of the image may be visible.›          ›         -Detects when too little memory is available when program loads,›          prompts you to try again.›          ›         -Tells you when it can't find RGBTABL8.OBJ, allows you to swap in››››››››››                                                  APACVIEW V2.4 Docs page 6››››          the right disk and try again.›          ›         -No handling of left or top offsets.›          ›         -No allowing for multiple images in one file (does stop at end of›          first image).›          ›         -The program occupies RAM from $2600 to $BFFF.  This implies you›          must have a 48K Atari, with no cartridges installed, and a DOS›          that does not expect to use addresses above $2600.›          ›         -APACVIEW displays GIF interlace mode pictures by averaging the›          luminance between lines already drawn on the screen with new›          ones.  The fourth pass over a screen with height divide = 4 does›          nothing (press SELECT to skip).›          ›          ›     ABOUT GIF›     ›     GIF, or Graphics Interchange Format, is a hardware-independent›     graphics file format developed by CompuServe.  It is an adaptation of›     the Lempel-Ziv Welch compression algorithm, which is also used by the›     ARC/UNARC and AlfCrunch programs.›     ›     This version does not handle any updates to the GIF specification not›     coincident with the 'GIF87a' format.  There is now a new release›     (GIF89a) of this specification.  Any users out there who desperately›     need compatibility with the new format, please send a lot of cash, and›     I'll eventually get to it :-).  Note that this version only checks for›     the word 'GIF' in the header, and will thus accept GIF89a pictures. ›     No support of the new features or extension blocks is implied.›     ›     ›     COLOR TUNING›     ›     Included in this ARChive is the file COLORS.GIF (a new test pattern I›     created, which saves a lot of disk space).  Load this file and refer›     to the following table:›     ››››››››››››››››››››››››                                                  APACVIEW V2.4 Docs page 7››››                      -----------------------------------›                     :        :  DARK  :  LIGHT :        :›                     : BLACK  :  GRAY  :  GRAY  : WHITE  :›                     :        :        :        :        :›                      -----------------------------------›                     :        :        :        : YELLOW :›                     :  RED   : ORANGE : YELLOW : GREEN  :›                     :        :        :        :        :›                      -----------------------------------›                     :        :  GREEN :        :  CYAN  :›                     : GREEN  :  CYAN  :  CYAN  :  BLUE  :›                     :        :        :        :        :›                      -----------------------------------›                     :        :  BLUE  :        :MAGENTA :›                     :  BLUE  :MAGENTA :MAGENTA :  RED   :›                     :        :        :        :        :›                      -----------------------------------›     ›     ›     Adjust your monitor until these colors look as close as possible.  On›     my monitor, the only color that's a little off is BLUE MAGENTA, which›     looks a little too magenta to me.  And maybe the red tends a little›     toward "rust"...›     ›     ›     CREATING .PZM OR .ILC FILES›     ›     Note that the file format for either of these is identical: 7680 bytes›     of graphics 9 information, followed by 7680 bytes of graphics 11›     information.  So the creation process is quite simple:  use [M] to›     select "Gr.9" and load a GIF file.  After it has loaded, use [S] to›     save it.  Use a filename with a .ILC or .PZM extender.  Press [M]›     again to select "Gr.11" mode, and reload the same GIF file.  After it›     has loaded, use [S] to save it to the same filename.  You will notice›     that "SAVE" now asks if you wish to "Overwrite" or "Append".  Type "A"›     to append the graphics 11 screen.  After it has been saved in this›     manner, you can reload it with [I] or [P] (whichever you prefer, both›     can load the same files).  I'll admit I haven't tuned the colors for›     the best response with Pryzm; I look to the users for creative›     criticism :-).›     ›     Note that .PZM/.ILC format appears to be compatible with K.O.›     Distributors' Escalpaint program.›     ›     ›     COLRVIEW COMPATIBILITY›     ›     COLRVIEW, if you haven't heard of it, loads three color separation›     files, and displays, in graphics 9 resolution, an image that provides›     up to 4096 colors (!).  Alternately it can display in graphics 15›     resolution with up to 64 colors.  These files can be created in the›     following manner:›     ››››››››››                                                  APACVIEW V2.4 Docs page 8››››     After possibly viewing the .GIF file in APAC mode, use the M command›     to select red mode (red9 or red15, depending on what resolution you›     wish to create).  Load the file, then save it to some filename with›     the extension ".R".  Use the M command to select green mode, reload›     the file and save it with a ".G" extension.  Use the M command again›     to select blue mode, reload the file and save it with a ".B"›     extension.›     ›     To save a section of the image which you have "zoomed in on", do your›     zooming on the red screen.  Save the file as you did above, and change›     to green mode.  Use V to view the image.  Press OPTION to put up the›     cursors.  Don't move them, and press the joystick button to reload the›     same area of the image in green mode.  After it has loaded, save it. ›     Change to blue mode, and use V to view the image.  Press OPTION again,›     and press the joystick button to reload the same area of the image in›     blue mode.  After the blue image loads, save it.  Experiment a little›     if these instructions seem confusing.›     ›     Sorry, but there is not enough room (RAM in a 48K 8-bit Atari) to›     decode and display a GIF picture in COLRVIEW mode.  You must exit›     APACVIEW and load COLRVIEW in order to see your pictures in this new›     mode.  Please upload your favorite pictures to the pay services and›     BBSes (preferably ARC'ed to save disk space), and drop me a line about›     them.›     ›     WHERE TO FIND GIF FILES›     ›     Being the inventor of the GIF standard, CompuServe has the largest›     selection of online art.  A recent issue of CompuServe Magazine (April›     1992) lists the following forums where online art can be located:›     ›          ART GALLERY FORUM (GO ARTGALLERY)›          COMPUTER ART FORUM (GO COMART)›          QUICK PICTURES FORUM (GO QPICS)›          PHOTOGRAPHY FORUM (GO PHOTOFORUM)›     ›     ...and of course you can just type GO GRAPHICS to enter the main›     graphics forum.  Also be sure to check the individual computer›     sections, which may have an art section (GO ATARIARTS, GO AMIGAARTS,›     etc.).  The Graphics File Finder (GO GRAPHFF) can also be used to›     search for GIF files by subject matter.   CompuServe has also started›     releasing a quarterly hardcopy directory called "Best of 'Go›     Graphics'", which can be ordered online (GO GRAPHICS).›     ›     GEnie also has a large amount of online art in GIF format.  Check into›     the Photobase Library (PHOTO), the individual computer libraries›     (Atari 8-bit, IBMPC, Amiga, Macintosh, Apple II, Atari ST, etc.). ›     Also check out the Japan RoundTable if you are a fan of Anime (art›     from Japanese animated shows).›     ›     Also check out your local bulletin board systems.  Even BBSes that›     aren't Atari will most likely have a collection of GIF files online.›     ››››››››››                                                  APACVIEW V2.4 Docs page 9››››     ›     FINAL NOTES›     ›     This program has mostly been the result of my research and toiling.  I›     am depending on YOU, the Atari users, to give me feedback on what's›     missing, what I've done wrong, and (hopefully) what you like about the›     program.  My thanks to Don Davis, R. Woodruff, Bob Puff, David›     Beifeld, Charles Blaquiere, Ken Wickert, and Wendell Hong for their›     useful suggestions.›     ›     I have tested this program with MyDOS 4.5.  It should work properly›     with Atari DOS 2.0 and 2.5 and SpartaDOS 3.2.  If you have trouble›     with SpartaDOS, try disabling the TD line, KEY, and Verify.  Sparta›     DOS X apparently does not leave RAMTOP low enough for this program. ›     With any DOS, be sure to disable BASIC, whether it is built-in, or a›     separate cartridge.›     ›     Be sure to check out my other programs: ›     ›     APACSHOW  This is a slideshow program that loads APAC mode files from›               disk for display one after another.  A random-pixel dissolve›               from one image to another occurs every several seconds,›               which can be interrupted and restarted.›               ›     COLRVIEW  This program is the viewer for ColorView files created with›               APACVIEW, or downloaded from Bulletin Boards.  The latest›               version (2.6) lets you view all the ColorView files on a›               disk in "slideshow" mode.›               ›     DEGASRD   This program lets you view Atari ST Degas format (standard›               or compressed, any resolution) in Graphics 9 or 15›               monochrome, or in ColorView's 64 or 4096 color modes. ›               Version 1.1 provides the same "slideshow" feature mentioned›               above.›               ›     GIFNCODE  This program allows you to load four popular Atari picture›               formats (MicroPainter, Micro Illustrator/Koala, Graphics 8›               and 9) and convert them to GIF files.  This can be done›               interactively, letting you convert an entire disk of›               pictures one after another without memorizing the filenames.›               This is useful for Atarians who want to exchange their›               pictures with other computer users via bulletin boards.›               ›     ILBMREAD  This program lets you load and view Amiga IFF pictures in›               APAC mode.  The flexible joystick interface allows you to›               select rectangular sections of the image for further›               inspection.  ILBMREAD also saves the output in APAC mode.›               ›     If you cannot find these programs on your local bulletin board or pay›     service, they can be ordered directly from me for the following›     rates:›     ›››››››››››                                                  APACVIEW V2.4 Docs page 10››››                          PROGRAM    VERSION    PRICE›                          --------   -------    -----›                          APACSHOW     2.3       6.50›                          COLRVIEW     2.6       8.50›                          DEGASRD      1.1       8.50›                          GIFNCODE     1.0       6.50›                          ILBMREAD     2.1       6.50›     ›     ›     Prices include postage and handling, in U.S. dollars.  Printed docs›     will be provided.  Disks will be SSSD unless specified otherwise (I›     can provide up to DSDD).›     ›     APACVIEW is a shareware product.  If you use and enjoy this program,›     please express your satisfaction with a letter and the $10.00›     registration fee.  In return you will receive an autographed,›     registered copy (without the shareware notice) of the most recent›     version, with printed documentation.  I can also arrange to notify you›     (electronic mail or otherwise) when a new version of this program is›     available.  Registered owners can receive the next version for a›     nominal fee to cover materials and postage.  Registering also›     encourages me to create enhancements to this program, and to create›     other Atari 8-bit software.  It would also help pay some of my bills›     on the pay services, providing support and seeking feedback.  If you›     haven't noticed, the market for Atari 8-bit software has diminished›     such that large commercial software houses cannot justify producing›     new releases.  So I encourage all 8-bit users of shareware to register›     and support the remaining small software developers.›     ›     Please use the easy-response letter on the next page.›     ›                                  Jeff Potter›                                814 Banbury Dr.›                             Port Orange, FL 32119›     ›                                GEnie: JDPOTTER›                                CIS: 74030,2020›                      Computer World BBS: 1-716-247-8355›     ›     All company and product names are trademarks or registered trademarks›     of their respective companies.›     ›››››››››››››››››››››                                                  APACVIEW V2.4 Docs page 11››››     Easy-response letter:›     ›     mail to:›                             Jeff Potter          ›                             814 Banbury Dr.      ›                             Port Orange, FL 32119›     ›     ›     ›     Jeff,›     ›          I used your APACVIEW program on my Atari ________ computer.  I›     found that the colors did( )/sorta did( )/did not( ) look correct on›     my monitor (which is a ___________________).  I own a ____________›     disk drive, which operates in SSSD( ), SSED( ), SSDD( ), DSDD( ).›     ›          I rate this program in the following ways:›     ›                              Excellent     Good     Fair     Poor›     ›     Color Fidelity              ( )         ( )      ( )      ( )›     ›     Sharpness                   ( )         ( )      ( )      ( )›     ›     Ease of Use                 ( )         ( )      ( )      ( )›     ›     ›          I found this program on the following bulletin board/pay›     service:›     ______________________________________________________________________›     ›     Phone Number (if BBS): ____________________›     ›          I would be interested in receiving upgrades to this program( ). ›     Please contact me in the following way:›     ______________________________________________________________________›     ›          Comments:›     ›     ______________________________________________________________________›     ______________________________________________________________________›     ______________________________________________________________________›     ______________________________________________________________________›     ______________________________________________________________________›     ______________________________________________________________________›     ›          My name and address are:›     ›     ______________________________________________________________________›     ______________________________________________________________________›     ______________________________________________________________________›