››››            ›            ›                           Stereo Sound for Action!›            ›            ›                                 December 1989›            ›                                      By›            ›                                 Marty Albert›            ›            ›            ›            This  document  and the Action! routines attached are in›            no  way  copyrighted.  They may be freely distributed to›            all  that  may  have  a  need for them. Please pass them›            around,  but  keep  this text file as part of the ARC to›            help folks along.›            ›            ›            ›            One  of the most exciting things to happen for the Atari›            8-bits  in the last month or so of 1989 is the advent of›            the  Stereo  modification  by Chuck Steinman, nick named›            the "Gumby" mod.›            ›            In  a  nut  shell, this modification adds a second POKEY›            chip  to  your  computer  and  allows  you  to  have two›            channels  of  4  voices  each. This leads to TRUE stereo›            sound  output  from  the  computer, something that Atari›            should have done years ago.›            ›            ›            These   five   Action!   routines   will  allow  Action!›            programmers to access the new voices in the same fashion›            as the original voices.›            ›            ›            Included here are four new routines:›            ›                                     SndLo›                                     SndHi›                                     SRLo ›                                     SRHi ›                                     Gumby›            ›            ›            ›            ›                             Turning The Sound On›            ›            ›            The PROC SndLo is *exactly* the same as the current PROC››››››››››››››            Sound. It has simply been renamed to comply with the new›            PROC for the other channel.›            ›            The  PROC  SndHi is the one that will let you access the›            new voices.›            ›            ›            For both PROCs, the command format is:›            ›            ›                 Snd??(Byte Voice, Pitch, Distortion, Volume)›            ›            Where:›            ›               Voice is a value from 0 to 3 for the voice you wish›                     to access›            ›               Pitch is a value from 0 to 255, Low to High tones›            ›               Distortion is a value from 0 to 14 (even only) with›                     10 being a "pure" tone›            ›               Volume is a value from 0 to 16, from Low to High›                     volume›            ›            ›            In  other  words,  call these PROCs just like the normal›            Action!  library  call.  The only difference is that you›            now have access to TWO channels of 4 voices each.›            ›            ›            As  stated  above,  the  PROC  SndLo  is the same as the›            Action!  library PROC Sound. You need not use PROC SndLo›            unless  you  want  to,  but  I  find  that it makes life›            simpler to have the two commands with similar names.›            ›            ›            ›            ›                             Turning The Sound Off›            ›            ›            The  PROC  SRLo  is  *exactly*  the  same os the Action!›            library routine PROC SndRst. It has been renamed only to›            provide continuity.›            ›            To  turn  off  the sound on one of the channels, use the›            command:›            ›                                    SR??()›            ›            This  will  reset  ALL voices for the channel to make no›            sound.››››››››››››››            ›            ›            Again,  you  need  not use the PROC SRLo since it is the›            same  as  the library PROC SndRst, but I find it simpler›            to do so.›            ›            ›            ›            ›                            Seeing If Gumby Is Home›            ›            ›            The  FUNC  Gumby  will  allow you to test for the second›            POKEY  chip  in  order  to let your program determine is›            Gumby has been installed. The call to this FUNC is:›            ›                                 Byte Test   ›            ›                                 Test=Gumby()›            ›            ›            One  of two values will be returned in the variable Test›            as follows:›            ›                            0 = Gumby Installed    ›                            1 = Gumby NOT Installed›            ›            ›            Note  that  when  you make the FUNC call to this routine›            that  ALL  interrupts  are  disabled  while the check is›            made.  Upon  return, the interrupt status is restored to›            its  prior  setting.  This  s  done  to prevent possible›            spurious responses from the old and/or new POKEY chips.›            ›            ›                                   WARNING!›            ›            Use  of  the  PROC  SndHi  or  PROC SRHi on non-upgraded›            machines may have unpredictable results!! Unless you are›            100%  *sure*  that  your  program  will  be used only on›            machines  with  Gumby installed, you should always check›            first!›            ›            ›            ›            ›                                    Credits›            ›            ›            These  PROCs were derived from the Public Domain Action!›            Run Time system by Jeff Reister. Thanks again!!›            ›                                                                    ››››››››››››››