ATARIO

    ATARIO is a TURBO Pascal program to read on an IBM PC true double
    density diskettes from an ATARI double density drive.  That is to say
    it will not read diskettes created on an ATARI 1050 drive in "density
    and a half" mode.  This restriction (and the inability to read single
    density diskettes) is due to the IBM PC diskette adapter.

    This program assumes that the ATARI diskette is in drive A and that the
    current IBM drive is other than A:.  Since source code is provided, you
    may recode for any other assumptions or generality that you prefer.

    When offered a numbered menu choice, you may either enter the digit
    specified, or the corresponding Function key.  For example the digit 1
    and F1 are equivalent, as are 0 and F10.

    Main Menu:

            1: Dump Sectors
            2: Copy File
            3: Directory List
            4: Configure

            0: Exit

    Configuring ATARIO:

    Choosing option 4 from the main menu brings up the configuration menu.
    Three items are offered:

            1: Side 1
            2: DOS 2.x
            3: Atari XF551
            4: Drive A
            5: Text Color Change
            6: Text Background Change

            0: Main Menu

    Choice 1 acts as a toggle between Side 1 and Side 2 of a diskette
    formatted on a double side drive.  THIS WILL NOT READ THE THE BACK SIDE
    OF A "FLIPPY" DISKETTE WITHOUT FLIPPING IT.  Furthermore, this was
    written using the assumption that the diskette was formatted in the
    Percom style, where sectors 1-720 are on side one and 721-1440 are on
    side 2. Furthermore, it is assumed that side 2 is logical diskette by
    itself (as Dave's DOS does).  If you have a two sided diskette and your
    DOS (such as MYDOS) treats the diskette as one large filespace (i.e.
    sectors 1-1440), then you don't need this paramter at all.

    Choice 2 acts as a toggle between ATARI DOS 2.1 and LJK Dos.  The
    default is DOS 2.1.

    Choice 3 acts as a toggle that affects how the program reads the second
    side of a DS/DD disk.  It is set up to work with the Atari XF551.  If
    you are having problems reading the second side of a disk and are not
    using an XF551, try changing this parameter.

    Choice 4 allows you to use another drive on your PC.  It uses DOS absolute
    drive letters, which can be different from what you are used to, especially
    if you have an external drive.  Try a directory after changing this to
    see if the right drive is selected.

    Choices 5 and 6 are self-explanatory, and are, I admit, a bit frivilous.


    Dumping Sectors:

    Choosing option 1 from the main menu allows one to dump in ASCII and
    HEX format sectors from the ATARI diskette to the screen.  You are
    prompted for a sector number (in decimal) to enter.  Simply pushing
    enter will bump the current sector number by 1. Enter a value of 0 will
    return you to the main menu.




    Copying Files:

    Choosing option 3 from the main menu brings you to the file copy menu.
    You are offered 3 choices:

            1: Text Copy
            2: Image Copy

            0: Main Menu

    Whether option 1 or 2 is chosen, you will be prompted for an ATARI file
    name.  An file of the same name will then be created on the current IBM
    drive (which means that the current drive should not be the A: drive).

    Text Copy:

    Choosing option 1 invokes the Text Copy.  A Text Copy treats logical
    records on the ATARI disk (a string of bytes terminated by a 9B) as a
    logical record on the IBM file (a string of bytes terminated by a
    CR-LF).

    Image Copy:

    Choosing option 2 invokes the Image Copy.  An Image Copy transfer the
    ATARI file to the IBM file as is with no interpretation of the data.


    Directory List:

    Choosing option 3 from the main menu will give you a directory list of
    the ATARI diskette.  Pressing any key will return you to the main menu.


    Should a physical I/O error on the ATARI diskette occur during any
    operation, the partial file will be deleted from the IBM drive and
    an error display will appear with the following heading:

        Dos_Sector  Bios_Side   Bios_Track   Bios_Sector   Return_Code

    Where  Dos_Sector  : Atari sector number
            Bios_Side   : Physical Side of the Disk
            Bios_Track  : Physical Track on the Side
            Bios_Secotr : Physical Sector on the Track
            Return_Code : IBM BIOS return code
                          80 : Time out
                          40 : Seek operation failed
                          20 : NEC controller has failed
                          10 : Bad CRC on diskette read
                          09 : Attempt to DMA across 64K boundary
                          08 : DMA overrun on operation
                          04 : Requested sector not found
                          03 : Write attempted on write protected disk
                          02 : Address mark not found
                          01 : Bad command passed to disketted I/O

    Return codes of 40, 10, 04, and 02 should be the most common error
    codes, probably from copy protected diskettes.  If the physical error
    occurs while copying a file, you will be given the option to delete
    the incomplete file on the IBM disk.


    Dave Brandman
    805 Rotherham Drive
    Manchester, MO  63011

    Modified to add support for the Atari XF551, other drives on a PC,
    changing colors, and deleting incomplete files on September 6, 1991 by

    Kevin White
    235 Race St.
    Berea, OH 44017