SAMPLING: PRACTICE
          ------------------
          
          By Frankenstein
          
          On side two you'll find a bunch of Atmas II sources. These are
          ment for the assembler programmers among us.
          
          FASTPLAY.SRC
          ------------
          This is the "worthless" routine to play 4-bit samples at the
          highest possible rate (68KHz).
          To play one sample (one nibble), we only need 26 clock cycles.
          
          This gives: 1.79 MHz
                      -------- = about 68 KHz
                         26
          
          If you're able to improve this routine (to speed it up), I
          certainly want to know how you did it.
          
          CDPLAY.SRC
          ----------
          By inserting some NOPs in our previous routine, we are able to
          approach the speed of a CD-player! (44.1 KHz).
          Herefore the routine should take 40 clock cycles.
          
          The prove:  1.79 MHz
                      -------- = about 44.1 KHz
                         40
          
          The routine is also a 4-bit player.
          I don't think you would ever use this routine, since 44.1 KHz
          with 4-bits resolution takes about 22KB of memory per second.
          
          PLAYBOTH.SRC
          ------------
          This source plays 2-bit samples (four samples in one byte) and
          if you hold OPTION, it will play the normal 4-bit samples (two
          samples in a byte).
          Maybe you know the digi samples from the BIG demo? (HTT). Those
          samples are 2-bit samples created by the sampler from Ralf David
          (Germany).
          When the BIG demo was made, we thought that the R.David sampler
          gave 4-bit samples, so the play-routine used in the BIG demo is
          wrong. Take a look at this source to find out how these samples
          SHOULD be played.
          By holding and releasing the OPTION key you can hear the
          difference between 2-bit samples being played as 2-bit (right)
          or 4-bit samples (wrong). As you will hear, there won't be a big
          difference though.
          
          PLAYCONS.SRC
          ------------
          Samples can be played without using the soundchip. This source
          shows how to do it. It uses the console "klick" output for
          playing samples with the great resolution of 1-bit.
          It plays one bit from each 2-bit sample or, if you hold FIRE
          (Stick 0), it will play one bit from each 4-bit sample.
          I discovered that this console "klick" output can be used for
          playing low digi sounds, like digital drums, but it really
          sounds awful on all other samples. I think this output is also
          not very reliable. When I was experimenting with it, it didn't
          always generate the same volume.
          
          PLAY6BIT.SRC
          ------------
          Finally, a much more interesting routine. This one plays the
          upper 6-bits of an 8-bit sample! A long time we thought that
          4-bits samples were the limit of our Atari XL/XE, but it seems
          that by combining the volumes of more channels, we can approach
          a resolution of 6-bits!
          For this we combine three channels, which gives a range of 0 to
          45.
          With help of a 6-bit lookup table, we'll get a 6-bit sample
          output which sounds much better that the normal 4-bits output.
          The lookup table in this source was ripped from the PD
          soundtracker player (from issue #4). This table probably came
          from the Atari ST. When you put the values in a graphic, you
          will see that the table is actually a curve. According to The
          GateKeeper, it's not necessary to use this table. He has tested
          it with a lineair table and it worked fine.
          
          OVERSHOW.TRB
          ------------
          This is a Turbo-Basic routine to show you the difference between
          normal sample playing and sample playing with singular
          oversampling.
          You can test any 4-bit sample with it.
          
          OVERPLAY.SRC
          ------------
          A routine to play samples with singular oversampling. The
          routine is made to use with BASIC as follows:
          
          X=USR(PRG,BUF,LEN)
          
          PRG: Start of routine
          BUF: Start of sample buffer
          LEN: Length of sample buffer
          
          Although this routine won't improve your sample output that
          much, it's great to impress your friends with. Like; "My Atari
          can do oversampling!"
          
          PLAY4VOL.SRC
          ------------
          Yeah! This is the first sample play routine with software volume
          control! It plays a 4-bit sample through the channels 0 and 1.
          The volume value goes into channels 2 and 3. Two channels are
          used to give a hearable difference, but ofcourse you can use
          less or more channels for the volume if you wish.
          Use the console keys!
          
          PLAY4BAL.SRC
          ------------
          A logical continuation of volume control is ofcourse balance
          control. This is possible if you have a stereo upgrade
          installed.
          For example, you could modify the routine a little, and let an
          airplane fly from one speaker to the other!
          
          The sample plays through left and right channel 0. The balance
          state is put into left and right channels 1 and 2.
          OPTION turns the balance to the right and SELECT turns it to the
          left.
          
          First the program puts both sides (left/right) into neutral
          position, by writing volume 7. Look....
          
          Balance   LEFT   RIGHT
          -------   ----   -----
             7    -   0  -  14   max. right
             6    -   1  -  13
             5    -   2  -  12
             4    -   3  -  11
             3    -   4  -  10
             2    -   5  -   9
             1    -   6  -   8
             0    -   7  -   7   neutral
             1    -   8  -   6
             2    -   9  -   5
             3    -  10  -   4
             4    -  11  -   3
             5    -  12  -   2
             6    -  13  -   1
             7    -  14  -   0   max. left
          
          
          Well, that's all I have right now. I hope it will help you to
          develop great demos, music composers or whatever!