SAMPLING: THEORY
          ----------------
          
          By Frankenstein
          
          Just cured from the packer virus, and now this! A sample virus.
          I cought it when I looked at the Falcon030 with its 16-bit
          sample resolution..
          
          Yes, we're going to talk about audio sampling! Every time you
          read sample in this article, you can also read 'audio sample'.
          We're going to dig deep into this subject, so it will be very
          useful for experienced users.
          
          
          SAMPLES?
          --------
          A sample is digital quantity converted from an analogue signal
          with help of an ADC. If you don't understand this, please read
          the article about sampling hardware.
          
          Playing samples has (normally) nothing to do with the great (or
          less great) facilities of your soundchip. By playing samples you
          directly send voltages to the speaker.
          
          Let me tell you something about audio speakers first. When a
          speaker is in rest (neutral position), there's no noise. It
          starts to produce noise if it vibrates. Lets see:
          
              speaker    /
              -------   /
                       /
          minimum   <- O -> maximum
          (negative)   \    (positive)
                        \
                         \
          
          After reading the article about sampling hardware from AlphaSys,
          we can conclude that sampling is nothing more than recording the
          state of the speaker (no.. really?).
          
          Resolution
          ----------
          An analogue signal can contain an unlimited amount of values,
          while a digital signal has only two values, you know: 0 and 1.
          Actually the number of available values to represent the
          analogue signal depends on the number of bits we use.
          
          Notice that we are talking about the amplitude of the signal
          now.

          The more bits we use, the more values we have to represent the
          amplitude.
          Or.. with more values we can divide the amplitude into smaller
          steps.
          
          The amount of values used to divide the signal, represented in
          bits is called the resolution.
          
          Now I have to tell you that most CD players use 16-bits. CD's
          are recorded at 16-bits resolution, so CD players get the most
          out of the CD when using the same resolution to play it back!
          You might have seen adverts of CD players which have more than
          16 bits (e.g. 18 or 20). Although those players still read
          16-bits from the CD, it's somehow possible to let it internally
          work with more bits.
          Don't worry about it right now. Just remember that it's
          possible.
          
          To be complete, its said that you can calculate the so called
          'signal-noise distance' (a measurement which has everything to
          do with the quality of the sound). This can be done by
          multiplying the number of bits by 6.
          
          S/N = resolution * 6
          
          Here are some facts:
          
          resolution signal-noise
          ---------- ------------
              1-bit         6 dB (PC)
              4-bit        24 dB (ATARI XL/XE)
              8-bit        48 dB (ST/STE/AMIGA)
             12-bit        72 dB (ST/STE)
             16-bit        96 dB (ATARI FALCON)
          
          (dB = decibels)
          
          A very good and expensive record player is able to reach about
          60 dB, while there are CD-players which can reach over the 100
          dB!
          
          
          Frequency and Memory
          --------------------
          There's another thing involved in the great quality of CD
          players and hifi samplers. This is the frequency of recording
          samples.
          
          The first thing noticed is that the human ear can only hear
          frequencies between about 20 and 20kHz. By recording we have to
          take advantage of this knowledge by using a filter (a so called
          'anti alias' filter), to get rid of the signals we can't hear
          anyway.
          There are people who still think this makes a hearable
          difference and therefore prefer the analogue record player above
          any CD-player (sick!).
          
          According to the theory of Nyquist and Shannon we have to use a
          play/record sample frequency of 'two times' the maximum
          frequency of the signal (which is 20 kHz as mentioned earlier).
          In other words; after recording with such a high sample rate, we
          can play it back and reconstruct the exact same analogue signal
          again <grin>.
          
          So, theoraticly we have to use a '2 times 20' = 40 kHz sample
          rate. Now take a look at CD players..
          CD-players use a playback frequency of 44.1 kHz. Calculating:
          
          44.100
          ------ = 22.050 kHz
             2
          
          This is a little more than the 20kHz we've mentioned. I've read
          that this has something to do with the angle of the filter which
          can't be exactly 90 degrees. That's all I know.
          (Alphasys: It is correct. For the Freax: When you are using a
          filter, you always have a Resistor/Capacitor set. The Complex
          notation of this is R+iC, which is the representation of a
          Vector. This vector would have an angle of 90 deg. when there is
          no Resistor. Too bad that you always need a Resistor to set the
          filter to a certain frequency. This means that the filter can
          never be 90 deg.)
          
          44.1 kHz you said? This means that it plays 44100 samples per
          second! So for one second we need about 86 kB (44100 x 16-bits)
          memory?
          Yes, but that's only mono! That's 172 kB per second in stereo!!
          Hmm.. that's about 10MB per minute. A CD can hold upto 80
          minutes, so that would be about 800MB!
          
          Practical use
          -------------
          Pfew! But do we really need such a high frequency? Well, in most
          cases we can record speech at a sample rate between 5 and 10kHz
          while reasonable quality music needs about 15kHz. Beware that
          every frequency under 40kHz is not perfect.
          
          Remember the rule of Nyquist and Shannon. Low frequencies only
          need a sample rate of two times the highest frequency of the
          signal. When I'm looking at the build in equalizer of my SONY
          stereo amplifier, I notice that the 15kHz bar barely moves when
          playing low-noise music like 'Obituary' (for example). The
          6.3kHz (and lower) bars are more important in that case. A
          frequency of two times 6.3kHz would be OK for this kind of
          music. Beware though that we're still talking about a resolution
          of 16-bits!
          When taking the track 'Stranger Aeons' from 'Entombed', we see
          the 15kHz bar bouncing much more. OK, just wait a second. I'll
          get some CD's from my younger brother.. 
          Here I've got 'Dangerous' from 'Michael Jackson'. This CD really
          moves the 15kHz bar high up in the air. Esspecially the songs
          'In the closet' and 'Dangerous'.
          
          If you like to experiment with measurements like this, I'll
          recomment you to buy the Atari Falcon030. This computer has a
          DSP (digital signal processor) which is capable of sorting out
          the frequencies (Fast Fourier Transformation) in REALTIME! With
          some software you can create equalizer graphics, voice
          recognition, music recognition (!) and much more neat stuff.
          
          Ofcourse you could also buy a NeXT computer which has this same
          DSP (but a NeXT is much more expensive).
          
          Let's get back to the subject..
          The playback resolution depends on which computer you're using.
          The ATARI XL/XE's are capable of 4-bit samples using POKEY or
          just 1-bit samples by using the keyclick bit from GTIA.
          4-bits resolution also means that we can store two samples in
          one byte! (saves us a lot of memory).
          
          In fact, playing samples on the XL/XE is very easy compared to
          the normal ST. We have a special option in our Pokey chip for
          'volume only' which the ST lacks. Therefore if you want to play
          samples on the normal ST, you need a 'sample to frequency' table
          for converting the samples (Quarted has made a great table with
          which you can reach 12-bit resolution!).
          
          Bluaaarchh! Fortunately the Atari STE/TT and Amiga ARE capable
          of playing samples without conversion. On these machines you can
          output samples of 8-bit resolution by using DMA! (direct memory
          access). This means that you can load a sample into ram, give
          the soundchip the start and end addresses of the sample and it
          will be played without help of the processor!
          
          This brings us to another point of the subject. How to play
          these samples on the ATARI XL/XE? Sorry guys, our Pokey chip has
          no DMA. Therefore we have to play samples by using almost every
          clock cycle of the 6502 processor.
          
          I've been experimenting with this for a while and was very
          surprised to find the maximum sample play rate to be about 68
          kHz! This rate isn't practical ofcourse since:
          
          68000 x 4-bits = 32000 bytes
          
          Bogus! 32k gone in one second!
          On side two of this issue you'll find the 'worthless' routine
          for 68kHz.
          Read the next article for the full details about the routines.
          
          Remember my drawing of the speaker? Aren't you curious which
          value represents which state of the speaker? Well.. I was. So
          after some experiments and reading some documents I could make
          this table:
          
          SPEAKER POKEY STE/AMIGA
          ------- ----- ---------
              +7    15         7
              +6    14         6
              +5    13         5
              +4    12         4
              +3    11         3
              +2    10         2
              +1     9         1
               0     8         0
              -1     7        15
              -2     6        14
              -3     5        13
              -4     4        12
              -5     3        11
              -6     2        10
              -7     1         9
              -8     0         8
          
          In this table I only showed the upper four bits of STE/Amiga
          samples.
          If you take a close look and compare the STE/Amiga values with
          the Pokey values, you'll see that only the 'negative' bit has to
          be exclusive or'ed to be compatible!
          (I figured this out a long time ago when I tried to play samples
          from SoundTrackers on my 800XL).
          The samples from the STE/Amiga are so called 'signed' samples
          (because of using the sign-bit).
          
          OVERSAMPLING
          ------------
          While reading about the interesting subject of sound sampling, I
          often saw this strange word: 'oversampling'.
          It turned into an obsession to find out what this actually ment.
         
          Oversampling is an extra trick to improve the sound quality.
          It's done by calculating the intermediate value of two samples.
          Let's give a drawing:
          
                   --- time --->
           7                            S
           6                          So
           5                         o
           4    S                   S
           3     oS
           2   o   oSoS
           1           oS
           0 -S----------o---------o-----
           1              S
          -2
          -3               o      S
          -4
          -5                S    o
          -6                 o
          -7                  SoS
          
          S : sample      (data)
          o : oversample  (calculated)
          
          This example shows 4-bit resolution samples with singular
          oversampling!
          To maintain the same frequency you have to play both samples and
          oversamples in the same time (not AT the same time!). So, if the
          frequency was for example 15kHz, you have to play samples and
          oversamples at 30kHz.
          
          How about multiple oversampling? I've been told that if you talk
          about multiple oversampling, you just keep on taking
          intermediate values between both samples and oversamples, like:
          
          Normal    S.......S.......S.......S
          1-time    S...O...S...O...S...O...S
          2-times   S.O.O.O.S.O.O.O.S.O.O.O.S
          3-times   SOOOOOOOSOOOOOOOSOOOOOOOS
          
          You can see that the frequency to play samples and oversamples
          can just be calculated by:
          
          Play freq.= Normal freq. x ( 2^n )
          
          (where 'n' is the times oversampling)
          
          I think this technique is not only handy to improve the sound
          quality, but also to adjust te sample frequency without 'not
          playing' data.
           
          That's the whole story. Read the next article to find out about
          the practical examples on this magazine.
          
          Hope you liked this article. There's at least one who liked it..
          that's me!
          
          <END>