SPEED UP YOUR DRAWINGS
          ----------------------
          
          By WosFilm
          
          
          Speed is fun! I've been looking for, and trying to develop
          myself, a very fast draw routine so I maybe can do some nice 3D
          effects in another stupid demo... And so in issue 6 of this
          wonder magazine, BEWESOFT published his routine together with
          the source for his vectorscroller demo. I checked that draw
          routine and found it pretty clumsy (no offence!) since it uses
          the entire zero-page area. That's too bad 'cause it's good for
          so much stuff! One other reason for me writing this article is
          the article about speeding up your code that I've already
          written. You'll see what I mean...
          
          Well what this is all about is the draw routine from BEWESOFT's
          vectorscroller. I've taken the liberty to extract it from the
          demo in a little more "usable-for-the-public" form. And on the
          way I've rewritten it a little, so that it only uses a few
          zero-page bytes. When I did this I went through the routine over
          and over again to search for a faster way to do things, like
          using more immediate addressing and so on. I've even used
          illegal opcodes at 2 places (witch isn't very neccesary since
          they only save 16 color clocks per drawn line). One thing you
          often can reduce in the code is unneccesary SECs and CLCs, like
          in some occations a BCS branch points to a SEC (like just before
          a subtraction). Such a SEC is totally unneccesary since the
          carry flag must always be set at that place, otherwise the
          branch wouldn't jump there. And also (as in BEWESOFT's draw
          routine) when doing subtractions like this:
          
               sec
               lda x2
               sbc x1
               sta dx
               sec
               lda y2
               sbc y1
               sta dy
          
          When, as in this case, you know that X2 is always bigger than
          X1, the second SEC is unneccesary since the carry flag doesn't
          change after the first subtraction. Ok, 4 color clocks isn't
          very much, but add a few together...
          
          I've tried to eliminate all these kinds of unneccesary code, and
          use more immediate addressing (especially in loops) instead of
          even zero-page addressing. This forces self-altering code, which
          of course is to be avoided, but whattaheck? I mean like this:
          
          label1    lda #f         4
                    sbc #hdxdy     4
                    bcs label2     8
                    adc #dx        4
                    sta label1+1  10
                    jmp ...
          label2    sta label1+1  10
          
          is faster than:
          (f, hdxdy and dx is zero-page)
          
                    lda f          8
                    sbc hdxdy      8
                    bcs label2     8
                    adc dx         8
                    sta f          8
                    jmp ...
          label2    sta f          8
          
          The numbers to the right is the time (in color clocks) for each
          instruction. As you can see, the topmost routine is a lot
          faster, the only negative is of course that the values shall
          change as seldom as possible, and that before entering that
          code, all values must be set.
          
          For a good description of the drawing technique, look at
          BEWESOFT's article in issue 6.
          
          To compile and run the little demonstration of the draw routine:
          
          The source is written in MAC/65. At line 8000, write the path to
          the draw routine. Compile it. Load the file TABLE.OBJ, which
          contains pre-calculated x,y coordinates (from $7000 to $73FF),
          before you run the compiled file. When running, the first white
          block on the screen indicates the time it takes to draw one
          frame (4 lines) and the second white block indicates the time it
          takes to clear the small screen.
          
          Note that this routine only work with narrow screens, i.e. 32
          bytes wide scanlines (though I don't think it's too difficult to
          change that)!
          
          
          Good luck with all your vector demos!!! I'll try the best I can
          myself...