››                     MAP and UNMAP utilities for SpartaDOS X›››                                 By Pab Sungenis›››                        Copr. 1993 Low-Budget Productions›                           Another Shareware Offering.›››                                    ABOUT MAP›                                    =========››               SpartaDOS users have always had to make a trade-off in›          the area of random-access files; while the relative (instead›          of absolute, like other DOS's) NOTE and POINT commands›          allowed automatic access to any specific byte in a file on›          any disk, the sector-map format that made this power possible›          would get bogged-down if a file grew larger than, say, 30K.›          The DOS would have to look through so many linked sector maps›          that it could take up to 5-10 seconds just to locate a byte.››               When ICD created SpartaDOS X, they had intended to›          include a database program on the cartridge.  To make theirs›          the fastest available (and to overcome SpartaDOS's failings›          in the area), they devised a method now called "Super Sector›          Maps," which would allow SpartaDOS X to ignore the links›          normally used in sector maps, and locate the appropriate byte›          in hardly any time at all.  When the database was dropped in›          favor of the built-in ARC command, the Super Sector Map code›          remained but was, for some reason, never implemented into the›          DOS itself.››               The programs in this archive, MAP.COM and UNMAP.COM will›          install and remove (respectively) a Super Sector Map for a›          file you specify.›››                                    USING MAP›                                    =========››               The format for the MAP command is:››                    MAP [path]filename.ext›          ›          (Typing MAP without specifying a filename will remind you of›          this syntax.)  As with all other SDX commands, the default›          directory is used if no pathname is specified.  Wildcards›          must not be used; the MAP command can only handle one file at›          a time.  If a wildcard is used, the command will return a›          "File not found" error.››               The MAP command will first locate the specified file,›          then go through its sector maps one by one.  You will see the›          message:››                    Mapping [filename.ext]...›          ›          while the command is doing this.  Once the Super Map has been›          created, MAP will locate a free sector, store the Super Map›          there, and mark that sector as in-use in the bit-map.  MAP›          will then tell the file where to locate the Super Map, and›          return to SpartaDOS X.››               Note that a Super-Map need be created and installed only›          once.  Once the Super Map is installed, SDX will maintain and›          update it as needed.  If you try to install a Super Map on a›          file that already has one, the command will tell you so and›          abort.›››                                   USING UNMAP›                                   ===========››               The format for UNMAP is identical to that of MAP:››                    UNMAP [path]filename.ext›          ›               Super Maps should always be removed from a file before›          the file is deleted or overwritten.  Otherwise, the Super›          Map's sector will just sit there, marked in use.  Use UNMAP›          to remove the Super Map before doing anything other than›          appending to the file.››               Again, wildcards must not be used.  If you try to unmap›          a file which is not mapped, the command will tell you so and›          abort.›››                          WHAT TO MAP, WHAT NOT TO MAP›                          ============================››               While MAP can speed up random access files considerably,›          it does nothing with sequentially-read files (like text and›          programs).  Don't waste the time and space involved in›          mapping them.››               Since files should be unmapped before deleting or›          overwriting, never use MAP on a file which is likely to be›          erased.  This is important for users of SpartaDOS X's ARC›          command!  Never update or freshen an archive without›          unmapping it first.  (Users of Bob Puff's SuperARC can append›          to a mapped archive with no problem.)››               While MAP will technically work on any randomly accessed›          file, its effects aren't really noticed until around the 32K›          mark.  (16K on single-density drives.)  Don't bother mapping›          small files, unless they're likely to grow past this mark.››               While MAP and UNMAP will operate under earlier versions›          of SpartaDOS, the Super Map will not be recognized unless the›          disk is read by SpartaDOS X.›››                                 TECHNICAL STUFF›                                 ===============››               For those who must know, out of curiosity, how every›          single thing in a program works, here are the technical notes›          for MAP.  Read chapters 6 and 7 of the SDX manual if you›          don't understand any references made here.›››               The Super Map is addressed by the reverse-reference›          entry in the first sector map of a file.  This corresponds to›          bytes 3 & 4 of the sector.››               MAP uses the raw directory read mode to locate a file›          and its first sector map.  All other sector maps are located›          using the forward-reference entry (bytes 1 & 2) of each›          sector map.››               To speed up the locating of a free sector, MAP uses the›          "file allocation sector search" value located at byte 18 of›          Sector 1 as its starting point (as does SDX in all its write›          operations).  While there is a remote chance this technique›          will cause a spurious "Disk Full" error, this has not›          happened in over four months of testing and daily use by›          myself.››               MAP and UNMAP both use the SpartaDOS LSIO vector ››               MAP and UNMAP both load at location $6100, and use the›          memory from $3A00 to $60FF for various buffers and storage.›          This should not cause any conflicts under 99% of possible›          system configurations.  If you think you have a memory›          conflict, write to me, and I will set up a special version›          for you.›››                                   FINAL NOTES›                                   ===========››               Just like nearly everything I ever write, MAP and UNMAP›          are Shareware.  If you use and enjoy these programs, you are›          encouraged to send a donation.  There is no need to donate,›          but it would be very much appreciated.››               If you want to reach me, please use one of the following›          methods:››               Internet : pab.sungenis@ulbbs.sccsi.com›               FoReMNET    : Pab Sungenis at node 168›               Fido NetMail: Pab Sungenis at 1:266/47›               CompuServe  : 72632,52›               Snail Mail  : LOW-BUDGET PRODUCTIONS›                             PO BOX 306›                             AVALON NJ  08202-0306››               Thank you, and enjoy the program.››                                                                 -- Pab›