DOCUMENTATION FOR THE AMODEM VER.4  TERMINAL PROGRAM.      This file will permit the ATARI  to access an RCPM BBS that runs  under the CP/M operating system.  Also SOME ATARI BB Systems.  And allow ATARI to ATARI transfer.  It features uploading and downloading  at 300 baud and is extremely user  friendly.  The file may be listed here with  command D.     AMODEM4  <Y/N>N  Then captured and saved to disk.  Then ENTERed with the interface  "booted" by an AUTORUN.SYS file.      When RUN, it will go into terminal  mode at which time the user should  dial the BBS. Some systems are of  the RING-BACK variety, so you should  be prepared to let the phone ring  ONCE. You will then hang up and  re-dial 10-15 seconds later.  When the system connects, type a  few <returns>s until the BBS responds.  Follow the HELP commands of the  system from here.      TRANSLATION - SELECT T will toggle  the translation mode between ATARI  (No translation) and ASCII (Light  translation). Use ATARI on ATARI  Systems and ASCII on RCPM Systems.      MENU - For ATARI Disk systems, you  may list your Menus with SELECT M.  To find files or space for new files.      DUPLEX - For ATARI to ATARI file  transfer, you will need Half Duplex  Since AMODEM sends no echo.  You may toggle it with SELECT P.  NOTE; Use ATARI Mode on each end.      DOWNLOADING - To download from the  BBS you must remember that it is  controlled by a file called XMODEM.  To have this file send a program to  your ATARI, you must press <SELECT>  key and type R to tell the ATARI to  get ready to receive from XMODEM.  You must then provide a FILESPEC  to which the ATARI will save the  program. This does not necessarily  have to be the same name as the RCPM  has it saved as.  Once back in terminal mode, type the  command; XMODEM S <filename.ext>  and then RETURN at which time the  XMODEM controller will respond with  a statement that it has opened its  file and is prepared to transmit to  your ATARI. To begin the procedure,  press the START key and sit back  and relax. The XMODEM will send the  file, which can be of any type.  The screen will turn RED and when  the file has been downloaded, your  ATARI will save it to your filespec.  When the screen turns back to BLUE,  the process is complete.      TO UPLOAD - Reverse the procedure  by pressing the SELECT and S keys  to indicate you will Send to XMODEM  the ATARI <filespec><RETURN>.  Then type; XMODEM R <filename.ext>  and RETURN which will tell XMODEM to  prepare a filearea under that name  to store the program you are going  to send TO the BBS. To initiate  the upload, press the START key and  the computers will take over. Your  screen will turn GREEN until the  transfer is completed.      TO CAPTURE DATA - Press SELECT then  C and enter a filespec. To start   press the START or OPTION key.  All data that you see on the screen  will be saved to memory. You may  toggle the capture on and off with  the OPTION key. When you are done,  or the buffer is full, you can press;  SELECT and D. This will Dump the  memory to your filespec.      NOTE ABOUT ATARI <FILESPEC>  You may use any legal ATARI Device  and filename and type. Example;  D:MYFILE.BAS  or  D2:YOUR.PGM  C:  or  P:  or  R2:  or  E:  Remember that you can't send from  the Printer and you may send and  receive using the Editor (E:).          Please leave any questions on the  A.R.C.A.D.E. BBS at 313-978-8087  or Compuserve PEM-450: 70355,602  or write:  Jim Steinbrecher             37220 Tricia Drive             Sterling Hts, Mi 48077          ************************************    NOTE-      There are many different versions of  the AMODEM terminal program in use.  The major versions <2.0, 3.0, 4.0>  were released by the author, while  the "sub-versions <3.1, 3.2, 4.1...>  were mostly prepared as personal  modifications by ATARI enthusiasts  from all over the USA. For the most  part, they added features such as   mmultiple disk drive access or duplex  toggles that were gathered together  and refined by Jim, and included as  standard features in the subsequent  major version.     One such sequence of evolution that  illustrates this best, is the <M>enu  option.    Version 3.0 had send/recieve/menu   access from D1: only. Ver. 3.1 added  all 4 drive availability to this.  When 4.0 was released in 10/82 this  was a standard feature. Ver. 4.1  modifies line 4000 and adds 2 other  lines that permits the same <M>enu  scroll of every drive as 4.0, but  now permits the user to type simply  a single number <1,2,3,4> to have   only that single menu shown.     The 3 lines now become:      4000 ? :CLOSE #MODEM:SGL=0  4065 IF SGL=1 THEN 4080  6051 IF C>48 AND C<53 THEN SGL=1:    CLOSE #MODEM:GOTO 4020                           SYSOP/Ron Luks                    CEMSIG <PEM-450>                        71645,253