MACWDG IS A MACHINE LANGUAGE UTILITYDESIGNED FOR USE WITH THE MAC/65ASSEMBLER FROM OSS. IT IS FUNCTIONALLYEQUIVALENT TO MY EARLIER BASWDGPROGRAM, PROVIDING ACCESS TO SIMPLEDOS FUNCTIONS WITHOUT EXIT TODUP.SYS. If you already have BASWDG, you don'tneed this whole DOC file..thefunctions are pretty much the same.However READ THE NEXT 4 PARAGRAPHS!!! THERE IS A 'DOCUMENTED FEATURE' (I.E.WEIRD BUG) DO NOT PRESS <RESET> WHILE YOU ARE INTHE MACWDG MENU. IF, FOR SOME REASON YOU DO, YOURCOMPUTER WILL GET HINKY. FORTUNATELY,IT WON'T CRASH IMMEDIATELY. SAVE ANYWORK YOU NEED, AND THEN DO A COMPLETECOLD-START. IF YOU DON'T, MAC <WILL>COLD-START <ITSELF> ON THE NEXTRESET!! AAARGH!!!! I'VE BEEN TRYING TO TRACK THIS DOWNFOR A YEAR, WITH NO LUCK. BUT IHONESTLY THINK THAT THE PROGRAM ISUSEFUL ENOUGH THAT, AS LONG AS YOUDON'T DO THAT <BAD THING> ...            WHAT IT DOES Once MACWDG is installed, it takesover the computer's DOS vector. Whenyou issue a DOS command, instead ofloading DUP.SYS, you'll run MACWDG. Itpresents a Quick Menu for the mostcommonly used disk functions withoutdisturbing your code in EDIT or TEXT(so you can save those 45 sectors forMEM.SAV on D8.) Trust me. This is alot faster, and less hassle thanconstantly going to DUP. This is an Old Idea. I've tailoredMACWDG to match my own programmingneeds and quirks. You can do the samething. See MACWDG.M65 for SourceCode.               NUMBERS Check the title screen for CriticalValues. The RESET defaults are MACWDGshadows. You can change them with a Dcommand in DDT. TEXT and BACK setMAC's internal color registers (infofrom the ubiquitous Bill Wilkinson).Poke them as you would 709 and 710 inBasic. The keyboard is speeded up.These shadow 729,730.     ABSOLUTELY RESERVED MEMORY Starting at $1CFC, this block isQUITE SMALL. It should NEVER, EVER, beoverwritten. MACWDG lives mostly in 'SHADOW RAM',UNDER the OSS cartridge (another thankyou to OSS for info!) When you call itby typing DOS, MAC is disabled, andMACWDG runs. Exit and MAC is back.What that means is that you have a 1K+program that steals less than a pagefrom free memory. Handy, no?        MACWDG MENU FUNCTIONS              DIRECTORY Type the drive number. If RAMDISK.COMhasn't loaded, or if you're using DOS2.0, only 1 or 2 are allowed.Otherwise you have D8: to playwith...hoo-hah.            DEFAULT DRIVE That's the drive that doesn't need aDevice Spec (eg. D1:) when typing infile names. In DUP.SYS, the Default isalways D1: In the MACWDG menu, thingsare more flexible. THE MACWDG DEFAULT DRIVE IS THE LASTDRIVE FROM WHICH YOU READ ADIRECTORY. The intent is to default to the drivewhose files are currently listed onthe screen. This can be confusinguntil you get used to it. So there area couple of helps:  D: is ALWAYS translated to D1:  The FULL FILESPEC, as translated, isprinted on the screen before anyaction is taken. LOOK AT IT! If it'snot what you intended, you can bailout.         CHANGED YOUR MIND? The All Purpose Quit Key is BREAK. AtANY prompt, pressing it will exit tothe menu. BREAK disabled? There are a couple ofalternatives: AT FILE NAME 'INPUT' PROMPTS: use a'Null Input.' Press RETURN ONLY withno name. AT ANY OTHER PROMPT: hit ESCAPE.               CONFIRM Before MACWDG acts, it will ask'OK?', just to make sure that youreally want to do what you said. 1) Want to quit? Hit BREAK,ESCape, orN (for NO, of course.) 2) Go ahead? Any other key.            FILE COMMANDS These are E (Erase), R (Rename), andM (Move File) At the command prompts,INPUT the filename (remember, nodevice spec needed if you're using theDEFAULT.) Abort by pressing RETURNonly, or BREAK. ERASE zaps the selected file.  RENAME works in the normal fashion.Type the old name, a comma, and thenew name. Sorry, you STILL have towatch out for duplicate names (don'tblame me..I'm just using XIO 32!) UseRENAME with the target directory onthe screen to make sure you're notdoing something nasty. Make sure youcomplete INPUT, providing the commaand new name. Otherwise, you're liableto find your file renamed to SECTORS(what?)              MOVE IT! This is my favorite. The MOVE commandcombines the functions of COPY FILE(C) and DUPLICATE FILE (O) in theDUP.SYS menu. It's especially usefulwith D8. MOVE uses 'Free RAM', starting at thetop of your program, for its buffer(do you have data up there? Careful.)The smaller your program the biggerthe buffer. (Error 2 means your RAM isfull!)            MOVE COMMANDS There are SEPARATE PROMPTS for FROMand TO filenames. Remember to use theDefault to cut down on typing. Any legal device (E:, P:, C:, D:) canbe used. Please remember the colon!       THE LEYENBERGER OPTION If you want to use the SAME FILE NAMEfor a disk MOVE, you can type ONLY theDevice Spec (INCLUDING THE COLON!) atthe TO prompt. The FROM file name willbe appended.         COPY or DUPLICATE? COPY FILE (no swaps) is automaticallyassumed with files that don't go TOdisk. Handy for dumping text files toP: or screen (E:) Likewise if you use2 different drives (like MOVEing afile to D8 from D1) If the SAME D:num is used for FROMand TO, MACWDG invokes DUPLICATE FILE,and prompts for swaps. These work like 'OK?'  BREAK/ESC/N toexit, or RETURN to continue. Dependingon exactly where you are in theprocess, an exit may leave you with apartial file on the TO disk. Erase asnecessary. For severe problems,(inserted the wrong disk?) useDISKFIX.COM.           EXITING MACWDG Cart returns you to EDIT or TEXT. To go all the way and exit toDUP.SYS, type @ (SHIFT-8.) That'sintentionally a two-finger combo, toavoid accidents.              DUP.SYS?? I try to avoid DUP.SYS, but sometimesit's necessary (DISKFIX!) IF MEM.SAV IS ACTIVE WHEN YOU EXITDUP.SYS WITH THE B COMMAND, MACWDG isstill there. However, it has beenunhooked (safety first) To rehook it,go to DDT,*$0C, then DFC1C toreinstall the DOSINI hook. Exit DDT, and RESET. MACWDG is back.Do this BEFORE any drastic action likea RESET, LOAD, or NEW. DO make sure that MEM.SAV hasrestored the RAM. LIST if you're notsure. Remember that using options Cand O in DUP can zap MEM.SAV (That'swhy I wrote MOVE) IF MEM.SAV IS NOT ACTIVE, you canusually Reload MACWDG with the Lcommand. If in doubt, Reboot. Running DUP.SYS on D8 with noMEM.SAV, alters the sector count forthat file(??) Beats me. Even if itsays DUP.SYS is taking up 156 sectors,it's really only using 42, asconfirmed by FREE SECTORS. So far,this seems harmless. have fun....>>don                                      qqqqqqqqqqqqqqq