5-22-85                        RAMDISK2                     Page 1

       RAMDISK2 configures an ATARI 130XE's  Extra RAM for use with  ATARI DOS 
       2.0S or the OSS DOSXL File Management System.
       
       The Ramdisk (D4)  created by RAMDISK2  has 503 free  sectors, 4 through 
       359 and 369 through 515. Sectors  360 through 368 contain the VTOC  and 
       Directory as usual. Boot sectors 1  through 3 do not exist, but  a read 
       or  write  attempt  returns  a  'success'  status  code. Any attempt to 
       access sector 516 or higher returns an error 144.
       
                                    INSTALLATION
       
       Following  a  power  up  boot,  the  RAMDISK2 object file automatically 
       installs and formats the Ramdisk  when executed as a binary  load file. 
       It  may  alternatively  be  renamed  to  AUTORUN.SYS.  The installation 
       functions are:
       
       1. Verify that  the DOS File  Management System is  either the standard 
       Version 2 as supplied with ATARI DOS 2.0S and normal OSS DOSXL, or  the 
       modified version from DOSXL.XL. Exit if not.
       
       2.  Verify  that  the  computer  system  actually has Extra Ram at 4000 
       hexidecimal. Exit if not.
       
       3. Copy the relocatable driver code to the end of the FMS, and set  the 
       drive bit in DRVBYT for drive 4.
       
       4. Replace the FMS calls to  SIO and the OS Resident Disk  Handler with 
       calls to the relocated code.
       
       5.  If  the  FMS  was  the  standard  Version  2,  kill the 'write DOS' 
       function by pointing it to the Invalid Device Command error return.
       
       6.  Add  the  length  of  the  driver  code  to  SASA, the FMS start of 
       allocation address word.
       
       7. Reinitialize the FMS.
       
       8. If the Extra  RAM is not already  formatted as Ramdisk, clear  it to 
       zeroes and write the VTOC for the 503 available sectors.
       
                                       NOTES:
       
            Once the installation has been done, rerunning the RAMDISK2
            code will exit at function 1, thus avoiding multiple copies of
            the driver code.
       
            Function 8 allows rebooting the computer by forcing a
            coldstart. A  reboot without turning off the computer does
            not destroy the Ramdisk contents.
       
       













       5-22-85                        RAMDISK2                     Page 2

       
                                         USE
       
       Once RAMDISK2 has set up  D4 in the Extra Ram  it may be used like  any 
       other drive interfaced through DOS.
       
       The bit map in the VTOC created with the Ramdisk indicates sectors  516 
       through 720 are in use, so the  FMS will not attempt to write to  them. 
       However, if you reformat the  Ramdisk, the driver code merely  corrects 
       the maximum  and free  sector counts  in the  VTOC written  by FMS. The 
       same  logic  applies  to  a  sector  copy  routine  like the the DUPDSK 
       extrinsic command of DOSXL, which directly copies each sector shown  in 
       use by  the bit  map. The  FMS merely  maintains the  sector counts for 
       your convenience, and  actually uses the  bit map for  all decisions on 
       what sectors are available. Therefore this logic allows duplicating  an 
       actual  disk  to  the  Ramdisk  and  back  to disk again, so long as no 
       sector above 515 is in use.  I strongly rcommend, however, that a  COPY 
       with wildcards be used instead, as  that will maintain the bit map  and 
       sector counts together.
       
       
                                      WARNINGS
       
       Any program which does not use  the DOS File Management System for  all 
       disk  handling  will  probably  not  work.  For  example,  the DOS 2.0S 
       DUP.SYS has  its own  call to  the OS  Resident Disk  Handler for drive 
       status.  The  other  problem  with  using  DUP.SYS  is that the Ramdisk 
       driver uses 255 of the measly 768 bytes allowed by the system for  VTOC 
       and Sector buffers.  As with the  addition of any  other single density 
       disk, the  FMS allocates  an additional  128 byte  space for  the VTOC. 
       Thus, installation of the Ramdisk increases LOMEM 383 bytes.
       
       The Ramdisk will obviously be incompatible with any program which  uses 
       the 130XE Extra Ram for other purposes.
       
       The  modifications  affect  the  FMS  code  which would be written by a 
       'write DOS.SYS' operation. Since the Ramdisk driver code would not  yet 
       be  loaded  when  the  boot  code  attempted  Serial  IO,  a  cold boot 
       operation would  immediately lock  up the  computer. It  would then  be 
       necessary  to  power  down,  thereby  losing  any  information  on  the 
       Ramdisk. The installation code forces  the 'write DOS.SYS' code in  the 
       standard FMS to return an invalid command (168) error code. If you  see 
       it, do not  attempt to boot  from the disk  which was being  written at 
       that time.
       
       
       
       
       
            Josef W. Segur [74676,3047]   5-25-85