››››   COPYOS  Version 1.2                                     Barry Gordon 1/92›     ›     ›     This program will copy the Operating System from an Atari XL/XE to›     disk for use with an EPROM burner.›     ›     ›     The Atari XL/XE Operating System chip is layed out in four sections:›     ›      ROM            Computer       XL/XE OS›      Address        Address        Function›     ›      $0000-$0FFF    $C000-$CFFF    Interrupt handlers, misc routines›      $1000-$17FF    $5000-$57FF    Self Test code (enabled by PORTB)›      $1800-$1FFF    $D800-$DFFF    Floating Point routines›      $2000-$3FFF    $E000-$FFFF    Operating System›     ›     ›     The Classic 800 OS had no Self Test memory, and did not allow ROM›     banking of the $C000 memory. Custom Operating Systems for the XL/XEs›     are usually based on this OS and will use these two areas to their›     fullest advantage.›     ›     COPYOS will create a file exactly 16,390 ($4006) bytes long. It will›     contain the above listed areas in the ROM address format, preceeded by›     a binary file header. This file can then be modifed and used by an›     EPROM burner to create a new OS chip.›     ›     The Self Test routines and the Floating Point routines were given›     special consideration when writing this program. The Self Test›     routines (which must be banked in by clearing Bit 7 of PORTB) are›     automatically disabled by the OS during disk I/O. The Floating Point›     routines are automatically banked out by the OS when a parallel device›     is accessed (i.e. a Hard Drive). The high-speed floppy operations in›     the Black Box also disable the Floating Point routines during disk›     I/O. Both of these routines are copied to a safe place in memory and›     written out to disk from there.›     ›     This program was not written for purposes of pirating copyrighted›     Operating System chips, but rather to encourage experimentation with›     firmware programming.›     ›     Happy EPROM burning!›     ›                                                                           ›