KOALA PICTURE FILES
          -------------------
          
          By Jiri Bernasek (BEWESOFT)
          
          
          A short time ago I made a program, which is (besides of other
          great functions) able to display nearly any picture from the
          disk. It's simple of course. But... The trouble was with loader
          for KOALA files. I have a lot of them (Source listings, utility 
          etc. etc.), but the correct one is missing! Finally I was forced
          to crack the original KOALA MICROILLUSTRATOR program. But let's
          start from the begin...
          
          There are many formats of picture-files on Atari XL/XE. The most
          used formats are MICRO PAINTER and KOALA. MICRO PAINTER format
          is quite simple: The first 7680 bytes of the file contains the
          whole screen-memory, and the last four bytes contains colors in
          order: Background, color 0, color 1, and color 2.
          
          KOALA files contains packed pictures, so they are not so simple.
          At the begin of every KOALA file there is a header:
          
          File position    Function
          ---------------------------------------
          0...3    Identification of KOALA file.
                     Allways FF 80 C9 C7 (hex.)
          4, 5     Length of header -1 (Normal
                     length is $1B)
          6        ???  (Allways 01)
          7        Compression method. It can be
                     00, 01, or 02.
          8        ???  (Allways 0E)
          9...C    Position and size of window
                    for loading the picture in.
          D...11   Colors. (Copy of memory range
                    $2C4...$2C8)
          12, 13   Length of the whole file -1
          14...1A  ???  (Allways 00 00 9B 9B 9B
                         9B A2)
          ---------------------------------------
          
          Position and size of window are defined by four bytes: Starting
          X-position (in bytes - NOT in pixels!), ending X-position (The
          first position AFTER the picture), starting Y-position, and
          ending Y-position.
          The KOALA program uses allways 00 28 00 C0 (the whole screen)
          while saving a picture, but there can be files with only parts
          of the screen - original KOALA can load them.
         
          Three compression methods can be used (see byte 7 of the
          header). 00 is without of compression - the rest of the file
          (after header) contains directly the screen-memory. (But don't
          forget that it needn't to be the whole screen - see above.)
          01 is the most common method. It contains packed data, which
          will be placed on screen in well known "vertical" order: First
          bytes of lines 0, 2, 4, 6 etc., then first bytes of lines 1, 3,
          5, 7 etc., and then next columns in the same way.
          Method 02 contains packed data too, but they will be placed on
          the screen in normal order - the same as method 00.
          
          The format of packed data is simple. There are two types of
          entries:
          - Non-packed data. The first byte has "1" in the bit D7 (128),
          rest of this byte is length of the data block (max. 127). If
          this length is zero, then there are two bytes more - they are
          the actual length (16 bits - High byte first!). Next bytes are
          data.
          - Packed data. The first byte has "0" in the bit D7, the rest is
          the length - the same as described above. There is only one
          data-byte, which will fill all the bytes in the block.
          
          You can also look at the example below. (All the entries will
          make two bytes with value FF.) There is the example:
          82 FF FF        ;Non-packed block
          80 00 02 FF FF  ;Long non-packed block
          02 FF           ;Packed block
          00 00 02 FF     ;Long packed block
          
          The trouble is that most of "Koala loaders" can load only files
          with standard length of header ($1B), with compression method
          01, and with the whole screen. Simply: Most of loaders supports
          only one thing from the header: Color bytes!
          
          Another trouble is that there are mistakes in the KOALA
          MICROILLUSTRATOR program itself! Yes! I found three mistakes
          while cracking it:
          - It can't load files with a long headers. (There is a mistake
          in the program, so it'll skip one byte more.) You need to change
          bytes at adress $4AA0 from 20 F8 48 A5 8C D0 04 C6 8D 30 05 C6
          8C to A5 8C D0 04 C6 8D 30 08 C6 8C 20 F8 48 to repair this.
          - With compression method 00 (no compression) it'll allways load
          the whole screen - never mind the X/Y ranges from the header.
          (There isn't any simple correction for this, but it isn't very
          fatal mistake.)
          - With compression method 00 (no compression) it'll save the
          screen in a wrong way: It'll add lots of nonsences before the
          picture-data, so the file will be very long (I think that it was
          about 30 kB!), and it's impossible to load such a file back.
          (Because the loader is reading the begin of the file, where are
          nonsences...) To repair this (most fatal) bug, you need to
          change the byte at adress $4981 from C9 to C0.
          
          And now a little test. It'll show which KOALA loaders are good,
          and which are not.
          We'll make three KOALA files. The first one can be any picture
          which is in the common "vertical loading" format.
          Load the KOALA MICROILLUSTRATOR program, and paint large
          horizontal lines on the screen. (For example two scanlines full
          of a color, two empty scanlines, and so on...) Save it on the
          disk - it's the second file.
          For the third file we'll make a little BASIC program:
          10 OPEN #1,8,0,"D:PICTURE":FOR A=1 TO 7684:PUT #1,PEEK
          (53770):NEXT A:CLOSE #1:END
          This program will make a Micropainter-file with random
          (non-packable) contents. Then load KOALA MICROILLUSTRATOR (With
          the correction of the third mistake - see above), switch to the
          picture with SPACE BAR (this is necessary because of another bug
          in the program), and press "<" key. Your random picture will
          appear. Paint only a few lines on this screen (we'll see if is
          it displayed correctly then), and save it as the third file.
          Now try to load these files with several loaders, which you
          have. The first file will work well with every loaders, but the
          second and third file will be displayed correctly only by really
          good loaders. Personally I have only two good loaders: The
          original KOALA, and the one written by me...
          
          And there is the end of this article!
          
          Editor's note: where?